SNR-OR-114-09V2   Optical Receiver

SNR-OR-114-09V2 is our latest high-class CATV network optical receiver. This equipment adopts GaAs MMIC amplify module. Optimization circuit design, coupled with the company 10 years professional design experience, makes the equipment achieve high performance index. The parameters will be displayed by singlechip to make engineering debug be more convenient. It is the best choice for CATV network.

Ⅰ. Performance Characteristics

- Excellent optical AGC control technique, when the input optical power range is －9～＋2dBm, the output lever, CTB and CSO basically unchanged;

- Two-way optical signal receiving, back up each other， arbitrarily set the auto-switching conditions and can also be set to manual switch;

- Downlink working frequency extended to 1GHz, RF amplifier part adopts the high performance low power consumption GaAs chip, the highest output level up to 108 dBuv;

- EQ and ATT both use the professional electric control circuit, makes the control more accurate, operation more convenient;

- Built-in the national standard II class network management transponder, support remote network management (optional);

- Compact structure, convenient installation, is the first choice equipment of FTTB CATV network;

- Built-in high reliability low power consumption power supply;

II. Technical Parameter

| Item | Unit | Technical Parameter |
| --- | --- | --- |
| Optical Parameter |
| Model |  | SNR-OR-114-09V2 |
| Receive Optical Power | dBm | -9 ~ +2 |
| Optical Return Loss | dB | >45 |
| Optical Receiving Wavelength | nm | 1100 ~ 1600 |
| Connector Type |  | SC/APC or specified by the user |
| Fiber Type |  | Single Mode |
| Link Parameter |
| C/N | dB | ≥ 51 | EQ 6dB， Output level 108 dBμV 42-channel signal source input, -2dBm optical power received |
| C/CTB | dB | ≥ 60 |  |
| C/CSO | dB | ≥ 60 |  |
| RF Parameter |
| Frequency Range | MHz | 45 ~1000 |
| Flatness in Band | dB | ±0.75 |
| Rated Output Level | dBμV | ≥ 108 |
| Max Output Level | dBμV | Optical AGC-9dBm—+2dBm时≥ 110 | Optical AGC-7dBm—+2dBm时≥ 114 |
| Output Return Loss | dB | ≥16 |
| Output Impedance | Ω | 75 |
| Optical AGC range |  | （-9dBm/-8dBm /-7dBm /-6dBm /-5dBm /-4dBm）—(+2dBm) adjustable |
| Electrical control EQ range | dB | 0～15 |
| Electrical control ATT range | dBμV | 0～15 |
| Generic characteristic |
| Power Voltage | V | AC（150~265）V |
| Operating Temperature | ℃ | -40~60 |
| Consumption | VA | ≤8 |
| Dimension | mm | 190（L）* 110（W）* 52（H） |

III. Block Diagram

IV. Relation Table of Input Optical Power and CNR

V. Function Display and Operating Instruction

  - Mode: Mode selection button, a total of twelve modes, presses the mode selection button to enter the corresponding status display, twelve modes to cycle.

The following is the detailed instructions：