MEMO UPS Software Upgrade SOP

- Choose the target chip address (normally just use the default value is ok).

- Choose the target file to download.

- Set the communication.

3.1. Choose COM.

Choose COM according to the rear computer port name. For example, my (engineer) computer displays COM5 after the USB connect with UPS. (Make sure the port number is between COM1—COM9 when choose it.) The way to check the port name: my computer--- devmgmt.msc---port (COM & LPT). Below picture shows the details, but our computer are in Chinese.

3.2 Delay value set

The bigger this delay value is, the slower the programming process is, but the more stable it is. If it interrupts during the first equipment programming, then we should set this value bigger. Normally 2-5 is ok.

After the setting, press “Open Device” button.

( Only for the first installation “ToBin” button must be pushed and continue after appearing OK message. )

- Download file.

  - CASE 1:

Normally press “Update” after choosing the target file to start the programming.

  - CASE 2:

If the programming process interrupts, turn off the UPS equipment and turn on again, and then press “Re-Update”.

- Programming process.

。Messages window will display the current programming data.

Progress bar will show the completion percent.

NOTE: This process is a bit log, pls wait patiently. Normally it’s 5min around.

- Programming finished.

It will show the programming result.

- Cautions:

(1). If the programming process is interrupted, turn off the UPS equipment and turn on again, then press “Re-Update” and waiting for the process finished.

（2）Before programming the UPS, pls turn the UPS in Bypass mode.

Kstar Engineering

2013-10-30