Network Management Configuration Commands

Table of Contents

Chapter 1 Network Management Configuration Commands	1

1.1 SNMP Commands	1

1.1.1 snmp-server community	2

1.1.2 snmp-server contact	3

1.1.3 snmp-server engineID local	4

1.1.4 snmp-server group	5

1.1.5 snmp-server [host|hostv6]	6

1.1.6 snmp-server location	8

1.1.7 snmp-server packetsize	9

1.1.8 snmp-server queue-length	10

1.1.9 snmp-server trap-source	11

1.1.10 snmp-server trap-timeout	12

1.1.11 snmp-server user	13

1.1.12 snmp-server view	14

1.1.13 snmp-server source-addr	15

1.1.14 snmp-server udp-port	16

1.1.15 snmp-server encryption	17

1.1.16 snmp-server trap-add-hostname	18

1.1.17 snmp-server trap-logs	18

1.1.18 snmp-server set-snmp-dos-max	19

1.1.19 snmp-server keep-alive	20

1.1.20 snmp-server necode	21

1.1.21 snmp-server event-id	21

1.1.22 snmp-server getbulk-timeout	22

1.1.23 snmp-server getbulk-delay	23

1.1.24 show snmp	24

1.1.25 debug snmp	27

1.2 RMON Configuration Commands	30

1.2.1 rmon alarm	30

1.2.2 rmon collection stats	31

1.2.3 rmon collection history	32

1.2.4 rmon event	33

1.2.5 show rmon	34

# Network Management Configuration Commands

## SNMP Commands

SNMP commands are listed below:

- snmp-server community

- snmp-server contact

- snmp-server engineID local

- snmp-server group

- snmp-server host/hostv6

- snmp-server location

- snmp-server packetsize

- snmp-server queue-length

- snmp-server trap-source

- snmp-server trap-timeout

- snmp-server user

- snmp-server view

- snmp-server source-addr

- snmp-sever udp-port

- snmp-server encryption

- Snmp-server trap-add-hostname

- snmp-server trap-logs

- snmp-server set-snmp-dos-max

- snmp-server keep-alive

- snmp-server encode

- snmp-server event-id

- show snmp

- debug snmp

### snmp-server community

Syntax

To set the community access string of the accessible SNMP protocol, run snmp-server community in global configuration mode.

snmp-server community [0|7] string [view view-name] [ro | rw] [word]

no snmp-server community string

no snmp-server community

Parameter

| Parameter | Description |
| --- | --- |
| 0 | Sets the community string of the text., |
| 7 | Sets the encrypted public string of the text. |
| string | Means the community string of the accessible SNMP protocol, which is similar to the password. |
| view view-name | (optional) stands for the previously defined view's name. In this view, the MIB objects, which are effective to the community, are defined. |
| ro | (Optional) Designates the read-only permission. Those authorized workstations can only read the MIB objects. |
| rw | (Optional) Designates the read-write permission. Those authorized workstations can read and modify the MIB objects. |
| word | (optional) Specifies the name of IP ACL of the SNMP proxy, which can be accessed by the community string. |

Default value

By default, the SNMP community string allows the read-only permission to all objects.

Command mode

Global configuration mode

Usage guidelines

The following command shows how to delete a designated community.

no snmp-server community string

The following command shows how to delete all communities.

no snmp-server community

Example

The following example shows how to distribute the “comaccess” string to SNMP, allow the read-only access and designate IP ACL to use the community string.

snmp-server community comaccess ro allowed

The following example shows how to distribute the “mgr” string to SNMP, allow to read and write the objects in the Restricted view。

snmp-server community mgr view restricted rw

The following example shows how to delete the “comaccess” community.

no snmp-server community comaccess

Related command

access-list

snmp-server view

### snmp-server contact

Syntax

To set the information about the contact person in a management node, run snmp-server contact text.

snmp-server contact text

no snmp-server contact

Parameter

| Parameter | Description |
| --- | --- |
| text | Means the string of the information about the contact person. |

Default value

The information about contact person is not set.

Command mode

Global configuration mode

Usage guidelines

It corresponds to the sysContact of the MIB variable in the System group.

Example

The following example shows the information about the contact person in a node.

snmp-server contact Dial_System_Operator_at_beeper_#_27345

### snmp-server engineID local

Syntax

To configure SNMP engineID of the local agent, run the following command. To return to the default setting, use the no form of this command.

snmp-server engineID local engineID

no snmp-serverr engineID local engineID

Parameter

| Parameter | Description |
| --- | --- |
| engineID | SNMP engine ID |

Default value

No setting.

Command mode

Global configuration mode

Usage guidelines

The command is used to configure the SNMP engine ID of the local agent.

Example

snmp-server engineID local 80000cf80300e00f3f56e3

### snmp-server group

Syntax

To create or update a SNMP group in global configuration mode, run the following first command; to cancel this SNMP group, run the following second command.

snmp-server group [groupname { v3 [auth | noauth | priv]}][read readview][write writeview] [notify notifyview] [access access-list]

Parameter

| Parameter | Description |
| --- | --- |
| groupname | Stands for the name of the created or modified SNMP group. |
| v3 | Means the version ID of the SNMP protocol. |
| auth¦noauth¦priv | Stands for the lowest security level of users in the SNMPv3 group. |
| readview | Means the access permission of GET operations, which is defined by the view. |
| writeview | Means the access permission of SET operations, which is defined by the view. |
| notifyview | Stands for the access permission during the transmission of Trap packets, which is defined by the view. |
| access-list | Allows users in the SNMP group to get through the IP access control list. |

Default value

The readview allows all leaves of the Internet sub-tree to be accessed.

Command mode:

Global configuration mode

Usage guidelines

The SNMP group is used to designate the access permission of the users in this group.

Example

In the following example, an SNMP group is set and named as setter, the version ID of the SNMP protocol is 3, the security level is authentication and encryption, and the view that is accessed by the set operation is v-write.

snmp-server group setter v3 priv write v-write

Related command

snmp-server view

snmp-server user

### snmp-server [host|hostv6]

Syntax

To specify the receiver of SNMP trap operation, run the first of the following commands in global configuration mode. To cancel this designated host, run the following second command.

snmp-server host|hostv6 host [vrf word] [udp-port port-num] [permit|deny event-id] {{version [v1 | v2c | v3]} | {[informs | traps] | [auth |noauth]}} community-string/user [authentication |  configure| snmp]

no snmp-server host host community-string

Parameter

| Parameter | Description |
| --- | --- |
| host¦hostv6 | Sets the IPv4 or IPv6 host. |
| host | Means the host’s name or the address of the Internet. |
| [vrf word] | (Optional) binds VRF. |
| [udp-port port-num] | (Optional) Specifies the ID of the UDP port, which transmits the traps. |
| [permit¦deny event-id] | (Optional) Allows or blocks to transmit a designated event. |
| {version [v1¦v2c¦v3]} | (Optional) Means the version ID of the SNMP protocol, which is used to transmit traps. |
| [informs ¦ traps] | (Optional) Specifies the type of trap for version V2C. Informs: means the type of trap is “informs”. Traps: means the type of trap is “traps”. |
| [auth ¦noauth] | Specifies the trap authentication mode for version V3. auth: authentication noauth: no authenticatication |
| community-string/user | Means a community string in version 1 and version 2c which is similar to the password and sent with the trap operations or means the username in version 3. |
| [authentication ¦ configure¦ snmp] | (optional) if no trap is designated, all generated traps will be sent to the host. authentication: allows to transmit those authentication-error traps. configure: allows to transmit the SNMP-configure traps. snmp: allows to transmit the SNMP traps. |

Default value

This command is invalid in default settings. That is to say, no trap will be sent by default.

Command mode

Global configuration mode

Usage guidelines

If this command is not entered, the traps will not be sent. In order to enable a switch to send the SNMP traps, you must run snmp-server host. If the keyword “trap-type” is not contained in this command, all kinds of traps of this host will be activated. If the keyword “trap-type” is contained in this command, all trap types related with this keyword are activated. You can specify multiple trap types in this command for each host.

If you designate multiple snmp-server host commands on the same host, the SNMP trap messages that are sent to the host will be decided by the community string and the trap type filtration in this command. (Only one trap type can be configured for a same host and a same community string).

The availability of the trap-type option depends on the switch type and the attributes of routing software, which is supported by this switch.

Example

The following example shows how to transmit the RFC1157-defined SNMP traps to host 10.20.30.40. The community string is defined as comaccess.

snmp-server host 10.20.30.40 comaccess snmp

The following example shows that the switch uses the public community string to send all types of traps to host 10.20.30.40.

snmp-server host 10.20.30.40 public

The following example shows that only the authentication traps are effective and can be sent to host bob.

snmp-server host bob public authentication

Related command

snmp-server queue-length

snmp-server trap-source

snmp-server trap-timeout

snmp-server event-id

snmp-server user

### snmp-server location

Syntax

To set the location string of a node, run the first one of the following two commands in global configuration mode. To cancel this location string, run the following second command.

snmp-server location text

no snmp-server location

Parameter

| Parameter | Description |
| --- | --- |
| text | Describes the location string of a node. |

Default value

The location string of a node is not set by default.

Command mode

Global configuration mode

Usage guidelines

It corresponds to the sysLocation of the MIB variable in the System group.

Example

The following example shows how to define the actual location of a switch.

snmp-server location Building_3/Room_214

Related command

snmp-server contact

### snmp-server packetsize

Syntax

To define the maximum size of the SNMP packet when the SNMP server receives requests or responds, run the following first command in global configuration mode.

snmp-server packetsize byte-count

no snmp-server packetsize

Parameter

| Parameter | Description |
| --- | --- |
| byte-count | Stands for the integer bytes between 484 and 17940. The default value is 3000 bytes. |

Default value

3000 byte

Command mode

Global configuration mode

Usage guidelines

It corresponds to the sysLocation of the MIB variable in the System group.

Example

The following example shows how to set up a filter to filter those packets whose maximum length is 1024 bytes.

snmp-server packetsize 1024

Related command

snmp-server queue-length

### snmp-server queue-length

Syntax

To set the queue length for each trap host, run the following first command in global configuration mode.

snmp-server queue-length length

no snmp-server queue-length

Parameter

| Parameter | Description |
| --- | --- |
| length | Stands for the number of trap events which can be saved in the queue (1-1000). |

Default value

10 trap events.

Command mode

Global configuration mode

Usage guidelines

This command is used to set the queue length for each trap host. Once the trap messages are successfully transmitted, the switch will empty the queue.

Example

The following example shows how to set up a message queue which can capture four events.

snmp-server queue-length 4

Related command

snmp-server packetsize

### snmp-server trap-source

Syntax

To designate an interface to be the source address of all traps, run the following first command in global configuration mode. To cancel this interface, run the following second command.

snmp-server trap-source interface

no snmp-server trap-source

Parameter

| Parameter | Description |
| --- | --- |
| interface | Stands for the interface where SNMP traps generate. The parameters include the interface type and interface ID of the syntax mode of specific platform. |

Default value

The interface is not designated.

Command mode

Global configuration mode

Usage guidelines

When the SNMP server sends out a SNMP trap on whichever interface, the SNMP trap shall carry a trap address. If you want to use the trap address for tracking, you can use this command.

Example

The following example shows how to designate interface vlan1 as the source address of all traps.

snmp-server trap-source vlan1

Related command

snmp-server queue-length

snmp-server host

### snmp-server trap-timeout

Syntax

To set the timeout value of retransmitting traps, run the following first command in global configuration mode.

snmp-server trap-timeout seconds

no snmp-server trap-timeout

Parameter

| Parameter | Description |
| --- | --- |
| seconds | Means an interval for retransmitting traps, whose unit is second (1-1000). |

Default value

30 seconds

Command mode

Global configuration mode

Usage guidelines

Before switch software tries to send traps, it is used to look for the route of destination address. If no routes exists, traps will be saved in the retransmission queue. The server trap-timeout command decides the retransmission interval.

Example

The following example shows how to set the retransmission interval to 20 seconds:

snmp-server trap-timeout 20

Related command

snmp-server host

snmp-server queue-length

### snmp-server user

Syntax

To create or update an SNMP user in global configuration mode, run the following first command; to cancel this SNMP user, run the following second command. If the remote parameter is designated, a remote user will be configured; when a remote user is configured, the SNMP engine ID that corresponds to the IP address of this management station must exist.命令格式如下

snmp-server user username groupname { v3 [ encrypted | auth ] [ md5 | sha ] auth-password }

Parameter

| Parameter | Description |
| --- | --- |
| username | Stands for the name of the created or modified SNMP user. |
| groupname | Stands for the group where the user is. |
| v3 | Stands for the SNMP version. |
| [ encrypted ¦ auth ] | Encryption type: Encrypted: packet encryption auth: packet authentication |
| [ md5 ¦ sha ] | Means the method of encryption authentication. |
| auth-password | Stands for the authentication password of the user. If this password is localized, it will be used as the authentication key and the encryption key of SNMPv3. |

Default value

N/A

Command mode

Global configuration mode

Usage guidelines

This command is used to set the username and the password.

Example

In the following example, an SNMP user is created, whose name is set-user and which belongs to group setter, the version of the SNMP protocol is version 3, the security level is authentication and encryption, the password is 12345678, and MD5 is used as the harsh algorithm.

snmp-server user set-user setter v3 encrypted auth md5 12345678

Related command

snmp-server view

snmp-server group

### snmp-server view

Syntax

To create or update a MIB view, run the first one of the following two commands in global configuration mode. To cancel a view in the SNMP server, run the second one of the following two commands.

snmp-server view view-name oid-tree {included | excluded}

no snmp-server view view-name

Parameter

| Parameter | Description |
| --- | --- |
| view-name | Updates or creates the label of a view. |
| oid-tree | Means the object IDs of the ASN.1 sub-tree that must be contained or excepted from a view. The identifier sub-tree is used to designate a numeral-contained string, e.g., 1.3.6.2.4 or a system sub-tree. The sub-tree name can be found in all MIB trees. |
| included ¦ excluded | Means the view type. The parameter “included” or “excluded” must be specified. |

Default value

N/A

Command mode

Global configuration mode

Usage guidelines

If other SNMP commands need a view as a parameter, you can use this command to create a view. By default, you need not define the view and you can see all the views, equivalent to Cisco-predefined everything views.

Example

The following example shows how to create the views of all objects in the MIB-II sub-tree.

snmp-server view mib2 mib-2 included

The following example shows how to create the views of all objects, including those objects in the system group.

snmp-server view phred system included

The following example shows how to create the views of all objects that includes the objects in the system groups but excludes the objects in system7 and interface 1.

snmp-server view agon system included

snmp-server view agon system.7 excluded

Related command

snmp-server community

### snmp-server source-addr

Syntax

To specify a source address for answering all SNMP requests, run the second one of the following two commands in global configuration mode. To cancel this address, run the second one of the following commands.

snmp-server source-addr a.b.c.d

no snmp-server source-addr

Parameter

| Parameter | Description |
| --- | --- |
| a.b.c.d | Means the source address for all SNMP requests to be answered. |

Default value

The default source address is the nearest routing address.

Command mode

Global configuration mode

Usage guidelines

When the SNMP server transmits an SNMP request, you can run this command to designate a special source address.

Example

The following example shows how to designate the IP address “1.2.3.4” of the designated interface as the source address of all SNMP packets.

snmp-server source-addr 1.2.3.4

Related command

N/A

### snmp-server udp-port

Syntax

To specify the port number for the SNMP agent to receive packets, run the following first command in global configuration mode.

snmp-server udp-port portnum

no snmp-server udp-port

Parameter

| Parameter | Description |
| --- | --- |
| udp-port | Stands for the ID of the destination port to which SNMP traps are sent, which cannot be a command port ID. |

Default value

It is the listening port of SNMP agent by default, that is, port 162.

Command mode

Global configuration mode

Usage guidelines

The SNMP agent will listen to this port when SNMP server transmits SNMP packets.

Example

The following example shows how to specify the listening port of SNMP agent to port 1234.

snmp-server udp-port 1234

Related command

N/A

### snmp-server encryption

Syntax

To display the configured SNMP community, the SHA encryption password and the MD5 encryption password, run snmp-server encryption in global mode. This command is a once-for-all command, which cannot be saved or canceled by its negative form.

snmp-server encryption

Parameter

N/A

Default value

The default settings is to display the SNMP community, the SHA encryption password and the MD5 encryption password in plain text.

Command mode

Global configuration mode

Usage guidelines

This command is used to display the SNMP community, the SHA encryption password and the MD5 encryption password in plain text. In this way, the security of the password is guaranteed.

Example

The following example shows how to show in the plain text the SNMP community, the SHA encryption password and the MD5 encryption password, which are set for host 90.0.0.3.

snmp-server encryption

Related command

snmp-server community

snmp-server user

### snmp-server trap-add-hostname

Syntax

snmp-server trap-add-hostname

no snmp-server trap-add-hostname

Parameter

None

Default value

None

Command mode

Global configuration mode

### snmp-server trap-logs

Syntax

snmp-server  trap-logs

no snmp-server  trap-logs

Parameter

The command has no parameters or keywords.

Command mode

Global configuration mode

### snmp-server set-snmp-dos-max

Syntax

To set the incorrect community login retry times in five minutes on the SNMP server, run the first one of the following two commands.

snmp-server   set-snmp-dos-max retry times

no snmp-server set-snmp-dos-max

Parameter

The retry times parameter stands for the login times for a user to conduct the incorrect community login in five minutes.

Default value

The incorrect community login times is not limited.

Command Mode

Global configuration mode

Usage guidelines

This command can be used to prevent those SNMP host from guessing the device’s community viciously, which lessening unnecessary CPU consumption of the device.

Example

The following example shows how to set the maximum retry times in five minutes to 10:

Router_config# snmp-server set-snmp-dos-max 10

### snmp-server keep-alive

Syntax

To set the interval for a device to send the heart-beat trap, run the first one of the following two commands in global mode.

snmp-server keep-alive times

no snmp-server keep-alive

Parameter

| Parameter | Description |
| --- | --- |
| times | Stands for the interval of transmitting heart-beat traps. |

Default value

This command does not exist in the default settings and the heart-beat traps are not sent.

Command Mode

Global configuration mode

Usage guidelines

This command is used together with the snmp-server host command.

Example

The following example shows how to set the heart-beat traps to be transmitted every 3 seconds.

snmp-server keep-alive 3

Related Command

snmp-server host

snmp-server hostv6

### snmp-server necode

Syntax

To set  the  management node  (unique device  ID),  run  the  first  one  of  the  following two commands in global mode.

snmp-server necode text

no snmp-server necode

Parameter

| Parameter | Description |
| --- | --- |
| text | Stands for the information of the management node (unique device ID). |

Default value

The management node is not set.

Command Mode

Global configuration mode

Usage guidelines

It corresponds to the value of the private SNMP MIB variable.

Example

The following example shows how to set the information about a management node.

snmp-server necode Dial_System_Operator_at_beeper_#_27345

### snmp-server event-id

Syntax

To create and set the event list, run the first one of the following two commands in global mode.

snmp-server event-id number trap-oid oid

no snmp-server event-id number [trap-oid oid]

Parameter

| Parameter | Description |
| --- | --- |
| number | Stands for the unique code of event ID. |
| oid | Stands for the trap OID which is contained by the event ID. |

Default value

The event list is not set.

Command Mode

Global configuration mode

Usage guidelines

It is used in the host configuration.

Example

The following example shows how to configure an event list by setting a trap OID from

1.2.3.4.5 to event ID 1:

snmp-server event-id 1 trap-oid 1.2.3.4.5

### snmp-server getbulk-timeout

Syntax

To set the maximum timeout time of GetBulk request, run the first one of the following two commands in global mode.

snmp-server getbulk-timeout seconds

no snmp-server getbulk-timeout

Parameter

| Parameter | Description |
| --- | --- |
| seconds | Stands for the maximum timeout time for handling the GetBulk request. |

Default value

The maximum timeout time for handling the GetBulk request is not set.

Command Mode

Global configuration mode

Usage guidelines

This command is used to set the maximum timeout time of GetBulk request. If the system cannot handle over all GetBulk requests in this timeout time, the existing result will be directly returned.

Example

The following example shows how to set the GetBulk-timeout list and how to set the maximum timeout time to 5 seconds.

snmp-server getbulk-timeout 5

### snmp-server getbulk-delay

Syntax

To prevent SNMP occupying too much CPU when the SNMP agent handles the getbulk requests, you  need  to  set  the  getbulk  delay  by  using  the  first  one  of  the  following two commands.

snmp-server getbulk-delay ticks

no snmp-server getbulk-delay

Parameter

| Parameter | Description |
| --- | --- |
| ticks | Sets the CPU interval when GetBulk requests are handled. |

Default value

When CPU handles the Getbulk requests in its full load, the CPU interval is not employed.

Command Mode

Global configuration mode

Usage guidelines

When the SNMP agent handles the Getbulk requests, SNMP may occupy too much CPU. In this case, you need to set the getbulk-delay.

Example

The following example shows how to set the getbulk-delay to 1.

snmp-server getbulk-delay 1

### show snmp

Syntax

To monitor SNMP output and input, run show snmp. To display the information of SNMP engine information, run show snmp engineID. To display the information about the SNMP trap host, run show snmp host. To display the SNMP views, run show snmp view. To display the MIB registration, run show snmp mibs. To display the SNMP groups, run show snmp group. To display the SNMP users, run show snmp user.

show snmp [engineID |host | view | mibs |group|user]

Parameter

| Parameter | Description |
| --- | --- |
| engineID | Displays SNMP engine. |
| host | Displays the SNMP trap host. |
| View | Displays the SNMP views. |
| mibs | Displays the SNMP MIB registration. |
| group | Displays the SNMP groups. |
| user | Displays the SNMP users. |

Default value

None

Command Mode

EXEC or global configuration mode

Usage guidelines

The show snmp command is used to list out the SNMP output and input statistics.

The show snmp engineID command is used to display the information about SNMP engine.

The show snmp host command is used to display the information about the SNMP trap host.

The show snmp view command is used to display the SNMP views.

The show snmp mibs command is used to display the MIB registration information.

The show snmp group command is used to display the SNMP groups.

The show snmp user command is used to display the SNMP users.

Example

The following example shows how to list out the SNMP output/input statistics.

Switch#show snmp

37 SNMP packets input

0 Bad SNMP version errors

4 Unknown community name

0 Illegal operation for community name supplied

0 Snmp encoding errors

24 Number of requested variables

0 Number of altered variables

0 Get-request PDUs

28 Get-next PDUs

0 Set-request PDUs

78 SNMP packets output

0 Too big errors (Maximum packet size 1500)

0 No such name errors

0 Bad values errors

0 General errors

24 Get-response PDUs PDUs

13 SNMP trap PDUs

The following list shows the meanings of all the domains in the above-mentioned information about the packets transmitted and received by the SNMP agent.

| Displayed Information | Meaning |
| --- | --- |
| Unknown community name | Stands for an unidentifiable community name. |
| Illegal operation for community name supplied | Stands for illegal operations. |
| Encoding errors | Stands for the incorrect encode. |
| Get-request PDUs | Stands for the Get-Request packet. |
| Get-next PDUs | Stands for the Get-Next packet. |
| Set-request PDUs | Stands for the Set-Request packet. |
| Too big errors | Means that the related packet is too much to respond to. |
| No such name errors | Means that no designated instance exists. |
| Bad values errors | Means that the configured value type is wrong. |
| General errors | Means general errors. |
| Get-response PDUs | Stands for the Get-Response packets. |
| Trap PDUs | Stands for the SNMP trap packets. |

The following example displays the SNMP trap host.

Switch#show snmp host

Notification host: 192.2.2.1    udp-port: 162   type: trap

user: public     security model: v1

The following example displays the SNMP views.

Switch#show snmp view

mib2    mib-2   -       included        permanent       active

Related Command

snmp-server host

snmp-server view

### debug snmp

Syntax

To displays SNMP events, packet transmission/reception and packet errors, run the following command.

debug snmp [ error | event | packet ]

no debug snmp [ error | event | packet ]

Parameter

| Parameter | Description |
| --- | --- |
| error | Enables the debugging switch of the SNMP event. |
| event | Enables the debugging switch of the SNMP events. |
| packet | Enables the debugging switch of SNMP input/output packets. |

Command Mode

EXEC

Usage guidelines

After the SNMP debugging switch is enabled, the SNMP events, packet transmission and reception and errors are displayed, which will help users to diagnose SNMP troubles.

Example

The following example shows how to debug SNMP packets.

switch#debug snmp packet

Received 49 bytes from 192.168.0.29:1433

0000: 30 82 00 2D  02 01 00 04  06 70 75 62  6C 69 63 A0    0..-.....public.

0016: 82 00 1E 02  02 7D 01 02  01 00 02 01  00 30 82 00    .....}.......0..

0032: 10 30 82 00  0C 06 08 2B  06 01 02 01  01 03 00 05    .0.....+........

0048: 00                                                    .

Sending 52 bytes to 192.168.0.29:1433

0000: 30 82 00 30  02 01 00 04  06 70 75 62  6C 69 63 A2    0..0.....public.

0016: 82 00 21 02  02 7D 01 02  01 00 02 01  00 30 82 00    ..!..}.......0..

0032: 13 30 82 00  0F 06 08 2B  06 01 02 01  01 03 00 43    .0.....+.......C

0048: 03 00 F4 36                                           ...6

Received 51 bytes from 1192.168.0.29:1434

0000: 30 82 00 2F  02 01 00 04  06 70 75 62  6C 69 63 A0    0../.....public.

0016: 82 00 20 02  02 6B 84 02  01 00 02 01  00 30 82 00    .. ..k.......0..

0032: 12 30 82 00  0E 06 0A 2B  06 01 02 01  02 02 01 02    .0.....+........

0048: 01 05 00                                              ...

Sending 62 bytes to 192.168.0.29:1434

0000: 30 82 00 3A  02 01 00 04  06 70 75 62  6C 69 63 A2    0..:.....public.

0016: 82 00 2B 02  02 6B 84 02  01 00 02 01  00 30 82 00    ..+..k.......0..

0032: 1D 30 82 00  19 06 0A 2B  06 01 02 01  02 02 01 02    .0.....+........

0048: 01 04 0B 45  74 68 65 72  6E 65 74 30  2F 31          ...Ethernet0/1

| Domain | Description |
| --- | --- |
| Received | SNMP received packets |
| 192.168.0.29 | Source IP address |
| 1433 | Port ID of the source address |
| 51 bytes | Length of the received packet |
| 30 82 00 2D 02 01 00 04 06 70 75 62 6C 69 63 A0 82 00 1E 02 02 7D 01 02 01 00 02 01 00 30 82 00 10 30 82 00 0C 06 08 2B 06 01 02 01 01 03 00 05 00 | Packets encoded by SNMP ASN |
| 0..-.....public. .....}.......0.. .0.....+........ . | ASCII code presentation of packet receptionThose out of the range of ASCII code presentation are shown as “.”. |
| sending | SNMP-transmitted packet |
| 192.168.0.29 | Destination IP address |
| 1433 | Port ID of the destination address |
| 52 bytes | Length of the transmitted packet |
| 30 82 00 30 02 01 00 04 06 70 75 62 6C 69 63 A2 82 00 21 02 02 7D 01 02 01 00 02 01 00 30 82 00 13 30 82 00 0F 06 08 2B 06 01 02 01 01 03 00 43 03 00 F4 36 | Packets encoded by SNMP ASN |
| 0..0.....public. ..!..}.......0.. .0.....+.......C ...6 | ASCII code presentation of packet transmission Those out of the range of ASCII code presentation are shown as “.”. |

The following example shows how to debug SNMP events.

switch#debug snmp event

Received SNMP packet(s) from 192.2.2.51

SNMP: GETNEXT request

-- ip.ipReasmFails.0

SNMP: Response

>> ip.ipFragOKs.0 = 1

Received SNMP packet(s) from 192.2.2.51

SNMP: GETNEXT request

-- ip.ipFragOKs.0

SNMP: Response

>> ip.ipFragFails.0 = 0

Received SNMP packet(s) from 192.2.2.51

SNMP: GETNEXT request

-- ip.ipFragFails.0

SNMP: Response

>> ip.ipFragCreates.0 = 2

| Domain | Description |
| --- | --- |
| SNMP | Currently debugged SNMP |
| GETNEXT request | SNMP GetNext request |
| RESPONSE | SNMP response |
| -- | Received packet |
| >> | Transmitted packet |
| ip.ipReasmFails.0 | MIB OID that is accessed by the request |
| ip.ipFragOKs.0 = 1 | Accessed MIB OID and its return value |

## RMON Configuration Commands

Configuration commands include:

- rmon alarm

- rmon event

- show rmon

### rmon alarm

Syntax

rmon alarm index variable interval {absolute | delta} rising-threshold value

[eventnumber] falling-threshold value [eventnumber] [repeat] [owner string]

To configure an RMON alarm entry, run the above-mentioned command.

Parameter

| Parameter | Description |
| --- | --- |
| index | Means the index of event entries. Value range: 1-65535 |
| variable | Means those to-be-monitored objects. Value range: OID of the tested object |
| interval | Means the sampling interval. Range: 1-2147483647 seconds |
| value | Means the alarm threshold. Range: minus 2147483648-2147483647 |
| eventnumber | Means the event index which is triggered when the threshold is reached. Range: 1-65535 |
| repeat | Means those events that are allowed to be triggered repeatedly. |
| string | Means the description of the holder. Value range: 1-31 |

Default value

Eventnumber is not set by default.

repeat is not set by default.

Usage guidelines

This command is configured in global mode and it is used to monitor the value of a designated object. If the value surpasses the threshold, the designated event will be triggered.

Example

The following example shows that an alarm entry is set, the monitored object is ifInOctets.2, the sampling interval is 10, event 1 is triggered when the value excesses 15, and event 2 is triggered when the value declines more than 25.

rmon alarm 1 1.3.6.1.2.1.2.2.1.10.2 10 absolute rising-threshold 15 1 falling-threshold 25 2 repeat owner switch

### rmon collection stats

Syntax

To set rmon statistics function, run the following command.

rmon collection stats  index [owner string]

Parameters

| Parameters | Description |
| --- | --- |
| index | Stands for the index of the statistics entry. Value range: 1~65535. |
| string | Stands for the owner character string. Value range: the length of the character string is 1~31. |

Default Value

None

Usage guidelines

The command must be configured in the interface mode.

Example

The following example shows how to enable the statistics function on gigabit Ethernet interface g0/1.

int g0/1

rmon collection stats 2 owner switch

### rmon collection history

Syntax

To configure a history control entry, run the following command.

rmon collection history  index [buckets bucket-number] [interval second] [owner owner-name]

Parameters

| Parameters | Description |
| --- | --- |
| index | index Value range: 1-65535 |
| bucket-number | The entry of all history record control entries nearest to the bucket-number need to be reserved. Value range: 1~65535. |
| second | Stands for the time interval. Value range: 1~3600. |
| owner-name | Stands for the owner character string. Value range: the length of the character string is 1~31. |

Default Value

The default bucket-number is 50 and the default second is 1800.

Usage guidelines

The command is used to configure in the interface mode. It is used for adding one entry to the history control table.

Example

The following example shows how to add the history control entry on the gigabit Ethernet interface g0/1 and save the statistics of latest 20 time intervals.(Each time interval is 10 seconds.)

int g0/1

rmon collection history 2 buckets 20 interval 10 owner switch

### rmon event

Syntax

rmon event index [description des-string] [log] [owner owner-string] [trap community] [ifctrl interface]

To configure an RMON event entry, run the above-mentioned command.

Parameter

| Parameter | Description |
| --- | --- |
| index | Means the index of event entries. Value range: 1-65535 |
| des-string | Stands for the character string of event’s description. Value range: 1-127 |
| owner-string | Means the character string of the holder. Value range: 1-31 |
| community | Means the community name during trap generation. Value range: 1-31 |
| interface | Designates a shutdown port that the event needs to control. |

Default value

None

Usage guidelines

This command is used to set an RMON event entry, which is used for alarming.

Example

The following example shows that an RMON event is set. The index of this RMON event is 6, the character string of its description is example, and when an event is triggered, an entry will be added to the log list and also a trap whose community name is public is generated.

rmon event 6 log trap public description example owner switch

### show rmon

Syntax

show rmon [alarm] [event] [statistics] [history]

To display RMON configuration, run the above-mentioned command.

Parameter

None

Default value

None

Usage guidelines

This command is used to display RMON configuration.

Example

The following example shows how to display RMON configuration.

show rmon