DHCP-Snooping Configuration Commands

# Table of Contents

DHCP-Snooping Configuration Commands	1

Table of Contents	I

Chapter 1 DHCP-Relay Snooping Configuration Commands	1

1.1.1 ip dhcp-relay snooping	2

1.1.2 ip dhcp-relay snooping vlan	2

1.1.3 ip dhcp-relay snooping vlan vlan_id max-client	3

1.1.4 ip dhcp-relay snooping database-agent	4

1.1.5 dhcp-relay snooping db-file	4

1.1.6 dhcp-relay snooping write-time	5

1.1.7 ip dhcp-relay snooping write-immediately	6

1.1.8 ip dhcp-relay snooping log	6

1.1.9 ip dhcp-relay snooping rapid-refresh-bind	7

1.1.10 dhcp-relay snooping information option	8

1.1.11 ip verify source vlan	8

1.1.12 ip arp inspection vlan	9

1.1.13 ip source binding	10

1.1.14 arp inspection trust	11

1.1.15 dhcp snooping trust	11

1.1.16 dhcp snooping deny	12

1.1.17 dhcp snooping information circuit-id	12

1.1.18 dhcp snooping information remote-id string	13

1.1.19 dhcp snooping information vendor-specific	14

1.1.20 dhcp snooping information append	15

1.1.21 dhcp snooping information drop	16

1.1.22 dhcp snooping information replace	17

1.1.23 dhcp snooping information transmit	18

1.1.24 ip-source trust	18

1.1.25 show ip dhcp-relay snooping	19

1.1.26 show ip dhcp-relay snooping binding	20

1.1.27 debug ip dhcp-relay snooping	20

1.1.28 debug ip dhcp-relay event	21

1.1.29 debug ip dhcp-relay binding	22

# DHCP-Relay Snooping Configuration Commands

The DHCP-relay snooping configuration commands include:

ip dhcp-relay snooping

ip dhcp-relay snooping vlan

ip dhcp-relay snooping vlan vlan_id max-client

ip dhcp-relay snooping database-agent

ip dhcp-relay snooping db-file

ip dhcp-relay snooping write-time

ip dhcp-relay snooping write-immediately

ip dhcp-relay snooping log

ip dhcp-relay snooping rapid-refresh-bind

ip dhcp-relay snooping information option

ip verify source vlan

ip arp inspection vlan

ip source binding

arp inspection trust

dhcp snooping trust

ip-source trust

show ip dhcp-relay snooping

show ip dhcp-relay snooping binding

debug ip dhcp-relay snooping

debug ip dhcp-relay event

debug ip dhcp-relay binding

### ip dhcp-relay snooping

Syntax

ip dhcp-relay snooping

no ip dhcp-relay snooping

To enable the DHCP-relay snooping function in a VLAN, run ip dhcp-relay snooping. To resume the default settings, run no dhcp-relay snooping.

Parameter

None

Default value

The dhcp-relay snooping function is disabled by default.

Usage guidelines

None

Example

The following example shows how to enable the DHCP-relay snooping function:

switch(config)# ip dhcp-relay snooping

switch(config)#

### ip dhcp-relay snooping vlan

Syntax

ip dhcp-relay snooping vlan vlan_id

no ip dhcp-relay snooping vlan vlan_id

Parameter

| Parameter | Description |
| --- | --- |
| vlan id | ID of a VLAN Range: 1-4094 |

Default value

None

Usage guidelines

This command is used to configure the VLAN of DHCP snooping.

Example

The following example shows how to conduct the snooping inspection to the DHCP packets in VLAN2.

switch(config)# ip dhcp-relay snooping vlan 2

switch(config)#

### ip dhcp-relay snooping vlan vlan_id max-client

Syntax

ip dhcp-relay snooping vlan vlan_id max-client number

no ip dhcp-relay snooping vlan vlan_id max-client

Parameter

| Parameter | Description |
| --- | --- |
| vlan_id | VLAN ID. The value ranges from 1 to 4094. |
| number | Available max user number: 0~65535 |

Default value

The max user number is 65535 by default.

Usage Guidelines

The command is used to configure the max user number of VLAN. If the user number reaches the top number, no new client will be distributed.

Example

The following example shows how to conduct snooping of DCHP packets on VLAN 2 and set the max user number to 3.

Switch_config#ip dhcp-relay snooping vlan 2 max-client 3

Switch_config#

### ip dhcp-relay snooping database-agent

Syntax

ip dhcp-relay snooping database-agent A.B.C.D

no ip dhcp-relay snooping database-agent

To configure the TFTP server for backing up DHCP-snooping binding, run ip dhcp-relay snooping database-agent A.B.C.D.

Parameter

| Parameter | Description |
| --- | --- |
| A.B.C.D | Stands for the IP address of the TFTP server. |

Default value

There is no standby servers by default.

Usage guidelines

If the address of the TFTP server is not configured, the binding backup is not conducted.

Example

The following example shows how to set the address of a server of backing up DHCP snooping binding to 192.168.1.1.

switch(config)# ip dhcp-relay snooping database-agent 192.168.1.1

switch(config)#

### dhcp-relay snooping db-file

Syntax

ip dhcp-relay snooping db-file name

no ip dhcp-relay snooping db-file

Parameter

| Parameter | Description |
| --- | --- |
| Name | File name which is saved during DHCP snooping binding backup. |

Default value

There is no file.

Usage guidelines

If the file name is not configured, the binding backup is not conducted.

Example

The following example shows how to set the file name of binding backup to dhcp_binding.txt.

switch(config)# ip dhcp-relay snooping db-file dhcp_binding.txt

switch(config)#

### dhcp-relay snooping write-time

Syntax

ip dhcp-relay snooping write-time num

no ip dhcp-relay snooping write-time

Parameter

| Parameter | Description |
| --- | --- |
| Num | Stands for the interval of backing up the DHCP snooping binding. |

Default value

The default value of the interval is 30 minutes.

Usage guidelines

The binding update will be checked during interval configuration. If the binding is updated, the binding information need be backed up.

Example

The following example shows how to set the interval of backing up the binding to 60 minutes.

switch(config)# ip dhcp-relay snooping write 60

switch(config)#

### ip dhcp-relay snooping write-immediately

Syntax

ip dhcp-relay snooping write-immediately

no ip dhcp-relay snooping write-immediately

Parameter

None

Default value

None

Usage Guidelines

If there is any entry update, the entry will be written into the entry database immediately. It is suggested do not enable this function if there are many entries working.

Example

The following example shows how to back up the binding table immediately after the configuration entry is updated.

Switch_config#ip dhcp-relay snooping write-immediately

Switch_config#

### ip dhcp-relay snooping log

Syntax

ip dhcp-relay snooping log

no ip dhcp-relay snooping log

Parameter

None

Default value

None

Usage Guidelines

After enabling log, if there are packets if dhcp serve on the non-trust port, there will be syslog and indicates in which port there is dhcp server.

Example

The following example shows how to enable log of dhcp snooping.

Switch_config#ip dhcp-relay snooping log

Switch_config#

### ip dhcp-relay snooping rapid-refresh-bind

Syntax

To enable dhcp snooping rapid refresh bind, run the following command. To return to the default setting, use the no form of this command.

ip dhcp-relay snooping rapid-refresh-bind

no ip dhcp-relay snooping rapid-refresh-bind

Parameter

None

Default value

None。

Usage Guidelines

If this function is enabled, dchp attack which fakes mac will be shut down and this function allows the user end to acquire address before the expiration of ip address leasing after the client changes the access port.

If this function is disabled, if the client changes the access port, the device configured snooping will be takes as dchp packet attack of fake mac, the dhcp packet will be dropped.

Example

None

### dhcp-relay snooping information option

Syntax

ip dhcp-relay snooping information option [ format snmp-ifindex | manual | hw-type | cm-type | hn-type [host] ]

no ip dhcp-relay snooping information option [ format snmp-ifindex | manual | hw-type | cm-type | hn-type [host] ]

Parameter

| Parameter | Description |
| --- | --- |
| format snmp-ifindex | Fills in option 82 in SNMP ifindex mode (optional). |
| format manual | Fills in option 82 in manual operation mode (optional). |
| format hw-type | Fills in option 82 in hw-type (optional). |
| format cm-type | Fills in option 82 in cm-type (optional). |

Default value

Option 82 will not be added to or removed from the report by default.

Usage guidelines

This command is used to set whether DHCP option82 can be handled when a switch is conducting DHCP snooping. If format snmp-ifindex is designated, Use the SNMP ifindex mode to fill in option 82; otherwise, fill in option 82 according to RFC3046.

Example

The following example shows how to fill in option 82 in SNMP ifindex mode.

Switch_config#ip dhcp-relay snooping information option format snmp-ifindex

### ip verify source vlan

Syntax

ip verify source vlan vlanid

no ip verify source vlan vlanid

Parameter

| Parameter | Description |
| --- | --- |
| vlan id | ID of a VLAN Range: 1-4094 |

Default value

None

Usage guidelines

This command is used to configure a VLAN for monitoring the source IP address. The “no” form of this command is used to cancel this VLAN.

Example

The following example shows how to conduct source IP address monitoring to the packets from all physical interfaces (except trusted interfaces) in VLAN2.

switch(config)# ip verify source vlan 2

switch(config)#

### ip arp inspection vlan

Syntax

ip arp inspection vlan vlanid

no ip arp inspection vlan vlanid

Parameter

| Parameter | Description |
| --- | --- |
| vlan id | Queries the time of the timer. Range: 1-255 |

Default value

None

Usage guidelines

This command is used to configure a VLAN for monitoring the source address of the ARP packet. The “no” form of this command is used to cancel this VLAN.

Example

The following example shows how to conduct source address monitoring to the ARP packets from all physical interfaces (except trusted interfaces) in VLAN2.

switch(config)# ip arp inspection vlan 2

switch(config)#

### ip source binding

Syntax

ip source binding xx-xx-xx-xx-xx-xx A.B.C.D interface name

no ip source binding xx-xx-xx-xx-xx-xx A.B.C.D

To add MAC-to-IP binding to an interface, run ip source binding xx-xx-xx-xx-xx-xx A.B.C.D interface name.

Parameter

| Parameter | Description |
| --- | --- |
| xx:xx:xx:xx:xx:xx | MAC address. |
| A.B.C.D | IP address |
| Name | Name of the interface |
| vlan-id | vlan id |

Default value

None

Usage guidelines

None

Example

The following example shows how to bind MAC address 08:00:3e:00:00:01 to IP address 192.168.1.2 on interface fastEthernet0/0.

switch(config)# ip source binding  08:00:3e:00:00:01 192.168.1.2 interface fastEthernet0/0

switch(config)#

### arp inspection trust

Syntax

arp inspection trust

Parameter

None

Default value

The interfaces are distrusted ones by default.

Usage guidelines

The ARP monitoring is not conducted to the ARP-trusted interface. The “no” form of this command is used to configure the default value of this interface.

Example

The following example shows how to set interface fastEthernet 0/0 to an ARP-trusted interface.

Switch_config_f0/0# arp inspection trust

### dhcp snooping trust

Syntax

dhcp snooping trust

Parameter

None

Default value

The default interface is a distrusted one.

Usage guidelines

DHCP snooping is not conducted to the DHCP-trusted interface. The “no” form of this command is used to resume the default value of this interface.

Example

The following example shows how to set interface fastEthernet 0/0 to a DHCP-trusted interface.

Switch_config_f0/0# dhcp snooping  trust

### dhcp snooping deny

Syntax

dhcp snooping deny

Parameter

None

Default value

DHCP snooping is allowed on the default interface.

Usage guidelines

After this command is configured, DHCP snooping trust, IP-sourcetrust and ARP inspection trust are automatically enabled. The “no” form of this command is used to configure the default value of this interface.

Example

The following example shows how to disable DHCP snooping on interface fastEthernet0/0.

Switch_config_f0/0# dhcp snooping deny

### dhcp snooping information circuit-id

Syntax

dhcp snooping information circuit-id {string [STRING] | hex xx-xx-xx-xx-xx-xx}

Parameter

| Parameter | Description |
| --- | --- |
| string STRING | Means the character string of option82 circuit-id sub-option |
| hex xx-xx-xx-xx-xx-xx | Means hex of option82 circuit-id sub-option |

Default value

None

Usage Guidelines

The command can be configured on every port connecting with clients. This command enables to configure dhcp packet option82 sub-option which sent to dhcp server by dhcp client which monitored by dchp snooping. (Configure option82 manually, refer to the command ip dhcp-relay snooping information option format manual)

Example

The following example shows how to manually configure option82 sub-option on port g0/3 as group 1 and g0/3 belongs to vlan1.

Switch_config#ip dhcp-relay snooping

Switch_config#ip dhcp-relay snooping vlan 1

Switch_config#ip dhcp-relay snooping information option format manual

Switch_config#interface g0/3

Switch_config_g0/3#dhcp snooping information circuit-id string group1

### dhcp snooping information remote-id string

Syntax

dhcp snooping information remote-id {string [STRING] | hex xx-xx-xx-xx-xx-xx}

Parameter

| Parameter | Description |
| --- | --- |
| string STRING | Means the character string of option82 remote-id sub-option |
| hex xx-xx-xx-xx-xx-xx | Means hex of option remote-id sub-option |

Default value

None

Usage Guidelines

The command can be configured on every port connecting with clients. This command enables to configure dhcp packet option82 sub-option which sent to dhcp server by dhcp client which monitored by dchp snooping. (Configure option82 manually, refer to the command ip dhcp-relay snooping information option format manual)

Example

The following example shows how to manually configure option82 sub-option on port g0/3 as group 1 and g0/3 belongs to vlan1.

Switch_config# ip dhcp-relay snooping

Switch_config# ip dhcp-relay snooping vlan 1

Switch_config#ip dhcp-relay snooping information option format manual

Switch_config#interface g0/3

Switch_config_g0/3# dhcp snooping information remote-id string group1

### dhcp snooping information vendor-specific

Syntax

dhcp snooping information vendor-specific {string [STRING] | hex xx-xx-xx-xx-xx-xx}

Parameter

| Parameter | Description |
| --- | --- |
| string STRING | Means the character string of option82 verdor-specific sub-option |
| hex xx-xx-xx-xx-xx-xx | Means the hex of option82 verdor-specific sub-option |

Default value

None

Usage Guidelines

The command can be configured on every port connecting with clients. This command enables to configure dhcp packet option82 sub-option which sent to dhcp server by dhcp client which monitored by dchp snooping. (Configure option82 manually, refer to the command ip dhcp-relay snooping information option format manual)

Example

On port g0/3, configure option82 vendor-specific(suboption 9) with the hex: 00-00-00-09-0d-01-0b-78-69-61-6f-6d-69-6e-37-31-31-34.

Switch_config# ip dhcp-relay snooping

Switch_config# ip dhcp-relay snooping vlan 1

Switch_config#ip dhcp-relay snooping information option format manual

Switch_config#interface g0/3

Switch_config_g0/3# dhcp snooping information vendor-specific hex 00-00-00-09-0d-01-0b-78-69-61-6f-6d-69-6e-37-31-31-34

### dhcp snooping information append

Syntax

dhcp snooping information append

dhcp snooping information append first-subop9-param { hex xx-xx-xx-xx-xx-xx | hostname | vlanip }

dhcp snooping information append second-subop9-param { hex xx-xx-xx-xx-xx-xx | hostname | vlanip }

no dhcp snooping information append

no dhcp snooping information append first-subop9-param

no dhcp snooping information append second-subop9-param

Parameter

| Parameter | Description |
| --- | --- |
| first-subop9-param hex [xx-xx-xx-xx-xx-xx] | Means hex of the first parameter of the option82 vendor-specific (suboption9) |
| second-subop9-param hex [xx-xx-xx-xx-xx-xx] | Means hex of the second parameter of the option82 vendor-specific（suboption9） |
| hostname | The parameter of the option82 vendor-specific（suboption9）is host name. |
| vlanip | The parameter of option82 vendor-specific（suboption9）is ip address of interface vlan. |

Default value

None

Usage Guidelines

The command can be configured on every port connecting with clients. This command enables to configure dhcp packet option82 sub-option which sent to dhcp server by dhcp client which monitored by dchp snooping.

The command without parameter is enable/disable. If append is enabled, the information will be added to suboption9 of option82. The added information is first-subop9-param and second-subop9-param.

Example

On port g0/3 expand dhcp packets with option82 and configure suboption9 adding to parameter 1 with the hex: 61-62-63-61-62-63.

Switch_config_g0/3# dhcp snooping information append

Switch_config_g0/3#dhcp snooping information append first-subop9-param hex 61-62-63-61-62-63

Among which 61-62-63-61-62-63 is the hex of the added parameter.

### dhcp snooping information drop

Syntax

dhcp snooping information drop

no dhcp snooping information drop

Parameter

None

Default value

None

Usage Guidelines

The command can be configured on every port connecting with clients.

After the command is configured, the requirement packets including option82 will be dropped on the certain port.

Example

The following example shows how to drop dhcp packets with option82 on g0/3.

Switch_config_g0/3# dhcp snooping information drop

### dhcp snooping information replace

Syntax

dhcp snooping information replace

no dhcp snooping information replace

Parameter

None

Default value

None

Usage Guidelines

The command can be configured on every port connecting with clients.

After the command is configured, the option82 field of dhcp requirement packets will be replaced on the certain port. .

Example

Replace dhcp packets of option82 on g0/3.

Switch_config_g0/3# dhcp snooping information replace

### dhcp snooping information transmit

Syntax

dhcp snooping information transmit

no dhcp snooping information transmit

Parameter

None

Default value

None

Usage Guidelines

The command can be configured on every port connecting with clients.

After the command is configured, the DCHP packets with option82 from relay will be transparently transmitted.

Example

On port g0/3, configure dhcp packets with option82 from relay will be transparently transmitted.

Switch_config_g0/3# dhcp snooping information transmit

### ip-source trust

Syntax

ip-source trust

Parameter

None

Default value

The default interface is a distrusted one.

Description

Source IP address snooping is not conducted to the source-IP-trusted interface. The “no” form of this command is used to resume the default value of this interface.

Example

The following example shows how to set interface fastEthernet 0/0 to a source-ip-trusted interface.

Switch_config_f0/0# ip-source trust

### show ip dhcp-relay snooping

Syntax

show ip dhcp-relay snooping

Parameter

None

Default value

None

Usage guidelines

This command is used to display the information about DHCP-relay snooping configuration.

Example

The following example shows how to display the information about DHCP-relay snooping configuration.

switch(config)# show ip dhcp-relay snooping

### show ip dhcp-relay snooping binding

Syntax

show ip dhcp-relay snooping binding [all]

Parameter

None

Default value

None

Usage guidelines

This command is used to display the binding information about DHCP-relay snooping.

If the all parameter is in the command sentence, all binding information about DHCP-relay snooping will be displayed.

Example

The following example shows how to display the binding information about DHCP-relay snooping.

switch(config)# show ip dhcp-relay snooping binding

### debug ip dhcp-relay snooping

Syntax

debug ip dhcp-relay snooping

no debug ip dhcp-relay snooping

Parameter

None

Default value

None

Usage guidelines

This command is used to enable or disable the debugging switch of DHCP-relay snooping.

Example

The following example shows how to enable the debugging switch of DHCP-relay snooping.

switch(config)# debug ip dhcp-relay snooping

switch(config)#

### debug ip dhcp-relay event

Syntax

debug ip dhcp-relay eventr

no debug ip dhcp-relay event

Parameter

None

Default value

None

Usage guidelines

This command is used to enable or disable the event debugging switch of DHCP-relay.

Example

The following example shows how to enable the  event debugging switch of DHCP-relay.

switch(config)# debug ip dhcp-relay event

switch(config)#

### debug ip dhcp-relay binding

Syntax

debug ip dhcp-relay binding

no debug ip dhcp-relay binding

Parameter

None

Default value

None

Usage guidelines

This command is used to enable or disable the binding debugging switch of DHCP-relay snooping.

Example

The following example shows how to enable the binding debugging switch of DHCP-relay snooping.

switch(config)# debug ip dhcp-relay binding

switch(config)#