Instructions for Upgrading OTDR Firmware

Step 1: Activate the firmware upgrading mode

Press the “Menu” key, “Info” key and “”  key on the operating panel for 3 seconds; after the VLS and SCAN lamp are on and off in turns, which means the system is ready for upgrading firmware.

Step 2: USB connection

Connect the PC and the OTDR with the USB cable; find the “BOOTLOADER” mobile hard disc  from the "My Computer" ; double click the  to open the file READY.TXT; till now the firmware upgrade path is ready.

Step 3: Copy the program upgrade file to

Copy the program upgrade file to ; this process shall accompany with the following phenomena:

（1）The VLS lamp of the OTDR flashes, which means the data is being transmitted; after the process is end, the VLS lamp shall be off and the SCAN lamp shall be normally on.

（2）The file copying progression dialogue box will be opened on the PC screen; after the copy is finished, the dialogue box will be closed automatically; find the “BOOTLOADER” mobile hard disc  from the “My Computer” and open it again; if you see the file SUCCESS.TXT, which means the upgrade is done successfully.

If the wrong upgrade file is copied or if some data are lost in the upgrading process, the following phenomena shall occur:

（1）The VLS lamp of the OTDR is normally off, but the SCAN lamp is flickering regularly;

（2）The file copying progression dialogue box shall be closed automatically; find the “BOOTLOADER” mobile hard disc  from the “My Computer”; open it again to see the file FFAILED. TXT

Step 4: Power off

Keep pressing the“”key till the OTDR powers off.

Notes:

（1）If you would like to upgrade again after the primary upgrade fails, you are needed to power off the OTDR firstly, and then power on the OTDR;

（2）Under the upgrading mode and for the purpose of avoiding from pressing key wrongly, you should keep pressing“”key, and the power off function can only be activated after the accumulative running time of the OTDR goes beyond 15 seconds;

（3）Please do not move the equipment, USB cable or press any key randomly in the upgrading process.