Professional COFDM Modulator

User Manual

CONTENT

1.Introduction	1

2. Features	2

3. Specification	2

4. Structure	5

4.1 Front Panel	5

4.2 Rear Panel	5

5. Menu Structure and Operation	6

5.1 Inputs Menu	8

5.1.1 Status Menu	8

5.1.2 QPSK Menu	8

5.1.3 Status Menu	9

5.1.4 QAM Menu	9

5.1.5 Status Menu	10

5.1.6 DVB-S2 Menu	10

5.1.7 Status Menu	10

5.1.8 COFDM Menu	10

5.2 Outputs Menu	11

5.2.1 Status Menu	11

5.2.2 CI Menu	11

5.2.3 Decoder Menu	11

5.2.4 ASI Menu	12

5.2.5 COFDM Menu	12

5.2.6 Ethernet Menu	12

5.3 System Menu	13

5.3.1 Local Setup: parameters of local device	13

5.3.2 Trap IP Addr: SNMP trap IP address	13

5.3.3 Unit Name: Name of this device	13

5.3.4 Properties:	13

5.3.5 Factory Setting: Recover to factory default setting	13

5.3.6 Machine Type: show machine type	13

6. Safety	14

7. Installation	15

8. Accessories	15

DCH-4000PM Professional COFDM Modulator

1.Introduction

DCH-4000PM is a professional COFDM modulator which combines IRD and COFDM modulator together into a single unit. With PCMCIA CI slot, it can support various CA systems such as Conax, Cryptoworks, Irdeto, NDS, ediaguard, SECA, and Viaccess. It has many kinds of inputs (including DVB over ASI, IP, QPSK, QAM, COFDM and DS3) and outputs (RF, ASI, DS3 and IP). An appropriate IP port equipped as an option supports DVB over IP applications. LAN control and monitoring are achieved. With features of high output level and low BER, DCH-4000PM becomes the best choice for digital TV headend system

There are many models of DCH-4000PM following different requirements from customers:

| DCH-4000PM Professional Digital TV Processor Option List |
| --- |
|  | Model NO | DCH-4000PM-ST | DCH-4000PM-S2T | DCH-4000PM-CT | DCH-4000PM-DT | DCH-4000PM-TT |
| Function |  |  |  |  |  |  |
| IP OUT | ■ | ■ | ■ | ■ | ■ |
| IP INPUT | ■ | ■ | ■ | ■ | ■ |
| DS3 Input/Loop through |  |  |  | ■ |  |
| DVB-S Input | ■ |  |  |  |  |
| DVB-S2 Input |  | ■ |  |  |  |
| DVB-C Input |  |  | ■ |  |  |
| DVB-T Input |  |  |  |  | ■ |
| PCMCIA Slot | ■ | ■ | ■ | ■ | ■ |
| ASI Input/Output | ■ | ■ | ■ | ■ | ■ |
| RF OUT | ■ | ■ | ■ | ■ | ■ |
| LAN control | ■ | ■ | ■ | ■ | ■ |

2. Features

Comply with MPEG-2 (MP@ML) and DVB-S/-C/-T/S2 standards

Support multiple Input/loop through methods such as QPSK, ASI, DS3

Support various CA systems such as Ideto, Viaccess, NDS, etc

Can show work status and parameters settings on LCD

LAN control based on SNMP protocol

DS3 is compatible with multiple network adapter protocols such as Bacro, Huawei

Support ASI output; can output original TS or processed TS (1＋1Backup)

Can re-create PSI/SI table

Support IP input/output

Teletext VBI, EBU subtitle and DVB subtitle

Upgradeable through LAN

Auto-save when power off suddenly

3. Specification

Input

QPSK Demodulation

Input frequency range	950~2150MHz

Input level	-65~-25dBm

Input impedance	75Ω

Connector	F Connector

Symbol rate	2~45MBauds

Rolling off factor	0.35

Punctured rates	1/2,2/3,3/4,5/6,7/8

Reeds Solomon decoding	I=12

LNB power voltage	0, 13V, 18V optional

0/22K	0/22KHz optional

DVB-C QAM Demodulation

Input frequency	48～862MHz

Input symbol rate	1～7Mbps

Demodulation methods	16/32/64/128/256/64B/256B QAM

FEC	1/2, 2/3, 3/4, 5/6, 7/8

Input level	-15～15dBmV

Input connector	IEC Female

Input impedance	75Ω

DVB-T COFDM Demodulation

Input frequency	174～230MHz（VHF）

470～862MHz（UHF）

Input level	-20～-70dBmV

Constellation 	QPSK, 16-QAM, 64-QAM

Tuner bandwidth	7/8 MHz

FFT mode	2K

Guard interval 	1/4, 1/8, 1/16, 1/32, off

FEC	1/2, 2/3, 3/4, 5/6, 7/8

Input connector	IEC Female

Input impedance	75Ω

ASI Input	Connector	75Ω, BNC

ASI mode	Byte/Burst self-adjustable

Package	188 or 204

DS3 Input	Connector	75Ω, BNC

Max input code rate	44.736Mbps

Format                       Framed or unframed framing according to G804/G752

Output

ASI Output	Connector	75Ω, BNC

Max output rate	270Mb/s

ASI mode	Byte

Package	188 or 204

Signal level	800mVpp±10%

DS3 Loop through    Connector	75Ω, BNC

Max output code rate	44.736Mbps

Format	Framed or unframed framing according to G804/G752

TS IP Input/Output	Connector	RJ45 100Base-T

Max. output rate	70Mbits/s

UDP/RTP	Multicast or Unicast

Multicast control protocol	IGMPV2

RF Output           Connector	75Ω, F-type

Bandwidth                   5/6/7/8MHz

Output frequency range       48MHz~862MHz

Output level                 100～118 dB (adjustable)

QAM mode                  QPSK/16QAM/64QAM

FEC                        1/2;2/3;3/4;5/6;7/8

Guard interval               1/32;1/16;1/8;1/4

Frequency spectrum          NORMAL/INVERT

General	Weight	5kg

Dimension	44×431×402（mm）

Working temperature	0-40℃

Storage temperature	-20~70℃

Humidity	<95%

Power supply	AC90~250V, 50/60Hz

Power consumption	30W

4. Structure

4.1 Front Panel

A1 POWER	Power indicator, green light means power is OK

A2 TUNER LOCK	Tuner lock indicator, green light means signal is locked; if thee is no light, that means no signal input or wrong parameters setting.

A3 ALARM	Alarm indicator

A4 LCD	2 × 20 character LCD

A5-A10 buttons	〔〕〔〕〔〕〔〕〔ENTER〕〔EXIT〕 buttons

〔〕〔〕 are used to up/down pages of menu or increase/decrease value when edit numbers

〔〕〔〕 are used to move cursor

〔ENTER〕is used to enter sub menu or confirm operation

〔EXIT〕is used to return previous menu or cancel operation

A11 Common Interface	PCMCIA Module slot

A12 RF monitor          Output -20dB RF signal for monitor usage

4.2 Rear Panel

B1       RF OUT	RF signal output port

B2       TS/IP	IP input/output port

B3       RS-232	serial port for printing information

B4       LAN CONTROL	LAN port for software update

B5       ASI IN	ASI input port

B6, B7   ASI OUT               ASI output port; B7 and B6 output the same signal

B8       LOOP THRU           Tuner signal loop through

B9       TUNER IN	Tuner signal input	ASI IN	ASI输入接口

B10	Power socket	AC 90~250V input

5. Menu Structure and Operation

Note: The input menu may be changed when use different tuners. The other menu won’t be changed

When use DVB-S TUNER, INPUT menu is shown as below:

I

When use DVB-C TUNER, INPUT menu is shown as below:

When use DVB-T TUNER, INPUT menu is shown as below:

When use DVB-S2 TUNER, INPUT menu is shown as below:

Menu Operation

There is a 2×20 character LCD in front panel. After turn on power, it will show boot information

First line is product model; Second line is IP address of this device. Press 〔ENTER〕 button to enter main menu:

(1) Input Setup	Set input parameters

(2) Output Setup	Set output parameters

(3) System	Set system parameters

5.1 Inputs Menu

When use DVB-S TUNER, INPUT menu is shown as below:

There are two options: Status and QPSK:

5.1.1 Status Menu

It contains two options, ASI and TUNER, to show the status of signal input:

ASI: When signal from ASI input port is locked, it will display package format and code rate; if signal is not locked, it will show Unlock.

TUNER: When signal from tuner input port is locked, it will display package format and code rate; if signal is not locked, it will show Unlock.

5.1.2 QPSK Menu

It contains 5 options for SVB-S parameters setting. When signal is locked, the TUNER LOCK indicator on front panel will turn green.

LNB Frequency: Set LNB frequency. E.g.: C band is 5150MHz, Ku band is 11300MHz

Satellite Frequency: Input downstream frequency of satellite

Symbol Rate: Input symbol rate of satellite

LNB Voltage: LNB power voltage. OFF/18V/13V selectable

LNB 22KHz: 0 or 22K switch. Can select OFF/ON

When use DVB-C TUNER, INPUT menu is shown as below:

There are two options: Status and QAM:

5.1.3 Status Menu

It contains two options, ASI and TUNER, to show the status of signal input:

ASI: When signal from ASI input port is locked, it will display package format and code rate; if signal is not locked, it will show Unlock.

TUNER: When signal from tuner input port is locked, it will display package format and code rate; if signal is not locked, it will show Unlock.

5.1.4 QAM Menu

There are 3 options to set QAM parameters. After signal is locked, the TUNER LOCK indicator on front panel will turn green.

Constellation: User can select 16QAM, 32QAM, 64QAM, 128QAM, 256QAM

Frequency: Input QAM frequency

Symbol Rate: Input QAM symbol rate

When use DVB-S2 TUNER, INPUT menu is shown as below:

There are two options: Status and DVB-S2:

5.1.5 Status Menu

It contains two options, ASI and TUNER, to show the status of signal input:

ASI: When signal from ASI input port is locked, it will display package format and code rate; if signal is not locked, it will show Unlock.

TUNER: When signal from tuner input port is locked, it will display package format and code rate; if signal is not locked, it will show Unlock.

5.1.6 DVB-S2 Menu

There are 8 options to set DVB-S2 parameters. After signal is locked, the TUNER LOCK indicator on front panel will turn green.

LNB Frequency: Input LNB frequency

Satellite Frequency: Input downstream frequency of satellite

Symbol Rate: Input symbol rate of satellite

LNB Voltage: LNB power voltage. OFF/18V/13V selectable

LNB 22KHz: 0 or 22K switch. Can select OFF/ON

Demodulator Mode: Can select DVB-S/DVB-S2

Operation Mode: Can select QPSK 1/2,2/3,3/4,3/5,4/5,5/6,8/9,9/10

8PSK 2/3,3/4,3/5,5/6,8/9,9/10

Pilot: Can select ON/OFF

Roll-Off Factor: Can select 0.2/0.25/0.35

When use DVB-T TUNER, INPUT menu is shown as below:

There are two options: Status and COFDM:

5.1.7 Status Menu

It contains two options, ASI and TUNER, to show the status of signal input:

ASI: When signal from ASI input port is locked, it will display package format and code rate; if signal is not locked, it will show Unlock.

TUNER: When signal from tuner input port is locked, it will display package format and code rate; if signal is not locked, it will show Unlock.

5.1.8 COFDM Menu

There is 1 option to set COFDM parameters. After signal is locked, the TUNER LOCK indicator on front panel will turn green.

Frequency: Input COFDM frequency

5.2 Outputs Menu

There are six options: Status, CI, Decoder, ASI, COFDM and Ethernet:

5.2.1 Status Menu

It shows information of Decoder, CI and Ethernet

Decoder: Shows PID of PMT, PID and PN（Program Number）of AV

CI: Shows information of CI cards in Slot1/Slot2

Ethernet: Shows information of TS/IP port

5.2.2 CI Menu

It contains two options, CI Source and CI Setup, to set parameters of CI

CI Source: Set signal source. Can select TUNER or ASI Input

CI Setup: Press   buttons to select the program which is expected to be descrambled; Press ENTER button to select Slot1/Slot2 or Bypass; then after press EXIT button, it will show “Confirm changed”, then select “YES”

0-xxxxx show program name whose signal source is ASI

1-xxxxx show program name whose signal source is TUNER

2-xxxxx show program name whose signal source is TS/IP

3-xxxxx undefined

5.2.3 Decoder Menu

User can set parameters of Video and Audio demodulation

Program: Select program which is expected to be broadcasted. Press   buttons to select the program, press   buttons to select 0-3, then press ENTER button to confirm.

0-xxxxx show program name whose signal source is ASI

1-xxxxx show program name whose signal source is TUNER

2-xxxxx show program name whose signal source is TS/IP

3-xxxxx show program name whose signal source is CI

Video: it includes Video Standard, Screen, DVB Subtitle Lang, EBU Subtitle Lang, Subtitle Priority and Fail Mode

Video Standard: Select video output standard, includes Auto, SECAM, NTSC or PAL

Screen: Select screen display modes, includes 4:3 Full, 16:9 Full or 4:3 Letterbox

DVB Subtitle Lang: Select DVB subtitle language

EBU Subtitle Lang: Select EBU subtitle language

Subtitle Priority: Set priority of subtitle. Can select DVB First or EBU First

Fail Mode: includes Black Screen, No Sync and Still Picture

Audio: Includes Audio Level, Audio Mode and Audio Language

Audio Level: Can adjust with range 0-99

Audio Mode: Can select Stereo, Left, Right, Dual and Mono

Audio Language: Can select audio language

5.2.4 ASI Menu

It contains two options, ASI Source and ASI Package Length, to set parameters of ASI

ASI Source: Select signal source, includes CI De-encrypted, TUNER or ASI Input

ASI Package Length: Can select 188 or Bypass

5.2.5 COFDM Menu

It contains ten options to set parameters of COFDM

INPUT SOURCE: Select input signal source, includes ASI Input, MUX TS, CI De-encrypted or Tuner

QAM-Order: Set COFDM modulation modes, includes QPSK/16QAM/64QAM

Bandwidths: Set bandwidths. Can select 6/7/8M

FEC: Set FEC parameters. Can select 1/2; 2/3; 2:3/4; 5/6; 7/8

Guard interval: Can select 1/32; 1/16; 1/8; 1/4

Modulation: Set carrier parameter. Can select ON/OFF

RF frequency: Set RF frequency. The range is 48MHz~862MHz

SPEC: Set frequency spectrum. Can select NORMAL or INVERT

RF ATTEN: Set RF attenuation. The range is 00dB~18dB

STATUS: Show COFDM output status. If output well, it will show “OK”; else, over flow, it will show “over flow”

5.2.6 Ethernet Menu

It includes Stream IP Addr, Stream Netmask, Stream Gateway, Stream Mac Address, Stream UDP Port, Multicast IP Addr, Multicase UDP Port, Protocol, TS Pkts Per UDP, Time To Live, Type of Service and Source

Stream IP Addr: IP address of signal source

Stream Netmask: Netmask of signal source

Stream Gateway: Gateway of signal source

Stream Mac Address: Mac address of signal source

Stream UDP Port: UDP port number of signal source

Multicast IP Addr: IP address of multicast

Multicase UDP Port: UDP port of multicast

Protocol: Can select UDP or RTP

TS Pkts Per UDP: the TS packets number per UDP. Can select 1~7

Time To Live: The quantity of effective routers. The range is 1~5

Type of Service: Can select Normal, Min Monetary Cost, Max Reliability, Max Throughput and Min Delay

Source: Output signal source. Can select ASI Input, CI De-encrypted and TUNER

5.3 System Menu

There are six sub-menus:

5.3.1 Local Setup: parameters of local device

IP Address: IP address of this device

Network Mask: Network mask of this device

Gateway: Gateway of this device

5.3.2 Trap IP Addr: SNMP trap IP address

5.3.3 Unit Name: Name of this device

5.3.4 Properties:

MAC Address: show MAC address of this device

FW Version: MCU software version

SW Version: FPGA software

5.3.5 Factory Setting: Recover to factory default setting

5.3.6 Machine Type: show machine type

6. Safety

CAUTION

Unauthorized maintenance or the use of non-approved replacements may affect the equipment specification and invalidate any warranties.

7. Installation

- Fix the device in 19” EIA rack with screw

- Power on the device. Turn on the switch. The POWER LED will light. If don’t use this device, please turn off switch and unplug power cord. The reboot interval should be more than 5 seconds.

- Tuner signal is inputted from TUNER IN port on rear panel.

- User can connect CVBS1 Port on rear panel with TV, and ASI OUT port with other devices.

8. Accessories

Power cord   	x 1

User Manual  	x 1

CD       	x 1

ASI cable 	x 1

XLR connector       	x 2

Warranty card       	x 1

# Text boxes

Local

Setup

Trap IP

Addr

QPSK：Lock/Unlock

ASI：Lock/Unlock

SPI：Lock/Unlock

DS3：Lock/Unlock

Stream IP Addr:

Stream Netmask:

Stream Gateway:

Stream Mac Address:

Stream UDP Port:

Multicast IP Addr:

Multicast UDP Port:

Protocol: UDP/RTP

TS Packts per UDP: 1-7

Time to Live: 1-5

Type of Service: Normal/Min monetary cost/

Max Reliability/Max Throughput/Min Delay

Source: ASI Input/CI De-encripted/TUNER

ASI

Beijing Jaeger Communication Electronic Technology Co., Ltd.

Tel: +86-10-62475893     Fax: +86-10-62473278

http://www.pbi-china.com

Ethernet

INPUT SOURCE: ASI Input / MUX TS/               CI De-encripted / Tuner

QAM_ORDER: QPSK/16QAM/64QAM

Bandwidths: 6MHz/7MHz/8MHz

FEC: 1/2;2/3;2:3/4;5/6;7/8

Guard interval: 1/32;1/16;1/8;1/4

Modulation:Yes/No

RF Frequency 400MHz

SPEC: NORMAL / INVERT

RF ATTEN: 00dB~18dB

STATUS：COFDM OK/over flow

Decoder

COFDM

ASI Source: ASI Input/CI De-encripted/TUNER

ASI Package Length: 188/Bypass

ASI

Unit

Name

Local Setup: IP Address

NetworkMask

Gateway

Trap IP Address:

Unit Name:

Properties: MacAddress

FW Version

SW Version

CM Version

Factory Setting: YES/NO

Machine Type:

Symtem

Properties

ASI: LOCK/UNLOCK

TUNER: LOCK/UNLOCK

Decoder

Status

CI

CI

Status

Factory

Settings

QPSK

Status

Machine Type

Main Menu

Status

Inputs

COFDM

Program: 0-3

Video:  Video Standard:Auto/SECAM/NTSC/PAL

Screen: 4:3 Full/16:9 Full/4:3 Letterbox

DVB Subtitle Lang: English

EBU Subtitle Lang: English

Subtile Priority: DVB First/EBU First

Fail Mode:Black Screen/No Sync/Still Picture

Audio: Audio Level: 0-99

Audio Mode: Stereo/Left/Right/Mono/Dual

Audio Language: English

Outputs

System

Status

QPSK

System

CI Source: Tuner/ASI Input

Setup: Bypass/Slot1/Slot2

DS3 Protocol

Decoder:PMT/PN/AV/Video/Audio

CI: Slot1/Slot2

Ethernet:

Modulation: ON/OFF

Status

LNB Frequency: 5150MHz

Satelite Frequency: 4000MHz

Symbol Rate: 26850Kb

LNB Voltage: oFF/18V/13V

LNB 22KHz: OFF/ON

QPSK

ASI: LOCK/UNLOCK

TUNER: LOCK/UNLOCK

Status

CI

Decoder

ASI

COFDM

Ethernet

Inputs

DVB-S2

Outputs

Inputs

Avoid any contact with liquid and corrosive substances

×

Never attempt to disassemble the unit.

Only trained and approved persons are permitted to service this unit.

This unit should be operated only under voltages of AC 250V(10% 50Hz(10%

This unit must be properly earthed

COFDM

Status

QAM

Status

QPSK

Status

COFDM

Status

Inputs

DVB-S2

Status

Inputs

QAM

Status

Inputs

Frequency: 794MHz

Status

COFDM

ASI: LOCK/UNLOCK

TUNER: LOCK/UNLOCK

LNB Frequency: 5150MHz

Satelite Frequency: 4000MHz

Symbol Rate: 26850KB

LNB Voltage: oFF/18V/13V

LNB 22KHz: OFF/ON

LNB Frequency: 5150MHz

Satelite Frequency: 4000MHz

Symbol Rate: 26850KB

LNB Voltage: oFF/18V/13V

LNB 22KHz: OFF/ON

Demodulator Mode:DVB-S/DVB-S2

Operation Mode:

QPSK 1/2,2/3,3/4,3/5,4/5,5/6,8/9,9/10

8PSK 2/3,3/4,3/5,5/6,8/9,9/10

Pilot: ON/OFF

Roll-Off Factor: 0.2/0.25/0.35

ASI: LOCK/UNLOCK

TUNER: LOCK/UNLOCK

Status

DVB-S2

Constellation:16/32/64/128/256

Frequency: 500MHz

Symbol Rate: 6.875Mb

ASI: LOCK/UNLOCK

TUNER: LOCK/UNLOCK

Status

QAM

Outputs

Status

QPSK

Main Menu

Ethernet