SMA-701

CATV Adjacent Agile Modulator Bank

SMA-701 Modulator Bank offers a compact CATV Headend with a 19” chassis and 8 slots for analog or digital plug-in modules. SMA-701 modules family provide a wide choice reception for DVB-S, DVB-T, DVB-C and analog AV signal, and the RF output fully respect most of analog TV modulation standards, such as PAL, NTSC or SECAM. The Tuner-saved TS modules share descrambled streams from the master module, which supports Common Interface and could descramble several streams at the same time*. Migration from analog CATV system to digital could be achieved with different modules in one chassis.

*Note: Multi-decryption function should be supported by CAM.

Features

* 48MHz to 860MHz full band adjacent agile alignment

* Combined DVB receiver and Analog TV modulator on each slot

* Easy configuration through External control unit

* Main Frame supports all future modules, rack mount or wall mount

* RF output level: 100dBμV/ch

* Spurious less than -60dBc (110dBμV/ch@25℃)

* Support Common Interface and multi-decryption CAMs

* Tuner-saved design by TS sharing among slots

* Worldwide Analog TV standards, including A2 and NICAM

* ITU J.83 Annex A and B compatible QAM Module

Application

The SMA-701 is perfectly suited for any small to large size operators who want to build their SMATV networks cost efficiently.

Module Cards

| Function | Model | Input | RF Output | CI |
| --- | --- | --- | --- | --- |
|  |  | DVB-S | DVB-C | DVB-T | AV | PAL B/G** |  |
| Master module | SMA-701PM-13S | √ | - | - | - | √ | √ |
|  | SMA-701PM-13C | - | √ | - | - | √ | √ |
|  | SMA-701PM-13T | - | - | √ | - | √ | √ |
| Slave module | SMA-701RM-13D | - | - | - | - | √ | - |
| AV modulator | SMA-701M-13M | - | - | - | √ | √ | - |

**Note: Other standards available upon request

Accessories

SMA701MF: Main frame which can accommodate up to 8 modules with power supply.

SMA701CU: the external control unit.

Specifications

| Input |
| --- |
| DVB-S |  |
| RF input | 75Ω, F type |
| RF output | 75Ω, F type |
| Input Frequency Range | 950~2150MHz |
| Input Level | -25~-65dBm |
| Symbol Rate | 2~45Mb/s |
| Rolling Off Factor | 0.20 or 0.35 |
| Punctured Rated | 1/2, 2/3, 3/4, 5/6, 6/7, 7/8 |
| Reeds Salomon Decoding | 204, 188 T=8 & I=12 |
| LNB Power | 13V, 18V Switchable |
| LNB Switch | 0, 22KHz and DiSEqC 1.0 |
| Common Interface | 1 x PCMCIA Slot |
| DVB-C |
| RF input | 75Ω, F type |
| RF output | 75Ω, IEC type |
| input frequency | 40~860MHz |
| input level | 40~85dBμV @ 64QAM |
| QAM Mode | 16, 32, 64, 128, 256QAM |
| symbol rate | 2.5~6.952MSym/s |
| Common Interface | 1 x PCMCIA Slot |
| DVB-T |
| RF input | 75Ω, F type |
| RF output | 75Ω, F type |
| Input Frequency Range | 174~230MHz, 470~860MHz |
| Input Level | -25~-65dBm |
| Symbol Rate | 3.6~6.952Mb/s |
| Used Bandwidth | 7MHz (174~230MHz), 8MHz (470~860MHz) |
| Punctured Rated | 1/2, 2/3, 3/4, 5/6, 7/8 |
| Reeds Salomon Decoding | 204, 188 T=8 & I=12 |
| Guard interval | 1/4,1/8,1/16,1/32 |
| FFT Mode | 2k, 8k |
| Common Interface | 1 x PCMCIA Slot |
| RF Output |
| Video Carrier Frequency Range | 48.25~860.25MHz(Adjustable, step by 1MHz) |
| Power Level Attenuation | 0~18dB (Adjustable, step by 1dB) |
| Picture Carrier Accuracy | ≤±5KHz (VHF); ≤±10KHz (UHF) |
| Audio Carrier Frequency (main) | 6.5MHz (D/K,L)；6.0MHz；5.5MHz；4.5MHz |
| Audio Carrier Frequency Accuracy | ±2KHz |
| Video/Audio Carrier Ratio (main) | 12dB/16dB selectable |
| Audio Carrier Frequency (second) | 6.742MHz (D/K) |
|  | 6.258MHz |
|  | 5.742MHz |
|  | 4.724MHz |
| Video/Audio Carrier Ratio (second) | 20dB |
| Video Modulation index | 77.5~97.5%, step by 1% (D/K,B/G,I,M/N) |
| Audio Modulation deviation peak-peak | 40~160KHz, step by 10KHz (B/G,D/K,I) |
|  | 20~80KHz, step by 5KHz (M/N) |
| Video |  |
| K2T | ≤4% |
| Video S/N Ratio | ≥45dB (8ch combined) |
| Frequency Response | ≤±1 dB |
| Differential Gain | ≤4% |
| Differential Phase | ≤4° |
| C/L Delay | ≤45ns |
| Audio |  |
| Pre-emphasis time constant | 50μS (B/G,D/K,I) |
|  | 75μS (M/N) |
| Total Harmonic Distortion | ≤1% |
| Frequency Response | ≤±1.5dB (40Hz~15KHz) |
| SMA-701MF |
| Interface |  |
| Slot for modules | 8 |
| RF Output port interface | 75Ω, F-female |
| Test Port(-20dB) interface | 75Ω, F-female |
| RF Output Return Loss | ≥12dB (VHF) ≥10dB (UHF) |
| Output Level | 100dBμV/ch |
| Output Level accuracy | ± 3dB (47 to 862MHz; 0 to 45℃) |
| Harmonics and Spurious | 60dBc typ.; 56dBc min. |
| Others |  |
| Power supply | 90~250ACV, 50/60Hz |
| Power consumption | 200Watts Max. |
| Main Frame Dimensions | 434mm*340.5mm*160.5mm |
| Operation Temperature | 0~45℃ |
| Recommended Operation Humidity | 20~80% Non-condensed |
| Storage Temperature | -20~80℃ |

Application Diagram