IP QAM Modulator

User Manual

About This Manual

Intended Audience

This user manual has been written to help people who have to use, to integrate and to install the product. Some chapters require some prerequisite knowledge in electronics and especially in broadcast technologies and standards.

Disclaimer

No part of this document may be reproduced in any form without the written permission of the copyright owner.

The contents of this document are subject to revision without notice due to continued progress in methodology, design and manufacturing. We shall have no liability for any error or damage of any kind resulting from the use of this document.

Copy Warning

This document includes some confidential information. Its usage is limited to the owners of the product that it is relevant to. It cannot be copied, modified, or translated in another language without prior written authorization from us.

Directory

Chapter 1 Product Overview	1

1.1 Outline	1

1.2 Key Features	1

1.3 Inner Structure	1

1.4 Carrier Setting Illustration	2

1.5 Specifications	2

1.6 Appearance and Illustration	3

Chapter 2 Installation Guide	5

2.1 Acquisition Check	5

2.2 Installation Preparation	5

Chapter 3 Web NMS Management	9

3.1 Login	9

3.2 Operation	9

3.2.1 Summary	9

3.2.2 Parameters	10

3.2.3 System	17

Chapter4 Troubleshooting	20

Chapter 5 Packing list	21

Chapter 1 Product Overview

1.1 Outline

SNR-IPQAM-32 modulator is Mux-scrambling-modulating all-in-one device developed by us. It has 32 multiplexing channels, 32 scrambling channels and 32 QAM (DVB-C) modulating channels, and supports maximum 1024 IP input through the GE port and 32 non-adjacent carriers (50MHz~960MHz) output through the RF output interface. The device is characterized with dual RF output ports which broaden the bandwidth for QAM carriers.

1.2 Key Features

- 2 GE input, Data1 and Data2 (SFP interface optional)

- Supports up to 1024 IP input through GE1 & GE2 over UDP/RTP

- Max 840Mbps for each GE input

- Supports accurate PCR adjusting, CA PID filtering, PID remapping and PSI/SI editing

- Supports up to 256 PID remapping per channel

- Support DVB general scrambling system (ETR289), simulcrypt standards ETSI 101 197 and  ETSI 103 197

- Support 32 multiplexed or scrambled IP out over UDP/RTP/RTSP

- 32 non-adjacent QAM carriers output with 2 RF ports, compliant to DVB-C (EN 300 429) and ITU-T J.83 A/B

- Supports RS (204,188) encoding

- Support Web-based Network management

1.3 Inner Structure

1.4 Carrier Setting Illustration

1.5 Specifications

| Input | Input | 512×2 IP input, 2*100/1000M Ethernet Port(SFP interface optional) |
| --- | --- | --- |
|  | Transport Protocol | TS over UDP/RTP, unicast and multicast, IGMP V2/V3 |
|  | Transmission Rate | Max 840Mbps for each GE input |
| Mux | Input Channel | 1024 |
|  | Output Channel | 32 |
|  | Max PIDs | 256 per channel |
|  | Functions | PID remapping(auto/manually optional) |
|  |  | PCR accurate adjusting |
|  |  | PSI/SI table automatically generating |
| Scrambling Parameters | Max simulscrypt CA | 4 |
|  | Scramble Standard | ETR289, ETSI 101 197, ETSI 103 197 |
|  | Connection | Local/remote connection |
| Modulation Parameters | DVB-C Modulator Sectioon | J.83A | Constellation :16/32/64/128/256QAM |
|  |  |  | Bandwidth :8M |
|  |  | J.83B | Constellation :64/256QAM |
|  |  |  | Bandwidth :6M |
|  | QAM Channel | 32 non-adjacent carrier |
|  | Modulation Standard | EN300 429/ITU-T J.83A/B |
|  | Symbol Rate | 5.0~7.0Msps, 1ksps stepping |
|  | Constellation | 16, 32, 64 , 128, 256QAM |
|  | FEC | RS (204, 188) |
| RF Output | Interface | 2 F type output ports for 32 carriers, 75Ω |
|  | RF Range | 50~960MHz, 1kHz stepping |
|  | Output Level | -20dBm~+10dBm(87~117dbµV), 0.1dB stepping |
|  | MER | ≥ 40dB |
|  | ACLR | -60 dBc |
| TS output | 32 IP output over UDP/RTP/RTSP, unicast/multicast, 2*100/1000M Ethernet Ports (SFP) |
| System | Network management software (NMS) supporting |
| General | Demission | 420mm×440mm×44.5mm (WxLxH) |
|  | Weight | 3kg |
|  | Temperature | 0~45℃(operation), -20~80℃(storage) |
|  | Power Supply | AC 100V±10%, 50/60Hz or AC 220V±10%, 50/60Hz |
|  | Consumption | 15.4W |

1.6 Appearance and Illustration

Front panel Illustration

Rear Panel Illustration:

| 1 | NMS: network management port |
| --- | --- |
| 2 | Indicators |
| 3 | 2 RF output ports |
| 4 | Reset IP: Reset webmaster IP address, recover it to default IP address |
| 5 | Data Input /Output 1/2 |
| 6 | Power switch |
| 7 | AC Power Socket |
| 8 | Grounding |

Chapter 2 Installation Guide

2.1 Acquisition Check

When user opens the package of the device, it is necessary to check items according to packing list. Normally it should include the following items:

- IP QAM Modulator

- User’s Manual

- Power Cord

If any item is missing or mismatching with the list above, please contact local dealer.

2.2 Installation Preparation

When users install device, please follow the below steps. The details of installation will be described at the rest part of this chapter. Users can also refer rear panel chart during the installation.

The main steps of the installation include:

- Checking the possible device missing or damage during the transportation

- Preparing relevant environment for installation

- Installing SNR-IPQAM-32 Modulator

- Connecting signal cables

- Connecting communication port (if it is necessary)

2.2.1 Device’s Installation Flow Chart Illustrated as follows：

2.2.2 Environment Requirement

| Item | Requirement |
| --- | --- |
| Machine Hall Space | When user installs machine frame array in one machine hall, the distance between 2 rows of machine frames should be 1.2~1.5m and the distance against wall should be no less than 0.8m. |
| Machine Hall Floor | Electric Isolation, Dust Free Volume resistivity of ground anti-static material: 1X107~1X1010, Grounding current limiting resistance: 1M (Floor bearing should be greater than 450Kg/㎡) |
| Environment Temperature | 5~40℃(sustainable ), 0~45℃(short time) installing air-conditioning is recommended |
| Relative Humidity | 20%~80% sustainable 10%~90% short time |
| Pressure | 86~105KPa |
| Door & Window | Installing rubber strip for sealing door-gaps and dual level glasses for window |
| Wall | It can be covered with wallpaper, or brightness less paint. |
| Fire Protection | Fire alarm system and extinguisher |
| Power | Requiring device power, air-conditioning power and lighting power are independent to each other. Device power requires AC power 220V ±10% 50/60Hz or 110V ±10% 50/60Hz. Please carefully check before running. |

2.2.3 Grounding Requirement

- All function modules’ good grounding is the basis of reliability and stability of devices. Also, they are the most important guarantee of lightning arresting and interference rejection. Therefore, the system must follow this rule.

- Coaxial cables’ outer conductor and isolation layer should keep proper electric conducting with the metal housing of device.

- Grounding conductor must adopt copper conductor in order to reduce high frequency impedance, and the grounding wire must be as thick and short as possible.

- Users should make sure the 2 ends of grounding wire well electric conducted and be antirust.

- It is prohibited to use any other device as part of grounding electric circuit

- The area of the conduction between grounding wire and device’s frame should be no less than 25mm2.

2.2.4 Frame Grounding

All the machine frames should be connected with protective copper strip. The grounding wire should be as short as possible and avoid circling. The area of the conduction between grounding wire and grounding strip should be no less than 25mm2.

2.2.5 Device Grounding

Connecting the device’s grounding rod to frame’s grounding pole with copper wire.

2.3 Wire’s Connection

2.3.1 Power cord connection

The power socket is located on the right of rear panel, and the power switch is on the left of front panel. User can plug one end of the power cord to the socket and insert the other end to AC power. When the device solely connects to protective ground, it should adopt independent way, say, share the same ground with other devices. When the device adopts united way, the grounding resistance should be smaller than 1Ω.

Caution: Before connecting power cord to SNR-IPQAM-32 Modulator, user should set the power switch to “OFF”.

2.3.2 Signal and NMS Cable Connection

The signal connections include the connection of input signal cable and the connection of output signal cable. The details are as follows:

IP QAM Modulator Cable Illustration:

- RF Input/Loop Cable Illustration:

- NMS Cable illustration (CAT5):

Chapter 3 Web NMS Management

This device does not support the LCD operation, and the modification can only be operated under Web NMS.

3.1 Login

The factory default IP address is 10.0.0.101/102/103 the module which closes to power is 10.0.0.101, and users can connect the device and web NMS through this IP address.

Connect the PC (Personal Computer) and the device with a net cable, and use ping command to confirm they are on the same network segment. For instance, the PC IP address is 192.168.99.252, we then change the device IP to 192.168.99.xxx (xxx can be 0 to 255 except 252 to avoid IP conflict).

Launch the web browser an input the device IP address in the browser’s address bar and press Enter.

It displays the Login interface as Figure-1. Input the Username and Password (Both the default Username and Password are “admin”. And then click “Login” to start the device setting.

Figure-1

3.2 Operation

3.2.1 Summary

When we confirm the login, it displays the summary interface as Figure-2.

Figure-2

3.2.2 Monitor

Monitor → Input Status:

Clicking “Input Status”, it will display the interface as Figure-3 where users can check the input status of GE1 and GE 2. Users need to add IP input in “TS Config” part. Otherwise, it will monitor nothing.

Figure-3

Monitor → Output Status:

Clicking “Output Status”, it will display the interface as Figure-4 where users can check output status of the 32 IPs and 32 carriers. User need to enable the output status in “Modulator” and “IP Stream” part. Otherwise, it will monitor nothing as Figure-5.

Figure-4

Figure-5

3.2.3 Parameters

Parameters → TS Config:

- Output TS X

Click “Output TS X”, it displays the interface as Figure-6. Users can select the output TS channels.

Click “Stream Select”, it displays the interface where users can choose the programs to Mux out.

Figure-6

- Stream Select

Clicking “Stream Select”, and click “+” to add IP input, then select one channel to parse, it will display the interface where users can choose the programs to Mux out. (Figure-7)

Figure-7

Configure ‘Input Area’ and ‘Output Area’ with buttons in ‘Operation Area’. Instructions are as below:

: To add input channel which come from GE1 or GE 2 or connector

: To edit the input channel

: To delete the input channel

: To delete all inputs channel

: To check input IP lock or not, green means current IP locked

: To check current TS overflow or not, red color means current TS overflow, need reduce program

：Enable/disable the CA Filter function. Clicking the box, user can filter the input CA to avoid disturbing with the device scrambling function.

: To enable/disable the PID remapping

To refresh the input program information

To refresh the output program information

Select one input program first and click this button to transfer the selected program to the right box to output.

Similarly, user can cancel the multiplexed programs from the right box.

To select all the input programs

To select all the output programs

To parse programs time limitation of parsing input programs

Program Modification:

The multiplexed program information can be modified by clicking the program in the ‘output’ area. For example, when clicking, it triggers a dialog box (Figure-8) where users can input new information.

Figure-8

- General

Click “General”, it displays the interface where users can set parameters for each output channel. (Figure-9)

Figure-9

- PID Pass

Clicking “PID Bypass”, it will display the interface as Figure-10 where user can add PIDs to be passed, click the “+” symbol, input current IP channel number, then input current IP source PID and output PID which is customer needed , then click “set” to apply the parameters.

Figure-10

Parameters → Scrambler:

Clicking “Scrambler”, it will display the interface where users can choose the programs to scramble. (Figure-11)

Figure-11

Parameters → Modulator:

Clicking “Modulator”, it will display the interface as Figure-12/13 where to set RF output parameters. This device supports output 32 DVB-C carriers through 2 RF ports, so users can select output all the 32 carriers through one RF port or through two RF ports. Carrier 1-16 out through RF1 port and carrier 17-32 out through RF 2 port usually.

RF1:

Figure-12

RF2:

Figure-13

When users click “quickly config” button, it triggers a dialog box (Figure-14) where users can set all channels configurations.

Figure-14

Click “Channel config” button, it triggers a dialog box (Figure-15) where users can set the corresponding channel configuration.

Figure-15

Parameters → IP Stream:

This device supports TS to output in IP (32*MPTS) format through the GE1 &GE2 ports.

Click “IP Stream”, it displays the interface as Figure-16 where to set IP out parameters.

Figure-16

When users click “quickly config” button, it triggers a dialog box (Figure-17) where users can set all channels configurations.

Figure-17

Click “Channel config” button, it triggers a dialog box (Figure-18) where users can set the corresponding channel configuration.

Figure-18

3.2.3 System

System → Network:

Click ‘Network’, it displays the interface as Figure-19 where to set network parameters.

Figure-19

System → Password:

Click “Password”, it displays the screen as Figure-20 where to set the login account and password for the web NMS.

Figure-20

System → Configuration:

Click “Configuration”, it displays the screen as Figure-21 where to set your configurations for the device.

Figure-21

System → Firmware:

Click “Firmware”, it displays the screen as Figure-22 where to update firmware for the device.

Figure-22

System → Date/Time:

Clicking “Date/Time”, it will display the interface as Figure-23 where users can set date/time for this device.

Figure-23

System → Log:

Click “Log”, it displays the screen as Figure-24 where to check the “Log”.

Figure-24

Chapter 4 Troubleshooting

Our ISO9001 quality assurance system has been approved by CQC organization. For guarantee the products’ quality, reliability and stability. All of our products have been passed the testing and inspection before ship out factory. The testing and inspection scheme already covers all the Optical, Electronic and Mechanical criteria which have been published by us. To prevent potential hazard, please strictly follow the operation conditions.

Prevention Measure

- Installing the device at the place in which environment temperature between 0 to 45 °C

- Making sure good ventilation for the heat-sink on the rear panel and other heat-sink bores if necessary

- Checking the input AC voltage within the power supply working range and the connection is correct before switching on device

- Checking the RF output level varies within tolerant range if it is necessary

- Checking all signal cables have been properly connected

- Frequently switching on/off device is prohibited; the interval between every switching on/off must greater than 10 seconds.

Conditions need to unplug power cord

- Power cord or socket damaged.

- Any liquid flowed into device.

- Any stuff causes circuit short

- Device in damp environment

- Device was suffered from physical damage

- Longtime idle.

- After switching on and restoring to factory setting, device still cannot work properly.

- Maintenance needed

Chapter 5 Packing list

- IP QAM Modulator                                     1 pc

- Power Cord                                           1 pc

# Text boxes

User can click any item here to enter the corresponding interface to check information or set the parameters.

This field indicates the current multiplexed outputting programs. The programs selected will be scrambled.

Scramble channel (1-32) select

CA channel select

EMMG and ECMG working state, green means it work normally, while red means communication error or no communication.

Channel Config:

Click to set each channel (1~16) RF QAM output parameters

Select areas

Quickly Config:

Click to set all channels RF QAM output parameters

To select “Kernel log” and “System Log”

1

4

2

3

To select output TS channel 1-32

Channel Config:

Click to set each channel (17~32) RF QAM output parameters

Click the box to enable the status

Quickly Config

Channel Config

Click to enable the status and select TS out thru Data 1 & Data 2

Login this IP address to management device

Set output IP address

Set data port IP address

Input Area

Output Area

Operation Area

Set output IP address of streamer

5

6

7

8