User Manual

SNR VP - 7040

IP Phone

Table of Content

1.	WELCOME	3

2.	WHAT IS IN THE PACKAGE	3

3.	PRODUCT OVERVIEW	3

4.	Key Features	3

4.1.	Hardware specification	4

5.	INSTALLATIONS	5

6.	Get Familiar With The Buttons	7

6.1.	Keypad Button	7

7.	BASIC OPERATIONS	8

7.1.	Make Phone call	8

7.1.1.	Handset, Speakerphone and Headset Mode	8

7.1.2.	Multiple SIP Accounts and Lines	8

7.1.3.	Completing Calls	9

7.1.4.	Making Calls using IP Addresses	11

7.1.5.	Quick IP Call Mode	12

7.2.	ANSWERING PHONE CALLS	12

7.2.1.	Receiving Calls	12

7.3.	PHONE FUNCTIONS DURING A PHONE CALL	13

7.3.1.	Call Hold	13

7.3.2.	Call Waiting	13

7.3.3.	Call Transfer	13

7.3.3.1	Blind Transfer	13

7.3.3.2	Attended Transfer	13

7.3.4.	Conference Call	14

7.3.5.	Mute/Delete/Reject incoming calls	14

7.3.6.	Voice Messages (Message Waiting Indicator)	14

7.3.7.	SMS (Short Messaging Service)	14

7.3.8.	Do Not Disturb	15

7.4.	CALL FEATURES	15

7.4.1.	Call Features Tables	15

7.4.2.	XML Phonebook	15

8.	CONFIGURATION GUIDE	16

8.1.	CONFIGURATION VIA KEYPAD	16

8.2.	Configuring SNR VP - 7040 using Web Browser	19

8.2.1.	Accessing the Web Configuration	19

8.2.1.1	Programming SNR VP - 7040 via the LAN Port	20

8.2.1.2	Programming SNR VP - 7040 via the WAN Port	20

8.2.2.	User Programming and Configuration	20

8.2.3.	Passwords	21

8.2.4.	Configuration Options and Explanations	21

8.2.4.1	Device Status	21

8.2.4.2	Basic Options	22

8.2.4.3	Super Options	23

8.2.4.4	Account 1&2 Options	25

8.3.	Saving the Configuration Changes	32

8.4.	Rebooting the SNR VP - 7040	32

8.5.	Configuration through a Central Server	32

9.	SOFTWARE UPGRADE	33

10.	RESTORE TO FACTORY DEFAULT SETTINGS	33

11.	TECHNICAL SUPPORT CONTACT	34

# WELCOME

The IP PHONE SNR VP - 7040 is an internet telephone set that features superb audio quality, rich functionalities, high level of integration, and compactness. By converting analog voice for transmission over the internet, the IP Phone SNR VP - 7040 allows users with broadband internet connections to make calls to and from anywhere in the world. The  IP PHONE SNR VP-7040 is fully compatible with SIP industry standard and can     interoperate with many other SIP compliant devices and software on the market

# WHAT IS IN THE PACKAGE

The SNR VP - 7040 package contains:

- One SNR VP - 7040 VoIP Phone

- One universal power supply

- One Ethernet cable

# PRODUCT OVERVIEW

# Key Features

- Support SIP 2.0 (RFC 3261), TCP/UDP/IP, RTP/RTCP, HTTP, ICMP, ARP/RARP, DNS, DHCP, NTP, PPPoE, STUN, UPNP,TFTP, etc.

- Powerful Digital Signal Processing (DSP) technology to ensure superior audio quality

- Support  various  codecs  including  G.711  (PCM  a-law  and  u-law),  G.723.1 , G.729A, G.726.

- Support standard encryption and authentication (DIGEST using MD5, MD5-sess)

- Support for Layer 2 (802.1Q VLAN, 802.1p) and Layer 3 QoS (ToS, DiffServ, MPLS)

- Support  Silence  Suppression,  VAD  (Voice  Activity  Detection),  CNG  (Comfort  Noise Generation), Acoustic Echo Cancellation (AEC) with Acoustic Gain Control(AGC) for speakerphone mode.

- Support automated provisioning for mass deployment ,RTP and TLS (pending)for security protection

- Support automated NAT traversal without manual manipulation of firewall/NAT

- Support numeric  Caller  ID  Display, Hold, Transfer, Forward, 3-way Conference, in-band and out-of-band DTMF, Download Phone Book(XML, up to 120 items), Call Waiting, Call Log, Off-hook Auto Dial, Auto Answer, Downloadable Ringtones, SMS,Direct IP Call, Intercom, Paging, Pick up.

- Support syslog, full duplex hands-free speakerphone with advanced acoustic echo cancellation, redial, volume control, voice mail with indicator, downloadable ring tones.

- Provide  easy  configuration  through  manual  operation  (phone  keypad),  Web  interface  or automated centralized configuration file via TFTP or HTTP

- Support 5 navigation/menu/volume keys, 13 dedicated function keys for: HOLD, SPEAKERPHONE, SEND/REDIAL, MUTE, TRANSFER, CONFERENCE, and MESSAGE(with message indicator),LINE1,LINE2,DND,INTERCOM,PHONE BOOK,PICK UP,PAGING.

- Support multi-language: English, Chinese, Japan, etc

Feature Highlights

- 80×39mm LCD with back-lit，support 4 lines with 16 characters every line

- 2 line appearances with LED and 2 independent SIP accounts

- dual switched audio –sensing 10/100Mbps network ports with integrated POE(option)

- Support headset jack

- Support xml phone book, paging, intercom, pick up, SMS etc.

## Hardware specification

| Model | SNR VP - 7040 |
| --- | --- |
| LAN interface | 1x RJ45 100Base-T |
| PC interface | 1x RJ45 100Base-T |
| Universal switching power supply | Input: 100-240VAC 50-60 Hz Output: +5VDC, 1200mA CE/FCC/UL certification |
| Dimension | 220 x 185 x 55 mm (L x W x H) |
| Weight | 1.08kg |
| Temperature | 40 – 130 F 5 – 45 C |
| Humidity | 10 - 90% |

# INSTALLATIONS

| Power Jack | 5V DC power port; UL Certified |
| --- | --- |
| PC | 10/100Mbps RJ-45 ports for PC (downlink) connection. |
| LAN+POE(option) | 10/100Mbps RJ-45 port for LAN (uplink) connection. Supports PoE (802.3af).Draws power from either spare line or signal line. |
| Headset Jack | 3.5mm |

Following are the steps to install a SNR VP - 7040 :

- Insert power adapter into back of the phone and connect it to a power outlet

- Connect internet cable from back of the phone (WAN Port) to broadband modem, router, hub, or switch

- connect internet cable from back of the phone(PC Port) to a PC.

SAFETY COMPLIANCES

The SNR VP-7040 phone complies with FCC/CE and various safety standards. The SNR VP-7040 power adaptor is compliant with the UL standard. Only use the universal power adaptor provided with the SNR VP-7040 package. The manufacturer’s warranty does not cover damages to the phone caused by unsupported power adaptors.

WARRANTY

If you purchased your SNR VP-7040 from a reseller, please contact the company where you purchased your phone for replacement, repair or refund. If you purchased the product directly from SNR contact your SNR sales and Service Representative for a RMA (Return Materials Authorization) number before you return the product. SNR reserves the right to remedy warranty policy without prior notification.

SNR VP-7040 interface wiring schema:

Note: SNR VP-7040 use 3.5mm headset.

# Get Familiar With The Buttons

## Keypad Button

| Kepad Buttons | Kepad Buttons Definitions |
| --- | --- |
|  | Return to the last screen and shortcut key for Received calls. |
|  | Scroll to previous menu/submenu selection, or rise the volume of the loudhailer |
|  | Enter Keypad Configuration “MENU” mode when phone is in IDLE mode. Use as ENTER key when in Keypad Configuration. |
|  | Scroll to next menu/submenu selection, or lower the volume of the loudhailer |
|  | Go to the next screen and shortcut key for Dialed calls. |
| Line Buttons | Line keys with LED, can be configured to different SIP profiles |
| DND | DO NOT DISTURB key; Press DND to turn “Do not disturb” function on or off. |
|  | Enter to retrieve voice mails or other messages |
| 0 - 9, *(.), # | To input: numbers, *(.), # |
| TRNF | Transfer the present call to another number |
| HOLD | Hold the present call for the moment |
|  | Brings phonebook on screen |
|  | Delete the call history, voice message, etc. |
| INTERCOM | Turn intercom function on/off |
| PICK UP | Turn pick up function on/off |
| CONF | Conference call for three sides |
| SEND | Press SEND to dial a new number or redial the last number dialed. Press send button to send a call immediately before “no key entry timeout” value Ex`pires |
|  | Enable/Disable hands-free speaker mode |

# BASIC OPERATIONS

## Make Phone call

### Handset, Speakerphone and Headset Mode

Handset can be toggled between Speaker and Headset. To switch between Handset and

Speaker/Headset, press the SPEAKER button.

### Multiple SIP Accounts and Lines

SNR VP-7040 can support 2 independent SIP accounts depending on the product model. Each account is capable of independent SIP server, user and NAT settings. Each of the line buttons is “virtually” mapped to an individual SIP account. The name of each account is conveniently printed next to its corresponding button. In off-hook state, select an idle line and the name of the account (as configured in the web interface) is displayed on the LCD and a dial tone is heard.

For example: Configure ACCOUNT 1 and ACCOUNT 2 with Account Name as “VoIP 1”, “VoIP 2”, respectively and ensure that they are active and registered. When LINE1 is pressed, you will hear a dial tone and see “VoIP 1” on the LCD display; when LINE2 is pressed, you will hear a dial tone and see “VoIP 2” on the LCD display.

To make a call, select the line you wish to use. The corresponding LINE LED will light up in green. User can switch lines before dialing any number by pressing the same LINE button one or more times. If you continue to press a LINE button, the selected account will circulate among the registered accounts.

For example: when LINE1 is pressed, the LCD displays “VoIP 1”; If LINE1 is pressed twice, the LCD displays “VoIP 2” and the subsequent call will be made through SIP account 2.

Incoming calls to a specific account will attempt to use its corresponding LINE if it is not in use. When the “virtually” mapped line is in use, the SNR VP-7040 will flash the next available LINE (from left to right, or from top to bottom for Multi Purpose Keys) in green.. A line is ACTIVE when it is in use and the corresponding LED is green..

### Completing Calls

There are seven ways to complete a call:

- DIAL: To make a phone call.

• Take Handset/SPEAKER/Headset off-hook

or press an available LINE key (activates speakerphone)

• The line will have a dial tone and the primary line (LINE1) LED is green..

If you wish, select another LINE key (alternative SIP account).

• Enter the phone number

• Press the SEND key

- REDIAL: To redial the last dialed phone number.

When redialing the phone will use the same SIP account as was used for the last call. Thus, when the second SIP account was made for the last call/call attempt, the phone will use the second account to redial.

• Take Handset/SPEAKER/Headset off-hook or

press an available LINE key (activates speakerphone), the corresponding LED will be green..

• Press the SEND button

- USING THE CALL HISTORY: To call the a phone number in the phone’s history

When using the call history, the phone will use the same SIP account as was used for the last call/call attempt. Thus, when returning a call made to the third SIP account, the phone will use the third SIP account return the call.

•Press the MENU button to bring up the Main Menu.

•Select Call History and then “Received Calls”, “Missed Calls” or “Dialed Calls” depending on your needs

• Select phone number using the arrow keys

• Press OK to select

• Press OK again to dial.

- USING THE PHONEBOOK: Calling a phone in from the phone’s phonebook.

Each entry in the phonebook can be attached to an individual SIP account. The phone will use that SIP account to make the phone call.

• Go to the phonebook by:

.  Pressing the phonebook button , or

Pressing the menu button and Selecting “Phone book” and Press MENU

• Select the phone number by using the arrow keys

• Press OK so select

• Press OK again to dial.

- PAGING:

The paging function can only be used if the SERVER/PBX supports this feature and both the phones and PBX are correctly configured.

• Take the Handset/SPEAKER/Headset off-hook,

• Select the LINE key associated with account

• Press menu key to display LCD: LINEx: PAGE USING.

• Dial the phone number you want to Page

• Press SEND key.

NOTE: Dial-tone and dialed number display occurs after the handset is off-hook and the line key is selected. The phone waits 4 seconds (by default; No key Entry Timeout) before sending and initiating the call. Press the “SEND” or “#” button to override the 4 second delay.

- INTERCOM:

The intercom function can only be used if the SERVER/PBX supports this feature and both the phones and PBX are correctly configured.

• Take the Handset/SPEAKER/Headset off-hook,

• Select the LINE key associated with account

• Press intercom key

• Dial the phone number you want to Intercom

• Press SEND key.

NOTE: Dial-tone and dialed number display occurs after the handset is off-hook and the line key is selected. The phone waits 4 seconds (by default; No key Entry Timeout) before sending and initiating the call. Press the “SEND” or “#” button to override the 4 second delay.

- Pick up:

The pick up function can only be used if the SERVER/PBX supports this feature and both the phones and PBX are correctly configured.

• Take the Handset/SPEAKER/Headset off-hook,

• Select the LINE key associated with account

• Press pick up key.

• Dial the phone number you want to pick up.

• Press SEND key.

NOTE: Dial-tone and dialed number display occurs after the handset is off-hook and the line key is selected. The phone waits 4 seconds (by default; No key Entry Timeout) before sending and initiating the call. Press the “SEND” or “#” button to override the 4 second delay.

### Making Calls using IP Addresses

Direct IP calling allows two phones to talk to each other in an ad hoc fashion without a SIP proxy. VoIP calls can be made between two phones if:

• Both phones have public IP addresses, or

• Both phones are on a same LAN/VPN using private or public IP addresses, or

• Both phones can be connected through a router using public or private IP addresses (with necessary port forwarding or DMZ)

To make a direct IP call, please follow these steps:

1. Press MENU button to bring up MAIN MENU.

2. Select “Direct IP Call” using the arrow-keys.

3. Press OK to select.

4. Input the 12-digit target IP address. (Please see example below).

5. Press OK key to initiate call.

To make a quick IP call, please see next section.

For example: If the target IP address is 192.168.1.60 and the port is 5062 (e.g. 192.168.1.60:5062), input the following: 192*168*1*60*5062 - The “ * ” key represent the dot“.” And colon “:”.

Press OK to dial out

### Quick IP Call Mode

The SNR VP-7040 also supports Quick IP call mode. This enables the phone to make direct IP-calls, using only the last few digits (last octet) of the target phone’s IP-number.

This is possible only if both phones are in under the same LAN/VPN. This simulates a PBX function using the CMSA/CD without a SIP server. Controlled static IP usage is recommended.

For example:

192.168.0.2 calling 192.168.0.3 -- dial *473 follow by SEND or #

192.168.0.2 calling 192.168.0.23 -- dial *4723 follow by SEND or #

192.168.0.2 calling 192.168.0.123 -- dial *47123 follow by SEND or #

192.168.0.2: dial *473 and *4703 and *47003 results in the same call -- call 192.168.0.3

NOTE: If you have a SIP Server configured, a Direct IP-IP still works. If you are using STUN, the Direct IPIP call will also use STUN. Configure the “Use Random Port” to “NO” when completing Direct IP calls.

## ANSWERING PHONE CALLS

### Receiving Calls

1. Incoming single call: Phone rings with selected ring-tone. The corresponding account LINE flashes green. Answer call by taking Handset/SPEAKER/Headset off hook or pressing SPEAKER or by pressing the corresponding account LINE button.

2. Incoming multiple calls: When another call comes in while having an active call, the phone will produce a Call Waiting tone (stutter tone). Next available lines will flash green. (as described in section 4.3.2). Answer the incoming call by pressing its corresponding LINE button. The current active call will be put on hold.

3. Paging/Intercom Enabled: Phone beeps once and automatically establishes the call via SPEAKER. (PBX (or Server) must also supports this feature)

## PHONE FUNCTIONS DURING A PHONE CALL

### Call Hold

While in conversation, pressing the “Hold” button will put the remote end on hold. Pressing the “Hold” button again will release the previously Hold state and resume the bi-directional media.

### Call Waiting

If call waiting feature is enabled, while the user is in a conversation, he will hear a special stutter tone if there is another incoming call. User then can press LINE1 or LINE2 button to put the current call party on hold automatically and switch to the other call. Pressing LINE1 or LINE2 button toggles between two active calls.

### Call Transfer

SNR VP - 7040 supports both blind and attended call transfer. Each is easy to use. Use blind transfer if you want to transfer a call without speaking with someone first; use attended transfer if you want to speak with the someone prior to transferring call.

#### Blind Transfer

Transfer an active call to a third party without announcement.

Press the TRANSFER button and wait for a dial tone. Dial the third party’s phone number followed by the SEND button.

NOTE: The “Enable Call Feature” must be configured to “Yes” in the web configuration page to enable this feature.

#### Attended Transfer

Press “LINEx” button to make a call and automatically place the ACTIVE LINE on HOLD. Once the call is established, press “TRNF” key to transfer the call and hang up.

NOTE: To transfer calls across SIP domains, SIP service providers must support transfer across SIP domains. Blind transfer will usually use the primary account SIP profile.

### Conference Call

SNR VP - 7040 phone supports 3-way conference.

Assuming that call party A and B are in conversation. A wants to bring C in a conference:

- A presses the another idle line button to get a dial tone and put B on hold

- A dials C’s number then “SEND” key to make the call

- If C answers the call, then A presses “CONF” button to bring B, C in the conference.

- If C does not answer the call, A can press Line button back to talk to B.

NOTE:

- During the conference, if B or C drops the call, the remaining two parties can still talk. However, if A the conference initiator hangs up, all calls will be terminated.

### Mute/Delete/Reject incoming calls

1. Press the button to enable/disable muting the microphone.

2. The “Line Status Indicator” will show “LINEx: SPEAKING” or “LINEx: MUTE” to indicate whether the microphone is muted.

NOTE: Pressing button for an incoming call will reject the call. button also functions as delete key when user wish to delete the last entered digit.

### Voice Messages (Message Waiting Indicator)

A blinking green MWI (Message Waiting Indicator) indicates a message is waiting. Press the MSG button to retrieve the message. An IVR will prompt the user through the process of message retrieval. Press a specific LINE to retrieve messages for a specific line account.

NOTE:

- Each line has a separate voicemail account. Each account requires a voicemail portal number to be configured in the “voicemail user id” field.

- To check which line account has a message 1) press the message button (this always checks the primary account), 2) check each line for stutter tone or 3) check missed calls using the menu.

### SMS (Short Messaging Service)

The sms can only be used if the SERVER/PBX supports this feature.

If the phone has received a sms, the LCD screen will display the NEW IM.

Press the MENU key, and select the Instand Message, and press OK, the you can check the Input message.

### Do Not Disturb

Press the “DND” button to set phone to ‘do not disturb’ (it will be on the screen). The phone will not ring and send caller directly to voicemail.

## CALL FEATURES

### Call Features Tables

Following table shows the call features of SNR VP - 7040 :

| Key | Call Features |
| --- | --- |
| *30 | Block Caller ID (for all subsequent calls) |
| *31 | Send Caller ID (for all subsequent calls) |
| *67 | Block Caller ID (per call) |
| *82 | Send Caller ID (per call) |
| *50 | Disable Call Waiting (for all subsequent calls) |
| *51 | Enable Call Waiting (for all subsequent calls) |
| *70 | Disable Call Waiting. (Per Call) |
| *71 | Enable Call Waiting (Per Call) |
| *72 | Unconditional Call Forward. To use this feature, dial “*72” and get the dial tone. Then dial the forward number and “#” for a dial tone, then hang up. |
| *73 | Cancel Unconditional Call Forward. To cancel “Unconditional Call Forward”, dial “*73” and get the dial tone, then hang up. |
| *90 | Busy Call Forward. To use this feature, dial “*90” and get the dial tone. Then dial the forward number and “#” for a dial tone, then hang up. |
| *91 | Cancel Busy Call Forward. To cancel “Busy Call Forward”, dial “*91” and get the dial tone, then hang up. |
| *92 | Delayed Call Forward. To use this feature, dial “*92” and get the dial tone. Dial the forward number and “#” for a dial tone and then hang up. |
| *93 | Cancel Delayed Call Forward. To cancel this feature, dial “*93”, get the dial tone, and then hang up. |
| Flash/Hook | call waiting indication. When in conversation without an incoming call, this action will switch to a new channel to make a new call. |

### XML Phonebook

The SNR VP-7040 supports a download XML phonebook.

# CONFIGURATION GUIDE

## CONFIGURATION VIA KEYPAD

To enter the MENU, press the central button. Navigate the menu by using the arrow keys: up/down and left/right.

| Call History | Displays histories of incoming, dialed and missed calls. |
| --- | --- |
| Phone Book | Displays the New Entry and you can download the phonebook. |
| Status | Displays the network status, account statuses, software version and MAC-address of the phone. |
| Instant Message | Goes to instant messages |
| Direct IP Call | Displays the ip call options menu |
| Config | Press Menu button to display the configuration selections: • Network To enable/disable DHCP. To setup IP-address, Net mask and Gateway address • Account • Upgrade In this menu setting regarding the firmware server and configure server can be changed. It also enables the user to make the phone attempt to download new firmware. • Factory Reset Press Menu button and the Confirm Factory Reset to reset FACTORY DEFAULT setting. Do not use Factory Reset unless you want to restore factory settings Press ‘’ to return the main menu. |
| Preference | Press Menu button to enter this sub menu including • Ring Tone Choose different ring tones in the “Ring Tone” menu. • Ring Volume Press Menu button to hear the selected ring volume, press ‘’ or ’’ to hear and adjust the ring tone volume.. Press ‘’ to return to the main menu. |
| Factory Functions | Press Menu to display the factory function items including • Audio Loopback Speak into the handset. If you hear your voice in the handset, your audio works fine. • Diagnostic Mode All LEDs will light up Press any key on the keypad, to display the button name in the LCD. Lift and put back the handset. Press ‘’ to return to the main menu. |
| Reboot | Press Menu button to reboot the device And choose Confirm Reboot or Cancel Reboot. |

The main configuration menu is the Config menu. This menu consists of four submenus that allow you to configure and display information about the SNR VP - 7040. Table 5 shows the available menus and their uses.

Configuration Menus and Their Functions

| option | Used To |
| --- | --- |
| Network | assign network settings such as the IP Mode, IP, Netmask and Gateway |
| Account | assign Account information such as the SIP Proxy, Outbound Proxy, User ID, Auth ID, Password, User Name, Audio, Confirm Save, Return & Cancel. |
| Upgrade | assign Upgrade Settings such as the Firmware Server, Configure Server, Upgrade Via. |
| Factory Reset | Choose whether to restore factory settings |

Navigating the Menus

The following information will help you understand the interface for the configuration menus.

- Press the MENU key to access the Setup menu.

- Use the ▲ and ▼ keys to scroll through the menu choices.

- When the desired menu option is indicated by →, press the MENU key again to select the indicated option.

- Press the  to return to the previous screen.

Network Setting

The Network Setting sub-menu is used to assign network settings such as the IP Mode, IP, Netmask and Gateway. All sub-menus under Network Setting are password protected and can be altered only by an administrator. Users may view the information but not change it.

Step1: Press the MENU key to enter the Setup menu

Step2: Choose the Config sub-menu and press MENU again.

Step3: Choose the Network sub-menu and press MENU

Step4: Chooose the IP Mode sub-menu and press MENU

Step5: Use the ▼ and ▲ keys to choose the mode you want

Then press  to go to the sub-menu IP Mode, and config IP, Netmask, Gateway as above.

IP display the IP address at the moment, you can input new IP address while the DHCP is set OFF.(Press MENU key to return to the previous screen.)

Account Setting

The Account Setting sub-menu is used to assign Account information such as the SIP Proxy, Outbound Proxy, User ID, Auth ID, Password, User Name, Audio, Confirm Save and Return & Cancel.

Step1: Return to the Config sub-menu

Step2: Choose the Acct sub-menu and press MENU again.

Step3: Choose the SIP Proxy sub-menu and press MENU again.

Step4: Input the valid SIP proxy server and press MENU key to return to the previous screen.

You can config Outbound Proxy, User ID, Auth ID, Password, User Name, Audio as above.(the specifications of these can be found from 8.2.4.4  Account 1 Options) and choose Confirm Save or Return & Cancel after you finish configuration.

Another Account can be configured as the same.

Upgrade Setting

The Upgrade Setting sub-menu is used to assign Upgrade Settings such as the Firmware Server, Configure Server and Upgrade Via.

Step1: Return to the Config sub-menu.

Step2: Choose the Upgrade sub-menu and press MENU again.

Step3: Choose the Firmware Server sub-menu and press MENU again.

Step4: Input the valid Firmware Server and press MENU key to return to the previous screen

You can config Configure Server, Upgrade Via as above. (the specifications of these can be found from 8.2.4.3 Super Options )

Factory Reset Setting

Step1: Return to the Config sub-menu.

Step2: Choose the Factory Reset sub-menu and press MENU again.

Step3:Choose Confirm Factory Reset or Cancel Factory Reset.

## Configuring SNR VP - 7040 using Web Browser

SNR VP - 7040  has embedded Web server and HTML pages that allow users to configure the SNR VP - 7040  through an easy-to-use Web browser interface such as Microsoft’s Internet Explorer or Netscape browser. Below is a screen shot of the SNR VP - 7040  configuration page:

### Accessing the Web Configuration

The SNR VP - 7040 configuration page can be accessed via the LAN or WAN port.

The GUI interface can be download at bellow:

This gui include bellow pages:

- SCREENSHOT OF DEVICE STATUS PAGE

- SCREENSHOT OF BASIC OPTIONS PAGE

- SCREENSHOT OF SUPPER OPTIONS PAGE

- SCREENSHOT OF ACCOUNT 1 PAGE

- SCREENSHOT OF ACCOUNT 2 PAGE

#### Programming SNR VP - 7040 via the LAN Port

To program SNR VP - 7040 via the LAN port, directly connect an Ethernet cable from your PC to the LAN port of the SNR VP - 7040.  After connecting the cable, confirm that the green light of the LAN port is on. If the green light is not on, this means that your PC is not yet properly connected to the SNR VP - 7040 via the LAN port.

For LAN port configuration, use the following default IP address to access the device:

http://192.168.22.1

#### Programming SNR VP - 7040 via the WAN Port

The WAN port access for web configuration is disabled by default from the factory. To access the web configuration menu from the WAN port, you must first access the device via the device LAN port (see instructions above “Programming SNR VP - 7040 via the LAN port”) and enable the “Enable WAN Web Access” option.

After enabling WAN access, be sure that the WAN port of the SNR VP - 7040 is connected to an uplink (i.e. router, hub, switch, etc). Then, get the WAN IP address of the SNR VP - 7040 by following section 5.1 of this user manual and selecting menu option 02.  Then, access the SNR VP - 7040 via your web browser by entering the WAN IP address:

http://SNR VP - 7040’s IP Address

Be sure that your PC is connected to the router/hub/switch directly or via the LAN port (which also serves as a pass-through connection for internet/network access for your PC) of the SNR VP - 7040.

### User Programming and Configuration

From your web browser, the SNR VP - 7040 will show the following login screen:

Enter the password and click on the “Login” button

### Passwords

Passwords are case sensitive and all SNR VP - 7040 devices come with factory default passwords as indicated below:

Advanced User Password for access to Super User Options:  admin

End User Password for access to Basic User Options:  1234

Pages available for the end-user are:

• Device Status

• Basic Options

Additional pages available to super user are:

• Super Options.

• ACCOUNT 1

• ACCOUNT 2

### Configuration Options and Explanations

After a correct password is entered in the login screen, the embedded web server inside the SNR VP - 7040 will show the configuration page, which is explained in details below:

#### Device Status

| DEVICE STATUS |
| --- |
| Setting Options | Definitions |
| MAC Address | The device ID, in HEX format. This is a very important ID for ISP troubleshooting. |
| WAN IP Address | This field shows IP address of device |
| Product Model | This product model is SNR VP-2101 |
| Software Version | Information of software |
| System Uptime | Show system uptime since last reboot |
| PPPoE Link Up | Indicates where the PPPoE connection is up if the Uicorn2101 is connected to the DSL modem. |
| NAT | Indicate the NAT type behind which the device is when the stun feature is defined. |
| Port Status | Indicate the current status of the device such as hook (on/off),registion(registered/unregistered) etc. |

#### Basic Options

| BASIC OPTIONS Setting |
| --- |
| Setting options | Definitions |
| Web Port | The default is 80. |
| IP Address | There are 3 modes under which the SNR VP - 2101 can operate: - If DHCP mode is enabled, then all the field values for the Static IP mode are not used (even though they are still saved in the chipset's memory). The SNR VP - 2101 will acquire its IP address from the first DHCP server it discovers from the office/home network it is connected to. -To use the PPPoE feature, the PPPoE account settings need to be set. The SNR VP - 2101 will attempt to establish a PPPoE session if any of the PPPoE fields have been entered with data. - If Static IP mode is enabled, then the IP address, Subnet Mask, Default Router IP address, DNS Server 1 (primary), DNS Server 2 (secondary) fields will need to be configured by the user. These fields are reset to zero by default. |
| Time Zone | This parameter controls how the displayed date/time will be adjusted according to the specified time zone. |
| Allow DHCP Option 2 to override Time Zone setting | If set yes and under DHCP mode,the device will try to get option 2 from DHCP configure and overwrite Time Zone. |
| Daylight Savings Time | This parameter controls whether the displayed time will be daylight savings time or not. If set to Yes, then the displayed time will be 1 hour ahead of normal time. |
| Date Display Format | Choose one of following format: Year-Month-Day Month-Day-Year Day-Month-Year |
| Display Info of LCD | Choose one of following ways: Display IP Address Display Information Display alternately IP and above Information |
| Keypad DTMF Tone Off | Default is NO. |
| Device Mode | This parameter controls whether the device is working in NAT router mode or Bridge mode. Need save the setting and reboot the device before the setting start to work |
| LAN Subnet Mask | Sets the LAN subnet mask. Default value is 255.255.255.0 |
| LAN DHCP Base IP | Base IP for the LAN port which functions as a Gateway for the subnet. Default value is 192.168.22.1 |
| DHCP IP Lease Time | Value is set in units of hours. Default value is 120 hrs (5 Days.) The time IP address is assigned to the LAN clients. |
| Port Map | Forwards a matching (TCP/UDP) port to a specific LAN IP address with a specific (TCP/UDP) port. |
| End User Password | This contains the password to access the Web Configuration Menu. This field is case sensitive. |
| Reply to ICMP on WAN Port | If set to Yes, the SNR VP-2101 will respond to the PING command from other computers, but it also is vulnerable to the DOS attack. Default is No. |
| WAN Side Http Access | If this parameter is set to No, the Http access via WAN port is disabled. |

#### Super Options

| SUPER OPTIONS |
| --- |
| Setting options | Definitions |
| Admin Password | This contains the password to access the Advanced Web Configuration page. This field is case sensitive. Only the administrator can configure the “Advanced Settings” page. Password field is purposely left blank for security reasons after clicking update and saved. The maximum password length is 26 characters,only digit or letter. |
| STUN server | IP address or domain name of stun server. |
| keep-alive interval | This parameter specifies how often the SNR VP - 2101 sends a blank UDP packet to the SIP server in order to keep the “hole” on the NAT open. |
| No Key Entry Timeout | Default is 4 seconds. |
| Layer 3 QoS | This field defines the layer 3 QoS parameter which can be the value used for IP Precedence or Diff-Serv or MPLS. Default value is 48. |
| Layer 2 QoS | This contains the value used for layer 2 VLAN tag. Default setting is 0. |
| Data VLAN Tag | When using Bridge Mode, Data VLAN Tag is supported. when your PC connect to LAN Port, data (from your PC to switch) will be tagged with "Data VLAN Tag". |
| Firmware Upgrade and Provisioning | Upgrade or provisioning through TFTP or TFTP server. --Upgrade Via:select HTTP or TFTP mode. --Allow DHCP Option: support 66,128,150. If select yes,device will get server information from DHCP option and ignore the Config Server Path. Option 66--TFTP server name(if you select Upgrade Via->TFTP), HTTP server name(if you select Upgrade Via->HTTP) Option 128--TFPT Server IP address.(if you select Upgrade Via->TFTP), HTTP Server IP address(if you select Upgrade Via->HTTP) Option 150--TFTP server address.(if you selectUpgrade Via->TFTP), HTTP server address(if you select Upgrade Via->HTTP) |
| Phonebook XML | Enable the XML phonebook via TFTP or HTTP. Define XML server path and download mode. |
| NTP Server | This parameter defines the URI or IP address of the NTP server which is used by the SNR VP - 2101 to set the current date/time. |
| Allow DHCP Option 42 to override NTP server | If set Yes,device can get NTP server from DHCP option 42. |
| Authenticate Conf File | configure file would be authenticated before acceptance if set to Yes |
| Override MTU Size | Override the MTU size to meet some special network settings. |
| Lock Keypad Update | If this parameter is set to Yes, the configuration update via keypad is disabled. |
| Syslog Server | The IP address or URL of System log server. This feature is especially useful for the ITSP (Internet Telephone Service Provider) |
| Syslog Level | Default is blank, the feature is useful for the Internet Telephone Service Provider. |
| Download Device Configuration: | User can download configuration from the web page and save to configuration file. |
| Distinctive Ring Tone | Caller ID must be configured. Select a Distinctive Ring Tone 1 through 3 for a particular Caller ID. The device will ONLY use selected ring tones for particular Caller IDs. For all other calls, the device will use System Ring Tone. When selected and no Caller ID is configured, the selected ring tone will be used for all incoming calls.. |
| Call Progress Tones | Using these settings, users can configure tone frequencies and cadence according to their preference. By default they are set to North American frequencies. Configure these settings with known values to avoid uncomfortable high pitch sounds. ON is the period of ringing (“On time” in ‘ms’) while OFF is the period of silence. In order to set a continuous tone, OFF should be zero. Otherwise it will ring ON ms and a pause of OFF ms and then repeat the pattern. Example configuration for N.A. Dialtone: f1=350@-13,f2=440@-13,c=0/0; Syntax: f1=freq@vol, f2=freq@vol, c=on1/off1-on2/off2-on3/off3; [...] (Note: freq: 0 - 4000Hz; vol: -30 - 0dBm) |
| System Ring Tone | System ring tone. Default is North American standard. Adjust system ring tone frequencies and cadences based on local telecom standard. |
| Restore Configuration | User can restore the before configuration from the configuration file saved at local pc |

#### Account 1&2 Options

| ACCOUNT |
| --- |
| Setting options | Definitions |
| Account Active: | Set to the YES, the account can be available |
| SIP Server | SIP Server’s URI or IP address |
| Outbound Proxy | SIP Outbound Proxy Server’s URI or IP address |
| NAT Traversal | This parameter defines whether the SNR VP - 2101 NAT traversal mechanism will be activated or not. If Choosing No,nothing to do. If Choosing No, but send keep-alive, the SNR VP - 2101 will periodically (every 20 seconds or so) send a blank UDP packet (with no payload data) to the SIP server to keep the “hole” on the NAT open. If choosing STUN and a STUN server is also specified, then the SNR VP - 2101 will behave according to the STUN client specification. Under this mode, the embedded STUN client inside the SNR VP - 2101 will attempt to detect if and what type of firewall/NAT it is sitting behind through communication with the specified STUN server. If the detected NAT is a Full Cone, Restricted Cone, or a Port-Restricted Cone, the SNR VP - 2101 will attempt to use its mapped public IP address and port in all its SIP and SDP messages. If choosing STUN with no specified STUN server, the SNR VP - 2101 will periodically (every 20 seconds or so) send a blank UDP packet (with no payload data) to the SIP server to keep the “hole” on the NAT open. If choosing UPNP, the embedded UPNP client inside the SNR VP - 2101 will attempt to mapping ports with the router by upnp protocol. |
| SIP User ID | SIP service subscriber’s User ID |
| Authenticate ID | SIP service subscriber’s Authenticate ID. Can be identical to or different from SIP User ID |
| Authenticate Password | SIP service subscriber’s account password |
| Name | SIP service subscriber’s name which will be used for Caller ID display |
| Use DNS SRV | Default is No. If set to Yes the client will use DNS SRV for server lookup |
| User ID is phone number | If the SNR VP - 2101 has an assigned PSTN telephone number, this field should be set to “Yes”. Otherwise, set it to No. If Yes is set, a “user=phone” parameter will be attached to the “From” header in SIP request |
| SIP Registration | This parameter controls whether the SNR VP - 2101 needs to send REGISTER messages to the proxy server. The default setting is Yes. |
| Unregister On Reboot | Default is No. If set to Yes, the SIP user will be unregistered on reboot. |
| Register Expiration | This parameter allows the user to specify the time frequency (in minutes) the SNR VP - 2101refreshes its registration with the specified registrar. The default interval is 6 minutes, The maximum interval is 65535 minutes (about 45 days). |
| Outgoing Call without Registration | Default is No. If set to “Yes,” user can place outgoing calls even when not registered (if allowed by ITSP) but is unable to receive incoming calls. |
| Local SIP port | This parameter defines the local SIP port the SNR VP - 2101 will listen and transmit. The default value for FXS port is 5060. The default value for FXO port is 5062. |
| Local RTP port | This parameter defines the local RTP-RTCP port pair the SNR VP - 2101 will listen and transmit. It is the base RTP port for channel 0. When configured, channel 0 will use this port _value for RTP and the port_value+1 for its RTCP; channel 1 will use port_value+2 for RTP and port_value+3 for its RTCP. The default value for FXS port is 5004. The default value for FXO port is 5008. |
| Use random port | This parameter, when set to YES, will force random generation of both the local SIP and RTP ports. This is usually necessary when multiple SNR VP - 2101 are behind the same NAT. |
| Refer-To Use Target Contact | Default is NO. If set to YES, then for Attended Transfer, the “Refer-To” header uses the transferred target’s Contact header information. |
| Voice Mail UserID | When configured, user can access messages by pressing “MSG” button. This ID is usually the VM portal access number. |
| Intercom Dial Code | This field is used to configure the Intercom key in the phone. If the phone is working with a IP-PBX which support intercom/page function,it can be configured in the following manner: • To page an extension : [intercom feature code]+[*]+[extension number] • To page a group : [paging group feature code]+[*]+[group extension] |
| Pick Up Dial Code | This field is used to configure the pick up key in the phone. If the phone is working with a IP-PBX which support pick up function,it can be configured in the following manner: When extension A(for example, it’s number is 201) is ringing, you press the pick up key of your phone, and then dial the 201, you can pick up this call. |
| DTMF Payload Type | Sets the payload type for DTMF using RFC2833 |
| DTMF in Audio | This parameter specifies the mechanism to transmit DTMF digit in audio which means DTMF is combined in audio signal(not very reliable with low-bit-rate codec), Default is YES. |
| DTMF via RFC2833 | This parameter specifies the mechanism to transmit DTMF digit via RTP (RFC2833). Default YES. |
| DTMF via SIP INFO | This parameter specifies the mechanism to transmit DTMF digit via SIP INFO. Default is NO. |
| Send Flash Event | This parameter allows users to control whether to send an SIP NOTIFY message indicating the Flash event, or just to switch to the voice channel when users press the Flash key. |
| Enable Call Features | Default is No. If set to Yes, Call Forwarding & Do-Not-Disturb are supported locally |
| Offhook Auto-Dial | This parameter allows users to configure a User ID or extension number to be automatically dialed upon offhook. Please note that only the user part of a SIP address needs to be entered here. The SNR VP - 2101 will automatically append the “@” and the host portion of the corresponding SIP address. |
| Proxy-Require | SIP Extension to notify SIP server that the unit is behind the NAT/Firewall. |
| Use NAT IP | NAT IP address used in SIP/SDP message. Default is blank. |
| Preferred Vocoder | The SNR VP-2101 supports up to 5 different Vocoder types including G.711 A-/U-law, G.726 (Supports bit rates 32K), G.723.1, G.729A/B. The user can configure Vocoders in a preference list that will be included with the same preference order in SDP message. The first Vocoder is entered by choosing the appropriate option in “Choice 1”. The last Vocoder is entered by choosing the appropriate option in “Choice 6”. |
| Voice Frames per TX | This field contains the number of voice frames to be transmitted in a single packet. When setting this value, the user should be aware of the requested packet time (used in SDP message) as a result of configuring this parameter. This parameter is associated with the first vocoder in the above vocoder Preference List or the actual used payload type negotiated between the 2 conversation parties at run time. e.g., if the first vocoder is configured as G723 and the “Voice Frames per TX” is set to be 2, then the “ptime” value in the SDP message of an INVITE request will be 60ms because each G723 voice frame contains 30ms of audio. Similarly, if this field is set to be 2 and if the first vocoder chosen is G729 or G711 or G726, then the “ptime” value in the SDP message of an INVITE request will be 20ms. If the configured voice frames per TX exceeds the maximum allowed value, the SNR VP - 2002 will use and save the maximum allowed value for the corresponding first vocoder choice. The maximum value for PCM is 10(x10ms) frames; for G726, it is 20 (x10ms) frames; for G723, it is 32 (x30ms) frames; for G729/G728, 64 (x10ms) and 64 (x2.5ms) frames respectively. |
| G723 Rate: | This defines the encoding rate for G723 vocoder. By default, 6.3kbps rate is chosen. |
| VAD | Default is “No”. VAD allows detecting the absence of audio and conserve bandwidth by preventing the transmission of "silent packets" over the network. |
| Symmetric RTP | Default is No. When set to Yes the device will change the destination to send RTP packets to the source IP address and port of the inbound RTP packet last received by the device. |
| Jitter Buffer Type | Select either Fixed or Adaptive based on network conditions. |
| Jitter Buffer Length | Select Low, Medium or High based on network conditions. |
| Account Ring Tone | There are 4 uniquely defined ring tones: • One (1) System Ring Tone: when selected, all calls will ring with system ring tone. • Three (3) Customer Ring Tones: when selected, incoming calls from designated account will play selected ring tone. |
| Ring Timeout | An incoming call will stop ringing when not picked up given a specific period of time. |
| Use # as Dial Key | This parameter allows users to configure the “#” key to be used as the Send (or Dial) key. If set to Yes, pressing this key will immediately trigger the sending of dialed string collected so far. In this case, this key is essentially equivalent to the Re(Dial) key. If set to No, this “#” key will then be included as part of the dial string to be sent out. |
| Dial Plan | Dial Plan Rules: 1. Accept Digits: 1,2,3,4,5,6,7,8,9,0 , *, #, A,a,B,b,C,c,D,d 2. Grammar: x - any digit from 0-9; a. xx+ - at least 2 digits number; b. xx. ?at least 2 digits number; c. ^ - exclude; d. [3-5] - any digit of 3, 4, or 5; e. [147] - any digit 1, 4, or 7; f. <2=011> - replace digit 2 with 011 when dialing Example 1: {[369]11 ¦ 1617xxxxxxx} Allow 311, 611, 911, and any 10 digit numbers of leading digits 1617 Example 2: {^1900x+ ¦ <=1617>xxxxxxx} Block any number of leading digits 1900 and add prefix 1617 for any dialed 7 digit numbers Example 3: {1xxx[2-9]xxxxxx ¦ <2=011>x+} Allow any length of number with leading digit 2 and 10 digit-numbers of leading digit 1 and leading exchange number between 2 and 9; if leading digit is 2, replace leading digit 2 with 011 before dialing. 3. Default: Outgoing - {x+} Example of a simple dial plan used in a Home/Office in the US: { ^1900x. ¦ <=1617>[2-9]xxxxxx ¦ 1[2-9]xx[2-9]xxxxxx ¦ 011[2-9]x. ¦ [3469]11 } Explanation of example rule (reading from left to right): ^1900x. - prevents dialing any number started with 1900 <=1617>[2-9]xxxxxx - allows dialing to local area code (617) numbers by dialing 7 numbers and 1617 area code will be added automatically 1[2-9]xx[2-9]xxxxxx ¦- allows dialing to any US/Canada Number with 11 digits length 011[2-9]x. - allows international calls starting with 011 [3469]11 - allow dialing special and emergency numbers 311, 411, 611 and 911 Note: In some cases user wishes to dial strings such as *123 to activate voice mail or other application provided by service provider. In this case * should be predefined inside dial plan feature and the Dial Plan should be: { [x*]+ }. More information can be availabled at Dail Plan Notes. |
| SUBSCRIBE for MWI | Default is No. When set to Yes a SUBSCRIBE for Message Waiting Indication will be sent periodically. |
| Send Anonymous | If this parameter is set to Yes, the “From” header in outgoing INVITE message will be set to anonymous, essentially blocking the Caller ID from displaying. |
| Anonymous Call Rejection | Default is NO, if set to YES, the anonymous call will be rejected with busy message. |
| Check SIP User ID for incoming INVITE | Check the SIP User ID in Request URI. If they don’t match, the call will be rejected. |
| Auto Answer | Default is No. If set to “Yes”, SNR VP-7040 will automatically switch on speaker to answer the incoming call. Set to Intercom/Paging mode, it will answer the call based on the SIP info header from the server. |
| Allow Auto Answer by Call-Info | If the Call-Info header contains answer-after=0, the call be answered automatically (so called paging mode). |
| Session Expiration | The session timer extension enables SIP sessions to be periodically “refreshed” via a re-INVITE request. Once the session interval expires, if there is no refresh via a re-INVITE message, the session will be terminated. Session Expiration is the time (in seconds) at which the session is considered timed out, if no successful session refresh transaction occurs beforehand. The default value is 180 seconds. |
| Min-SE | The minimum session expiration (in seconds). Default is 90 seconds. |
| Caller Request Timer | If selecting “Yes” the device will use session timer when it makes outbound calls if remote party supports session timer. Default is NO. |
| Callee Request Timer | If selecting “Yes” the phone will use session timer when it receives inbound calls with session timer request. Default is NO. |
| Force Timer | If selecting “Yes” the device will use session timer even if the remote party does not support this feature. Selecting “No” will allow the device to enable session timer only when the remote party support this feature. To turn off Session Timer, select “No” for Caller Request Timer, Callee Request Timer, and Force Timer. Default is NO. |
| UAC Specify Refresher | As a Caller, select UAC to use the device as the refresher, or UAS to use the Callee or proxy server as the refresher. Default is Omit |
| UAS Specify Refresher | As a Callee, select UAC to use caller or proxy server as the refresher, or UAS to use the device as the refresher. Default is UAC. |
| Force INVITE | Session Timer can be refreshed using INVITE method or UPDATE method. Select “Yes” to use INVITE method to refresh the session timer. Default is NO. |
| Hook Flash Timing | Time period when the cradle is pressed (Hook Flash) to simulate FLASH. To prevent unwanted activation of the Flash/Hold and automatic phone ring-back, adjust this time value. |
| Special Feature | Choose the selection to meet some special requirements from Soft Switch vendors. Default is standard. |

## Saving the Configuration Changes

Once a change is made, users should click on the “SaveSet” button in the Configuration page, as follow:

The SNR VP - 7040 will then display the following screen to confirm that the changes have been saved. Please allow 5 to 10 seconds before rebooting the device.

## Rebooting the SNR VP - 7040

You can reboot the SNR VP - 7040 by clicking on the “Reboot” button after each update to the configuration page.  Alternatively, you can reboot by unplugging the power supply of the SNR VP - 7040 and then powering it on again. If your SNR VP - 7040 ever becomes “stuck” or un-responsive, you can unplug the power supply to reboot it. Frequent rebooting by unplugging the power supply is not recommended and should not be necessary.

## Configuration through a Central Server

SNR VP - 7040 devices can be automatically configured from a central provisioning system.

When SNR VP - 7040 boots up, it will send TFTP or HTTP request to download configuration files. There are two configuration files, one is “cfg.txt” and the other is“cfg001fc1xxxxxx”, where “001fc1xxxxxx” is the MAC address of the SNR VP - 7040.

For more information regarding configuration file format, please refer to the related technical documentation.

The configuration file can be downloaded via TFTP or HTTP from the central server. A service provider or an enterprise with large deployment of SNR VP - 7040s can easily manage the configuration and service provisioning of individual devices remotely and automatically from a central server. The central provisioning system uses enhanced (NAT friendly) TFTP or HTTP (thus no NAT issues) and other communication protocols to communicate with each individual SNR VP - 7040 for firmware upgrade, etc.

# SOFTWARE UPGRADE

To upgrade software, SNR VP - 7040 can be configured with a TFTP server where the new code image is located. The TFTP upgrade can work in either static IP or DHCP mode using private or public IP address. It is recommended to set the TFTP server address in either a public IP address or on the same LAN with the SNR VP - 7040.

There are two ways to set up the TFTP server to upgrade the firmware, namely through voice menu prompt or via the SNR VP - 7040 ’s Web configuration interface. To configure the TFTP server via voice prompt, follow section 8.1, once set up the TFTP IP address, power cycle the SNR VP-7040, the firmware will be fetched once the SNR VP-7040 boots up.

To configure the TFTP server via the Web configuration interface, open up your browser to point at the IP address of the SNR VP - 7040. Input the admin password to enter the configuration screen. From there, enter the TFTP server address in the designated field towards the bottom of the configuration screen.

Once the TFTP server is configured, please power cycle the SNR VP - 7040.

TFTP process may take as long as 1 to 2 minutes over the Internet, or just 20+ seconds if it is performed on a LAN. Users are recommended to conduct TFTP upgrade in a controlled LAN environment if possible. For those who do not have a local TFTP server, SNR provides a NAT-friendly TFTP server on the public Internet for firmware upgrade. Please check the Service section of SNR’s Web site to obtain this TFTP server’s IP address.

NOTES:

When SNR IP Phone boot up, it will send TFTP or HTTP request to download configuration files, there are two configuration files, one is “cfg.txt” and the other is “cfg001fc1xxxxxx”, where “001fc1xxxxxx” is the MAC address of the SNR VP - 7040 . These two files are for initial automatically provisioning purpose only, for normal TFTP or HTTP firmware upgrade, the following error messages in a TFTP or HTTP server log can be ignored.

# RESTORE TO FACTORY DEFAULT SETTINGS

Warning:

Restoring to the factory default settings will delete all configuration information of the device.

Steps to follow in restoring to factory default settings:

Step1: Return to the Config sub-menu.

Step2: Choose the Factory Reset sub-menu and press MENU again.

Step3:Choose Confirm Factory Reset or Cancel Factory Reset.

# TECHNICAL SUPPORT CONTACT

Email: support@nag.ru