SNR-CVT-SERIAL Simple instructions

Set the computer the same IP and SNR-CVT-SERIAL, see user’s manual. Such as: When the SNR-CVT-SERIAL IP is 192.168.2.1, The computer will be 192.168.2.***.

Connect to the network and power on.

1. Open Internet Explorer, enter the IP 192.168.2.1, Enter the web setup interface, according to the needs of your device settings.

Figure 1

Figure 2

Figure 3

Figure 4

2. If you are directly connected with the IP, then set above it. If it is a virtual serial port connection, Will have to install our software VCOM, and set as follows.

(1). Open software，Click search, The right box will show the SNR-CVT-SERIAL IP. Figure 5：

Figure 5

(2). Click com mapping. Figure:

Figure 6

(3). Click add. Figure:

Figure 7

(4). In the above box to select IP, the following will display settings. Only can change com, click OK. Set up. as shown, the success of virtual com10.

Figure 8