SNR-CVT-SERIAL-M1/M4 Simple instructions

Set the computer the same IP and SNR-CVT-SERIAL-M1, see user’s manual. Such as: When the SNR-CVT-SERIAL-M1 IP is 192.168.168.125, The computer will be 192.168.168.***.

Connect to the network and power on.

1. Open Internet Explorer, enter the IP 192.168.168.125, Enter the account password，into the web setup interface, according to the needs of your device settings. Figure 1.

Figure 1

2. If you are directly connected with the IP, then set above it. If it is a virtual serial port connection, Will have to install our software VCOM, and set as follows.

(1). Open software，Click to “Tool(T)”, in the drop-down menu, select “IP search”,. figure 2. It will pop up a dialog box, figure 3.

Figure 2

Figure 3

In the figure 3. First click “Refresh” (①), In the box will display the search out of the SNR-CVT-SERIAL-M1, select the IP Address (②), specific information will appear in ③. Double-click the IP Address, can enter page. IP Address in the ③ can be modified, and then click “Alter” (④) enter the password changed successfully.

Note: Use the IP Search must make sure the connection is to use the first network card. IP Search is one available way to find and modify the IP.

(2). Virtual serial port settings as follows. First select a COM (①), and then Click to “Create” (②). In the dialog box enter the IP Address and Port (③), then click Add (④), the final OK and Create.

Figure 4

(3). COM5 successfully set, figure:

Figure 5

(4). VCOM also has a version, use basically the same, as shown below:

Click ① to IP search, a dialog box pops up the same as step (1).

Set up a virtual serial port as follows: Select the COM Port in ②, click the Create Comm (③), ④ on the left shows COM Port.

Select the COM Port in ⑤, fill the IP Address and Port in ⑦, click Add IP (⑧) and OK, COM 7 setting success.

Figure 6

Note: In the use of SNR-CVT-SERIAL-M4, only need to modify Port (⑥), other steps the same.