LLDP Configuration Commands

Table of Contents

Chapter 1 LLDP Configuration Commands	1

1.1 LLDP Commands	1

1.1.1 ldp  run	1

1.1.2 lldp　holdtime	2

1.1.3 lldp　timer	2

1.1.4 lldp　reinit	3

1.1.5 lldp　tlv-select	4

1.1.6 lldp　dot1-tlv-select	5

1.1.7 lldp　dot3-tlv-select	6

1.1.8 lldp　med-tlv-select	7

1.1.9 lldp　transmit	8

1.1.10 lldp　receive	9

1.1.11 lldp　 management-ip	9

1.1.12 lldp　 trap-send	10

1.1.13 location　elin　identifier　id　WORD	11

1.1.14 location　civic　identifier　id	12

1.1.15 location　elin/civic　id	14

1.1.16 show　lldp　errors	15

1.1.17 show　lldp　interface	15

1.1.18 show　lldp　neighbors	16

1.1.19 show　lldp　neighbors　detail	17

1.1.20 show　lldp　traffic	19

1.1.21 show　location　elin	20

1.1.22 show　location　civic　[identifier　id]	20

1.1.23 clear　lldp　counters	21

1.1.24 clear　lldp　table	22

# Chapter 1 LLDP Configuration Commands

## LLDP Commands

### ldp  run

Syntax

To enable LLDP, run lldp run; to disable LLDP, run no lldp run.

lldp　run

no　lldp　run

Parameters

None

Default Value

The debugging switch is disabled.

Usage Guidelines

The port will send lldp packets after the lldp function is enabled.

Command Mode

Global configuration mode

Example

The following command is used to enable LLDP.

switch_config# lldp　run

### lldp　holdtime

Syntax

To configure the ttl value of LLDP, run lldp holdtime time. To resume the default transmission delay, run no lldp holdtime.

lldp　holdtime　time

no　lldp　holdtime

Parameters

| Parameters | Description |
| --- | --- |
| time | Holdtime of the to-be-transmitted packet Range: 0-65535 seconds |

Default Value

120s

Usage Guidelines

In normal condition, the remote information stored in MIB will update before aging. But the frame may loss in sending and causes the information ages. For avoiding this, you need to set the value of TTL and ensure the update LLDP frame is forwarded time after time.

Command Mode

Global configuration mode

Example

The following example shows how to set the ttl value of LLDP to 100 seconds.

switch_config# lldp　holdtime 100

switch_config#

### lldp　timer

Syntax

To configure the transmission delay of LLDP, run lldp timer time. To resume the default transmission delay, run no lldptimer.

lldp　timer  time

no lldp　timer

Parameters

| Parameters | Description |
| --- | --- |
| time | Interval for LLDP to transmit the packets Range: 5-65534 seconds |

Default Value

30s

Usage Guidelines

The transmission interval of the LLDP message must be shorter than its storage time, ensuring multiple updates in the storage time and preventing error which is led by packet loss.

Command Mode

Global configuration mode

Example

The following example shows how to configure the transmission interval of LLDP to 24 seconds.

switch_config# lldp　timer　24

switch_config#

### lldp　reinit

Syntax

To configure the transmission delay of LLDP, run lldp reinit time. To resume the default transmission delay, run no lldp reinit.

lldp　reinit　time

no lldp　reinit

Parameters

| Parameters | Description |
| --- | --- |
| time | Transmission delay of LLDP, whose values range from two to five seconds Range: 2-5 seconds |

Default Value

２ s

Usage Guidelines

LLDP information will be forwarded automatically in two conditions: first, the status or value of one or more information elements (management objects) change; second, the sending timer timeouts. A single information change cause the LLDP packet is forwarded and a series of information change may cause many LLDP frames forwarded, but a frame can only report one change. For avoiding this, the web management defines the interval of two continuous LLDP frames.

Command Mode

Global configuration mode

Example

The following example shows how to set the transmission delay of LLDP to five seconds.

switch_config# lldp　reinit　５

switch_config#

### lldp　tlv-select

Syntax

To add TLV which is transmitted by the LLDP message, run lldp med-tlv-select tlv-type. To delete TLV which is transmitted by the LLDP message, run no lldp med-tlv-select tlv-type.

lldp　tlv-select　tlv-type

no lldp　tlv-select　tlv-type

Parameters

| Parameters | Description |
| --- | --- |
| tlv-type | Stands for TLV that are available for selective transmission. Its values are: management-address management address TLV port-description port description TLV system-capabilities system-capabilities TLV system-description system description TLV system-name system name TLV |

Default Value

All TLVs are sent.

Usage Guidelines

Three mandatory TLVs must be sent.

Command Mode

Global configuration mode

Example

The following example shows how to enable the port description not to be transmitted in the message.

switch_config#no　lldp　tlv-select　port-description

switch_config#

### lldp　dot1-tlv-select

Syntax

To add TLV which is transmitted by the LLDP message, run lldp med-tlv-select tlv-type. To delete TLV which is transmitted by the LLDP message, run no lldp med-tlv-select tlv-type.

lldp　dot1-tlv-select　tlv-type

no lldp　dot1-tlv-select　tlv-type

Parameters

| Parameters | Description |
| --- | --- |
| tlv-type | Stands for TLV that are available for selective transmission. Its values are: port-vlan-id port vlan address TLV protocol-vlan-id port and protocol VLAN ID TLV vlan-name vlan名TLV |

Default Value

All TLVs are sent.

Usage Guidelines

The TLV of the protocol identity does not support transmission but supports reception.

Command Mode

Port configuration mode

Example

The following example shows how to enable the TLV not to be transmitted by deletion of the VLAN address of a port in the transmitted packet.

switch_config#int g0/1

switch_config_g0/1#no　lldp　dot1-tlv-select　 port-vlan-id

switch_config_g0/1#

### lldp　dot3-tlv-select

Syntax

To add TLV which is transmitted by the LLDP message, run lldp med-tlv-select tlv-type. To delete TLV which is transmitted by the LLDP message, run no lldp med-tlv-select tlv-type.

lldp　dot3-tlv-select　tlv-type

no lldp　dot3-tlv-select　tlv-type

Parameters

| Parameters | Description |
| --- | --- |
| tlv-type | Stands for TLV that are available for selective transmission. Its values are: link-aggregation link aggregation TLV macphy-confg MAC/Phy configuration/status TLV max-frame-size max frame size TLV power Power Via MDI TLV |

Default Value

All TLVs are sent.

Usage Guidelines

None

Command Mode

Port configuration mode

Example

The following example shows how to enable the TLV not to be transmitted by deletion of the MAC/Phy configuration/status of a port in the transmitted packet.

switch_config#int g0/1

switch_config_g0/1#no　lldp　dot3-tlv-select　 macphy-confg

switch_config_g0/1#

### lldp　med-tlv-select

Syntax

To add TLV which is transmitted by the LLDP message, run lldp med-tlv-select tlv-type. To delete TLV which is transmitted by the LLDP message, run no lldp med-tlv-select tlv-type.

lldp　med-tlv-select　tlv-type

no lldp　med-tlv-select　tlv-type

Parameters

| Parameters | Description |
| --- | --- |
| tlv-type | Stands for TLV that are available for selective transmission. Its values are: network-policy network policy TLV inventory inventory management TLV location location identification TLV power-management expand Power Via MDI TLV |

Default Value

All TLVs are sent.

Usage Guidelines

By default, the TLV of MED cannot be transmitted. When the TLV of MED need be transmitted, the MED capability TLV must be transmitted. Hence it does not fall into the choice.

Command Mode

Port configuration mode

Example

The following example shows how to enable the TLV not to be transmitted by deletion of the detailed list management in a transmitted packet.

switch_config#int g0/1

switch_config_g0/1#no　lldp　med-tlv-select　inventory

switch_config_g0/1#

### lldp　transmit

Syntax

lldp　transmit

no lldp　transmit

To set the port to send the LLDP message, run lldp transmit. To forbid receiving the LLDP message, run no lldp transmit.

Parameters

None

Default Value

Transmittable LLDP message mode

Usage Guidelines

Only after the LLDP module is enabled can the command be valid.

Command Mode

Port configuration mode

Example

The following example shows how to set port g0/1 not to send the LLDP message.

switch_config_g0/1# no lldp　transmit

switch_config_g0/1#

### lldp　receive

Syntax

lldp　receive

no lldp　receive

To set the port to the receivable LLDP message mode, run lldp receive. To forbid receiving the LLDP message, run no lldp receive.

Parameters

None

Default Value

Receivable LLDP message mode

Usage Guidelines

Only after the LLDP module is enabled can the configuration be valid.

Command Mode

Port configuration mode

Example

The following example shows how to set port g0/1 not to receive the LLDP message.

switch_config_g0/1# no lldp　receive

switch_config_g0/1#

### lldp　 management-ip

Syntax

lldp　 management-ip　　A.B.C.D

no　lldp　 management-ip

To configure the management address of the LLDP port, run lldp management-ip A.B.C.D. To resume the default transmission delay, run no lldp management-ip.

Parameters

| Parameters | Description |
| --- | --- |
| A.B.C.D | Stands for the management IP address that will be specified. |

Default Value

The default management address is the IP address of the VLAN interface that pvid corresponds to; if this IP address does not exist, the default management address is 0.0.0.0.

Usage Guidelines

The configured management IP address should be the IP address related with a port.

Command Mode

Port configuration mode

Example

The following example shows how to set the management IP address of port g0/1 to 90.0.0.99.

switch_config_g0/1# lldp　management-ip 90.0.0.99

switch_config_g0/1#

### lldp　 trap-send

Syntax

lldp 	tranp-send	lldp-mib

To forward trap notification to lldp mib, run this command.

lldp 	tranp-send	ptopo-mib

To forward trap notification to ptopo mib, run this command.

Parameters

None

Default Value

None

Usage Guidelines

None

Command Mode

Global configuration mode

Example

The following example shows how to send trap notification to lldp mib.

switch_config#lldp trap-send lldp-mib

switch_config#

The following example shows how to send trap notification to ptopo mib.

switch_config#lldp trap-send ptopo-mib

switch_config#

### location　elin　identifier　id　WORD

Syntax

location elin identifier　id WORD

no location elin identifier　id

To add the elin information, run location elin identifier　id WORD; to delete the elin information, run no location elin identifier id.

Parameters

| Parameters | Description |
| --- | --- |
| id | Stands for the ID of the to-be-set elin, which ranges from 1 to 65535. |
| WORD | Stands for the content of the configured elin, which ranges from 10 to 25 bytes. |

Default Value

None

Usage Guidelines

None

Command Mode

Global configuration mode

Example

The following example shows how to set the identifier to 1 and the content of elin to 1234567890.

switch_config# location elin identifier 1 1234567890

switch_config#

### location　civic　identifier　id

Syntax

location civic identifier　id

no location civic identifier　id

To enter the location configuration mode and set the civic information, run location civic identifier id. To delete the civic information, run no location civic identifier id.

Parameters

| Parameters | Description |
| --- | --- |
| id | Stands for the ID of the to-be-set civic, which ranges from 1 to 65535. |

Default Value

None

Usage Guidelines

After the system enters the location configuration mode, you can run the following commands to conduct the corresponding configuration to the civic of the ID.

| Command | Purpose |
| --- | --- |
| (no) language WORD | Sets the language. |
| (no) state WORD | Sets the state’s (provincial) name, such as shanghai. |
| (no) county WORD | Sets the name of a county. |
| (no) city WORD | Sets the name of a city. |
| (no) division WORD | Sets the name of a division. |
| (no) neighborhood WORD | Sets the name of neighborhood. |
| (no) street WORD | Sets the name of a street. |
| (no) leading-street-dir WORD | Sets the direction of a main street, such as N (north). |
| (no) trailing-street-suffix WORD | Sets the suffix of a small street, such as SW. |
| (no) street-suffix WORD | Sets the suffix of a street, such as platz. |
| (no) number WORD | Sets the street number, such as number 123. |
| (no) street-number-suffix WORD | Sets the suffix of the street number, such as number 1/2 of A road. |
| (no) landmark WORD | Sets the landmark, such as Colombia University. |
| (no) additional-location WORD | Sets the additional location. |
| (no) name WORD | Sets the information about a resident, such as Joe’s haircut shop. |
| (no) postal-code WORD | Sets the postal code. |
| (no) building WORD | Sets the information about a building. |
| (no) unit WORD | Sets the information about a unit. |
| (no) floor WORD | Sets the information about a floor. |
| (no) room WORD | Sets the information about a room. |
| (no) type-of-place WORD | Sets the type of a place, such as office. |
| (no) postal-community WORD | Sets the name of a postal office. |
| (no) post-office-box WORD | Sets the name of a postal box, such as 12345. |
| (no) additional-code WORD | Sets the additional code. |
| (no) country WORD | Sets the name of a country. |
| (no) script WORD | Sets the script. |

Command Mode

Global configuration mode

Example

The following example shows how to set the civic information of identifier 1.

Switch_config#location civic identifier 1

Switch_config_civic#language English

Switch_config_civic#city Shanghai

Switch_config_civic#street Curie

Switch_config_civic#script EN

Switch_config_civic#quit

Switch_config#

### location　elin/civic　id

Syntax

location elin/civic　id

no location elin/civic

To set the location for a port, run location elin/civic id. To delete the location of a port, run no location elin/civic id.

Parameters

| Parameters | Description |
| --- | --- |
| id | Stands for the ID of the to-be-set elin/civic, which ranges from 1 to 65535. |

Default Value

None

Usage Guidelines

None

Command Mode

Port configuration mode

Example

The following example shows how to set the elin and the civic for a port.

Switch_config#int g0/8

Switch_config_g0/8#location elin 1

Switch_config_g0/8#location civic 1

### show　lldp　errors

Syntax

show　lldp　errors

To display the error information about the LLDP module, run this command.

Parameters

None

Default Value

None

Usage Guidelines

None

Command Mode

EXEC/global configuration mode

Example

The following example shows how to check the error information of lldp module.

switch_config#show lldp errors

LLDP errors/overflows:

Total memory allocation failures: 0

Total encapsulation failures: 0

Total table overflows: 0

switch_config#

### show　lldp　interface

Syntax

show　lldp　interface　interface-name

To check the transmission and reception mode, run show lldp interface interface name.

Parameters

| Parameters | Description |
| --- | --- |
| interface-name | The interrface name, for instance, "G0/1", "GigaEthernet0/1". |

Default Value

None

Usage Guidelines

Only when lldp is enabled can the state of the port, the transmission and reception mode of lldp packets can be checked.

Command Mode

EXEC/global configuration mode

Example

The following example shows how to check the transmission and reception mode of port g0/1.

switch_config#show lldp interface g0/1

GigaEthernet0/1:

Rx: enabled

Tx: enabled

switch_config#

### show　lldp　neighbors

Syntax

show lldp　neighbors

To display the simple information about neighbors, run this command.

Parameters

None

Default Value

None

Usage Guidelines

The command is used to display the simple information about neighbor list, including Device-ID, Local-Intf, Hldtme, Port-ID and Capability.

Command Mode

EXEC/global configuration mode

Example

switch_config#show lldp neighbors

Capability Codes:

(R)Router,(B)Bridge,(C)DOCsIs Cable Device,(T)Telephone

(W)WLAN Access Point, (P)Repeater,(s)station,(O)Other

Device-ID       Local-Intf      Hldtme       Port-ID      Capability

switch          Gig0/2          115          Gig0/32      B

switch          Gig0/32         114          Gig0/2       B

Total entries dispalyed: 2

switch_config#

### show　lldp　neighbors　detail

Syntax

show　lldp　neighbors　detail

It is used to display the detailed information about the neighbor.

Parameters

None

Default Value

None

Usage Guidelines

None

Command Mode

EXEC/global configuration mode

Example

switch_config#show lldp neighbors detail

chassis id: 00e0.0f61.ca53

port id: Gig0/32

port description: GigaEthernet0/32

system name: switch

system description: s3448 software, Version 2.0.1K

serial: s35000456

Compiled: 2008-11-13 13:33:36 by 16170F032B9F

Time remaining: 98

system capabilities: R B

enabled capabilities: B

Managment Address:

IP: 192.168.213.62

Auto Negotiation -- supported,enabled

Physical media capabilitise:

100baseTX(FD)

100baseTX(HD)

10baseT(FD)

10baseT(HD)

Media Attachment Unit type: 16

------------------------------------------

chassis id: 00e0.0f61.ca35

port id: Gig0/2

port description: GigaEthernet0/2

system name: switch

system description: s3448 software, Version 2.0.1K

serial: s35000456

Compiled: 2008-11-13 13:33:36 by 16170F032B9F

Time remaining: 95

system capabilities: R B

enabled capabilities: B

Managment Address:

IP: 90.0.0.66

Auto Negotiation -- supported,enabled

Physical media capabilitise:

100baseTX(FD)

100baseTX(HD)

10baseT(FD)

10baseT(HD)

Media Attachment Unit type: 16

------------------------------------------

Total entries dispalyed: 2

switch#

### show　lldp　traffic

Syntax

show　lldp　traffic

To display all statistics information about LLDP, run show lldp traffic.

Parameters

None

Default Value

None

Usage Guidelines

None

Command Mode

EXEC/global configuration mode

Example

switch_config#show lldp traffic

LLDP traffic statistics:

Total frames out: 1599

Total entries aged: 0

Total frames in: 624

Total frames received in error: 0

Total frames discarded: 0

Total TLVs unrecognized: 0

switch_config#

### show　location　elin

Syntax

show　location　 elin

To display the elin configuration of the location, run the previous command.

Parameters

None

Default Value

None

Usage Guidelines

None

Command Mode

EXEC/global configuration mode

Example

Switch_config#show location elin

elin information:

elin 2: 0987654321

elin 1: 1234567890

total: 2

Switch_config#

### show　location　civic　[identifier　id]

Syntax

show　 location　civic　[identifier　id]

To display the civic information of the location, run the previous command.

Parameters

| Parameters | Description |
| --- | --- |
| id | Stands for the ID of the to-be-set civic, which ranges from 1 to 65535. |

Default Value

None

Usage Guidelines

None

Command Mode

EXEC/global configuration mode

Example

Switch_config#show location civic

civic address information:

identifier: 2

Language: Chinese

Script: CN

-------------------------------------

identifier: 1

City: Shanghai

Language: English

Script: EN

-------------------------------------

total: 2

Switch_config#

### clear　lldp　counters

Syntax

clear　lldp　counters

To clear the statistics information, run clear lldp counters.

Parameters

None

Default Value

None

Usage Guidelines

None

Command Mode

EXEC

Example

switch#clear lldp counters

switch#

switch#show lldp traffic

LLDP traffic statistics:

Total frames out: 0

Total entries aged: 0

Total frames in: 0

Total frames received in error: 0

Total frames discarded: 0

Total TLVs unrecognized: 0

switch#

switch#show lldp errors

LLDP errors/overflows:

Total memory allocation failures: 0

Total encapsulation failures: 0

Total table overflows: 0

switch#

### clear　lldp　table

Syntax

clear　lldp　table

To remove the neighbor list, run cleas lldp table.

Parameters

None

Default Value

None

Usage Guidelines

None

Command Mode

EXEC

Example

switch#clear lldp table

switch#

switch#show lldp neighbors

Capability Codes:

(R)Router,(B)Bridge,(C)DOCsIs Cable Device,(T)Telephone

(W)WLAN Access Point, (P)Repeater,(s)station,(O)Other

Device-ID       Local-Intf      Hldtme       Port-ID      Capability

Total entries displayed: 0