# DoS-Attack Prevention Configuration Commands

# Table of Contents

Chapter 1 DoS Attack Prevention Configuration Commands	3

1.1 DoS-Attack Prevention Configuration Commands	3

1.1.1 dos enable	3

1.1.2 show dos	4

# DoS Attack Prevention Configuration Commands

## DoS-Attack Prevention Configuration Commands

DoS attack prevention configuration commands are shown below:

dos enable

show dos

### dos enable

Syntax

dos enable {all | tcpflags | tcpsmurf | icmpsmurf | ipsmurf}

no dos enable {all | tcpflags | tcpsmurf | icmpsmurf | ipsmurf}

Parameter

| Parameter | Description |
| --- | --- |
| all | Enables to prevent all kinds of DoS attacks. |
| tcpflags | Starts to check the TCP packets with illegal flags. |
| tcpsmurf | Starts to check the TCP packets with tcmsmurf. |
| icmpsmurf | Starts to check the icmp packets with icmpsmurf. |
| ipsmurf | Starts to check the ipsmurf packets with ipsmurd |

Default value

DoS attack prevention is disabled by default.

Usage guidelines

DoS attack prevention is configured in global mode.

The DoS tcpflags sub-function can drop the following 4 kinds of TCP packets: 1. TCP SYN flag=1 & source port<1024; 2.TCP control flags = 0 & sequence = 0; 3.TCP FIN URG PSH =1 & sequence = 0; 4.TCP FIN SYN =1.

The DoS tcpsmurf sub-function can drop TCP packets of destination IP whose last 8 bits are 255.

The DoS icmpsmurf sub-function can drop TCP packets of source and destination IP whose last 8 bits are 255.

The DoS ipsmurf sub-function can drop TCP packets of destination IP whose last 8 bits are 255.

Example

The following example shows how to set the global DoS attack prevention function to prevent TCP packets of destination IP whose last 8 bits are 255.

Switch_config#dos enable tcmpsmurf

### show dos

Syntax

show dos

It is used to show all DoS attack prevention functions that users have set.

Parameter

N/A

Default value

N/A

Usage guidelines

EXEC mode

Example

The following example shows how to display all DoS attack prevention functions.

Switch_config#dos enable all

Switch_config#show dos

dos enable tcpflags

dos enable tcpsmurf

dos enable icmpsmurf

dos enable ipsmurf

Switch_config#

The following example shows how to set dos enable icmp to display the sub-function that users have set.

Switch_config#dos enable tcpflags

Switch_config#show dos

dos enable tcpflags