Network Protocol Configuration Commands

# Table of Contents

Chapter 1 IP Address Configuration Commands	1

1.1 IP Address Configuration Commands	1

1.1.1 arp	1

1.1.2 arp pending-time	2

1.1.3 arp max-incomplete	3

1.1.4 arp max-gw-retries	3

1.1.5 arp retry-allarp	4

1.1.6 arp timeout	5

1.1.7 arp send-gratuitous	6

1.1.8 clear arp-cache	6

1.1.9 ip address	7

1.1.10 ip directed-broadcast	8

1.1.11 ip forward-protocol	8

1.1.12 ip helper-address	9

1.1.13 ip host	10

1.1.14 ip default-gateway	11

1.1.15 ip proxy-arp	11

1.1.16 show arp	12

1.1.17 show hosts	13

1.1.18 show ip interface	13

Chapter 2 DHCP Client Configuration Commands	16

2.1 DHCP Client Configuration Commands	16

2.1.1 ip address dhcp	16

2.1.2 ip dhcp client	17

2.1.3 ip dhcp-server	18

2.1.4 show dhcp lease	19

2.1.5 show dhcp server	20

2.1.6 debug dhcp	21

Chapter 3 DHCP Sever Configuration Commands	22

3.1 DHCPD Configuration Commands	22

3.1.1 ip dhcpd ping packet	22

3.1.2 ip dhcpd ping timeout	23

3.1.3 ip dhcpd write-time	23

3.1.4 ip dhcpd pool	24

3.1.5 ip dhcpd enable	25

3.2 DHCPD Address Pool Configuration Commands	25

3.2.1 network	26

3.2.2 range	26

3.2.3 default-router	27

3.2.4 dns-server	27

3.2.5 domain-name	28

3.2.6 lease	29

3.2.7 netbios-name-server	29

3.2.8 ip-bind	30

3.2.9 debug ip dhcpd packet	31

3.2.10 debug ip dhcpd event	31

3.2.11 debug ip dhcpd all	32

1.1 DHCPD Management Commands	32

1.1.1 show ip dhcpd statistic	33

1.1.2 show ip dhcpd binding	33

1.1.3 clear ip dhcpd statistic	34

1.1.4 clear ip dhcpd binding	34

Chapter 4 IP Service Configuration Commands	36

4.1 IP Service Configuration Commands	36

4.1.1 clear tcp	36

4.1.2 clear tcp statistics	38

4.1.3 debug arp	38

4.1.4 debug ip icmp	39

4.1.5 debug ip packet	42

4.1.6 debug ip raw	46

4.1.7 debug ip tcp packet	48

4.1.8 debug ip tcp transactions	49

4.1.9 debug ip udp	52

4.1.10 ip mask-reply	52

4.1.11 ip mtu	53

4.1.12 ip redirects	54

4.1.13 ip route-cache	55

4.1.14 ip route-cache hit-numbers	56

4.1.15 ip route-cache age-exf	57

4.1.16 ip route-cache cache-pbr	57

4.1.17 ip route-cache age-delay	58

4.1.18 ip route-cache softcache-alive-time	59

4.1.19 ip route-cache software-index	60

4.1.20 ip route-cache hardware-index	60

4.1.21 ip route-cache-aging-time	61

4.1.22 ip source-route	62

4.1.23 ip tcp synwait-time	62

4.1.24 ip tcp window-size	63

4.1.25 ip unreachables	64

4.1.26 show ip cache	65

4.1.27 show ip irdp	66

4.1.28 show ip sockets	66

4.1.29 show ip traffic	67

4.1.30 show tcp	68

4.1.31 show tcp brief	72

4.1.32 show tcp statistics	73

4.1.33 show tcp tcbI	75

4.2 ACL Configuration Commands	76

4.2.1 deny	77

4.2.2 ip access-group	79

4.2.3 ip access-list	80

4.2.4 permit	81

4.2.5 show ip access-list	84

4.3 IP ACL Configuration Commands Based on Physical Ports	85

4.3.1 deny	85

4.3.2 ip access-group	88

4.3.3 ip access-list	89

4.3.4 permit	90

4.3.5 show ip access-list	92

# IP Address Configuration Commands

## IP Address Configuration Commands

IP address configuration commands include：

arp

arp timeout

clear arp-cache

ip address

ip directed-broadcast

ip forward-protocol

ip helper-address

ip host

ip default-gateway

ip proxy-arp

show arp

show hosts

show ip interface

### arp

Syntax

To add a static and permanent entry in the Address Resolution Protocol (ARP) cache, use the arp command in global configuration mode. To remove an entry from the ARP cache, use the no form of this command.

arp ip-address hardware-address [alias]

no arp ip-address

Parameter

| parameter | description |
| --- | --- |
| ip-address | IP address corresponding to the local data-link address. |
| hardware-address | Physical address of local data-link address |
| alias | (optional) router responds to ARP requests as if it were the interface of the specified address. |

Default value

No entries are permanently installed in the ARP cache.

Command mode

global configuration mode

Usage guidelines

The common host all supports dynamic ARP analysis, so user doesn’t need to configure static ARP entries for host.

Example

The following is an example of a static ARP entry for a typical Ethernet host:

arp 1.1.1.1 00:12:34:56:78:90

Related commands

clear arp-cache

### arp pending-time

Syntax

To set the waiting time of ARP cache resolution, run the following command:

arp pending-time seconds

Parameter

| Parameter | Description |
| --- | --- |
| seconds | Sets the waiting time of ARP cache resolution, whose unit is second. |

Default value

15 seconds

Command mode

Global configuration mode

Usage guidelines

The first ARP cache resolution will generate an incomplete entry and this command will then be used to set the life-time of this incomplete entry.

Example

The following example shows how to set the waiting time of ARP cache resolution to 10 seconds.

arp pending-time 10

Related command

show arp

### arp max-incomplete

Syntax

To set the maximum number of incomplete ARP entries., run the preceding command.

arp max-incomplete number

Parameter

| Parameter | Description |
| --- | --- |
| number | Sets the maximum number of incomplete ARP entries. |

Default value

The default value is 0, meaning no threshold exists.

Command mode

Global configuration mode

Usage guidelines

This command can be used to set the maximum number of the incomplete entries during ARP cache resolution.

Example

The following example shows how to set the maximum number of the incomplete ARP cache entries to 10:

arp max-incomplete 10

Related command

show arp

### arp max-gw-retries

Syntax

To set the maximum retransmissions of the Re-Detect packets, run the following command:

arp max-gw-retries number

Parameter

| Parameter | Description |
| --- | --- |
| number | Sets the maximum retransmissions of the Re-Detect packets. |

Default value

3

Command mode

Global configuration mode

Usage guidelines

The ARP entries, which the routing entry gateway depends on, require being redetected at their aging so that the promptness and correctness of the hardware subnet routing can be guaranteed. This command is here used for setting the maximum ARP retransmissions in the redetection process. The bigger its value is, the greater chance the detection has.

Example

The following example shows how to set the maximum retransmissions of the Re-Detect packets to 5:

arp max-gw-retries 5

Related command

show arp

### arp retry-allarp

Syntax

To set whether to carry on redetection at the aging of ARP entries (not just meaning the gateway-related ARP entries), run the following command:

arp retry-allarp

Parameter

None

Command mode

Global configuration mode

Usage guidelines

By default, redetection is conducted only to the aging ARPs, which the routing entry gateway depends on.  However, if this command is enabled, redetection will be conducted towards all types of aging ARP entries.

Example

The following example shows how to enable redetection to be carried out to all aging ARP entries.

arp retry-allarp

Related command

show arp

### arp timeout

Syntax

To configure the exist time that a dynamic ARP entry remains in the Address Resolution Protocol (ARP) cache, use the arp timeout. To restore the default value, use the no form of this command or default arp timeout command.

arp timeout seconds

no arp timeout

default arp timeout

Parameter

| parameter | description |
| --- | --- |
| seconds | Time in seconds that an entry remains in the ARP cache. A value of zero means that entries are never cleared from the cache. |

Default value

14400 seconds (4 hours)

Command mode

interface configuration mode

Usage guidelines

This command is ignored when it is not configured on interfaces using ARP. The show interface command displays the ARP timeout value, as seen in the following example from the show interfaces command:

ARP type: ARPA, ARP timeout 04:00:00

Example

The following example sets the ARP timeout to 900 seconds on Ethernet 1/0 to allow entries to time out more quickly than the default

interface vlan 10

arp timeout 900

Related commands

show interface

### arp send-gratuitous

Syntax

To configure ARP send-gratuitous function, use the arp send-gratuitous command

arp send-gratuitous [ interval value ]

Parameter

| parameter | descruption |
| --- | --- |
| interval | Set the intervals of arp send-gratuitous |
| value | Set time interval, the default is 120 seconds. The range is 15 to 600 seconds |

Command mode

routing interface configuration mode

Usage guidelines

The following command start arp send-gratuitous on Interface Vlan 1, and set the send interval as 3 minutes

switch_config_v1#arp send-gratuitous interval 180

Related commands

arp

### clear arp-cache

Syntax

To clear all dynamic entries from the ARP cache, use the clear arp-cache command.

clear arp-cache [ ip-address [ mask ] ]

Parameter

| parameter | description |
| --- | --- |
| ip-address | IP or subnets |
| mask | Subnets mask |

Command mode

EXEC

Example

The following example removes all dynamic entries from the ARP cache:

clear arp-cache

Related commands

arp

### ip address

Syntax

To set an IP address and mask for an interface, use the ip address command. Currently, there is no strict regulation to distinguish A.B.C IP address. But multicast address and broadcast address can not be used( all host section is ‘1’). Other than the Ethernet,multiple interfaces of other types can be connected to the same network. Other than the unnumbered interface, the configured network range ot the Ethernet interface can not be the same as the arbitrary interfaces of other types. You should configure the primary address before configuring the secondary address. Also you should delete all secondary addresses before deleting the primary address. IP packets generanted by the system, if the upper application does not specify the soruce address, the router will use the IP address configured on the sending interface that on the same network range with the gateway as the source address of the packet. If the IP address is uncertain (like interface route), the router will use the primary address of the sending interface. If the ip address is not configured on an interface, also it is not the unnumbered interface, and then this interface will not deal with any IP packet.To remove an IP address or disable IP processing, use the no form of this command.

ip address ip-address mask [secondary]

no ip address ip-address mask

no ip address

Parameter

| parameter | description |
| --- | --- |
| ip-address | IP address |
| mask | IP mask |
| secondary | (optional) Specifies that the configured address is a secondary IP address. If this keyword is omitted, the configured address is the primary IP address. |

Default value

No IP address is defined for the interface.

Command mode

interface configuration mode

Usage guidelines

If any router on a network segment uses a secondary address, all other devices on that same segment must also use a secondary address from the same network or subnet. Inconsistent use of secondary addresses on a network segment can very quickly cause routing loops. When you are routing using the Open Shortest Path First (OSPF) algorithm, ensure that all secondary addresses of an interface fall into the same OSPF area as the primary addresses

Example

In the following example, 202.0.0.1 is the primary address, 255.255.255.0 is the mask and 203.0.0.1 and 204.0.0.1 are secondary addresses for Ethernet interface 1/0:

interface vlan 10

ip address 202.0.0.1 255.255.255.0

ip address 203.0.0.1 255.255.255.0 secondary

ip address 204.0.0.1 255.255.255.0 secondary

### ip directed-broadcast

Syntax

To enable the translation of a directed broadcast to physical broadcasts, use the ip directed-broadcast interface configuration command

ip directed-broadcast [access-list-namer]

no ip directed-broadcast

Parameter

| parameter | description |
| --- | --- |
| access-list-name | (Optional) Access list name. If specified, a broadcast must pass the access list to be forwarded. |

Default value

By default, all IP directed broadcasts are dropped.

Command mode

interface configuration mode

Example

The following example enables forwarding of IP directed broadcasts on Ethernet interface 1/0:

interface vlan 10

ip directed-broadcast

### ip forward-protocol

Syntax

After the ip helper-address command is configured on interface, the ip forward-protocol command is used to specify which UDP to be forwarded.

ip forward-protocol udp [port]

no ip forward-protocol udp [port]

default ip forward-protocol udp

Parameter

| parameter | description |
| --- | --- |
| port | (optional) Destination port that controls which UDP requests are forwarded |

Default value

Request that forwards NETBIOS Name Service.

Command mode

global congiration mode

Usage guidelines

The netbios name service request is forwarded by default. Not to forward netbios name service request, use one of the following commands:

no ip forward-protocol udp netbios-ns

no ip forward-protocol udp 137

To stop forwarding all UDP broadcasting requests, use the following command.

no ip forward-protocol udp

Example

switch_config#ip forward-protocol udp 137

Related commands

ip helper-address

### ip helper-address

Syntax

To enable the forwarding of User Datagram Protocol (UDP) broadcasts to specific IP helper-addresses which can berm of this command.

ip helper-address address

no ip helper-address [address]

Parameter

| parameter | description |
| --- | --- |
| address | IP helper address。 |

Default value

IP helper-address is not configured

Command mode

interface configuration mode

Usage guidelines

The ip helper-address command does not work on an X.25 interface on a destination router because the router cannot determine if the packet was intended as a physical broadcast.

Example

The following example configures IP helper-address 1.0.0.1 on the interface vlan 10

interface vlan 10

ip helper-address 1.0.0.1

Related commands

ip forward-protocol udp

### ip host

Syntax

To define a static host name-to-address mapping in the host cache, use the ip host command in global configuration mode. To remove the host name-to-address mapping, use the no form of this command.

ip host name address

no ip host name

Parameter

| parameter | description |
| --- | --- |
| name | Host name |
| Address | IP address |

Default value

disabled

Command mode

global configuration mode

Example

The following example shows how to configure host name dns-server to IP host address 202.96.1.3:

ip host dns-server 202.96.1.3

### ip default-gateway

Syntax

To configure the default gateway of switch, use the ip default-gateway command. To delete the default gateway of switch, use the no form of this command.

ip default-gateway address

no ip default-gateway

Parameter

| parameter | description |
| --- | --- |
| address | IP address |

Default value

no configuration

Command mode

global configuration mode

Example

The following example configure the IP address 202.96.1.3 as default-gateway

ip default-gateway 202.96.1.3

### ip proxy-arp

Syntax

To enable proxy Address Resolution Protocol (ARP) on an interface, use the ip proxy-arp command. To disable proxy ARP on the interface, use the no form of this command.

ip proxy-arp

no ip proxy-arp

Parameter

This command has no parameters

Default value

proxy ARP

Command mode

interface configuration mode

Usage guidelines

When routing switch receives ARP requirements, if routing switch has the routing path to required IP address, and the routing interface and the interface receive the requirements are different, routing switch will send ARP reaction from its own MAC address, and then it forward actual data packets when receive them. In this case, even if one host does not know the network topology, or without configured accurate routing, it can also communicate with remote terminal. The remote host is connected with the routing switch in the same physical subnet.

If the host need routing switch to provide such function, then the host and the routing switch must be in the same IP network, or its IP address is regarded in the IP subnet of routing switch, or rather, they can use different masks, or routing switch can not provide such service.

Example

The following example open the proxy ARP function on the interface VLAN 10

interface vlan 10

ip proxy-arp

### show arp

Syntax

To display the entries in the Address Resolution Protocol (ARP) table, including the ARP mapping of interface IP address, the static ARP mapping that user configures and the dynamic ARP mapping, use the show arp command.

show arp

Parameter

this command has no parameters or keywords

Command mode

EXEC

Usage guidelines

The display includes:

| parameter | description |
| --- | --- |
| Protocol | Displays the type of the network address that maps with the physical address. IP, for example. |
| Address | Displays the network address that maps with the physical address. IP address, for example. |
| Age | Displays the age in seconds. The router will refresh the time to 0 when using this ARP entry. |
| Hardware Address | Displays the physical address that corresponds to the network address. It is empty for the unanalyzed entries. |
| Type | Specifies request encapsulation types that the interface use, including ARPA, SNAP and so on. |

Example

The following command displays ARP cache.

switch#show arp

Protocol   IP Address      Age(min)  Hardware Address   Type  Interface

IP     192.168.20.77         11   00:30:80:d5:37:e0  ARPA  vlan 10

IP     192.168.20.33          0     Incomplete

IP     192.168.20.22          -   08:00:3e:33:33:8a  ARPA  vlan 10

IP     192.168.20.124         0   00:a0:24:9e:53:36  ARPA  vlan 10

IP     192.168.0.22           -   08:00:3e:33:33:8b  ARPA  vlan 11

### show hosts

Syntax

To display all entries of the host name—address cathe, use the show hosts command.

show hosts

Parameter

This command has no parameters or keywords.

Command mode

EXEC

Example

The following command shows how to display all host names/address mappings.

show hosts

Related commands

clear host

### show ip interface

Syntax

To display the IP configuration on interface, use the show ip interface command

show ip interface [type number]

Parameter

| parameter | description |
| --- | --- |
| type | (Optional) Interface type. |
| number | (Optional) Interface number. |

Command mode

EXEC

Usage guidelines

If the interface link layer is usable, the line protocol is marked "Protocol up." If you configure IP address on this interface, the router will add a direct route to the routing table. If the link layer protocol is marked “Protocol down”, the direct route will be deleted. This command displays the specified interface information if specified interface type and number, or IP configuration information of all interfaces will be displayed.

Example

The following example shows how to display IP configuration on interface e0/1.

switch#show ip interface vlan 11

vlan 10 is up, line protocol is up

IP address : 192.168.20.167/24

Broadcast address : 192.168.20.255

Helper address : not set

MTU : 1500(byte)

Forward Directed broadcast : OFF

Multicast reserved groups joined:

224.0.0.9 224.0.0.6 224.0.0.5 224.0.0.2

224.0.0.1

Outgoing ACL : not set

Incoming ACL : not set

IP fast switching : ON

IP fast switching on the same interface : OFF

ICMP unreachables : ON

ICMP mask replies : OFF

ICMP redirects : ON

display description :

| domain | description |
| --- | --- |
| Ethernet1/0 is up | If the interface hardware is usable, the interface is marked "up." For an interface to be usable, both the interface hardware and line protocol must be up. |
| line protocol is up | If the interface can provide two-way communication, the line protocol is marked "up." For an interface to be usable, both the interface hardware and line protocol must be up. |
| IP address | IP address and mask for interface |
| Broadcast address | Displays broadcast address |
| MTU | Displays the MTU value set on the interface. |

# DHCP Client Configuration Commands

## DHCP Client Configuration Commands

The following are DHCP Client configuration command:

ip address dhcp

ip dhcp client

ip dhcp-server

show dhcp lease

show dhcp server

debug dhcp

The chapter describes the DHCP configuration commands. These commands are used to configure and monitor the DHCP running on the switch.

### ip address dhcp

Syntax

Run the ip address dhcp command to obtain an IP address for the interface through the dynamic host configuration protocol (DHCP). Run the no ip address dhcp command to delete the obtained IP address.

ip address dhcp

no ip address dhcp

Parameter

None

Default value

None

Command mode

Interface configuration mode

Usage guidelines

The ip address dhcp command is used to allow the interface to obtain the IP address through DHCP, which is very helpful for dynamically connecting the Internet service provider (ISP) through the Ethernet interface. When the dynamic IP address is obtained and the ip address dhcp command is configured, the switch sends the DHCPDISCOVER message to the DHCP server in the network. When the dynamic IP address is obtained and the no ip address dhcp command is configured, the switch sends the DHCPRELEASE message.

Example

The following example shows that the vlan11 interface obtains the IP address through the DHCP protocol.

!

interface vlan11

ip address dhcp

Related command

ip dhcp client

ip dhcp-server

show dhcp lease

show dhcp server

### ip dhcp client

Syntax

It is used to configure parameters at the DHCP client server of the local switch.

ip dhcp client { minlease seconds | retransmit count | select seconds }

no ip dhcp client { minlease | retransmit | select }

Parameter

| Parameter | Description |
| --- | --- |
| minlease seconds | Acceptable minimum lease time (optional), ranging from 60 to 86400 seconds |
| retransmit count | Times of retransmitting the protocol message (optional), ranging from 1 to 10 |
| select seconds | Interval for selecting default parameter values (optional), ranging from 0 to 30 |

Default value

minleaseParameterDefault is 60 seconds.

retransmitParameterDefault is four times.

selectParameterDefault is zero second.

Command mode

Global configuration mode

Usage guidelines

These commands can adjust these parameters according to network structure and requirements of DHCP server.

If the negative forms of these commands are configured, these parameters are resumed to the default settings.

Example

The following example shows that the minlease parameter is set to 100 seconds at the client side of the switch:

ip dhcp client minlease 100

The following example shows that the retransmit parameter is set to 3 times at the client side of the switch:

ip dhcp client retransmit 3

The following example shows that the SELECT parameter is set to 10 seconds at the client side of the switch:

ip dhcp client select 10

Related command

ip address dhcp

ip dhcp-server

show dhcp lease

show dhcp server

### ip dhcp-server

Syntax

Run the ip dhcp-server command to specify the IP address of the DHCP server:

ip dhcp-server ip-address

no ip dhcp-server ip-address

Parameter

| Parameter | Description |
| --- | --- |
| ip-address | IP address of the DHCP server |

Default value

The DHCP server has no default IP address.

Command mode

Global configuration mode。

Usage guidelines

It is used to specify an IP address for the DHCP server. The command cannot replace the previously specified IP address of the DHCP server.

You can run the negative form of the command to clear the previously configured IP address of the DHCP server.

Example

The following example shows that the server whose IP address 192.168.20.1 is designated as the DHCP server:

ip dhcp-server 192.168.20.1

Related command

ip address dhcp

ip dhcp client

show dhcp lease

show dhcp server

### show dhcp lease

Syntax

Run the show dhcp lease command to check the information about the DHCP server distribution used by the current switch:

Show dhcp lease

Parameter

None

Default value

None

Command mode

Management mode

Usage guidelines

It is used to check the information about the DHCP server distribution used by the current switch.

Example

The following example shows that the information about the DHCP server distribution used by the current switch is displayed:

switch#show dhcp lease

Temp IP addr: 192.168.20.3  for peer on Interface: vlan11

Temp  sub net mask: 255.255.255.0

DHCP Lease server: 192.168.1.3, state: 4 Rebinding

DHCP transaction id: 2049

Lease: 86400 secs,  Renewal: 43200 secs,  Rebind: 75600 secs

Temp default-gateway addr: 192.168.1.2

Next timer fires after: 02:34:26

Retry count: 1   Client-ID: router-0030.80bb.e4c0-v11

Related command

ip address dhcp

ip dhcp client

ip dhcp-server

show dhcp server

debug dhcp

### show dhcp server

Syntax

Run the show dhcp server command to display the known DHCP server information:

show dhcp server

Parameter

None

Default value

None

Command mode

Management mode

Usage guidelines

It is used to display the known DHCP server information.

Example

The following example shows that the known DHCP server information is displayed:

switch#show dhcp sever

DHCP server: 255.255.255.255

Leases:  0

Discovers: 62 Requests: 0     Declines: 0     Releases: 0

Offers:    0  Acks:     0     Naks:     0     Bad:      0

Subnet: 0.0.0.0,      Domain name:

Related command

ip address dhcp

ip dhcp client

ip dhcp-server

show dhcp lease

### debug dhcp

Syntax

Run the debug dhcp command to check the running state of the DHCP:

debug dhcp [detail]

no debug dhcp [detail]

Parameter

| Parameter | Description |
| --- | --- |
| detail | Displays the content of the DHCP message. |

Default value

The relevant information is not displayed.

Command mode

Management mode

Usage guidelines

The following example shows that important information about the running of DHCP is displayed.

switch#debug dhcp

switch#2000-4-22 10:50:40 DHCP: Move to INIT state, xid: 0x7

2000-4-22 10:50:40 DHCP: SDISCOVER attempt # 1, sending 277 byte DHCP packet

2000-4-22 10:50:40 DHCP:        B'cast on vlan11 interface from 0.0.0.0

2000-4-22 10:50:40 DHCP: Move to SELECTING state, xid: 0x7

2000-4-22 10:50:46 DHCP: SDISCOVER attempt # 2, sending 277 byte DHCPpacket

2000-4-22 10:50:46 DHCP:        B'cast on vlan11 interface from 0.0.0.0

2000-4-22 10:50:54 DHCP: SDISCOVER attempt # 3, sending 277 byte DHCPpacket

Related command

show dhcp lease

# DHCP Sever Configuration Commands

## DHCPD Configuration Commands

The following are DHCPD configuration commands:

ip dhcpd ping packet

ip dhcpd ping timeout

ip dhcpd write-time

ip dhcpd pool

ip dhcpd enable

ip dhcpd disable

### ip dhcpd ping packet

Syntax

ip dhcpd ping packet pkgs

Parameter

| Parameter | Description |
| --- | --- |
| pkgs | Number of ICMP packets sent when the DHCP server detects whether the address is distributed |

Default value

2

Command mode

Global configuration mode

Usage guidelines

You can run the following command to configure the DHCP server to send n ICMP packets when the DHCP server checks whether the IP address is distributed.

ip dhcpd ping packets n

Example

The following example shows that the DHCP server has sent one ICMP packet when it checks whether the IP address is distributed.

ip dhcpd ping packets 1

### ip dhcpd ping timeout

Syntax

ip dhcpd ping timeout timeout

Parameter

| Parameter | Description |
| --- | --- |
| timeout | Timeout time waiting for the ICMP response message when the DHCP server checks whether the IP address is distributed (Unit: 100 ms) |

Default value

5

Command mode

Global configuration mode

Usage guidelines

The following command can be used to configure the timeout time of the ICMP response message to n*100 ms when the DHCP server checks whether the IP address is distributed.

ip dhcpd ping timeout n

Example

The following example shows that the timeout time of the ICMP response message is set to 300 ms when the DHCP server checks whether the IP address is distributed

ip dhcpd ping timeout 3

### ip dhcpd write-time

Syntax

ip dhcpd write-time time

Parameter

| Parameter | Description |
| --- | --- |
| time | Interval when the DHCP server stores the address distribution information into the database (unit: minute) |

Default value

60

Command mode

Global configuration mode

Usage guidelines

The following command can be used to configure that the DHCP server stores the address distribution information into the database every n minutes.

ip dhcpd write-time n

It is recommended not to set the write-time to a value smaller than the default value.

Example

The following example shows that the DHCP server stores the address distribution information into the database every 1440 minutes.

ip dhcpd write-time 1440

### ip dhcpd pool

Syntax

ip dhcpd pool name

Parameter

| Parameter | Description |
| --- | --- |
| name | Name of the DHCP address pool |

Default value

None

Command mode

Global configuration mode

Usage guidelines

The following command is used to add a name DHCP address pool and enter the dhcp address pool configuration mode.

ip dhcpd pool name

Example

The following example shows that a test DHCP address pool is added and the dhcp address pool configuration mode is entered.

ip dhcpd pool test

### ip dhcpd enable

Syntax

ip dhcpd enable

no ip dhcpd enable

Parameter

None

Default value

The DHCP server is disabled.

Command mode

Global configuration mode

Usage guidelines

The following command is used to enable the DHCP service. In this case, the DHCP server supports the relay operation. For the address request that cannot be distributed, the port where ip helper-address is configured can forward the DHCP request.

ip dhcpd pool name

Example

The following example shows that the DHCP server is enabled

ip dhcpd enable

## DHCPD Address Pool Configuration Commands

The following are DHCPD address pool configuration commands:

network

range

default-router

dns-server

domain-name

lease

netbios-name-server

host

hardware-address

client-identifier

client-name

### network

Syntax

network ip-addr netmask

Parameter

| Parameter | Description |
| --- | --- |
| ip-addr | Network address of the address pool for automatic allocation |
| netmask | Subnet mask |

Default value

None

Command mode

DHCP address pool configuration mode

Usage guidelines

The command is used to configure the network address of the address pool for automatic allocation. The command is only used in automatic allocation mode.

When configuring the command, make sure that the port receiving the DHCP message has a network number of the port IP address similar to network.

Example

The following example shows that the network address of the DHCP address pool is set to 192.168.20.0 and the subnet mask is set to 255.255.255.0.

network 192.168.20.0 255.255.255.0

### range

Syntax

range low-addr high-addr

Parameter

| Parameter | Description |
| --- | --- |
| low-addr | Original address for automatically allocating the address range |
| hogh-addr | End address for automatically allocating the address range用于 |

Default value

None

Command mode

DHCP address pool configuration mode

Usage guidelines

The command is used to configure the address range for automatic allocation. Up to eight address ranges can be configured for each address pool. Each range must be in the network. The command is used only in automatic allocation mode.

Example

The following example shows that the address allocation range of the DHCP address pool is between 192.168.20.210 and 192.168.20.219.

range 192.168.20.210 192.168.20.219

### default-router

Syntax

default-router ip-addr

Parameter

| Parameter | Description |
| --- | --- |
| ip-addr | Default route distributed to the client |

Default value

None

Command mode

DHCP address pool configuration mode

Usage guidelines

The command is used to configure the default route. Up to four default routes can be configured, which are separated by space.

Example

The following example shows that the default route allocated to the DHCP client is 192.168.20.1.

default-router 192.168.20.1

### dns-server

Syntax

dns-server ip-addr …

Parameter

| Parameter | Description |
| --- | --- |
| ip-addr | DNS server address allocated to the client |

Default value

None

Command mode

DHCP address pool configuration mode

Usage guidelines

The command is used to configure the DNS server address that is allocated to the client. Up to four DNS servers can be configured, which are sparated by space.

Example

The following example shows that the DNS server address allocated to the client is 192.168.1.3.

dns-server 192.168.1.3

### domain-name

Syntax

domain-name name

Parameter

| Parameter | Description |
| --- | --- |
| name | Domain name distributed to the client |

Default value

None

Command mode

DHCP address pool configuration mode

Usage guidelines

The command is used to configure the domain name which is distributed to the client.

Example

The following example shows that the domain name of the client is configured to test.domain.

domain-name test.domain

### lease

Syntax

lease {days [hours][minutes] | infinite}

Parameter

| Parameter | Description |
| --- | --- |
| days | Days after the address is allocated |
| hours | Hours after the address is allocated |
| minutes | Minutes after the address is allocated |
| infinite | Permanent address allocation |

Default value

One day

Command mode

DHCP address pool configuration mode

Usage guidelines

The command is used to configure the lease time of the distributed address.

Example

The following example shows that the lease time of the address distributed to the client is set to 2 days and 12 hours.

Lease 2 12

### netbios-name-server

Syntax

netbios-name-server ip-addr

Parameter

| Parameter | Description |
| --- | --- |
| ip-addr | IP address of the netbios name server allocated to the client |

Default value

None

Command mode

DHCP address pool configuration mode

Usage guidelines

The command is used to configure the address of the netbios name server. Up to four netbios name servers cam be configured, which is separated by space.

Example

The following example shows that the address of the of the netbios name server is set to 192.168.1.10.

netbios-name-server 192.168.1.10

### ip-bind

Syntax

ip-bind ip-addr hardware-address WORD [type] | host-name WORD | identifier WORD

no ip-bind ip-addr

Parameter

| Parameter | Description |
| --- | --- |
| hardware-address WORD [type] | WORD is used to match the hardware address of the client machine. type used for matching the network type of the user |
| host-name WORD | Used for matching the host name of the user |

Default value

None

Command mode

DHCP address pool configuration mode

Usage guideline

The command can be used to configure the host address of the manual distributed address pool.

Example

The following example shows how to configure the hardware address to 10:a0:0c:13:64:7d of DHCP manual distributed address 1.1.1.1.

Ip-bind 1.1.1.1 hardware-address 10:a0:0c:13:64:7d

The following example shows how to configure the client ID to 01:10:a0:0c:13:64:7d of DHCP manual distributed address 1.1.1.2.

Ip-bind 1.1.1.2 identifier 01.10.a0.0c.13.64.7d

The following example shows how to configure the host name as Router-test of DHCP manual distributed address 1.1.1.3.

Ip-bind 1.1.1.3 host-name Router-test

### debug ip dhcpd packet

Syntax

debug ip dhcpd packet

Parameter

None

Default value

None

Command mode

Exec

Usage guideline

The command can be used to enable debug on-off of DHCPD data packet information.

Example

The following example shows how to enable debug on-off of DHCPD data packet information.

debug ip dhcpd packet

### debug ip dhcpd event

debug ip dhcpd event

Parameter

None

Default value

None

Command mode

Exec

Usage guideline

The command can be used to enable debug on-off of DHCPD event information.

Example

The following example shows how to enable debug on-off of DHCPD data event information.

debug ip dhcpd event

### debug ip dhcpd all

debug ip dhcpdall

Parameter

None

Default value

None

Command mode

Exec

Usage guideline

The command can be used to enable debug on-off of DHCPD all debug information.

Example

The following example shows how to enable debug on-off of DHCPD debug information.

debug ip dhcpd all

## DHCPD Management Commands

DHCPD management command include:

- show ip dhcpd statistic

- show ip dhcpd binding

- clear ip dhcpd statistic

- clear ip dhcpd binding

### show ip dhcpd statistic

Syntax

show ip dhcpd statistic

Parameter

None

Default value

None

Command mode

All modes except the user mode

Usage guideline

The command can be used to display DHCPD statistics, including number of packets and address numbers of auto-distribution and manual-distribution.

Example

The following example shows how to display statiscs of DHCPD.

show ip dhcpd statistic

### show ip dhcpd binding

show ip dhcpd binding {ip-addr}

Parameter

| Parameter | Description |
| --- | --- |
| ip-addr | Shows address of the binding informatione. |

Default value

Display the binding information of all addresses.

Command mode

All modes except the user mode

Usage guideline

The command can be used to display DHCPD address binding information, including IP address, hardware address, binding type and time-out.

Example

The following example shows how to display the binding information of DHCPD.

show ip dhcpd binding

### clear ip dhcpd statistic

Syntax

clear ip dhcpd statistic

Parameter

None

Default value

None

Command mode

Exec

Usage guideline

The command can be used to delete statistics about numbers of DHCPD packets.

Example

The following example shows how to delete statistics about numbers of DHCPD packets.

clear ip dhcpd statistic

### clear ip dhcpd binding

Syntax

clear ip dhcpd binding {ip-addr|*}

Parameter

| Parameter | Description |
| --- | --- |
| ip-addr | Address needs to delete binding information |
| * | Delete all binding information |

Default value

Delete binding information of designated address.

Command mode

Exec

Usage guideline

The command can be used to delete binding information of designated address.

Example

The following example shows how to delete binding information of 192.168.20.210.

clear ip dhcpd binding 192.168.20.210

The following example shows how to delete binding information of 192.168.20.210 and 192.168.20.211.

clear ip dhcpd binding 192.168.20.210 192168.20.211

The following example shows how to delete all binding information.

clear ip dhcpd binding *

# IP Service Configuration Commands

## IP Service Configuration Commands

The following are IP service configuration commands:

clear tcp

clear tcp statistics

debug arp

debug ip icmp

debug ip packet

debug ip raw

debug ip tcp packet

debug ip tcp transactions

debug ip udp

ip mask-reply

ip mtu

ip redirects

ip route-cache

ip source-route

ip tcp synwait-time

ip tcp window-size

ip unreachables

show ip cache

show ip irdp

show ip sockets

show ip traffic

show tcp

show tcp brief

show tcp statistics

show tcp tcb

### clear tcp

Syntax

It is used to delete a TCP connection.

clear tcp {local host-name port remote host-name port | tcb address}

Parameter

| Parameter | Description |
| --- | --- |
| local host-name port | IP address and TCP port of the local host |
| remote host-name port | IP address and TCP port of the remote host |
| tcb address | TCB address of the to-be-deleted TCP connection TCB is an identifier of TCP connection in the inner system, which can be obtained by the command show tcp brief. |

Command mode

Management mode

Usage guidelines

The clear tcp command is mainly used to delete the terminated TCP connection. In some cases, such as faulty in communication lines, restarting TCP connection or the peer host, the TCP connections are terminated in fact. However, the system cannot obtain information about the terminated TCP connection because there is no communication on the TCP connections. In this case, you can run the clear tcp command to terminate these invalid TCP connections. The command clear tcp local host-name port remote host-name port is used to terminate the connections between the specified host's IP address/port and the remote host’s IP address/port. The command clear tcp tcb address is used to terminate the TCP connections identified by the TCB address.

Example

The following example shows that the TCP connection between 192.168.20.22:23 and 192.168.20.120:4420 is deleted. The show tcp brief command is used to show the information about the local host and the remote host in TCP connection.

switch#show tcp brief

TCB         Local Address         Foreign Address      State

0xE85AC8    192.168.20.22:23      192.168.20.120:4420   ESTABLISHED

0xEA38C8    192.168.20.22:23      192.168.20.125:1583   ESTABLISHED

switch#clear tcp local 192.168.20.22 23 remote 192.168.20.120 4420

switch#show tcp brief

TCB         Local Address         Foreign Address      State

0xEA38C8    192.168.20.22:23      192.168.20.125:1583   ESTABLISHED

In the following example, the TCP connection whose TCB address is 0xea38c8 is deleted. The command show tcp brief displays the TCB address of the TCP connection.

switch#show tcp brief

TCB         Local Address         Foreign Address      State

0xEA38C8    192.168.20.22:23      192.168.20.125:1583   ESTABLISHED

switch#clear tcp tcb 0xea38c8

switch#show tcp brief

TCB         Local Address         Foreign Address      State

Related command

show tcp

show tcp brief

show tcp tcb

### clear tcp statistics

Syntax

To clear the TCP statistics data, run the following command..

clear tcp statistics

Parameter

The command has no parameter or keyword.

Command mode

Management mode

Example

The following command is used to delete the TCP statistics data:

switch#clear tcp statistics

Related command

show tcp statistics

### debug arp

Syntax

To display the ARP interaction information, such as sending ARP requests, receiving ARP requests, sending ARP response and receiving ARP response, run the following command. When the switch cannot communicate with the host, the command is used to analyze the ARP interaction. You can run the no debug arp command to stop displaying the relative information.

debug arp

no debug arp

Parameter

The command has no parameter or keyword.

Command mode

Management mode

Example

switch#debug arp

switch#IP ARP: rcvd req src 192.168.20.116 00:90:27:a7:a9:c2, dst 192.168.20.111, vlan 10

IP ARP: req filtered src 192.168.20.139 00:90:27:d5:a9:1f, dst 192.168.20.82 00:

00:00:00:00:00, wrong cable, vlan 11

IP ARP: created an incomplete entry for IP address 192.168.20.77, vlan 10

IP ARP: sent req src 192.168.20.22 08:00:3e:33:33:8a, dst 192.168.20.77, vlan 10

IP ARP: rcvd reply src 192.168.20.77 00:30:80:d5:37:e0, dst 192.168.20.22, vlan 10

The first information indicates: the switch receives an ARP request on interface vlan 10; the IP address of the host that sends the ARP request is 192.168.20.116 and the MAC address of the host is 00:90:27:a7:a9:c2; the MAC address of the host 192.168.20.111 is IP ARP: rcvd req src 192.168.20.116 00:90:27:a7:a9:c2, dst 192.168.20.111, vlan 10.

The second information indicates that the switch receives an ARP request from 192.168.20.139 host on interface vlan 10. However, the interface is not in the network the host declares according to the interface configuration on the switch. The host may not be correctly configured. If the switch creates the ARP cache according to the information, it may not communicate with the host that is configured the same address and connected to the normal interface

IP ARP: req filtered src 192.168.20.139 00:90:27:d5:a9:1f, dst 192.168.20.82 00:

00:00:00:00:00, wrong cable, vlan 11

In the third information, to resolve the MAC address of host 192.168.20.77, the switch first creates an incomplete ARP item in the ARP cache. After receiving an ARP response, the MAC address is then added to the ARP cache. According to the location of the switch, the host connects the interface vlan 10.

IP ARP: created an incomplete entry for IP address 192.168.20.77, vlan 10

In the fourth information, the switch sends out the ARP request from the interface vlan 10. The IP address of the switch is 192.168.20.22. The MAC address of the interface is 08:00:3e:33:33:8a. The IP address of the requested host is 192.168.20.77. The fourth information is relative with the third information.

IP ARP: sent req src 192.168.20.22 08:00:3e:33:33:8a, dst 192.168.20.77, vlan 10

In the fifth information, the switch receives the ARP response on interface vlan 10 from host 192.168.20.77 to host 192.168.20.22. The switch is then informed that the MAC address of the host that returns the ARP response is 00:30:80:d5:37:e0. The information is relative to the third and fourth information.

IP ARP: rcvd reply src 192.168.20.77 00:30:80:d5:37:e0, dst 192.168.20.22, vlan 10

### debug ip icmp

Syntax

To display the ICMP interaction information, run the following command.. You can run the command no debug ip icmp to close the debugging output.

debug ip icmp

no debug ip icmp

Parameter

The command has no parameter or keyword.

Command mode

Management mode

Usage guidelines

The command is used to display the received or transmitted ICMP message, which helps to solve end-to-end connection problems. To know the detailed meaning of the command debug ip icmp, refer to RFC 792, “Internet Control Message Protocol”.

Example

switch#debug ip icmp

switch#ICMP: sent pointer indicating to 192.168.20.124 (dst was 192.168.20.22), len 48

ICMP: rcvd echo from 192.168.20.125, len 40

ICMP: sent echo reply, src 192.168.20.22, dst 192.168.20.125, len 40

ICMP: sent dst (202.96.209.133) host unreachable to 192.168.20.124, len 36

ICMP: sent dst (192.168.20.22) protocol unreachable to 192.168.20.124, len 36

ICMP: rcvd host redirect from 192.168.20.77, for dst 22.0.0.3 use gw 192.168.20.26, len 36

ICMP: rcvd dst (22.0.0.3) host unreachable from 192.168.20.26, len 36

ICMP: sent host redirect to 192.168.20.124, for dst 22.0.0.5 use gw 192.168.20.77, len 36

ICMP: rcvd dst (2.2.2.2) host unreachable from 192.168.20.26, len 36

Details about the first information are shown in the following table:

ICMP: sent pointer indicating to 192.168.20.124 (dst was 192.168.20.22), len 48

| Field | Description |
| --- | --- |
| ICMP | Information about the ICMP message |
| Sent | Sending the ICMP message |
| pointer indicating | ICMP message which means that the original parameters of the IP message are incorrect and incorrect domain is pointed out The following are other types of ICMP message: echo reply dst unreachable: ---net unreachable ---host unreachable ---protocol unreachable ---port unreachable ---fragmentation needed and DF set ---source route failed ---net unknown ---destination host unknown ---source host isolated ---net prohibited ---host prohibited ---net tos unreachable ---host tos unreachable source quench redirect messages: ---net redirect ---host redirect ---net tos redirect ---host tos redirect echo router advertisement router solicitation time exceeded : ---ttl exceeded ---reassembly timeout parameter problem : ---pointer indicating ---option missed ---bad length timestamp timestamp reply information request information reply mask request mask reply If the ICMP type is unknown, the system is to display the values of the ICMP type and code. |
| to 192.168.20.124 | Destination address of the ICMP message, which is also the source address of the original message that generates the ICMP message |
| (dst was 192.168.20.22) | Destination address of the original message that generates the ICMP message |
| len 48 | Length of the ICMP message, excluding the length of the IP header |

Details about the second information are shown in the following table:

ICMP: rcvd echo from 192.168.20.125, len 40

| Field | Description |
| --- | --- |
| rcvd | Receiving the ICMP message |
| echo | Echo request message, which is a type of the ICMP message |
| from 192.168.20.125 | Source address of the ICMP message |

Details about the third information are shown in the following table:

ICMP: sent echo reply, src 192.168.20.22, dst 192.168.20.125, len 40

| Field | Description |
| --- | --- |
| src 192.168.20.22 | Means that the source address of the ICMP message is 192.168.20.22. |
| dst 192.168.20.125 | Means that the destination address of the ICMP message is 192.168.20.125. |

According to the type of the ICMP message, the information that generates the ICMP message adopts different formats to display the message content.

For example, the redirect message of ICMP is printed in the following format:

ICMP: rcvd host redirect from 192.168.20.77, for dst 22.0.0.3 use gw 192.168.20.26, len 36

ICMP: sent host redirect to 192.168.20.124, for dst 22.0.0.5 use gw 192.168.20.77, len 36

In the first information, an ICMP redirect message from host 192.168.20.77 is received. Gateway 192.168.20.26 is recommended to reach the destination host 22.0.0.3. The length of the ICMP message is 36 bytes.

In the second information, the ICMP redirect message is sent to from host 192.168.20.124 to host 22.0.0.5 through gateway 192.168.20.77. The length of the ICMP message is 36 bytes.

The dst unreachable message of ICMP adopts the following format for printing:

ICMP: sent dst (202.96.209.133) host unreachable to 192.168.20.124, len 36

ICMP: rcvd dst (2.2.2.2) host unreachable from 192.168.20.26, len 36

In the first information, the switch cannot route a certain IP message, so it sends the destination (202.96.209.133) unreachable message to the source host (192.168.20.124). The length of the ICMP message is 36 bytes.

In the second information, after receiving an ICMP message from host192.168.20.26, the switch notifies host 192.168.20.26 that the destination address (2.2.2.2) cannot be reached. The length of the ICMP message is 36 bytes.

### debug ip packet

Syntax

It is used to display the IP interaction information. The command no debug ip packet is used to stop displaying information.

debug ip packet [detail] [ip-access-list-name]

no debug ip packet

Parameter

| Parameter | Description |
| --- | --- |
| detail | An optional parameter, which is used to export the protocol information about IP message encapsulation, such as protocol number, UDP, TCP port number and ICMP message type |
| ip-access-list-name | An optional parameter, which is used to filter the names of the IP access control list in the exported information Only the information about the IP message in the specified IP access control list can be exported. |
| access-group | An optional parameter, which is used to filter the names of the IP access control list in the exported information Only the information about the IP message in the specified IP access control list can be exported. |
| interface | An optional parameter, which is used to filter the port name of the exported information Only the information about the IP message satisfied the designated port can be exported. |

Command mode

Management mode

Usage guidelines

The command is used to find the destination of each received or locally generated IP message, which helps to detect the reason of communication problems.

The command is used in the following cases:

forwarded

forwarded as the multicast message or the broadcast message

addressing failure during message forwarding

Sending the redirect message

Rejected because of having the original routing option

Rejected because of illegal IP options

Original route

Message sent from the local machine should be segmented, but the DF is reset.

Receiving message

Receiving IP segment

Sending message

Sending broadcast/multicast

Addressing failure when message is generated locally

Locally generated message is segmented

Received message is filtered

Transmitted message is filtered

Link layer fails to be encapsulated (only for Ethernet)

Unknown protocol

This command may export lots of information. You'd better use it when the switch is in the free state. Otherwise, the performance of the system will be badly affected. You are recommended to filter the output information through the IP access control list, enabling the system to export the useful message.

Command mode

Management mode

Example

switch#debug ip packet

switch#IP: s=192.168.20.120 (vlan 10), d=19.0.0.9 (vlan 10), g=192.168.20.1, len=60, redirected

IP: s=192.168.20.22 (local), d=192.168.20.120 (vlan 10), g=192.168.20.120, len=56, sending

IP: s=192.168.20.120 (vlan 10), d=19.0.0.9 (vlan 10), g=192.168.20.1, len=60, forward

IP: s=192.168.20.81 (vlan 10), d=192.168.20.22 (vlan 10), len=56, rcvd

| Field | Description |
| --- | --- |
| IP | Means that the information is about the IP message. |
| s=192.168.20.120 (vlan 10) | Source address of the IP message and the interface name that receives message (for message that is not locally generated) |
| d=19.0.0.9 (vlan 10) | Destination address of the IP message and the interface name that sends message (if routing is successful) |
| g=192.168.20.1 | Next-hop destination address of the IP message, which may be the gateway’s address or the destination address |
| len | Length of the IP message |
| redirected | Means that the routing switch is to send the ICMP redirect message to the source host. Other cases are shown in the following: forward --- the message is forwarded. forward directed broadcast---the message is forwarded as the redirect message and the message will become the physical broadcast on the transmitting interface. unroutable---the message addressing fails and the message will be dropped. source route---source route rejected source route---the current system does not support the source route, therefore, the message with the IP source route is declined. bad options---the IP option is incorrect and the message will be dropped. need frag but DF set---the local message need be fragmented,while the DF is set. rcvd---the message is locally received. rcvd fragment---the message fragment is received. sending---the locally generated message is sent. sending broad/multicast---the locally generated broadcast/muticast message is sent. sending fragment--- the IP message locally fragmented is sent. denied by in acl---It is declined by the access control list on the reception interface. denied by out acl---It is declined by the transmitter access control on the transmitter interface. unknown protocol--- unknown protocol encapsulation failed---The protocol fails to be encapsulated.It is only for the Ethernet. When the message on the Ethernet is dropped because of the ARP resolution failure, the information is displayed. |

In the first information, the switch receives an IP message; the source address of the received message is 192.168.20.120; the message is from the network segment the vlan 10 interface connects; its destination address is 19.0.0.9. According to the routing table, the transmitter interface is vlan 10, the address of the gateway is 192.168.20.1 and the message length is 60 bytes. The gateway and the source host are directly connected in the same network, that is, the network that vlan 10 connects. In this case, the switch sends out the ICMP redirect message.

IP: s=192.168.20.120 (vlan 10), d=19.0.0.9 (vlan 10), g=192.168.20.1, len=60, redirected

In the second information, the transimmission of the ICMP redirect message is described. The source address is the local address 192.168.20.22. The destination address is 192.168.20.120. The message is directly sent from the vlan 10 interface to the destination address. Therefore, the gateway’s address is the detination address 192.168.20.120. The length of the ICMP redirect message is 56 bytes.

IP: s=192.168.20.22 (local), d=192.168.20.120 (vlan 10), g=192.168.20.120, len=56, sending

The third information shows that the IP layer receives an IP message. The source address and destination address of the IP message are 192.168.20.120 and 19.0.0.9 respectively. The reception interface is vlan 10. By checking the routing table, the system finds that the IP message need be forwarded to the vlan10 interface. The length of the IP message is 60 bytes. The third information shows that the message shown in the first information will be forwarded after the system sends the ICMP redirect message.

IP: s=192.168.20.120 (vlan 10), d=19.0.0.9 (vlan 10), g=192.168.20.77, len=60, forward

The fourth information shows that the IP layer receives an IP message. The source address and destination address of the IP message are 192.168.20.81 and 192.168.20.22 respectively. The reception interface is vlan 10. The length of the IP message is 56 bytes. The IP message is locally received.

IP: s=192.168.20.81 (vlan 10), d=192.168.20.22 (vlan 10), len=56, rcvd

The following is an example about the output information after running the debug ip packet detail command. Only the newly added parts are described.

switch#debug ip packet detail

switch#IP: s=192.168.12.8 (vlan 10), d=255.255.255.255 (vlan 10), len=328, rcvd, UDP: src=68, dst=67

IP: s=192.168.20.26 (vlan 10), d=224.0.0.5 (vlan 10), len=68, rcvd,	proto=89

IP: s=192.168.20.125 (vlan 10), d=192.168.20.22 (vlan 10), len=84, rcvd, ICMP: type=0, code = 0

IP: s=192.168.20.22 (local), d=192.168.20.124 (vlan 10), g=192.168.20.124, len=40, sending, TCP: src=1024, dst=23, seq=75098622, ack=161000466, win=17520, ACK

| Field | Description |
| --- | --- |
| UDP | Name of the protocol, such as UDP, ICMP and TCP Other protocols are represented by their protocol number. |
| type, code | Type and code of the ICMP message |
| src, dst | Source address and destination address of the UDP message and the TCP message |
| seq | Sequence number of the TCP message |
| ack | Acknowledge number of the TCP message |
| win | Window value of the TCP message |
| ACK | If ACK is set in the control bit of the TCP message, the acknowledge number is valid. Other control bits include SYN, URG, FIN, PSH and RST. |

The first information indicates that the UDP message is received. The source port is port 68 and the destination port is port 67.

IP: s=192.168.12.8 (vlan 10), d=255.255.255.255 (vlan 10), len=328, rcvd, UDP: src=68, dst=67

The second information indicates that the protocol number of the received message is 89.

IP: s=192.168.20.26 (vlan 10), d=224.0.0.5 (vlan 10), len=68, rcvd,	proto=89

The third information indicates that the ICMP message is received. Both the type and the code of the message are represented by the number 0.

IP: s=192.168.20.125 (vlan 10), d=192.168.20.22 (vlan 10), len=84, rcvd, ICMP: type=0, code = 0

The fourth information indicates that the TCP message is sent. The source port and destination port are port 1024 and port 23 respectively. The sequence number and the acknowledge number are 75098622 and 161000466 respectively. The size of the receiption window is 17520. The ACK logo is set. For details, refer to RFC 793— Transmission Control Protocol.

IP: s=192.168.20.22 (local), d=192.168.20.124 (vlan 10), g=192.168.20.124, len=40, sending, TCP: src=1024, dst=23, seq=75098622, ack=161000466, win=17520, ACK

The access control list is described in the following. For example, if the messages with the source address 192.168.20.125 require to be displayed, you need to define the standard access control list to permit only the IP message whose source address is 192.168.20.125. You then run the command debug ip packet to use the access control list.

switch#config

switch_config#ip access-list standard abc

switch_config_std_nacl#permit 192.168.20.125

switch_config_std_nacl#exit

switch_config#exit

switch#debug ip packet abc

switch#IP: s=192.168.20.125 (vlan 101), d=192.168.20.22 (vlan 101), len=48, rcvd

In the previous commands, the standard access control list is used. You can also use the extensible access control list.

Related command

debug ip tcp packet

### debug ip raw

Syntax

It is used to display the IP interaction information. Run the command no debug ip raw to stop displaying the information.

debug ip raw [detail] [access-list-group] [interface]

no debug ip raw

Parameter

| Parameter | Description |
| --- | --- |
| detail | An optional parameter, which is used to export the protocol information about IP message encapsulation, such as protocol number, UDP, TCP port number and ICMP message type |
| access-group | An optional parameter, which is used to filter the names of the IP access control list in the exported information Only the information about the IP message in the specified IP access control list can be exported. |
| interface | An optional parameter, which is used to filter the port name of the exported information Only the information about the IP message satisfied the designated port can be exported. |

Command mode

Management mode

Usage guidelines

The command is used to find the destination of each received or locally generated IP message, which helps to detect the reason of communication problems.

The command is used in the following cases:

Forwarded

Forwarded as the multicast message or the broadcast message

Addressing failure during message forwarding

Sending the redirect message

Rejected because of having the original routing option

Rejected because of illegal IP options

Original route

Message sent from the local machine should be segmented, but the DF is reset.

Receiving message

Receiving IP segment

Sending message

Sending broadcast/multicast

Addressing failure when message is generated locally

Locally generated message is segmented

Received message is filtered

Transmitted message is filtered

Link layer fails to be encapsulated (only for Ethernet)

Unknown protocol

This command may export lots of information. You'd better use it when the switch is in the free state. Otherwise, the performance of the system will be badly affected. You are recommended to filter the output information through the IP access control list, enabling the system to export the useful message.

Example

Similar to the debug ip packet command

Related command

debug ip tcp packet

### debug ip tcp packet

Syntax

It is used to display the TCP message. To stop displaying the TCP message, run the command no debug ip tcp packet.

debug ip tcp packet

no debug ip tcp packet

Parameter

The command has no parameter or keyword.

Command mode

Management mode

Example

switch#debug ip tcp packet

switch#tcp: O ESTABLISHED 192.168.20.22:23 192.168.20.125:3828 seq 50659460

DATA 1 ACK 3130379810 PSH WIN 4380

tcp: I ESTABLISHED 192.168.20.22:23 192.168.20.125:3828 seq 3130379810

DATA 2 ACK 50659460 PSH WIN 16372

tcp: O ESTABLISHED 192.168.20.22:23 192.168.20.125:3828 seq 50659461

DATA 50 ACK 3130379812 PSH WIN 4380

tcp: O FIN_WAIT_1 192.168.20.22:23 192.168.20.125:3828 seq 50659511

ACK 3130379812 FIN WIN 4380

tcp: I FIN_WAIT_1 192.168.20.22:23 192.168.20.125:3828 seq 3130379812

ACK 50659511 WIN 16321

tcp: I FIN_WAIT_1 192.168.20.22:23 192.168.20.125:3828 seq 3130379812

ACK 50659512 WIN 16321

tcp: I FIN_WAIT_2 192.168.20.22:23 192.168.20.125:3828 seq 3130379812

ACK 50659512 FIN WIN 16321

tcp: O TIME_WAIT 192.168.20.22:23 192.168.20.125:3828 seq 50659512

ACK 3130379813 WIN 4380

tcp: I LISTEN 0.0.0.0:23 0.0.0.0:0 seq 3813109318

DATA 2 ACK 8057944 PSH WIN 17440

tcp: O LISTEN 0.0.0.0:23 0.0.0.0:0 seq 8057944

RST

| Field | Description |
| --- | --- |
| tcp: | Information about the TCP message |
| O | Sending the TCP message |
| ESTABLISHED | Current state of the TCP connection For the description of the TCP connection state, refer to the description of the command debug ip tcp transactions. |
| 192.168.20.22:23 | Means that the source address of the message is 192.168.20.22 and the source port is port 23. |
| 192.168.20.125:3828 | Means that the destination address of the message is 192.168.20.125 and the destination port is port 3828. |
| seq 50659460 | Means that the sequence number of the message is 50659460. |
| DATA 1 | Means that the number of valid data bytes contained in the message is 1. |
| ACK 3130379810 | Means that the acknowledge number of the message is 3130379810. |
| PSH | Means that PSH in the control bits of the message is set. Other control bits include ACK, FIN, SYN, URG and RST. |
| WIN 4380 | It is used to notify the peer reception end of the cache size. The current cache size is 4380 sizes. |
| I | Receiving the TCP message |

If the previous fields are not displayed, the field in the TCP message does not have the valid value.

Related command

debug ip tcp transactions

### debug ip tcp transactions

Syntax

It is used to display the TCP interaction information, such as the change of the TCP connection state. Run the command no debug ip tcp transactions to stop displaying the information.

debug ip tcp transactions

no debug ip tcp transactions

Parameter

The command has no parameter or keyword.

Command mode

Management mode

Example

switch#debug ip tcp transactions

switch#TCP: rcvd connection attempt to port 23

TCP: TCB 0xE88AC8 created

TCP: state was LISTEN -> SYN_RCVD [23 -> 192.168.20.125:3828]

TCP: sending SYN, seq 50658312, ack 3130379657 [23 -> 192.168.20.125:3828]

TCP: state was SYN_RCVD -> ESTABLISHED [23 -> 192.168.20.125:3828]

TCP: connection closed by user, state was LISTEN [23 -> 0.0.0.0:0]

TCP: state was TIME_WAIT -> CLOSED [23 -> 192.168.20.125:3827]

TCP: TCB 0xE923C8 deleted

TCP: TCB 0xE7DBC8 created

TCP: connection to 192.168.20.124:513 from 192.168.20.22:1022, state was CLOSED to SYN_SENT

TCP: sending SYN, seq 52188680, ack 0 [1022 -> 192.168.20.124:513]

TCP: state was SYN_SENT -> ESTABLISHED [1022 -> 192.168.20.124:513]

TCP: rcvd FIN, state was ESTABLISHED -> CLOSE_WAIT [1022 -> 192.168.20.124:513]

TCP: connection closed by user, state was CLOSE_WAIT [1022 -> 192.168.20.124:513]

TCP: sending FIN [1022 -> 192.168.20.124:513]

TCP: connection closed by user, state was LAST_ACK [1022 -> 192.168.20.124:513]

TCP: state was LAST_ACK -> CLOSED [1022 -> 192.168.20.124:513]

TCP: TCB 0xE7DBC8 deleted

| Field | Description |
| --- | --- |
| TCP: | Means that the TCP interaction information is displayed. |
| rcvd connection attempt to port 23 | Means that the connection request from peer port 23 (telnet port) is received. |
| TCB 0xE88AC8 created | Means a new TCP connection control block is generated and its logo is 0xE88AC8. |
| state was LISTEN -> SYN_RCVD | Means that the state of the TCP state machine changes from the LISTEN state to the SYN_RCVD state. The TCP state may be one of the following: LISTEN---waiting for the TCP connection request from any remote host SYN_SENT---the connection request for creating TCP connection negotiation has been sent and the reply is being waited. SYN_RCVD---the connection request from the peer has been received and the acknowledgement information and its own connection request have also been sent out; the acknowledge information about the peer’s connection is being waited. ESTABLISHED---the connection is successful; the data is being transmitted; the data of the upper application can be received and sent. FIN_WAIT_1---the connection termination request has been sent to the peer; the acknowledgement information and the connection termination request from the peer are being waited. FIN_WAIT_2---the connection termination request has been sent to the peer and the acknowledgement information from the peer has been received; the connection termination request from the peer is being waited. CLOSE_WAIT--- the connection termination request from the peer has been received and the acknowledgement information has been sent out; the local user is being waited to close the connection. Once the user demands to close the connection, the system sends out the connection termination request. CLOSING--- the connection termination request has been sent to the peer and the connection termination request from the peer has been received and the acknowledgement information has been sent out; the system is waiting for the local connection termination request acknowledge from the peer. LAST_ACK---The system has received the connection termination request from the peer and acknowledged it; the system has already sent out connection termination request; the acknowledge is being waited for. TIME_WAIT---the period when the system waits for the peer to receive the acknowledgement of the connection termination request CLOSED---the connection is closed. For details, refer to RFC 793, Transmission Control Protocol. |
| [23 -> 192.168.20.125:3828] | The first field (23) in the bracket means the local TCP port. The second field (192.168.20.125) in the bracket means the remote IP address. The third field (3828) in the bracket means the remote TCP port. |
| sending SYN | Means a connection request message is sent out (SYN in the control bits of the TCP header is set). Other TCP control bits include SYN, ACK, FIN, PSH, RST and URG. |
| seq 50658312 | Means that the sequence number for sending the message is 50658312. |
| ack 3130379657 | Means that the acknowledgement number for sending the message is 3130379657. |
| rcvd FIN | Means that the connection termination request is received (FIN in the control bits of the TCP header is set). |
| connection closed by user | Means that the upper application requires closing the TCP connection. |
| connection timed out | Means that connection timeout is closed. |

Related command

debug ip tcp packet

### debug ip udp

Syntax

It is used to display the UDP interaction information. Run the command no debug ip udp to stop displaying the information.

debug ip udp

no debug ip udp

Parameter

The command has no parameter or keyword.

Command mode

Management mode

Example

switch#debug ip udp

switch#UDP: rcvd src 192.168.20.99(520), dst 192.168.20.255(520), len = 32

UDP: sent src 192.168.20.22(20001), dst 192.168.20.43(1001), len = 1008

| Field | Description |
| --- | --- |
| UDP: | Means that the information is about the UDP message. |
| rcvd | Means that the message is received. |
| sent | Means that the message is sent. |
| src | Means the source IP address of the UDP message and the UDP port. |
| dst | Means the destination IP address of the UDP message and the UDP port. |
| len | Means the length of the UDP message. |

The first line in the previous information shows that a UDP message is received. The UDP message is sent from host 192.168.20.99. Both the source port and the destination port are port 520. The destination address is 192.168.20.255. The length of the message is 32 bytes.

The second line in the previous information shows that a UDP message is sent. The local address and the destination address are 192.168.20.22 and 192.168.20.43 respectively. The source port and the destination port are port 20001 and port 1001 respectively. The length of the message is 1008 bytes.

### ip mask-reply

Syntax

It is used to enable the switch to reply the mask request of the IP address on the designated interface. Run the command no ip mask-reply to disable the function.

ip mask-reply

no ip mask-reply

default ip mask-reply

Parameter

The command has no parameter or keyword.

Default value

The mask request of the IP address is not replied.

Command mode

Interface configuration mode

Example

interface vlan 11

ip mask-reply

### ip mtu

Syntax

It is used to set the MTU of the IP message. To reuse MTUDefault, run the command no ip mtu.

ip mtu bytes

no ip mtu

Parameter

| Parameter | Description |
| --- | --- |
| bytes | Maximum transmission unit of the IP message, which is calculated by byte |

Default value

It varies with different physical media of the interface. It is the same as MTU. The minimum value is 68 bytes.

Command mode

Interface configuration mode

Usage guidelines

If the length of the IP message exceeds IP MTU configured on the interface, the switch fragments the message. All devices connecting on the same physical media need be configured the same MTU. The MTU affects the IP MTU. If the value of IP MTU is the same as that of the MTU, the value of IP MTU automatically changes to the new value of the MTU when the MTU value changes. The change of the IP MTU does not affectthe MTU.

The minimum value of IP MTU is 68 bytes and the maximum value of IP MTU cannot exceed the MTU value configured on the interface.

Example

The following example shows that IP MTU on interface vlan 10 is set to 200:

interface vlan 10

ip mtu 200

Related command

mtu

### ip redirects

Syntax

It is used to send the IP ICMP redirect message. You can run the command no ip redirects not to send the IP ICMP redirect message.

ip redirects

no ip redirects

Parameter

The command has no parameter or keyword.

Default value

The IP redirect message is sent by default. However, if you configure the hot standby switch protocol, the function is disabled automatically. If the hot standby switch protocol is cancelled, the function cannot be automatically enabled.

Command mode

Interface configuration mode

Usage guidelines

When the switch finds that the forwarding interface of the gateway is the same as the the reception interface and the source host directly connects the logical network of the interface, the switch sends an ICMP redirect message, notifying the source host to take the switch as the gateway to the destination address.

If the hot standby switch protocol is configured on the interface, the message may be dropped when the IP redirect message is sent.

Example

The following example shows that the ICMP redirect message can be sent on interface vlan 10:

interface vlan 10

ip redirects

### ip route-cache

Syntax

It is used to enable the route cache to forward the IP message. You can run the command no ip route-cache to deny the route cache.

ip route-cache

no ip route-cache

ip route-cache same-interface

no ip route-cache same-interface

Parameter

| Parameter | Description |
| --- | --- |
| same-interface | Enables the IP message to be rapidly forwarded from the receiption interface. |

Default value

The fast switching is allowed on the interface. The fast switching is forbidden on the same interface.

Command mode

Interface configuration mode

Usage guidelines

The route cache performs load balance to the messages transmitted or received through the source address and the destination address.

The route cache helps improving the message forwarding performance of the routing switch. However, the route cache need be denied on the low-speed path (64 k or below).

You can run the command ip route-cache same-interface to allow the rapid IP switching on the same interface, that is, the reception interface is the same as the transmitter interface. Normally, you are not recommended to enable the function because it collides with the redirect function of the routing switch. If you have an incompletely connected network, such as frame relay, you can enable the function on the interface of the frame relay. For example, the routing switches A, B and C constitute the frame relay network. Only the link from A to B and the link from B to C exist. The     communication from switch A to switch B must be relayed through switch B. Switch B receives the message from switch A through a DLCI, and then forwards the message to switch C through another DLCI.

Example

The following example shows that the rapid switching is permitted on the same interface:

ip route-cache same-interface

The following command is used to forbid the rapid switching, including on the same interface:

no ip route-cache

The following command is used to forbid the rapid switching only on the same interface:

no ip route-cache same-interface

The following command is used to resume the system to the default settings (the rapid switching is permitted, but the rapid switching is forbidden on the same interface):

ip route-cache

Related command

show ip cache

### ip route-cache hit-numbers

Syntax

Run the following command in global configuration mode to configure the hit number needed when the items in the software route cache are added to the hardware route cache.

[no] ip route-cache hit-numbers hit-number

Parameter

| Parameter | Description |
| --- | --- |
| hit-number | Hit number needed when the items in the software route cache are added to the hardware route cache |

Default value

The default value is 5.

Command mode

Global configuration mode

Usage guidelines

The command is used to configure the hit number needed when the items in the software route cache are added to the hardware route cache.

Example

The following example shows that the items in the software route cache are added to the hardware route cache when the items are hit twice.

ip route-cache hit-numbers 2

Related command

show ip cache

### ip route-cache age-exf

Syntax

To delete the hardware route of a host in case the next hop of the route of the indirectly connected host is same as that of a subnet route, run the following command in global mode:

[no] ip route-cache age-exf

Parameter

None

Default value

It is enabled by default.

Command mode

Global configuration mode

Usage guidelines

In case the next hop of the route of the indirectly connected host is same as that of a subnet route, the command will be used to decide whether to delete the hardware route of a host.

Example

After the no ip exf command is run in global mode, the dst:192.200.1.1 nh:192.3.3.2 route of the indirectly connected host will be generated due to the forwarding of L3 packets. If you want to open IP EXF globally in this case, two results, as shown below, will be obtained according to the shutdown or opening of ip route-cache age-exf.

- If the ip route-cache age-exf command is enabled, the hardware subnet route, dst:192.200.1.0/24 nh:192.3.3.2, will be generated and at the same time the hardware host’s route, dst:192.200.1.1 nh:192.3.3.2, will be deleted.

- If the ip route-cache age-exf command is disabled, the hardware subnet route, dst:192.200.1.0/24 nh:192.3.3.2, will be generated and at the same time the hardware host’s route, dst:192.200.1.1 nh:192.3.3.2, will be kept.

Related command

ip exf

show ip cache

### ip route-cache cache-pbr

Syntax

If you run this command in global configuration mode, the hosts that detect the routes through policy routing will also be added to the hardware host list; by default, these hosts will not be added to the list.

[no] ip route-cache cache-pbr

Parameter

None

Default value

Disabled by default

Command mode

Global configuration mode

Usage guidelines

After the policy routing is set, those route caches that look for routes through the policy routing cannot be added to the hardware table, and in this case the software forwarding reduces in its performance; after this command is set, these route caches can be added to the hardware table to improve the performance of the system.

Example

The following example shows how to enable the function in global mode:

ip route-cache cache-pbr

Related command

show ip cache

### ip route-cache age-delay

Syntax

To set the delay of the route cache, which is caused by ARP change, run the following command in global mode:

[no] ip route-cache age-delay age-delay

Parameter

| Parameter | Description |
| --- | --- |
| age-delay | Sets the delay of route hardware cache. |

Default value

The default value is 0.

Command mode

Global configuration mode

Usage guidelines

If the delay is set, the related hardware route cache will be kept from being deleted promptly at the change of ARP until the delay is done.

Note: In a network with a lot of directly connected hosts, ARP change will lead to the cancelation of related hardware route cache, leaving here a lot of packets to impact CPU, while the delay settings can provide a temporary protection to CPU. This command is always used together with another command, arp retry-allarp, and when both commands are executed, the system will learn ARP again and then reset the correct egress for IP cache as soon as possible.

Example

The following example shows how to set the delay of hardware route cache, which is caused by ARP change, to 60:

ip route-cache age-delay 60

Related command

show ip cache

### ip route-cache softcache-alive-time

Syntax

To set the lifetime of the route entries in the software cache, run the following command in global mode:

[no] ip route-cache softcache-alive-time alive-time

Parameter

| Parameter | Description |
| --- | --- |
| alive-time | Stands for the lifetime of the route entries in the software cache, whose unit is 10ms. |

Default value

The default value of the lifetime is 3000, that is, 30s.

Command mode

Global configuration mode

Usage guidelines

This command is used to set the lifetime of the entries in the software route cache.

Example

The following example shows how to set the lifetime of the entries in the software route cache to 40s:

ip route-cache softcache-alive-time 4000

Related command

show ip cache

### ip route-cache software-index

Syntax

To set the maximum time for the timer to operate the entries in the software route cache each time, run the following command in global mode:

[no] ip route-cache software-index ticks

Parameter

| Parameter | Description |
| --- | --- |
| ticks | Sets the maximum time for the timer to operate the entries in the software route cache each time. |

Default value

The default value of the lifetime is 1, that is, 10ms.

Command mode

Global configuration mode

Usage guidelines

This command is used to set the maximum time for the timer to operate the entries in the software route cache. The bigger the maximum time is, the sooner the invalid software route cache ages, especially when the system is busy. Hence, this command can be used to restrain the quantity of the invalid entries in the software route cache.

Example

The following example shows how to set the maximum time, which is for the timer to operate the entries in the software route cache, to 500ms:

ip route-cache software-index 50

Related command

show ip cache

### ip route-cache hardware-index

Syntax

To set the maximum time for the timer to operate the hardware route cache each time, run the following command in global mode:

[no] ip route-cache hardware-index ticks

Parameter

| Parameter | Description |
| --- | --- |
| ticks | Sets the maximum time for the timer to operate the entries in the software route cache each time. |

Default value

The default value of the lifetime is 50, that is, 0.5s.

Command mode

Global configuration mode

Usage guidelines

This command is used to set the maximum time for the timer to operate the entries in the hardware route cache. The bigger the maximum time is, the sooner the invalid hardware route cache ages, especially when the system is busy.

Example

The following example shows how to set the maximum time, which is for the timer to operate the entries in the software route cache, to 600ms:

ip route-cache hardware-index 60

Related command

show ip cache

### ip route-cache-aging-time

Syntax

To set the lifetime of the entries in the hardware cache, run the following command in global mode:

[no] ip route-cache-aging-time seconds

Parameter

| Parameter | Description |
| --- | --- |
| seconds | Sets the lifetime of the hardware route cache. |

Default value

The default value is 300s.

Command mode

Global configuration mode

Usage guidelines

This command is used to set the lifetime of the entries in the hardware route cache.

Example

The following example shows how to set the lifetime of the entries in the hardware route cache to 600s:

ip route-cache-aging-time 600

Related command

show ip cache

### ip source-route

Syntax

It is used to enable the routing switch to process the IP message with the source IP route. To enable the routing switch to drop the IP message with the source IP route, run the command no ip source-route.

ip source-route

no ip source-route

Parameter

None

Default value

The IP message with the source IP route is processed.

Command mode

Global configuration mode

Example

The following command enables the routing switch to process the IP message with the source IP route.

ip source-route

Related command

ping

### ip tcp synwait-time

Syntax

It is used to set the timeout time, which is used in the case when the switch waits for the successful TCP connection. To resume to the default time, run the command no ip tcp synwait-time.

ip tcp synwait-time seconds

no ip tcp synwait-time

Parameter

| Parameter | Description |
| --- | --- |
| seconds | Time for waiting for the TCP connection, which ranges from 5 to 300 seconds Its default value is 75 seconds. |

Default value

75 seconds

Command mode

Global configuration mode

Usage guidelines

When the switch originates the TCP connection, if the TCP connection is unsuccessful after the waiting time, the switch considers that the connection fails and sends the result to the upper application. You can set the waiting time for the successful TCP connection. The default value is 75 seconds. The option has nothing with the TCP connection message forwarded by the switch. However, it is relevant with the local TCP connection of the switch.

To know the current value of the waiting time, run the command ip tcp synwait-time ?. The value in the square bracket is the current value.

Example

The following example shows that the waiting time of the TCP connection is set to 30 seconds:

switch_config#ip tcp synwait-time 30

switch_config#ip tcp synwait-time ?

<5-300>[30] seconds     -- wait time

### ip tcp window-size

Syntax

It is used to set the size of the TCP window. To resume to the default value, run the command no ip tcp window-size.

ip tcp window-size bytes

no ip tcp window-size

Parameter

| Parameter | Description |
| --- | --- |
| bytes | Size of the window whose unit is second The maximum size is 65535 bytes. The default size is 2000 bytes. |

Default value

2000 bytes

Command mode

Global configuration mode

Usage guidelines

Do not hastly modify the default value of the window size unless you have a definite purpose. You can run the command ip tcp window-size ? to know the current value. The value in the square bracket is the current value.

Example

The following example shows that the size of the TCP window is set to 6000 bytes:

switch_config#ip tcp window-size 6000

switch_config#ip tcp window-size ?

<1-65535>[6000] bytes     -- Window size

### ip unreachables

Syntax

It is used to enable the switch to send the ICMP unreachable message. To stop sending the message, run the command no ip unreachables.

ip unreachables

no ip unreachables

Parameter

The command has no parameter or keyword.

Default value

The ICMP unreachable message is sent.

Command mode

Interface configuration mode

Usage guidelines

When the switch forwards the IP message, the message is dropped if the relevant route is not in the routing table. In this case, the switch sends the ICMP unreachable message to the source host. According to the information in the ICMP unreachable message, the source host promptly detects the fault and removes it.

Example

The following example shows that the interface vlan 10 is set to send the ICMP unreachable message:

interface vlan 10

ip unreachables

### show ip cache

Syntax

It is used to display the route cache, which is used for the rapid switching.

show ip cache [prefix mask]|software|hardware]

Parameter

| Parameter | Description |
| --- | --- |
| prefix mask | An optional parameter, which means that the destination address of the items and the items matching the designated prefix/mask are displayed |
| software | Means that only the itews stored in the software route cache are displayed. |
| hardware | Means that only the itews stored in the hardware route cache are displayed. |

Command mode

Management mode

Example

The following example shows that the route cache is displayed:

switch#show ip cache

Source          Destination     Interface        Next Hop

192.168.20.125  2.0.0.124       vlan 210        2.0.0.124

192.168.20.124  192.168.30.124  vlan 210        2.0.0.124

2.0.0.124       192.168.20.125  vlan 11      192.168.20.125

| Field | Description |
| --- | --- |
| Source | Source address |
| Destination | Destination address |
| Interface | Type and number of the transmitter interface |
| Next Hop | Address of the gateway |

The following example shows that the route cache whose destination address matches the designated prefix or mask is displayed:

switch#show ip cache 192.168.20.0 255.255.255.0

Source          Destination     Interface        Next Hop

2.0.0.124       192.168.20.125  vlan 101      192.168.20.125

The following example shows that the route cache whose transmitter interface matches the designated interface type or mask is displayed:

switch#show ip cache vlan210

Source          Destination     Interface        Next Hop

192.168.20.125  2.0.0.124       vlan 210        2.0.0.124

192.168.20.124  192.168.30.124  vlan 210        2.0.0.124

### show ip irdp

Syntax

It is used to display the irdp information.

Parameter

The command has no parameter or keyword.

Command mode

Management mode

Example

xuhao_config_vlan10#  show ip irdp

Async0/0 ICMP router discovery protocol(IRDP) : OFF

vlan 10 ICMP router discovery protocol(IRDP) : ON

Advertisements occur between every 450 and 600 seconds

Advertisements are sent as broadcasts

Advertisements valid in 1800 seconds

Default preference: 0

vlan 11 ICMP router discovery protocol(IRDP) : OFF

Null0 ICMP router discovery protocol(IRDP) : OFF

Loopback7 ICMP router discovery protocol(IRDP) : OFF

Loopback10 ICMP router discovery protocol(IRDP) : OFF

### show ip sockets

Syntax

It is used to display the socket information.

show ip sockets

Parameter

The command has no parameter or keyword.

Command mode

Management mode

Example

switch#show ip sockets

| Proto | Local | Port | Remote | Port | In | Out |
| --- | --- | --- | --- | --- | --- | --- |
| 17 | 0.0.0.0 | 0 | 0.0.0.0 | 0 | 161 | 0 |
| 6 | 0.0.0.0 | 0 | 0.0.0.0 | 0 | 513 | 0 |
| 17 | 0.0.0.0 | 0 | 0.0.0.0 | 0 | 1698 | 0 |
| 17 | 0.0.0.0 | 0 | 0.0.0.0 | 0 | 69 | 0 |
| 6 | 0.0.0.0 | 0 | 0.0.0.0 | 0 | 23 | 0 |
| 17 | 0.0.0.0 | 0 | 0.0.0.0 | 0 | 137 | 122590 |

| Field | Description |
| --- | --- |
| Proto | IP number The protocol number of UDP is 17 and the number of TCP is 6. |
| Remote | Remote address |
| Port | Remote port |
| Local | Local address |
| Port | Local port |
| In | Total number of the received bytes |
| Out | Total number of the transmitted bytes |

### show ip traffic

Syntax

It is used to display the statistics information about the IP traffic.

show ip traffic

Parameter

The command has no parameter or keyword.

Command mode

Management mode

Example

switch#show ip traffic

IP statistics:

Rcvd:  0 total, 0 local destination, 0 delivered

0 format errors, 0 checksum errors, 0 bad ttl count

0 bad destination address, 0 unknown protocol, 0 discarded

0 filtered , 0 bad options, 0 with options

Opts:  0 loose source route, 0 record route, 0 strict source route

0 timestamp, 0 router alert, 0 others

Frags: 0 fragments, 0 reassembled, 0 dropped

0 fragmented, 0 fragments, 0 couldn't fragment

Bcast: 0 received, 0 sent

Mcast: 0 received, 0 sent

Sent:  230 generated, 0 forwarded

0 filtered, 0 no route, 0 discarded

ICMP statistics:

Rcvd: 0 total, 0 format errors, 0 checksum errors

0 redirect, 0 unreachable, 0 source quench

0 echos, 0 echo replies, 0 mask requests, 0 mask replies

0 parameter problem, 0 timestamps, 0 timestamp replies

0 time exceeded, 0 router solicitations, 0 router advertisements

Sent: 0 total, 0 errors

0 redirects, 0 unreachable, 0 source quench

0 echos, 0 echo replies, 0 mask requests, 0 mask replies

0 parameter problem, 0 timestamps, 0 timestamp replies

0 time exceeded, 0 router solicitations, 0 router advertisements

UDP statistics:

Rcvd: 28 total, 0 checksum errors, 22 no port, 0 full sock

Sent: 0 total

TCP statistics:

Rcvd: 0 total, 0 checksum errors, 0 no port

Sent: 3 total

IGMP statistics:

Rcvd: 0 total, 0 format errors, 0 checksum errors

0 host queries, 0 host reports

Sent: 0 host reports

ARP statistics:

Rcvd: 8 total, 7 requests, 1 replies, 0 reverse, 0 other

Sent: 5 total, 5 requests, 0 replies (0 proxy), 0 reverse

| Field | Description |
| --- | --- |
| format errors | Means that the format of the message is incorrect, such as the incorrect length of the IP header. |
| bad hop count | Means that the TTL value decreases to 0 when the routing switch forwards the message. In this case, the message will be dropped. |
| no route | Means that the routing switch does not have relevant route message. |

### show tcp

Syntax

It is used to display the state of all TCP connections.

show tcp

Parameter

The command has no parameter or keyword.

Command mode

Management mode

Example

switch#show tcp

TCB 0xE9ADC8

Connection state is ESTABLISHED, unread input bytes: 934

Local host: 192.168.20.22, Local port: 1023

Foreign host: 192.168.20.124, Foreign port: 513

Enqueued bytes for transmit: 0, input: 934  mis-ordered: 0 (0 packets)

Timer          Starts    Wakeups            Next(ms)

Retrans            33          1                   0

TimeWait           0          0                   0

SendWnd           0          0                   0

KeepAlive         102          0             7199500

iss:  29139463  snduna:  29139525  sndnxt:  29139525     sndwnd:     17520

irs: 709124039  rcvnxt: 709205436  rcvwnd:      4380

SRTT: 15 ms, RXT: 2500 ms, RTV: 687 ms

minRXT: 1000 ms, maxRXT: 64000 ms, ACK hold: 200 ms

Datagrams (max data segment is 1460 bytes):

Rcvd: 102 (out of order: 0), with data: 92, total data bytes: 81396

Sent: 104 (retransmit: 0), with data: 31, total data bytes: 61

| Field | Description |
| --- | --- |
| TCB 0xE77FC8 | Internal identifier of the TCP connection control block |
| Connection state is ESTABLISHED | Currrent state of the TCP connection The TCP connection may be in one of the following state: LISTEN---waiting for the TCP connection request from any remote host SYN_SENT---the connection request has been sent and the reply is being waited. SYN_RCVD---the connection request from the peer has been received and the acknowledgement information and its own connection request have also been sent out; the acknowledge information about the peer’s connection is being waited. ESTABLISHED---the connection is successful; the data is being transmitted; the data of the upper application can be received and sent. FIN_WAIT_1---the connection termination request has been sent to the peer; the acknowledgement information and the connection termination request from the peer are being waited. FIN_WAIT_2---the connection termination request has been sent to the peer and the acknowledgement information from the peer has been received; the connection termination request from the peer is being waited. CLOSE_WAIT--- the connection termination request from the peer has been received and the acknowledgement information has been sent out; the local user is being waited to close the connection. Once the user demands to close the connection, the system sends out the connection termination request. CLOSING--- the connection termination request has been sent to the peer and the connection termination request from the peer has been received and the acknowledgement information has been sent out; the system is waiting for the local connection termination request acknowledge from the peer. LAST_ACK---The system has received the connection termination request from the peer and acknowledged it; the system has already sent out connection termination request; the acknowledgement is being waited for. TIME_WAIT---the period when the system waits for the peer to receive the acknowledgement of the connection termination request CLOSED---the connection is closed. For details, refer to RFC 793, Transmission Control Protocol. |
| unread input bytes: | Data that is processed by the lower-layer TCP and the upper application has not received |
| Local host: | Local IP address |
| Local port: | Local TCP port |
| Foreign host: | Remote IP address |
| Foreign port: | Remote TCP port |
| Enqueued bytes for transmit: | Bytes in the transmitter queue, including the data that is sent but not yet acknowledged and the data that is not sent |
| input: | Bytes in the reception queue After sorting, these data waits for the upper application to accept. |
| mis-ordered: | Number of bytes and messages in the misordered queue After other data is received, these data can enter the receiption queue in turn and then can be received by the upper application. For example, after messages 1, 2, 4, 5 and 6 are received, messages 1 and 2 can enter the receiption queue, but messages 4, 5 and 6 have to enter the misordered queue and wait for message 3. |

After that, the information about the timer of the current connection is displayed, including its startup times, timeout times and the next-time timeout time. The value 0 means that the timer does not run currently. Each connection has its own unique timer. The timeout times is less than the startup times because the timer may be reset in its process. For example, when the retransmission timer works, the system will receive the acknowledgements for all data from the peer. In this case, the retransmission timer stops running.

Timer          Starts    Wakeups            Next(ms)

Retrans            33          1                 0

TimeWait           0          0                  0

SendWnd           0          0                  0

KeepAlive         102          0             7199500

| Field | Description |
| --- | --- |
| Timer | Name of the timer |
| Starts | Startup times of the timer |
| Wakeups | Timeout times of the timer |
| Next(ms) | Next-time timeout time (unit: ms) The value 0 means the timer does not run. |
| Retrans | Retransmission timer, which is used to trigger resending data The timer is started up after the data is sent. If the data is not acknowledged by the peer within the timeout time, the data will be resent. |
| TimeWait | Time Waiting timer, which is used to know that the peer has already received the acknowledgement of the connection termination request. |
| SendWnd | Timer of the transmission window, which is used to asure that the transmission wind resume to the normal size after the TCP acknowledgement information is dropped |
| KeepAlive | Keep-alive timer, which is used to asure that the communication link is in normal state and the peer is still in the connection state It triggers the testing message to be sent for testing the state of the communication link and the peer. |

After the timer is displayed, the sequence number of the TCP connection is displayed. TCP uses the sequence number to gurantee reliable and orderly data transmission. The local or remote host can control the traffic and send the acknowledgement information according to the sequence number.

iss:  29139463  snduna:  29139525  sndnxt:  29139525     sndwnd:     17520

irs: 709124039  rcvnxt: 709205436  rcvwnd:      4380

| Field | Description |
| --- | --- |
| iss: | Sequence number of original transmission |
| snduna: | Sequence number of the first byte in the data that is already sent but whose acknowledgement information has not been received |
| sndnxt: | Transmission sequence number of the first data in the data that is sent later |
| sndwnd: | TCP window size of the remote host |
| irs: | Original receiption sequence number, that is, original transmission sequence number of the remote host |
| rcvnxt: | Receiption sequence number that is acknowledged recently |
| rcvwnd: | TCP window size of the local host |

The transmission time recorded by the local host is displayed afterwards. The system can adapt itself to different networks according to the transmission time.

SRTT: 15 ms, RXT: 2500 ms, RTV: 687 ms

minRXT: 1000 ms, maxRXT: 64000 ms, ACK hold: 200 ms

| Field | Description |
| --- | --- |
| SRTT: | Round-trip time after smooth processing |
| RXT: | Retransmission timeout time |
| RTV: | Change value of the round-trip time |
| MinRXT: | Permissible minimum retransmission timeout time |
| MaxRXT: | Permissible maximum retransmission timeout time |
| ACK hold: | Maximum delay time when the acknowledgement is delayed for being sent together with the data |

Datagrams (max data segment is 1460 bytes):

Rcvd: 102 (out of order: 0), with data: 92, total data bytes: 81396

Sent: 104 (retransmit: 0), with data: 31, total data bytes: 61

| Field | Description |
| --- | --- |
| max data segment is | Maximum length of the data segment which is permitted by the connection |
| Rcvd: | Number of messages that the local host receives during the connection procedure, including the number of the misordered messages |
| with data: | Number of messages that contain valid data |
| total data bytes: | Number of data bytes contained by the message |
| Sent: | Number of messages that are sent or resent by the local host during the connection procedure |
| with data: | Number of messages that contain valid data |
| total data bytes: | Number of data bytes contained by the message |

Related command

show tcp brief

show tcp tcb

### show tcp brief

Syntax

It is used to display the brief information about the TCP connection.

show tcp brief [all]

Parameter

| Parameter | Description |
| --- | --- |
| all | An optional parameter, which means that all ports are displayed If the parameter is not entered, the system does not display the ports in the LISTEN state. |

Command mode

Management mode

Example

switch#show tcp brief

TCB         Local Address           Foreign Address          State

0xE9ADC8    192.168.20.22:1023    192.168.20.124:513    ESTABLISHED

0xEA34C8    192.168.20.22:23      192.168.20.125:1472   ESTABLISHED

| Field | Description |
| --- | --- |
| TCB | Internal identifier of the TCP connection |
| Local Address | Local IP address and the TCP port |
| Foreign Address | Remote IP address and the TCP port |
| State | State of the connection For details, refer to the description of the show tcp command. |

Related command

show tcp

show tcp tcb

### show tcp statistics

Syntax

It is used to display the TCP statistics data.

show tcp statistics

Parameter

The command has no parameter or keyword.

Command mode

Management mode

Example

switch#show tcp statistics

Rcvd: 148 Total, 0 no port

0 checksum error, 0 bad offset, 0 too short

131 packets (6974 bytes) in sequence

0 dup packets (0 bytes)

0 partially dup packets (0 bytes)

0 out-of-order packets (0 bytes)

0 packets (0 bytes) with data after window

0 packets after close

0 window probe packets, 0 window update packets

0 dup ack packets, 0 ack packets with unsend data

127 ack packets (247 bytes)

Sent: 239 Total, 0 urgent packets

6 control packets

123 data packets (245 bytes)

0 data packets (0 bytes) retransmitted

110 ack only packets (101 delayed)

0 window probe packets, 0 window update packets

4 Connections initiated, 0 connections accepted, 2 connections established

3 Connections closed (including 0 dropped, 1 embryonic dropped)

5 Total rxmt timeout, 0 connections dropped in rxmt timeout

1 Keepalive timeout, 0 keepalive probe, 1 Connections dropped in keepalive

| Field | Description |
| --- | --- |
| Rcvd: | Statistics data about the messages received by the routing switch |
| Total | Total number of the received messages |
| no port | Number of messages showing the destination port does not exist |
| checksum error | Number of messages showing that sum check is incorrect |
| bad offset | Number of messages showing that the data offset is incorrect |
| too short | Number of messages showing that the message length is less than the minimum effective length |
| packets in sequence | Number of messages that are received in turn |
| dup packets | Number of received duplicate messages |
| partially dup packets | Number of received messages that are partly duplicated |
| out-of-order packets | Number of misordered messages |
| packets with data after window | Number of messages whose data exceeds the receiption window |
| packets after close | Number of messages that are received after the connection is closed |
| window probe packets | Number of received messages about window probe |
| window update packets | Number of received messages about window update |
| dup ack packets | Number of received messages that are duplicately acknowledged |
| ack packets with unsent data | Number of received messages that are acknowledged but has not been sent |
| ack packets | Number of received messages that are acknowledged |
| Sent | Statistics data about messages that are sent by the routing switch |
| Total | Total number of the transmitted messages |
| urgent packets | Number of the transmitted urgent messages |
| control packets | Number of the transmitted control messages (SYN, FIN or RST) |
| data packets | Number of the transmitted data messages |
| data packets retransmitted | Number of the retransmitted data messages |
| ack only packets | Number of the purely acknowledged messages |
| window probe packets | Number of the transmitted window probe messages |
| window update packets | Number of the transmitted window update messages |
| Connections initiated | Number of the locally initiated connections |
| connections accepted | Number of the locally received connections |
| connections established | Number of the locally established connections |
| Connections closed | Number of the locally closed connections |
| Total rxmt timeout | Total number of retransmission timeouts |
| Connections dropped in rxmit timeout | Number of the connections dropped because of retransmission timeout |
| Keepalive timeout | Number of Keepalive timeouts |
| keepalive probe | Number of the transmitted messages for keepalive probe |
| Connections dropped in keepalive | Number of the connections dropped because of Keepalive |

Related command

clear tcp statistics

### show tcp tcbI

Syntax

It is used to display the state of a certain TCP connection.

show tcp tcb address

Parameter

| Parameter | Description |
| --- | --- |
| address | TCB address of the TCP connection TCB is an identifier of the TCP connection in the system, which can be obtained by the command show tcp brief. |

Command mode

Management mode

Example

For detailed explanation, refer to the command show tcp.

switch_config#show tcp tcb 0xea38c8

TCB 0xEA38C8

Connection state is ESTABLISHED, unread input bytes: 0

Local host: 192.168.20.22, Local port: 23

Foreign host: 192.168.20.125, Foreign port: 1583

Enqueued bytes for transmit: 0, input: 0  mis-ordered: 0 (0 packets)

Timer          Starts    Wakeups            Next(ms)

Retrans            4          0                   0

TimeWait           0          0                   0

SendWnd           0          0                   0

KeepAlive          +5          0             6633000

iss:  10431492  snduna:  10431573  sndnxt:  10431573     sndwnd:     17440

irs: 915717885  rcvnxt: 915717889  rcvwnd:      4380

SRTT: 2812 ms, RXT: 18500 ms, RTV: 4000 ms

minRXT: 1000 ms, maxRXT: 64000 ms, ACK hold: 200 ms

Datagrams (max data segment is 1460 bytes):

Rcvd: 5 (out of order: 0), with data: 1, total data bytes: 3

Sent: 4 (retransmit: 0), with data: 3, total data bytes: 80

Related command

show tcp

show tcp brief

## ACL Configuration Commands

The following are the access control list (ACL) configuration commands:

deny

ip access-group

ip access-list

permit

show ip access-list

### deny

Syntax

You can run the deny command in IP ACL configuration mode to forbid some regulations. You can run the no deny command to remove the forbidden regulations from the IP ACL.

deny source [source-mask] [log]

no deny source [source-mask] [log]

deny protocol source source-mask destination destination-mask　[precedence precedence] [tos tos] [log]

no deny protocol source source-mask destination destination-mask　[precedence precedence] [tos tos] [log]

The following syntax can be appled to the ICMP protocol:

deny icmp source source-mask destination destination-mask [icmp-type] [precedence precedence] [tos tos] [log]

The following syntax can be appled to the IGMP protocol:

deny igmp source source-mask destination destination-mask [igmp-type] [precedence precedence] [tos tos] [log]

The following syntax can be appled to the TCP protocol:

deny tcp source source-mask [operator port] destination destination-mask [operator port ] [established] [precedence precedence] [tos tos] [log]

The following syntax can be appled to theUDP protocol:

deny udp source source-mask [operator port] destination destination-mask [operator port] [precedence precedence] [tos tos] [log]

Parameter

| Parameter | Description |
| --- | --- |
| protocol | Protocol name or IP number It can be a keyword, such as icmp, igmp, igrp, ip, ospf, tcp or udp; it can be an integer from 0 to 255. The keyword ip is used for matching any Internet protocol, including ICMP, TCP and UDP. Some protocols can be further limited. See the following description. |
| source | Source network or host number The following two ways can be used to specify the source: Binary system in 32 bits Decimal system separated by four dots The keyword any is used to stand for the abbreviation of the source 0.0.0.0 and the source mask. |
| source-mask | Network mask of the source address The keyword any is used to stand for the abbreviation of the source host 0.0.0.0 and the source mask. |
| destination | Destination network or host number The following two ways can be used to specify the destination: Binary system in 32 bits Decimal system separated by four dots The keyword any is used to stand for the abbreviation of the destination host 0.0.0.0 and the destination mask. |
| destination-mask | Network mask of the destination address The keyword any is used to stand for the abbreviation of the destination 0.0.0.0 and the mask of the destination address. |
| precedence precedence | An optional parameter, which means that the packets can be filtered by precedence It is specified with an integer from 0 to 7. |
| tos tos | An optional parameter, which means that the packets can be filtered by the service layer. It is specified with an integer from 0 to 15. |
| icmp-type | An optional parameter, which means that the ICMP packets can be filtered by the ICMP message type. The ICMP message type is specified with an integer from 0 to 225. |
| igmp-type | An optional parameter, which means that the IGMP packets can be filtered by the IGMP message type or the IGMP message name. The IGMP message type is specified with an integer from 0 to 15. |
| operator | An optional parameter, which means to compare the source or the destination port The operations include the lt (less than) operation, the gt (larger than) operation, the eq (equal to) operation and the neq (unequal to) operation. If the operator is behind the parameter source and source-mask, it must match the source port. If the operator is behind the parameter destination and destination-mask, it must match the destination port. |
| port | An optional parameter, which means a decimal number or name of the TCP/UDP port The port number is a number from 0 to 65535. The names of TCP ports are listed in the part “Usage Policy”. When the TCP is filtered, only the name of the TCP port can be used. The names of UDP ports are listed in the part “Usage guidelines”. When the UDP is filtered, only the name of the UDP port can be used. |
| established | An optional parameter to the TCP protocol, which means a connection has been established If the ACK bit or the RST bit in the TCP packet is set, a TCP connection is matched. You also can initialize a TCP packet to establish a connection. |
| log | An optional parameter, which is used to record the log |

Command mode

IP access control list configuration mode

Usage guidelines

You can control the virtual terminal path access and limit the content in the route choice update by transmitting the ACL control packet. After the matching operation, the extensible ACL stops to be checked. The IP segment is promptly received by any extensible IP ACL. The extensible ACL is used to control the virtual terminal path access and limit the content in the route choice update. The source ICP port, type of the service value or precedence of the packet need not be matched.

Note:

After an ACL is originally created, any following content is written to the bottom of the list.

The following are the TCP port names which are used to replace the port numbers. You can find relative references about these protocols according to the current distribution number. You can find the corresponding port numbers of these protocols by entering a question mask.

Bgp、ftp、ftp-data、login、pop2、pop3、smtp、telnet、www

The following are the UDP port names which are used to replace the port numbers. You can find relative references about these protocols according to the current distribution number. You can find the corresponding port numbers of these protocols by entering a question mask.

Domain、snmp、syslog、tftp

Example

The following example shows that network segment is forbidden:

ip access-list standard filter

deny 192.168.5.0 255.255.255.0

Note:

The IP ACL ends with an implicit deny regulation.

Related command

ip access-group

ip access-list

permit

show ip access-list

### ip access-group

Syntax

It is used to control an interface access. To delete the designated access group, run the command no ip access-group.

ip access-group {access-list-name}{in | out}

no ip access-group {access-list-name}{in | out}

Parameter

| Parameter | Description |
| --- | --- |
| access-list-name | Name of the access control list, which is a character string with up to 20 characters |
| in | Access control list used on the incoming interface |
| out | Access control list used on the outgoing interface |

Command mode

Interface configuration mode

Usage guidelines

The ACL can be used both on the incoming interface and the outgoing interface. For the standard incoming ACL, the source address of the packet can be checked according to the ACL after the packet is received. For the standard extensible ACL, the switch also checks the destination address. If the ACL permits the address, the system continues to process the packet. If the ACL denies the packet, the system drops the packet and returns an ICMP unreachable message.

For the standard outgoing ACL, after a packet is received and routed to the control interface, the switch ckecks the source address of the packey according to the ACL. For the extensible ACL, the switch also checks the ACL at the receiption end. If the ACL permits the address, the switch transmits the packet. If the ACL denies the address, the switch drops the packet and returns an ICMP unreachable message.

If the designated ACL does not exist, all packets can pass through.

Example

The following example shows that the filter list is applied on Ethernet interface 0:

interface ethernet 0

ip access-group filter out

Related command

ip access-list

show ip access-list

### ip access-list

Syntax

It is used to enter the IP ACL configuration mode where you can add or delete the access regulation. You can run the exit command to go back to the configuration mode.

You can run the command no ip access-list to delete an IP ACL.

ip access-list {standard | extended} name

no ip access-list {standard | extended} name

Parameter

| Parameter | Description |
| --- | --- |
| standard | Specifies a standard ACL |
| extended | Specifies an extensible ACL |
| name | Name of the ACL, which is a character string with up to 20 characters |

Default value

No IP access control list is defined.

Command mode

Global configuration mode

Usage guidelines

The command is used to enter the IP ACL configuration mode. In IP ACL configuration mode,you can run the deny command or the permit command to configure the access regulation.

Example

The following example shows that a standard ACL is configured.

ip access-list standard filter

deny 192.168.1.0 255.255.255.0

permit any

Related command

deny

ip access-group

permit

show ip access-list

### permit

Syntax

It is used in IP ACL configuration mode to configure the permit regulations. To remove the permit regulations, run the command no permit.

permit source [source-mask] [log]

no permit source [source-mask] [log]

permit protocol source source-mask destination destination-mask　[precedence precedence] [tos tos] [log]

no permit protocol source source-mask destination destination-mask　[precedence precedence] [tos tos] [log]

The following syntax can be applied to the ICMP protocol:

permit icmp source source-mask destination destination-mask [icmp-type] [precedence precedence] [tos tos] [log]

The following syntax can be applied to the IGMP protocol:

permit igmp source source-mask destination destination-mask [igmp-type] [precedence precedence] [tos tos] [log]

The following syntax can be applied to the TCP protocol:

permit tcp source source-mask [operator port] destination destination-mask [operator port ] [established] [precedence precedence] [tos tos] [log]

The following syntax can be applied to the UDP protocol:

permit udp source source-mask [operator port [port]] destination destination-mask [operator port] [precedence precedence] [tos tos] [log]

Parameter

| Parameter | Description |
| --- | --- |
| protocol | Protocol name or IP number It can be a keyword, such as icmp, igmp, igrp, ip, ospf, tcp or udp; it can be an integer from 0 to 255. The keyword ip is used for matching any Internet protocol, including ICMP, TCP and UDP. Some protocols can be further limited. See the following description. |
| source | Source network or host number The following two ways can be used to specify the source: Binary system in 32 bits Decimal system separated by four dots The keyword any is used to stand for the abbreviation of the source 0.0.0.0 and the source mask. |
| source-mask | Network mask of the source address The keyword any is used to stand for the abbreviation of the source host 0.0.0.0 and the source mask. |
| destination | Destination network or host number The following two ways can be used to specify the destination: Binary system in 32 bits Decimal system separated by four dots The keyword any is used to stand for the abbreviation of the destination host 0.0.0.0 and the destination mask. |
| destination-mask | Network mask of the destination address The keyword any is used to stand for the abbreviation of the destination 0.0.0.0 and the mask of the destination address. |
| precedence precedence | An optional parameter, which means that the packets can be filtered by precedence It is specified with an integer from 0 to 7. |
| tos tos | An optional parameter, which means that the packets can be filtered by the service layer. It is specified with an integer from 0 to 15. |
| icmp-type | An optional parameter, which means that the ICMP packets can be filtered by the ICMP message type. The ICMP message type is specified with an integer from 0 to 225. |
| igmp-type | An optional parameter, which means that the IGMP packets can be filtered by the IGMP message type or the IGMP message name. The IGMP message type is specified with an integer from 0 to 15. |
| operator | An optional parameter, which means to compare the source or the destination port The operations include the lt (less than) operation, the gt (larger than) operation, the eq (equal to) operation and the neq (unequal to) operation. If the operator is behind the parameter source and source-mask, it must match the source port. If the operator is behind the parameter destination and destination-mask, it must match the destination port. |
| port | An optional parameter, which means a decimal number or name of the TCP/UDP port The port number is a number from 0 to 65535. The names of TCP ports are listed in the part “Usage Policy”. When the TCP is filtered, only the name of the TCP port can be used. The names of UDP ports are listed in the part “Usage guidelines”. When the UDP is filtered, only the name of the UDP port can be used. |
| established | An optional parameter to the TCP protocol, which means a connection has been established If the ACK bit or the RST bit in the TCP packet is set, a TCP connection is matched. You also can initialize a TCP packet to establish a connection. |
| log | An optional parameter, which is used to record the log |

Command mode

IP access control list configuration mode

Usage guidelines

You can control the virtual terminal path access and limit the content in the route choice update by transmitting the ACL control packet. After the matching operation, the extensible ACL stops to be checked. The IP segment is promptly received by any extensible IP ACL. The extensible ACL is used to control the virtual terminal path access and limit the content in the route choice update. The source ICP port, type of the service value or precedence of the packet need not be matched.

Note:

After an ACL is originally created, any following content is written to the bottom of the list.

The following are the TCP port names which are used to replace the port numbers. You can find relative references about these protocols according to the current distribution number. You can find the corresponding port numbers of these protocols by entering a question mask.

Bgp、ftp、ftp-data、login、pop2、pop3、smtp、telnet、www

The following are the UDP port names which are used to replace the port numbers. You can find relative references about these protocols according to the current distribution number. You can find the corresponding port numbers of these protocols by entering a question mask.

Domain、snmp、syslog、tftp

Example

The following example shows that network segment 192.168.5.0 is permitted:

ip access-list standard filter

permit 192.168.5.0 255.255.255.0

Note:

The IP ACL ends with an implicit deny regulation.

Related command

deny

ip access-group

ip access-list

show ip access-list

### show ip access-list

Syntax

It is used to display the content of the current IP AC.

show ip access-list[access-list-name]

Parameter

| Parameter | Description |
| --- | --- |
| access-list-name | Name of the access control list, which is a character string with up to 20 characters |

Default value

All standard and extensible IP ACLs are displayed.

Command mode

Management mode

Usage guidelines

The command is used to specify a specific ACL.

Example

The following information appears after you run the command show ip access-list without a designated ACL:

Switch# show ip access-list

ip access-list standard aaa

permit 192.2.2.1

permit 192.3.3.0 255.255.255.0

ip access-list extended bbb

permit tcp any any eq www

permit ip any any

The following information appears after you run the command show ip access-list with a designated ACL:

ip access-list extended bbb

permit tcp any any eq www

permit ip any any

## IP ACL Configuration Commands Based on Physical Ports

The following are ACL configuration commands based on physical ports:

deny

ip access-group

ip access-list

permit

show ip access-list

### deny

Syntax

You can run the deny command in IP ACL configuration mode to configure deny regulations. You can run the no deny command to remove the forbidden regulations from the IP ACL.

deny source [source-mask]

no deny source [source-mask]

deny protocol source source-mask destination destination-mask [tos tos]

no deny protocol source source-mask destination destination-mask [tos tos]

The following syntax can be applied to the ICMP protocol:

deny icmp source source-mask destination destination-mask [icmp-type] [tos tos]

The following syntax can be applied to the IGMP protocol:

deny igmp source source-mask destination destination-mask [igmp-type] [tos tos]

The following syntax can be applied to the TCP protocol:

deny tcp source source-mask [operator port] destination destination-mask [operator port ] [tos tos]

The following syntax can be applied to the UDP protocol:

deny udp source source-mask [operator port] destination destination-mask [operator port] [tos tos]

Parameter

| Parameter | Description |
| --- | --- |
| protocol | Protocol name or IP number It can be a keyword, such as icmp, igmp, igrp, ip, ospf, tcp or udp; it can be an integer from 0 to 255. The keyword ip is used for matching any Internet protocol, including ICMP, TCP and UDP. Some protocols can be further limited. See the following description. |
| source | Source network or host number The following two ways can be used to specify the source: Binary system in 32 bits Decimal system separated by four dots The keyword any is used to stand for the abbreviation of the source 0.0.0.0 and the source mask. |
| source-mask | Network mask of the source address The keyword any is used to stand for the abbreviation of the source host 0.0.0.0 and the source mask. |
| destination | Destination network or host number The following two ways can be used to specify the destination: Binary system in 32 bits Decimal system separated by four dots The keyword any is used to stand for the abbreviation of the destination host 0.0.0.0 and the destination mask. |
| destination-mask | Network mask of the destination address The keyword any is used to stand for the abbreviation of the destination 0.0.0.0 and the mask of the destination address. |
| precedence precedence | An optional parameter, which means that the packets can be filtered by precedence It is specified with an integer from 0 to 7. |
| tos tos | An optional parameter, which means that the packets can be filtered by the service layer. It is specified with an integer from 0 to 15. |
| icmp-type | An optional parameter, which means that the ICMP packets can be filtered by the ICMP message type. The ICMP message type is specified with an integer from 0 to 225. |
| igmp-type | An optional parameter, which means that the IGMP packets can be filtered by the IGMP message type or the IGMP message name. The IGMP message type is specified with an integer from 0 to 15. |
| operator | An optional parameter, which means to compare the source or the destination port The operations include the lt (less than) operation, the gt (larger than) operation, the eq (equal to) operation and the neq (unequal to) operation. If the operator is behind the parameter source and source-mask, it must match the source port. If the operator is behind the parameter destination and destination-mask, it must match the destination port. |
| port | An optional parameter, which means a decimal number or name of the TCP/UDP port The port number is a number from 0 to 65535. The names of TCP ports are listed in the part “Usage Policy”. When the TCP is filtered, only the name of the TCP port can be used. The names of UDP ports are listed in the part “Usage guidelines”. When the UDP is filtered, only the name of the UDP port can be used. |
| established | An optional parameter to the TCP protocol, which means a connection has been established If the ACK bit or the RST bit in the TCP packet is set, a TCP connection is matched. You also can initialize a TCP packet to establish a connection. |
| log | An optional parameter, which is used to record the log |

Command mode

IP access control list configuration mode

Usage guidelines

You can control the virtual terminal path access and limit the content in the route choice update by transmitting the ACL control packet. After the matching operation, the extensible ACL stops to be checked. The IP segment is promptly received by any extensible IP ACL. The extensible ACL is used to control the virtual terminal path access and limit the content in the route choice update. The source ICP port, type of the service value or precedence of the packet need not be matched.

Note:

After an ACL is originally created, any following content is written to the bottom of the list.

Example

The following example shows that network segment 192.168.5.0 is forbidden:

ip access-list standard filter

deny 192.168.5.0 255.255.255.0

Note:

The IP ACL ends with an implicit deny regulation.

Related command

ip access-group

ip access-list

permit

show ip access-list

### ip access-group

Syntax

It is used to control an interface access. To delete the designated access group, run the command no ip access-group.

ip access-group {access-list-name}

no ip access-group {access-list-name}

Parameter

| Parameter | Description |
| --- | --- |
| access-list-name | Name of the access control list, which is a character string with up to 20 characters |

Command mode

Interface configuration mode

Usage guidelines

The ACL can be used on the incoming interface. For the standard incoming ACL, the source address of the packet can be checked according to the ACL after the packet is received. For the extensible ACL, the switch also checks the destination address. If the ACL permits the address, the system continues to process the packet. If the ACL denies the packet, the system drops the packet and returns an ICMP unreachable message.

If the designated ACL does not exist, all packets can pass through.

Example

The following example shows that the filter list is applied on Ethernet interface 10:

interface f0/10

ip access-group filter

Related command

ip access-list

show ip access-list

### ip access-list

Syntax

After you run the command, the system enters the IP ACL configuration mode. In this mode, you can add or delete the access regulations. You can run the exit command to enable the system to enter the configuration mode

You can run the command no ip access-list to delete the IP ACL.

ip access-list {standard | extended} name

no ip access-list {standard | extended} name

Parameter

| Parameter | Description |
| --- | --- |
| standard | Specifies a standard ACL. |
| extended | Specifies an extensible ACL. |
| name | Name of an ACL, which is a character string with up to 20 characters |

Default value

No IP ACL is defined.

Command mode

Global configuration mode

Usage guidelines

It is used to enter the IP ACL configuration mode. In this mode, you can run the deny or permit command to configure the access regulation.

Example

The following example shows that a standard ACL is configured.

ip access-list standard filter

deny 192.168.1.0 255.255.255.0

permit any

Related command

deny

ip access-group

permit

show ip access-list

### permit

Syntax

It is used in IP ACL configuration mode to configure the permit regulation. You can rum the command no permit to remove the permit regulations from the IP ACL.

permit source [source-mask]

no permit source [source-mask]

permit protocol source source-mask destination destination-mask [tos tos]

no permit protocol source source-mask destination destination-mask [tos tos]

The following syntax can be applied to the ICMP protocol:

permit icmp source source-mask destination destination-mask [icmp-type] [tos tos]

The following syntax can be applied to the IGMP protocol:

permit igmp source source-mask destination destination-mask [igmp-type] [tos tos]

The following syntax can be applied to the TCP protocol:

permit tcp source source-mask [operator port] destination destination-mask [operator port ] [tos tos]

The following syntax can be applied to the UDP protocol:

permit udp source source-mask [operator port [port]] destination destination-mask  [tos tos]

Parameter

| Parameter | Description |
| --- | --- |
| protocol | Protocol name or IP number It can be a keyword, such as icmp, igmp, igrp, ip, ospf, tcp or udp; it can be an integer from 0 to 255. The keyword ip is used for matching any Internet protocol, including ICMP, TCP and UDP. Some protocols can be further limited. See the following description. |
| source | Source network or host number The following two ways can be used to specify the source: Binary system in 32 bits Decimal system separated by four dots The keyword any is used to stand for the abbreviation of the source 0.0.0.0 and the source mask. |
| source-mask | Network mask of the source address The keyword any is used to stand for the abbreviation of the source host 0.0.0.0 and the source mask. |
| destination | Destination network or host number The following two ways can be used to specify the destination: Binary system in 32 bits Decimal system separated by four dots The keyword any is used to stand for the abbreviation of the destination host 0.0.0.0 and the destination mask. |
| destination-mask | Network mask of the destination address The keyword any is used to stand for the abbreviation of the destination 0.0.0.0 and the mask of the destination address. |
| precedence precedence | An optional parameter, which means that the packets can be filtered by precedence It is specified with an integer from 0 to 7. |
| tos tos | An optional parameter, which means that the packets can be filtered by the service layer. It is specified with an integer from 0 to 15. |
| icmp-type | An optional parameter, which means that the ICMP packets can be filtered by the ICMP message type. The ICMP message type is specified with an integer from 0 to 225. |
| igmp-type | An optional parameter, which means that the IGMP packets can be filtered by the IGMP message type or the IGMP message name. The IGMP message type is specified with an integer from 0 to 15. |
| operator | An optional parameter, which means to compare the source or the destination port The operations include the lt (less than) operation, the gt (larger than) operation, the eq (equal to) operation and the neq (unequal to) operation. If the operator is behind the parameter source and source-mask, it must match the source port. If the operator is behind the parameter destination and destination-mask, it must match the destination port. |
| port | An optional parameter, which means a decimal number or name of the TCP/UDP port The port number is a number from 0 to 65535. The names of TCP ports are listed in the part “Usage Policy”. When the TCP is filtered, only the name of the TCP port can be used. The names of UDP ports are listed in the part “Usage guidelines”. When the UDP is filtered, only the name of the UDP port can be used. |
| established | An optional parameter to the TCP protocol, which means a connection has been established If the ACK bit or the RST bit in the TCP packet is set, a TCP connection is matched. You also can initialize a TCP packet to establish a connection. |
| log | An optional parameter, which is used to record the log |

Command mode

IP access control list configuration mode

Usage guidelines

You can control the virtual terminal path access and limit the content in the route choice update by transmitting the ACL control packet. After the matching operation, the extensible ACL stops to be checked. The IP segment is promptly received by any extensible IP ACL. The extensible ACL is used to control the virtual terminal path access and limit the content in the route choice update. The source ICP port, type of the service value or precedence of the packet need not be matched.

Note:

After an ACL is originally created, any following content is written to the bottom of the list.

Example

The following example shows that network segment 192.168.5.0 is permitted:

ip access-list standard filter

permit 192.168.5.0 255.255.255.0

Note:

The IP ACL ends with an implicit deny regulation.

Related command

deny

ip access-group

ip access-list

show ip access-list

### show ip access-list

Syntax

It is used to display the content of the current IP ACL.

show ip access-list[access-list-name]

Parameter

| Parameter | Description |
| --- | --- |
| access-list-name | Name of an ACL, which is a character string with up to 20 characters |

Default value

All standard and extensible IP ACLs are displayed.

Command mode

Management mode

Usage guidelines

It is used to specify a specific ACL.

Example

The following information appears after you run the command show ip access-list without specifying an ACL.

Switch# show ip access-list

ip access-list standard aaa

permit 192.2.2.1

permit 192.3.3.0 255.255.255.0

ip access-list extended bbb

permit tcp any any eq 25

permit ip any any

The following information appears after you run the command show ip access-list with a specified ACL.

ip access-list extended bbb

permit tcp any any eq 25

permit ip any any