Digital TS Re-multiplexer

User Manual

Contents

Warnings and Notices	1

1 Overview	2

1.1 General	2

1.2 Features	2

1.3 Panels and Interface	2

1.3.1 Front Panel	2

1.3.2 Rear Panel	3

2 Specifications	3

3 Typical Application	4

4 Menu Structure and Operation	5

4.1 Menu Tree	5

4.2 Menu Operation	6

4.2.1 Initialization	6

4.2.2 Inputs Setup Menu	6

4.2.3 Outputs Setup Menu	7

4.2.4 Mux Menu	8

4.2.5 System Menu	9

5 Installation and Initial use	11

6 Accessories	13

Warnings and Notices

- Please follow the below instructions. Don’t connect power before you finish install ting and checking according to safe procedure.

DCH-3000MX TS Re-multiplexer

1 Overview

1.1 General

DCH-3000MX is a compact and cost-effective DVB MPEG-2 TS re-multiplexer which can multiplex up to 8 ASI transport streams and deliver with 2 ASI ports (1 for redundancy). The combination of PID-packet-exchanging based technology; Ethernet remote control and 19" rack mountable chassis make it an ideal device for a wide range of re-multiplexing applications including cable and terrestrial regional head-ends.

1.2 Features

- Fully compliant with DVB ETSI 300421 standard

- Processing of up to 8 SPTS or MPTS

- SI/PSI automatic regeneration

- Service and PID packet filtering and re-multiplexing

- Up to 160Mbps Mbps MPTS/ SPTS inputs

- Output rate up to 100 Mbps

- ASI input packet length 188/204 bytes Self-adapting. Output packet length 188/204 bytes optional.

- 8 ASI inputs, 2 ASI outputs (1 for redundancy)

- Standard 19” rack 1U chassis installation

- Network remote control and software upgrade

1.3 Panels and Interface

1.3.1 Front Panel

A1－A8	Indicators for ASI 1-ASI 8 Input Status, respectively

A9	2 × 24 character LCD Menu Display

A10-A13	Arrow buttons for menu navigating and parameters modifications

A14	【Enter】button for issuing a command or selecting an option

A15	【Exit】button for returning to previous menu

1.3.2 Rear Panel

B1	ASI OUT 2

B2	ASI OUT 1

B3-B10	ASI IN 8- ASI IN 1

B11	RS-232 port for debug

B12	Ethernet port

B13	Grounding Terminal

B14	Power cord socket 90V~260ACV, 50Hz/60Hz

2 Specifications

| ASI input |
| --- |
| ASI Input Connector | BNC female，75 Ω |
| ASI Input bit rate | Up to 160Mbps |
| Data format | Byte, Burst (self-adapting) |
| Packet length | 188/204 bytes (self-adapting) |
| ASI output |
| ASI Output Connector | 2 ASI Output (1 for redundancy), BNC connector, 75Ω |
| ASI Output bit rate | ≤100Mbps |
| Date transfer mode | Byte |
| Packet length | 188/204 bytes (selectable) |
| Signal level | 800mV±10% |
| Other |
| Net weight | 3Kg |
| Size | 44mm×240mm×430mm |
| Running temperature | 0~40℃ |
| Deposit temperature | -20~70℃ |
| Humidity | ＜85% |

3 Typical Application

4 Menu Structure and Operation

4.1 Menu Tree

4.2 Menu Operation

4.2.1 Initialization

Connect the DCH-3000MX to an appropriated AC power source, turn on the power switch on the rear panel, the unit will be booted up automatically, and the LCD displays as below：

The power on boot up might take several tenths of seconds. The LCD displays as below after initialization:

The unit name is displayed on the first row and IP on the second.

Press [ENTER] for entering the main menu，then press   or    to navigate through the menu:

The main menu includes four items：

Inputs Setup：Configuration of input parameters

Outputs Setup：Configuration of output parameters

Mux：mux options，press [ENTER] to activate

System：Configuration of system information

Press▲or ▼ to navigate upward and downward the menu, press【ENTER】to confirm the selection, press【EXIT】to exit the menu.

4.2.2 Inputs Setup Menu

Enter Inputs Setup menu，the LCD displays as below：

Bit rate of each ASI input port is displayed on the second row, effective TS rate is shown on the left and total TS rate on the right.

Press ▲or ▼ to check bit rate among ASI input ports.

Press [ENTER] to check the available services of current ASI input port. An ‘$’ sign next to the service name indicates the program is being encrypted. Please refer to the diagram below,“1/4”,as an example, indicates the service just being shown is the first of all 4 available ones. Press [ENTER] to confirm your selection and an ‘*’ sign indicates this service has just been selected, and will be multiplexed once the multiplexing process is being activated. Press [ENTER] again to de-select the service.

Press ▲ or ▼ to switch channels among ASI ports and press [EXIT] to back to the previous menu. If the any service has been selected, when you back to the main menu, the below message will be displayed on the LCD:

Press [ENTER] to multiplex the selected services and press [EXIT] to discard.

If there is no valid ASI input found, if press ENTER and then it displays ‘No Program List’ as below, then it returns to the previous menu automatically.

4.2.3 Outputs Setup Menu

This menu has 4 items：

Bit Rate：ASI output bit rate configuration；

Packet Size：packet size setting of ASI output；

Transport Stream ID：ID setting of TS multiplexed；

Outputs Program：Channel information output

Press ▲ or ▼ to switch. Press [ENTER] to enter the submenu.

4.2.3.1 Bit Rate

Enter the Bit Rate menu and the LCD displays as below：

Output bit rate is from 100kbps to 100000Kbps adjustable. Press  or   to move the cursor and press ▲or ▼ to change the numurical entry(ies). Press [ENTER] to confirm the numurical entry(ies).

Notice：To ensure the sum of all selected services, including some Variable Bit Rate ones, does not exceed the output bit rate actually set, it is recommended to set 1.1 times higher than the static sum of bit rates of all services selected. If the effective output bit rate exceeds the actual setting value, there will be a alarm on the root menu，as below：

where 42125Kbps indicates the effective bit rate detected of the Outputs Stream.

4.2.3.2 Packet Size

Packet Size: used for select output packet format，as below：

There are 2 kinds of ASI output packet format：188 Bytes and 204 Bytes. Use   or  to switch. Press [ENTER] to select.

Remark: The final effective output Bit rate will be reset, if the packet format is changed.

4.2.3.3 Transport Stream ID

The ID of TS stream is to distinguish from other streams in the same system . Press [ENTER] for entering, as below：

The valid range of ID of TS is 0～65535. Press    or   to move cursor, press   or   to change the digit values and press [ENTER] to select. This example shows an ID number of 8 is set for the final TS multiplexed.

4.2.3.4 Outputs Program

The menu is used for checking the information of the services multiplexed from each input, as below：

Port number of input ASI is displayed on the left of the first row. “1/7”, as an example, indicates this is the first service from 7 ones on this ASI input, and effective bit rate on the right. Press   or    to check all the services have been multiplexed. The second row is the service name have been multiplexed.

If there is no service being multiplexed, it will display as below：

4.2.4 Mux Menu

It is used to activate the multiplexing process. When complete the selecting ASI port input programs services from different ASI inputs, and the output parameters settings, press [ENTER], to activate the multiplexing process , the LCD on the front panel will display as below：

It backs to the main menu, when the process is completed.

4.2.5 System Menu

There are 11 items in the menu，as below：

Unit Name;

IP Address;

Network Mask;

Gateway;

Remote Server IP;

MAC Address;

Factory Setting;

Serial Number;

MCU Software Version;

FPGA Software Version;

Hardware Version;

Press   or   to switch among these 11 items, and press [EXIT] to back to the previous menu.

4.2.5.1 Unit Name

It is the nicked name of the unit, an example is shown below：

Press [ENTER] to enter, then press   or   to move the cursor and press   or   to change the character values, press [ENTER] to confirm the value.

4.2.5.2 IP Address

This menu is used for the IP address setting for this DCH-3000MX, this should be an unique address on a LAN network, an example is shown as below：

Press [ENTER] to activate, and then press    or    to move the cursor and press   or   to change the digit values, then press [ENTER] to confirm.

4.2.5.3 Network Mask

This menu is used for the network mask setting for the LAN network connected, an example is shown as below：

Press [ENTER] to activate, and then press    or    to move the cursor and press   or   to change the digit values, then press [ENTER] to confirm.

4.2.5.4 Gateway

It is used for the gateway setting for the LAN network, an example is shown as below：

Press [ENTER] to activate, and then press    or    to move the cursor and press   or   to change the digit values, then press [ENTER] to confirm.

4.2.5.5 Remote Server IP

It is used for the IP address setting of a computer for network management, this IP address must be the same of the IP address of the computer connected to this DCH-3000MX for remote management, an example is shown as below：

Press [ENTER] to activate, and then press    or    to move the cursor and press   or   to change the digit values, then press [ENTER] to confirm.

4.2.5.6 MAC Address

This menu is used for checking MAC address. MAC address is factory set and every MAC address of all PBI products are unique worldwide. User is not allowed to change the value of MAC address.  This sub-menu will show its MAC, and an example is shown below：

4.2.5.7 Factory Setting

This menu is used for recovering factory default settings of this unit，as below：

Press [ENTER] to select factory setting and [EXIT] to return to the last-level menu.

Notice：When factory setting is selected, all user set parameters will be lost and will be recovered to the factory default ones.

4.2.5.8 Serial Number

This menu is used for serial number checking of this machine, and an example is shown below：

4.2.5.9 MCU Software Version

This menu is used for checking MCU version of this machine, as below：

4.2.5.10 FPGA Software Version

This menu is used for checking FPGA version of this machine, as below：

4.2.5.11 Hardware Version

This menu is used for checking hardware version of this machine, as below：

5 Installation and Initial use

User and installer must read this user manual thoroughly and carefully before installation and use.

- Using screw bolts to fix the unit on a 19 inches cabinet.

- Ground the unit on the grounding bolt on the rear panel with appropriated grounding wire to the appropriated grounding terminal(s).

- Connect all input and output connectors to their appropriated sources or destinations.

- Verify the AC electricity source available is within the acceptant range of that of the equipment. Connect the unit to the AC source with power cord originally dispatched, then turn on the power switch near the AC inlet on the rear panel.  Please unplug when the unit if not in use for a long period, e.g. 1 week.

For your security, please take attention to the below：

◎ Do not use the equipment under strong electric field, strong magnetic field and heat sources；temperature range <40℃，relative humidity<85%

◎ Do not expose the equipment to excessive dust, high humidity nor high temperature；Do not expose the external surface to petrol, thinner or other volatile substances, such as pesticides；Use soft cloth to remove dust gently.

◎ Users are not allowed to remove the top cover of the equipment.  If there is any malfunction, please check the connection of the connectors and the power cord on the rear panel. If there is no any improvement, please ask for help from your supplier or service agent.

◎ Please connect to an appropriated AC power source which meets the requirement of this unit.

◎ Both this unit and the CATV system connected should be well grounded to an appropriated earth terminal(s).

6 Accessories

The following items are dispatched originally with the equipment as the accessory parts:

a Power cord (might differs from countries),

a ASI cable,

an User manual,

a CD (includes the remote network management software and electronic file of the user manual) ,

a Quality warrantee card .

# Text boxes

DVB-ASI

Simulate AV

DCH-3000EC

DVB MPEG2 Encoder

Bit Rate

038000Kbps

Inputs Setup

ASI 1 016464/019860Kbps

ASI 1    *  1/4

CCTV-4

Serial Number

12345678

TS8

Power Disconnect

Disconnect the power cord under the following conditions：

1.damage on cord and connector

2.equipment get wet or substantial moisture enter the chassis

3. Exposure to rain or water

4. equipment dropped or damaged

5.Apparent irregularity appears

Caution

1.Do not place this equipment on unstable support.

2.Do not place objects on top of the equipment to block up the ventilation opening.

3.Do not place radioactive instrument or object on top of adjacent to the equipment.

4.Provide proper room ventilation during operation of this equipment.

5.Verify with the repair engineer or authorized entity after repair is done to be sure the equipment can be put back to operation.

6.Read the operating manual prior to usage.

！

No Touching with

Bare Hands

Do not touch the equipment during heavy lightening condition.

No Heavy Stacking

Do not stack the equipment back to back to allow proper ventilation。

Avoid Moisture

Do not use this equipment in high moisture environment

Electrical Shock

Thoroughly check your electrical grounding and connectors prior to powering. Make sure all connectors are of the three-prong type to ensure proper grounding.

Whenever the equipment is not used for a prolong period of time, you should disconnect the power cord.

Don’t Open The

Equipment

1. Do not try to repair by yourself.

2. Do not use unauthorized part for repair.

3. Do not open the covers of the equipment without proper factory authorization.

Simulate AV

Factory Setting

ENTER=YES EXIT=NO

Encrypted

satellite signal

DCH-3000EC

DVB MPEG2 Encoder

DCH-3000P-30S

QPSK satellite digital CI modulator

DCH-3000P-30S

QPSK satellite digital CI modulator

DCH-3000TM

QAM modulator

Packet Size

188 Byte

TS7

CATV

Network

Inputs Setup

ASI 8 037171/043302Kbps

Transport Stream ID

00008

Outputs Setup

Packet Size           (

Unit Name

DCH-3000MX

MCU Software Version

00.03.15

MCU Software Version

00.03.15

TS1

TS2

Main Menu

Outputs Setup (

……

DCH-3000MX TS Re-multiplexer

Serial Number

12345678

Gateway

010.010.030.001

ASI1 1/7 34267 Kbps

CCTV-1

HNSTV-1

Factory Setting

ENTER=YES EXIT=NO

MAC Address

00:20:aa:21:01:05

■■■■■■■■■■■■

FPGA Software Version

Version : 12

Hardware Version

01.00

ASI 1   1/7    34267Kbps

CCTV-1

Remote Server IP

010.010.030.023

……

ASI 1     *      1/4

CCTV-4

ASI 1

No Program List

Network Mask

255.255.255.000

DCH-3000MX IP:010.010.030.058

Main Menu

System    (

Network Mask

255.255.255.000

Outputs Setup

Transport Stream ID   (

Outputs Setup

Outputs Program       (

Inputs Setup

ASI 1 016464/019860Kbps

MAC Address

00:20:aa:21:01:05

DCH-3000MX

Outputs 42125Kbps Overflow

Remote Server IP

010.010.030.023

Main Menu

Mux       (

DCH-3000MX SN:12345678

IP:010.010.030.058

Main Menu

Inputs Setup (

Packet Size

188 Byte

Bit Rate

038000Kbps

Start to Mux

please wait…

Gateway

010.010.030.001

IP Address

010.010.030.058

Unit Name

DCH-3000MX

Outputs Setup

No Program

Confirm Changed ?

ENTER=YES  EXIT=NO

Main Menu

Inputs Setup            (

Transport Stream ID

00008

Notice：Avoid strong magnetic and electric field

Notice: Corrosive

×

Notice：Please don’t open 		the chassis !

×

Notice：~220V	±10% 50Hz±10%

Notice：well grounding

Tel： +86 (0) 10-62475893     Fax：+86 (0) 10-62473278

Network control

LAN

Beijing Jaeger Communication Electronics & Technology Co., Ltd.

http://www.pbi-china.com

ASI 8       1/22

Service ID : fffe

IP Address

010.010.030.058

FPGA Software Version

Version : 12

Hardware Version

01.00

Outputs Setup

Bit Rate             (