DCP-3000

Digital Contents Processing Platform

Operation Guide

Version 1.1

About this Guide

Thank you for purchasing the digital TV headend equipment from PBI. This operation guide is intended for technical personnel who use Digital Contents Processing Platform, DCP-3000, It describes the operation of the equipment. In the following table, we provide the document release history.

Revision History

| Version | Date | Document Change |
| --- | --- | --- |
| 1.0 | 2017.05 | Initial Version |
| 1.1 | 2017.10 | Add P01MS and improve others based on new FW |

Contact Us

Address:	 No.3, Fengzhi East Road, Xibei Wang Town, Haidian District, Beijing, China, 100094

Telephone:	+86-10-5870 2000

Fax:		+86-10-5870 2016

E-mail:     sales@pbicn.com  sales@dh-tv.com

Website:   dtv.pbicn.com  www.dh-tv.com

WARRANTY AND SERVICE

PBI warrants to the Purchaser that the Products and any Repaired Products (Repairs) will be free from defects in material and workmanship for a period of one years from the date of shipment to the Purchaser.

The obligation of PBI under this warranty is limited to replacing or repairing, at PBI's option, Products or Repairs found by PBI to be defective within the warranty period. All such replacements and repairs shall be performed at facilities designated by PBI and shall be performed only after the customer has received a Return Material Authorization (RMA) number from PBI and has returned the Product to PBI, shipping and insurance prepaid by Purchaser.

The returned Product must be accompanied by the customer's name, address and telephone

number, the model and serial number of the Product, a statement of the purchase date and a detailed description of the problem. Products and Repairs returned by Purchaser shall be repaired by PBI using new or refurbished parts and shall be returned to Purchaser by PBI, shipping prepaid by PBI.

This warranty shall immediately become null and void if, in PBI's sole judgment, the Product has been subject to unauthorized modification, misuse, neglect, accident, improper installation or application, alteration or neglect in use, storage, transportation or handling, or if the serial number and/or other Product markings have been removed, defaced or altered.

PBI may, at its discretion, perform out-of-warranty repairs at PBI facilities in exchange of customary charges, or offer a written agreement extending the terms of this warranty at a price stated in such agreement. All repairs performed out of warranty or pursuant to an extended warranty agreement shall be subject to all of the applicable limitations and procedures of this Agreement.

The above warranties are in lieu of all other warranties, expressed, implied, or statutory or arising by custom of trade usage, including any warranty of merchantability of fitness for any unique, special or express purpose, and of all other obligations of liabilities whether in contract, tort or otherwise including, without limitation, liability for damages (whether general or special, direct or indirect, consequential, incidental, exemplary) or any claim for the loss of profits or business or for damage to goodwill.

EXTENDED WARRANTY OPTIONS

Please contact Customer Service or your reseller for information on optional extended warranties.

CUSTOMER SERVICE

Support functions provided by PBI's Customer Service include complete factory repair for both in-warranty and out-of-warranty equipment. You can contact your local PBI product distributor or reseller. Or you can call us or write to us for Customer Support.

A Customer Service engineer will answer warranty-related questions, discuss your specific equipment problems, and when necessary, give you shipping instructions for returning equipment to PBI for repair.

To return a Product for service or repair, you must obtain a RMA number from PBI's Customer Service.

The following information is required:

Customer name, address, telephone number

Model number

Serial number

Detailed description of problem

All customer-returned units must be shipped to PBI freight prepaid, in the original carton or equivalent. PBI is not responsible for damage in transit. All repairs will require return of the entire equipment to PBI. No individual modules will be accepted for repair under this contract.

Table of Contents

1. SAFETY PROTECTION	1

2. INTRODUCTION	2

2.1. Appearance	2

2.1.1. LED Indicators	2

2.1.2. LCD	3

2.1.3. Key pad	3

2.1.4. USB	3

2.1.5. RJ45	3

2.1.6. SFP	3

2.1.7. Mini USB	3

2.2. Function Cards Introduction	4

2.2.1. P01MS（reMUX & Scrambler Extension Module）	4

2.2.2. D01S2（4 x DVB-S/S2 Demodulator Module）	4

2.2.3. D02S2（4 x DVB-S/S2 Demodulator Module, Support Input Stream Indentifier）	4

2.2.4. D01T2（4 x DVB-C/T/T2 Demodulator Module）	5

2.2.5. P01CI（4 x CI De-encryption Module）	5

2.2.6. C01MOD（8 x QAM/2 x COFDM Modulator Module）	5

2.2.7. C01TM（4 x COFDM Modulator Module）	6

2.2.8. C01ASI（5 x ASI Input/Output Module）	6

2.2.9. P01DA（2 x DS3 Input/2 x DS3 Output/1 x ASI Adaptor Module）	7

2.2.10. D01PA（2 x Channels Multi-format Signal SD/HD Decoder Module）	7

2.2.11. D02PA（2 x Channels Multi-format Signal SD/HD Decoder Module）	7

2.2.12. P01EC（4 x HDMI MPEG-2/H.264 Transcoder/Encoder Module）	8

2.2.13. P02EC（4 x SDI MPEG-2/H.264 Transcoder/Encoder Module）	8

2.2.14. P01AT（4 x H.265/AVS+/MPEG-2/H.264 HD/SD Transcoder Module）	9

3. LCD MENU	10

3.1. Main Menu	12

3.2. Network	13

3.3. Misc	13

3.4. System	15

4. WEB INTERFACE	16

4.1. Status	16

4.1.1. System Status	16

4.1.2. TS/IP-In Status	16

4.1.3. TS/IP-Out Status	17

4.2. Modules	17

4.2.1. P01MS（reMUX & Scrambler Extenson Module）	18

4.2.2. D01S2（4 x DVB-S/S2 Demodulator Module）	18

4.2.3. D02S2（4 x DVB-S/S2 Demodulator Module, Support Input Stream Indentifier）	20

4.2.4. D01T2（4 x DVB-C/T/T2 Demodulator Module）	20

4.2.5. P01CI（4 x CI De-encryption Module）	23

4.2.6. C01QAM（8 x QAM Modulator Module）	25

4.2.7. C01MOD（8 x QAM/4 x COFDM Modulator Module）	30

4.2.8. C01ASI（5 x ASI Input/Output Module）	31

4.2.9. P01DA（2 x DS3 Input/2 x DS3 Output/1 x ASI Adaptor Module）	34

4.2.10. D01PA（2 x Channels Multi-format Signal SD/HD Decoder Module）	34

4.2.11. P01EC（4 x HDMI MPEG-2/H.264 Transcoder/Encoder Module）	38

4.3. TS over IP	44

4.4. System	47

4.5. Remux	49

# SAFETY PROTECTION

This User Guide is written for operators/users of the DCP-3000 to assist in installation and operation. Please read this User Guide carefully before installation and use of the device.

This equipment is provided with a protective earth grounding incorporated in the power cord. The main plug shall only be inserted in a socket outlet provided with a protective earth contact. Any interruption of the protective conductor, inside or outside the device, is likely to make the device dangerous. Do not remove the covers of this equipment. Hazardous voltages are present within this equipment and may be exposed if the covers are removed. Only trained and approved service engineers are permitted to service this equipment.

The supplied AC power cable must be used to power the device. If the power cord becomes damaged, it must be replaced. No operator serviceable parts inside. For the correct and safe use of the device, it is essential that both operating and servicing personnel follow generally accepted safety procedures in addition to the safety precautions specified in this manual. Whenever it is likely that safety protection is impaired, the device must be made in-operative and secured against unintended operation. The appropriate servicing authority must be informed. For example, safety is likely to be impaired if the device fails to perform the intended measurements or shows visible damage.

WARNINGS

- The mounting environment should be relatively dust free, free of excessive vibration and the ambient temperature between 10C° to 30C°. Relative humidity of 20% to 80% (non-condensed) is recommended.

- Avoid direct contact with water.

- Never place the equipment in direct sunlight.

- The outside of the equipment may be cleaned using a lightly dampened cloth. Do not use any cleaning liquids containing alcohol, methylated spirit or ammonia etc.

- For continued protection against fire hazard, replace line fused only with same type.

- Air intake for cooling is achieved via holes at the side of the device and the fans inside. The air flow should not be obstructed. Therefore, the device has to be placed on a flat surface, leaving some space at the sides of the device.

When in operation, the ambient temperature should not exceed the limit of 45C°.

# INTRODUCTION

## Appearance

DCP-3000 appearance is shown as Fig.2-1 DCP-3000 Appearance.

Fig.2-1 DCP-3000 Appearance

### LED Indicators

There are 11 LED indicators on DCP-3000 front panel which refer to Fig.2-2, including,

- Power

- Warning

- Alarm

- Module 1-6 Status

- User-defined A/B (not available in this version, and LED A is defined for P01MS)

Fig.2-2 LED Indicators

Connect to the power supply, the LED indicator of Power keep lighting. The LED indicator of Waring and Alarm will not be lighted when the device starts and operators normally. These two indicators will turn orange or red when the device operators abnormally, which prompts the user that an error has occurred.Operating indicators of Module 1-6 are used to indicate the operating status of slot 1 to 6 respectively, and the indicator of Warning and Alarm is used to indicate the device status.

### LCD

LCD is mainly for showing unit’s IP address for management. There are also some simple menus for main frame configurations. And user can make the daughter board reboot via LCD menu. For more details, please refer LCD menu.

### Key pad

There are six keys on front panel, UP, Down, Left, Right, Enter and Exit. User can check and setup LCD Menu with them.

### USB

USB is just for firmware update. USB is one of DCP-3000 three (USB, Telnet and Web) different types of firmware update methods. User need to put firmware into USB key root folder, update it through upgrade menu of LCD.

### RJ45

There are two RJ45 ports, CA and Control. CA is for scrambler connecting CA server. Control is the management port of DCP-3000.

### SFP

There are two SFP ports for TS over IP. They can work as backup or independent.

### Mini USB

Mini USB is for debugging problem. They are USB to RS232 port actually. Before using this function, user need to install a RS232, for example Putty.exe, to enable this function.

## Function Cards Introduction

### P01MS（reMUX & Scrambler Extension Subboard）

- 32 independent DVB-TS re-Multiplex and Scramblers

- Compliant with ISO13818 & EN300 468

- MPEG/H.264 TS re-Multiplexing & Scrambling

- Support 4 different local or remote CAS Simulcrypt processing

- Support DVB CAS & BISS 1/E

- Support error alarm of TS level

- Support PID filtering, pass through and remapping

- Support PSI/SI tables insertion or re-generation

- Support PCR re-stamp & calibrate

- Self temperature monitoring

### D01S2（4 x DVB-S/S2 Demodulator Module）

- 4 x F type Female, 75Ω

- Input Frequency Range: 950 ~ 2150 MHz

- Input RF level: -65dBm ~ -25dBm

- Symbol Rate: 2 ~ 45MSps

- Roll Off factor: 0.35(DVB-S QPSK), 0.35/0.25/0.2(DVB-S2 8PSK)

- FEC Puncture Rate: 2/3, 3/4, 3/5, 5/6, 8/9, 9/10(DVB-S2 8PSK), 1/2, 2/3, 3/4, 5/6, 6/7, 7/8(DVB-S QPSK)

- Support BISS-1/E de-encryption(up to 40 PIDs de-encryption per tuner input)

- Support T2-MI(up to 8 PLP IDs demodulation per tuner input)

### D02S2（4 x DVB-S/S2 Demodulator Module, Support Input Stream Indentifier）

- 4 x F type Female, 75Ω

- Input Frequency Range: 950 ~ 2150 MHz

- Input RF level: -65dBm ~ -25dBm

- Symbol Rate: 2 ~ 45MSps

- Roll Off factor: 0.35(DVB-S QPSK), 0.35/0.25/0.2(DVB-S2 8PSK)

- FEC Puncture Rate: 2/3, 3/4, 3/5, 5/6, 8/9, 9/10(DVB-S2 8PSK), 1/2, 2/3, 3/4, 5/6, 6/7, 7/8(DVB-S QPSK)

- Support BISS-1/E de-encryption(up to 40 PIDs de-encryption per tuner input)

- Support T2-MI(up to 8 PLP IDs demodulation per tuner input)

- Support PLS (0 ~ 262141)

- ISI ID: 1 ~ 255 user configurable

### D01T2（4 x DVB-C/T/T2 Demodulator Module）

- 4 x F type Female, 75Ω

- Full compliant for DVB-T2 v1.3

- Input Frequency, 48 ~ 860 MHz(DVB-C), 104 ~ 862 MHz(DVB-T/T2)

- Input Level, -15~ 15dBm(DVB-C), -70 ~ -20dBm(QEF, DVB-T/T2)

- Symbol Rate, 1 ~ 7MSps（ITU J.83 Annex A DVB-C）

- Constellation, 16/32/64/128/256 QAM(DVB-C), QPSK/16QAM/64QAM(DVB-T), QPSK/

16QAM/64QAM/256QAM(DVB-T2)

- Bandwidth, 6/7/8 MHz

- FFT Mode, 2K/8K(DVB-T), 1K/2K/4K/8K/16K/32K(DVB-T2)

- Guard Interval, 1/4, 1/8, 1/16, 1/32(DVB-T)  1/4, 5/32, 1/8, 5/64, 1/16, 1/32, 1/64, 1/128(DVB-T2)

- FEC Code Rate, 1/2, 2/3, 3/4, 5/6, 7/8(DVB-T)   1/2, 3/5, 2/3, 3/4, 4/5, 5/6(DVB-T2)

### P01CI（4 x CI De-encryption Module）

- 4 x Independent Common Interface(DVB-CI)slots

- Multiple programs CAS or BISS-1/E De-encryption

- CAM watchdog

- Compatible with most of popular CA systems

### C01MOD（8 x QAM/2 x COFDM Modulator Module）

- 2 x F type Female, 75Ω（1 x main output，1 x -20dB monitor output）

- Support QAM/COFDM Modulation Mode(cannot work at the same time)

- 2 groups of 4 adjacent channel carriers QAM RF output, 2 x Un-adjacent channel carries COFDM RF output

- RF output range: 48 ~ 996MHz, step by 1KHz

- Symbol rate: 2.5 ~ 6.99MBauds

- RF total output level: 94 ~ 120dBuV(111dBuV each carrier)

- FFT Mode, 2K/4K/8K

- Spurious rejection > 55dB

- Output return loss -10dB

- QAM Modulation, support ITU-T J.83 Annex A, C

- Modulation Mode, 16QAM, 32QAM, 64QAM，128QAM，256QAM

- MER > 36dB, BER < 10E-9

### C01TM（4 x COFDM Modulator Module）

- 2 x F type Female, 75Ω（1 x main output，1 x -20dB monitor output）

- 4 x Un-adjacent channel carries COFDM RF output

- RF output range: 100 ~ 862MHz, step by 10KHz

- RF total output level: 84 ~ 114dBuV

- Modulation Mode, QPSK/16QAM/64QAM

- FFT Mode, 2K/4K/8K

- Spurious rejection > 55dB

- Output return loss -10dB

- MER > 36dB, BER < 10E-9

### C01ASI（5 x ASI Input/Output Module）

- 5 x BNC Female, 75Ω

- Standard: DVB-ASI, EN50083-9

- Up to 5 x ASI Input

- Up to 5 x ASI Output

- Maximum bit rate(each ASI): 213Mbps

- Minimum accepting sensitivity: 200mV

- Maximum input Voltage: 880mV

- ASI Input or Output can be switched

- Support T2-MI (In the T2-MI mode,  ASI-5 is configured to input which can process 4 PLP ID, ASI-1 to ASI-4 are configured to output which can select PLP ID TS to output via Web)

### P01DA（2 x DS3 Input/2 x DS3 Output/1 x ASI Adaptor Module）

- 5 x BNC Female, 75Ω

- Standard: DVB-ASI, EN50083-9 / ITU-T G.703

- Frame Structure: ITU-T G.752 / ITU-T G.804

- ASI Input or Output can be switched

- Bit rate: 44.736Mbps

### D01PA（2 x Channels Multi-format Signal SD/HD Decoder Module）

- 2 x HDMI 1.3(up to 1080i), 1 x D-sub 15 female(can be translated 2 x CVBS via cable)

- Video Format: MPEG-2(MP@ML for SD, MP@HL for HD), MPEG-4/H.264 AVC Part 10(MP@L3 for SD,HP@L4.1 for HD), AVS+

- Audio Format: MPEG-1 Layer II, AAC-LC, HE AAC V1/V2, AC3, AC3+

- Aspect Ratio: 16:9, 4:3 Self-adaptation

- Resolution and Frame Rate: 1080ix30, 1080ix29.97, 1080ix25, 720px60, 720px59.94, 720px50, 576ix25, 480ix29.97

- Video PID Bit Rate: < = 50Mbps

### D02PA（2 x Channels Multi-format Signal SD/HD Decoder Module）

- 3 x BNC Female 75Ω for 2 x ASI/SDI , 1 x Genlock input

- BNC for SDI Output or ASI Input/Output can be switched

- 1 x D-sub 15 female(can be translated 2 x CVBS via cable)

- Video Format: MPEG-2(MP@ML for SD, MP@HL for HD), MPEG-4/H.264 AVC Part 10(MP@L3 for SD,HP@L4.1 for HD), AVS+

- Audio Format: MPEG-1 Layer II, AAC-LC, HE AAC V1/V2, AC3, AC3+

- Aspect Ratio: 16:9, 4:3 Self-adaptation

- Resolution and Frame Rate: 1080ix30, 1080ix29.97, 1080ix25, 720px60, 720px59.94, 720px50, 576ix25, 480ix29.97

- Video PID Bit Rate: < = 50Mbps

### P01EC（4 x HDMI MPEG-2/H.264 Transcoder/Encoder Module）

- 4 x HDMI Input interface

- Compliant with H.264/AVC Baseline, Main & High Profile @ L4.0 or less & MPEG-2 MP@ML

- Independent Transcoding/Encoding mode control

- Video Input Resolution: 1080i, 720p, 576i, 480i.

- Support video resoultion downscaling(vertical & horizontal adjustable respectively).

- Audio Coding: MPEG-1 Layer II, MPEG-2/4, AAC-LC/HE-AAC

- Support VBR & CBR mode

- Support GOP settings

- Sampling Format: 4:2:0, 10-bit, YCbCr

- Compression Bit Rate: 300K ~ 20Mbps

- Aspect Ratio: 4:3, 16:9

### P02EC（4 x SDI MPEG-2/H.264 Transcoder/Encoder Module）

- 4 x SDI Input, BNC Female 75Ω

- Compliant with H.264/AVC Baseline, Main & High Profile @ L4.0 or less & MPEG-2 MP@ML

- Independent Transcoding/Encoding mode control

- Video Input Resolution: 1080i, 720p, 576i, 480i.

- Support video resoultion downscaling(vertical & horizontal adjustable respectively).

- Audio Coding: MPEG-1 Layer II, MPEG-2/4, AAC-LC/HE-AAC

- Support VBR & CBR mode

- Support GOP settings

- Sampling Format: 4:2:0, 10-bit, YCbCr

- Compression Bit Rate: 300K ~ 20Mbps

- Aspect Ratio: 4:3, 16:9

- Support second audio encoding with the extension encoding card (P02EC-OB)

- Up to 8 x transcoder with the extension card (P02EC-OB)

### P01AT（4 x H.265/AVS+/MPEG-2/H.264 HD/SD Transcoder Module）

- Support H.265/AVS+ HD/SD transcode to H.264 HD/SD or MPEG2 SD, and MEPG2 HD/SD transcode to H.264 HD/SD, and H.264 HD/SD transcode to MPEG2 SD

- Support AC/AC3+ transcode to MPEG/AAC, or passthrough(cannot work in the same time)

- Compliant with H.264/AVC Baseline, Main & High Profile @ L4.0 or less & MPEG-2 MP@ML

- Support video resoultion downscaling(vertical & horizontal adjustable respectively).

- Audio Format: MPEG-1 Layer II, MPEG-2/4, AAC-LC/HE-AAC

- Support VBR & CBR mode

- Support GOP settings

- Sampling Format: 4:2:0, 10-bit, YCbCr

- Compression Bit Rate: 300K ~ 20Mbps

- Aspect Ratio: 4:3, 16:9

# LCD MENU

There is a LCD Menu for users to configure main frame and front interfaces. User can press enter key to start to setup the unit. The LCD menu overview showed as below:

## Main Menu

The LCD will show DCP-3000 and management IP address when it boot up. User can press any key of front panel to enter Main menu. Main menu includes 3 submenus, Network, Misc and System.

## Network

Network menu includes IP address, Subnet Mask, Gateway, MAC Address and Web GUI Login for management RJ45 port. User can see the below graph as reference. MAC address is read only. Web GUI Login is for setup or reset web browser login ID and password, especially users forgot the ID or password.

## Misc

This menu includes several unit’s status, Date, Time, Temperature, Fan status, Power supply, Error Operate and Device label. User can setup Date and Time to display via front panel. Temperature is unit inside temperature. Fan status will show error if any fan does not work. Power supply is the dual power supply’s status. It will show error information when the power supply doesn’t work. Error Operate is to reset warned errors. Device label is for setting up unit names which will show on LED and Web browser.

## System

System menu includes these sub-menus, S/N, Version, Reset Module, Switch USB-RS, Factory Settings and Machine Settings. S/N is the identification of the unit and it is an unique series number for each unit. It helps to verify if the unit comes original or not. Version is the information of firmware of the main frame. Reset Module is the function for reset daughter cards. Switches USB-RS is for setting up debug information output port. Factory Settings is for reset all settings to factory default. Machine Settings is limited for users.

# WEB INTERFACE

Web browser is the main management interface of DCP-3000. User can check the unit working status, setup and reset it etc. The suggestion browsers are Firefox and Chrome.

## Status

### System Status

This is the page for main frame working status. It includes hardware working temperature, fans speed, power supply status. If power status shows faulty, it means that the power is crashed or not installed.

### TS/IP-In Status

This is the page of TS over IP Input status. It includes port, source IP, protocol, target IP, port number, lock status, bit rate, packet length, IP frame and enable status.

### TS/IP-Out Status

This is the page of TS over IP Output status. It includes port, protocol, target IP, port number, mode, program and enable status.

## Modules

### P01MS（reMUX & Scrambler Extenson Subboard）

The P01MS is a 32 independent channels DVB-TS re-multiplex and Scrambler subboard which can support 32 scrambling transport streams to the TS/IP or other modules to output. There is no hardware input/output interface. It only can be installed on the main board in the chassis. It can support up to four different Simulcrypt scramble or BISS 1/E scramble by using the DVB common scrambling algorithm and built-in CW generator.

#### 4.2.1.1. Source and Services Settings

4.2.1.2. Services Re-Multiplex

4.2.1.3. Services Scramble

P01MS supports TS scrambling including BISS-1, BISS-E and 4 different Simulcrypt modes.User can scramble the re-multiplexed TS by following the operations below.

- BISS-1

On MUX page, click the button ‘Scrambler’ to open a submenu, user can set the option ‘Scrambling Mode’ to ‘BISS-1’ on the top of the submenu, click the button ‘SW Input’ to configure the Hex key, then selecting programs by hooking in the small box, as it shown in figure below. These selected programs will be scrambled, user can also choose only to scramble audio signal or video signal. After all parameters get ready, click the button ‘Apply’ to submit the configuration.

- BISS-E

On MUX page, click the button ‘Scrambler’ to open a submenu, user can set the option ‘Scrambling Mode’ to ‘BISS-E’ on the top of the submenu, click the button ‘SW Input’ to configure the Hex key and Hex ESW, then selecting programs by hooking in the small box, as it shown in figure below. These selected programs will be scrambled, user can also choose only to scramble audio signal or video signal. After all parameters get ready, click the button ‘Apply’ to submit the configuration.

- Simulcrypt

Step 1:

On MUX page, click the button ‘Scrambler’ to open a submenu, user can set the option ‘Scrambling Mode’ to ‘Simulcrypt’ on the top of the submenu. User can choose 4 different simulcrypt system by click buttons ‘Simulcrypt Channel 1/2/3/4’. hook the box ‘Enable’ to enable simulcrypt function, then user can configure parameters of ECM and EMM, as it shown in figure below. User has to configure these parameters according to different simulcrypt systems.

| Menu Name | Description |
| --- | --- |
| ECMG IP | The IP address of simulcrypt server for receiving ECM information. |
| ECMG PORT | The port number of simulcrypt sever for receiving ECM information. |
| Super CAS ID(HEX) | A examination key for exchanging ECM information between the module and the sever. |
| Channel ID | The sequence number of simulcrypt channel. |
| ignore | Some simulcrypt system doesn’t need EMMG function, user can close EMMG by hooking in the small box. |
| EMMG IP | The IP address of simulcrypt server for receiving EMM information. |
| Mode | The EMM package mode, user can select between TCP and UDP. |
| TCP Port | The port number of TCP package. |
| UDP Port | The port number of UDP package. |
| EMM PID(0x100~0x1fff) | The PID number of EMM. |

Step 2:

Following step 1, user has to click the button ‘AC List’ to configure AC data for each program, as it shown in figure below. ‘AC Index’ is the program sequence, ‘AC Data(hex)’ is the hex key of each program. The total quantity of AC list is based on the total quantity of programs which user wants to be scrambled. Click the button ‘Apply’ to submit your configuration.

Step 3:

After setup2, on left column, user can click program’s service name, and assign AC index number for each program. Then user can hook in the small box to select video PID and audio PID, as it shown in figure below, these hooked audio and video signals will be scrambled.

Step 4:

After setting all configuration ready, click ‘Apply’ to submit, as it shown in figure below. Wait for a while, the two gray lights on this page will turn to green if scrambling successful.

### D01S2（4 x DVB-S/S2 Demodulator Module）

The D01S2 is a 4 independent channels DVB-S/S2 demodulator module, users can setup them separately. And this card supports both BISS-1 and BISS-E decryption function too. There are 8 preset BISS keys for each transport stream.

Tuner Status

Tuner configure

| Menu Name | Description |
| --- | --- |
| LNB LO Frequency | To configure the local oscillator frequency according to the right satellite, its range is from 1000 to 26,500MHz. |
| Satellite Frequency | To configure the satellite down link frequency according to the right satellite, its range is from 1000 to 26,500MHz. |
| Symbol Rate | To configure the symbol rate of QPSK signal, its range is from 1000 to 45,000KBaud. |
| LNB Voltage | To select the correct LNB voltage output from the F-connector, user can choose between Off, 13V and 18V. |
| LNB 22KHz | To activate the LNB 22KHz control signal to the LNB, user can select between On and Off. |
| DiSEqC | To configure the DiSEqC control, user can select Port A, Port B, Port C, Port D or DiSEqC OFF. |
| PLS Gold Code | To configure the PLS gold code, its range is from 0 to 262,141. |

BISS configure

| Menu Name | Description |
| --- | --- |
| BISS1-4 | 1 to 1 (BISS1 to Tuner1 ) BISS setup menu |
| BISS Mode | To setup the BISS mode, user can choose between Mode-1 and Mode-E. |
| ID and Key | Input Key in BISS-1 mode and input ID and Key in BISS-E mode. |
| Program List | To configure the programs should be decrypted. |

### D02S2（4 x DVB-S/S2 Demodulator Module, Support Input Stream Indentifier）

Please refer 4.2.2.

### D01T2（4 x DVB-C/T/T2 Demodulator Module）

The D01T2 is a 4 independent channels DVB-T2/T/C demodulator module, it supports 3 different demodulation modes, DVB-T2, DVB-T and DVB-C. User can select the requirement modes. For setup as below:

Status

The default demodulation mode is DVB-T2, as below figure.

Default demodulation mode

Demodulation mode

Default demodulation bandwidth

| Menu Name | Description |
| --- | --- |
| Signal Type | Demodulation mode option |
| Frequency | Receiving signal frequency option |
| Bandwidth | Bandwidth option |
| Multi PLP ID | PLP option (Just for stream which includes PLP ID) |

### P01CI（4 x CI De-encryption Module）

The P01CI is a card for installing CAMs to decrypt scrambled services. It supports up to 4 CAM slots(2 inside, 2 outside). On the configure page, user will see total bitrate and valid bitrate which the slot using, CAM name which installed, transport stream source option and program list etc.

Default status

| Menu Name | Description |
| --- | --- |
| TS IN/TS OUT | Transport stream which input and output the CI slot |
| Slot | CAM name or No Module which mean CAM not installed or recognized |
| Source | Transport stream used for CI slot, it will show which module and source are available |
| Program | Program list from the selected transport stream |

Below is an example for CI setup:

Step1: select one available module or M/B (Main board)

Step2: select the transport stream which will be used for CI slot;

Step3: Select services which need to decrypting and click apply.

### C01QAM（8 x QAM Modulator Module）

The C01QAM is a 8 channels, 2 groups 4 adjacent frequencies, QAM modulator. Each channel has switch for enable or disable the RF output. And each channel also can be configured with independent transport stream. Status page will show each channels working status. The spot red means channel is off or not working, green means working fine.

Modulators Status

Default source options

Below is the procedure for setup modulator:

Step1: select module or M/B which will be used for modulator

Step2: select the specific transport stream for modulator

Step3: setup RF Level for output:

Step4: to setup modulation/RF switch as ON

Step4: to setup constellation

Step5: to setup I/Q Inversion

Step6: to setup band width:

Step7: to enter Frequency and Symbol rate, this just for Modulator-1 and Modulator-5, the reset will increased following up according to bandwidth.

Step8: to setup NIT filter, it will pass NIT if the option is enable, Disable will not pass through NIT. NIT PID is for customer defined PID which instead NIT pass through.

Step9: after all setups, need to click Apply to save and enable all of them.

### C01MOD（8 x QAM/4 x COFDM Modulator Module）

Under development!!!

### C01ASI（5 x ASI Input/Output Module）

This is a 5 BNC for ASI input and output software option card. User can define the input and output via Web interface configuration. And there is additional option for demodulating T2MI.

This Status page will show bitrate input or output from each of 5 BNC.

Status

This Source page just for ASI output option. If the BNC configured as input, there is no option on this page. When the BNC configured as Output, user will see options as below. User needs to select card module as picture or M/B first ASI output-1, and then select stream from the shown source as picture ASI output-2.

ASI output-1

ASI output-2

The ASI page is for configure BNC, input or output. There are two options for each BNC, ASI In or ASI Out.

BNC configure

For special using, user can set this card mode as T2MI mode, as picture showed below. After setup as T2MI mode, BNC 5 will fixed as ASI input for T2MI function.

Mode option

T2MI page will show up when the card set as T2MI mode. It will support demodulate 4 PLPs at same time. As below, user will see PLP ID List on left. There will be PLP IDs if the input stream included.

T2MI configure

### P01DA（2 x DS3 Input/2 x DS3 Output/1 x ASI Adaptor Module）

Under development!!!

### D01PA（2 x Channels Multi-format Signal SD/HD Decoder Module）

This the decoder card is two channels decoders with HDMI and CVBS interfaces. User can select stream from source menu and to configure the decoding on Decoder menu. Status page will show current decoding services status.

Decoder Status

Below is the procedure for setup Decoder:

Step1: select module or M/B which will be used for decoder and select stream from the selected module or M/B;

Decoder source-1

Step2: select which service will be used for decoding, user will see output from HDMI or CVBS after this step.Please refer Status page if there is no output. The possible issue could be the service is encrypted.

Decoder

Step3: user can adjust out video resolution if user want to see the particular resolution.

Resolution configure

Step4: user can adjust out Aspect Ratio too if user want to see the particular aspect ratio.

Aspect Ratio

Step5: user can use default setting under most situation, and configure it as required.

CVBS PAL

Step6: Audio mode include Auto, Stereo, Mono, Left and right. User can configure it as required.

### P01EC（4 x HDMI MPEG-2/H.264 Transcoder/Encoder Module）

This the HDMI encoder card of DCP-3000. It supports 4 channels HDMI encoder, and it can be used as a transcoder too. The 4 encoders are independent hardware, the options for each encoder will not effect others. Specially, there is a simple remux core on the card, user can use the remux to manage the streams after encoding or transcoding.

Encoder Status

Quick setup example:

Step1: select on encoder page from encoder 1 to 4.

Step2: configure the card operation mode, H264 or MPEG2 encoding or MPEG2 To H264 transcoding.  Encoder Bit Rate is for encoding output bit rate, Video + Audio + Null packets.

Step3: user can select Video Rate control from CBR and VBR.

Step4: user can setup video bit rate, video max bit rate and video min bit rate. The difference between Max and Min is the range for video encoding or transcoding. Aspect Ratio will be 16:9 or 4:3.

Step5: GOP size option will be enabled while the GOP Adaptive option is OFF. GOP Structure will IBBP, IPPP, IBP and IBBBP four options.

Step6: The Output Horizontal and Vertical can be enabled when the Output video format is Manual Settings. If it is Auto Settings, video output format will be same as input. The Input Format adaptive is for recognize input video format automatically. The Input video format menu will be disabled if it is ON. And, there will be one more option if the module card Operation Mode is encoding(option: h264 and MPEG2). It is Low delay mode. The delay could be less than 100ms if it is on.

Step7: There are four options of Audio Settings, such as Audio Channel Mode, Audio Format, Audio Bit rate and Audio level.

Audio Channel Mode: Stereo and Mono.

Audio Format: set the audio compression format MPEG-1 Layer II, MPEG-2 AAC LC, MPEG-4 AAC LC, MPEG-2 AAC HE-V1, MPEG-4 AAC HE-V1, MPEG-2 AAC HE-V2, MPEG-4 AAC HE-V2

Audio Bit Rate: Set the audio bitrate, available options: 64k bps /96k bps /112k bps /128k bps /160k bps /192k bps /224k bps /256k bps /320k bps /384k bps

Audio Level: Set the gain of output volume from -7dB to +12dB.

Step7: Advanced Settings is for PSI/SI setup option. User can configure them as required. Null Packets Filter will decide the encoding output stream with null packets or not.

Transcoding function setup is a little different with encoding. User needs to select streams for transcoding first on the page Source/Enc Mux.

After setup source, user needs to select service and audio on the Trans/Encoder page. The program source could be select from each of four transcoder sources. The rest options please refer to Encoder options process.

## TS over IP

There are two TS over IP ports on the main chassis. These two ports are duplex mode, can be used as input and output at same time.

TS over IP input:

Before users to setup the IP input channels, they need to Click Add button to add channels for configuring. It is similar when they use Quick setup. They need to add same or more channels as Quantity numbers before apply quick setup.

| Menu Name | Options |
| --- | --- |
| Redundancy | TS/IP port 1 and port 2 backup option |
| Interval | Web refresh interval |
| IGMP | IGMP option |
| Based on index | Quick setup start up index |
| Quantity | Numbers to setup by quick setup option |
| Increase | Quick setup by Increasing IP Address or Port number or both |
| Enable | Enable or disable single IP input stream |
| Uni/Multicast | IP input by Unicast or Multicast option |
| Target IP | Input IP address |
| Port | Input port number |
| SFP | The SFP will be show up when the redundancy option is disable. It is for select IP input port. |
| Edit |  |
| Apply | Submit single IP configuration |
| Delete | Delete single IP configuration |
| Add | Add IP channels |
| Apply checked | Enable selected channels |
| Delete checked | Delete selected channels |

TS over IP output:

It is same as TS over IP input, there is a Quick setup. The process is same as input too.

| Menu Name | Options |
| --- | --- |
| Add | Add TS over IP channels |
| Apply checked | Apply all checked rows settings |
| Delete checked | Delete all checked rows settings |
| Ethernet Port | IP channel will be output with SFP-1 or SFP-2 |
| SFP-1 Target IP | Output IP address setup as port 1 |
| SFP-2 Target IP | Output IP address setup as port 2 |
| SFP-1 Target Port | Output target port setup 1 |
| SFP-2 Target Port | Output target port setup 2 |
| Protocol | Stream over IP data protocol |
| FEC | Enable or disable FEC |
| Source Module | Source module selection |
| Source Channel | Source channel selection |
| Apply Row | Apply row settings |
| Delete | Delete row settings |

TS/IP Local

This menu is to setup TS over IP ports physical IP address, Network mask and Gateway IP address.

## System

The System page is for configuring management IP, Device label and Web login ID and Password etc.

| Menu Name | Options |
| --- | --- |
| IP Address | Management IP address |
| MAC Address | MAC address of ethernet |
| Network Mask | Network mask of management |
| Gateway IP Address | Gateway of management |
| Device label | Device label setup option |
| Serial Number | Serial number of the main chassis |
| Clock setting | Clock setup option |
| NTP Host IP | Network time protocol host IP option |
| Watchdog | Watchdog setup option |
| Reboot | Soft reboot option |
| Old user name | Web browser login user name option for change to new user name |
| Old password | Web browser login password option for change to new password |
| New user name | Web browser new login user name input |
| New password | Web browser new password input |

| Version | Main chassis firmware versions |
| --- | --- |
| Reboot Module | Sub-module reboot options, user can specific module to reboot independently |
| Parameter | Default Parameter is for facotory default Save Parameter is for saving configurations as a file Upload and Reset is for uploading configure file and reset the unit configure as saved file |
| Upgrade | Main chassis upgrade option |

## Remux

The main chassis will install the Remux function, the setup web page will be as below figure. On the left Source menu, user will see all enabled sources. On the right side is remux menu. There are 16 remuxes channels for users to use. These 16 channels can be used as TS over IP source and input source for CI, modulator, etc.

Quick setup example:
Step 1: select sources will be used as remux source, click Apply Src to sync sources before doing remux;

Step 2: move mouse cursor to the channels which under modules and click right button of mouse, Capture button will show up;

Step 3: click Capture button and all programs information will show up under channel menu;

Step 4: move mouse to program which will be used for remux and drag the channel to one of the 16 remux channel, or select more programs and drag to remux menu at once;

Step 5: click m1 edit button to setup remux channel;

Step 6: move mouse to program of remux and click right button of mouse to edit program;

Step 7: the last step is to enable remux channels by click Apply All or Apply Selected button;