Professional Digital Decoder

User’s Manual

DCH-4000P

http://www.pbi-china.com

# CONTENT

CONTENT	1

1. Warning	2

2. Introduction	3

2.1. Features:	3

2.2. Options:	3

3. Appearance Introduction	4

3.1. Front Panel List	4

3.2. Rear Panel List	4

3.3. Usage of Control Buttons	5

4. Operation on Front Panel	6

4.1. Inputs Menu	6

4.3. System Menu	10

5. Frequently Asked Question	12

6. Appendix	12

6.1. Specification	12

6.2. Option List	14

7. Technology Support	15

8. DVB-S2 Input Menu	15

# 1. Warning

* Please refer to the explanation below before operating to avoid user hurt or device breakdown. Please do NOT power on before safety installation procedure checking.

Product specification and appearance are based on the actual product purchased; any changes will not be notified accordingly.

# 2. Introduction

DCH-4000P is a professional IRD with a variety of input (including DVB over ASI, IP, QPSK, QAM, COFDM and DS3) and output (CVBS, SDI, ASI, DS3 and IP) combinations. An appropriate IP port equipped as an option supports DVB over IP applications. LAN control and monitoring are achieved with TCP/IP, SNMP and HDMS*.

(*Headend Devices Management System, a PBI's proprietary software)

## 2.1. Features:

Fully complies with MPEG-2, MP@ML and DVB-S/-T/-C standards

IP input or output with UDP/RTP (optional)

Multicast and Unicast on IP

Supports PAL, NTSC or SECAM

Supports various Conditional Access systems

SDI video output with digital audio embedded

Two sets of independent ASI outputs

Automatic PMT update

Compatible with Multiple De-encrypt CI modules

DS3 I/O for TS (optional)

Switchable audio sound track

Teletext VBI, EBU subtitle and DVB subtitle

Upgradeable through LAN

Easy-to-use LCD menu

## 2.2. Options:

DVB-S, DVB-T or DVB-C tuner input

High Speed 100M Base-T IP output

High Speed 100M Base-T IP input

DS3 I/O card

# 3. Appearance Introduction

## 3.1. Front Panel List

Figure 3.1 Front Panel of DCH-4000P

- PBI logo

- Power LED

- Tuner lock LED

- Alarm LED

- LCD ( 20×2 characters )

- Control Panel

- Common Interface (×2 slots)

## 3.2. Rear Panel List

Figure 3.2 Rear Panel of DCH-4000P

- TS/IP Input/Output interface

- XRL L interface

- XRL R interface

- RGB/YUV interface (G/Y)

- RGB/YUV interface (B/U)

- RGB/YUV interface (R/Y)

- CVBS1 interface

- L-Audio-R interface

- CVBS2 interface

- ASI IN interface

- ASI/SDI Output interface

- ASI Output interface

- RS-232 interface

- Ethernet interface

- Tuner Out interface

- Tuner In interface

- Power socket

- ON/OFF switcher

## 3.3. Usage of Control Buttons

Figure 3.3 Control Unit

ENTER	   Call the menu and confirm the performance

EXIT	      Go back to the previous menu or cancel the operation

&     Zapping or switch the options of the menu and modify the values of options

&	   Move cursor Left /Right

# 4. Operation on Front Panel

After power on and connecting necessary cables, the LCD will display below information:

There are three submenus in Main Menu, including Inputs, Outputs and System.

## 4.1. Inputs Menu

Under Inputs Menu, the user could monitor configure the parameters of the Tuner and IP input settings.

There are three submenus in Inputs menu, including Status, QPSK and Ethernet. Press ENTER button to enter edit mode. Press& buttons to move cursor and use & button to modify the value. Press ENTER button to confirm the operation and EXIT button to cancel.

4.2. Outputs Menu

Under Outputs Menu, the user could configure the settings of output programs, such as the source signal for CI (CI Source), video standard, aspect ratio, DVB/EBU Subtitle, Audio mode and language, the source for ASI/SDI output, SDI output with or without audio embedded etc.

There are five submenus in Outputs menu, including Status, CI, Decoder, ASI and ASI 2/SDI. Press ENTER button to enter edit mode. Use & button to move cursor and use & button to edit the value. Press ENTER button to confirm the operation and EXIT button to cancel.

## 4.3. System Menu

Under System Menu, the user could configure the IP address, unit name of the DCH-4000P, or recover to the factory default settings, also the user could configure the TS/IP convertor to be IP input or output.

There are six submenus in System menu, including Local Setup, Trap IP Addr, Unit Name, Properties, Factory Settings and Machine Type. Use ENTER button to enter edit mode. Press  button to move cursor and use  button to modify the value. Press ENTER button to confirm the operation and EXIT button to cancel.

# 5. Frequently Asked Question

1. Why is there no display on LCD?

Answer: Please check whether the power supply is connected well first. If not, insert it well and switch on.

2. Why is there no input signal?

Answer: Please check whether the input cable in connected well first. If not, insert it well. If it is connected well, please check whether there is any damage on it. If there is, please change a good cable.

3. Why can’t the Tuner be locked?

Answer: Please check the settings of the Tuner; be sure the settings are correct to receive the satellite signal come from the LNB.

4. Why can’t the ASI be locked?

Answer: Please check the BNC cable first, make sure the cable is connected well and there are programs transmitted to DCH-4000P via the BNC cable.

# 6. Appendix

## 6.1. Specification

| QPSK Demodulation & FEC Parameters |  |
| --- | --- |
| Input Frequency Range | C & Ku Band, 950~2150MHZ |
| Input Level | -25dBm ~ -65dBm |
| Input Impedance | 75ΩF type |
| Symbol Rate | 2~45Mb/s (SCPC or MCPC) |
| Rolling Off Factory | 0.20 or 0.35 |
| Punctured Rates | 1/2, 2/3, 3/4, 5/6, 6/7, 7/8 |
| Reeds Salomon Decoding | 204, 188, T = 8 & I=12 |
| DVB-C QAM Demodulation |  |
| Connector | IEC, Female (7/8MHz) or F Female (6MHz) Input |
| Input Symbol Rate Range | 1~7Mbs (PAL), 1~6Mbps (NTSC) |
| Demodulation | 16/32/64/128/256 QAM |
| Tuner Bandwidth | 6 MHz or 7 MHz or 8 MHz factory optional |
| FEC Decoder | 1/2, 2/3, 3/4, 5/6, 7/8; K=7 |
| Frequency Range | 50~860MHz |
| Digital Signal Input Level | -15~15dBmV |
| Input Impedance | 75ΩF-type |
| DVB-T COFDM Demodulation |  |
| Connector | IEC, Female (7/8MHz) or F Female (6MHz) Input |
| 1 IF Loop through | Yes |
| Frequency Range | 470-862MHz, 174-230MHz |
| Input Symbol Rate Range | 4.98~31.67Mbit/s (8MHz bandwidth) |
| Constellation | QPSK, 16-QAM, 64-QAM |
| Tuner Bandwidth | 8MHz |
| Digital Signal Input Level | -20 to -75dBmV |
| Input Impedance | 75Ωunbalanced |
| FFT mode | 2K/8K |
| Guard Interval | 1/4, 1/8, 1/16, 1/32, off |
| FEC Code Rate | 1/2, 2/3, 3/4, 5/6 and 7/8 |
| DS3 Input |  |
| Input Impedance | 75Ω |
| Connector | BNC |
| Maximum Input Code Rate | 44.736Mbit/s |
| Format | Unframed Framing according to G.804/G.752 (DS3) |
| DS3 Loop Through Output |  |
| Impedance | 75Ω |
| Maximum Output Code Rate | 44.736Mbit/s |
| Connector | BNC |
| Format | Unframed Framing according to G.804/G.752 (DS3) |
| TS over IP Output |  |
| Connector | 100base-T RJ45 |
| Output Bit Rate | 70Mbits/s Max. |
| UDP/RTP | Multicast or Unicast |
| Multicast Control Protocol | IGMPV2 |
| I/O Interface on back panel |  |
| LNB I/O | 1×Input, 1×loop through output |
| RS-232 | 1×9-pin D-sub male |
| RJ45 | 1×Ethernet control port, 1×TS over IP output (factory optional) |
| ASI input | 1 |
| ASI output | 2×Redundant output |
| SDI output | 1(user optional) |
| RGB output | 1×RCA |
| CVBS output | 1×RCA, 1×BNC |
| Audio XRL Balance Output | 1 |
| General |  |
| Operating Temperature | 0-45℃ |
| Storage Temperature | -20~70℃ |
| Humidity | <85% |
| Power Supply | Ac 90V~260V 50Hz/60Hz |
| Dimensions | 483mm×255mm×44mm |
| Approximately Net Weight | 5Kg |

## 6.2. Option List

# 7. Technology Support

ADD: Room216 Floor2B, Dingjun Building,

No. 75 SuZhou Street,

Beijing, 100080, China

TEL: +86-10-6263-8833

FAX: +86-10-6263-7776

E-mail: mkt@pbicn.com

# 8. DVB-S2 Input Menu

When use DVB-S2 input, there will be some differences in input menu. Please refer to below menu tree for more details .

# Text boxes

Urgent instance!

Please pull out the plug in any following cases：

1. Wire or plug is damaged.

2. Filtered by the liquid, or fall into water.

3. Poured by rain or water.

4. Drop from a high place or the chassis is broken.

！

No Dismantle!

1. Please do NOT dismantle the machine by yourself.

2. Please do NOT change the parts by yourself. If the machine cannot work, please call the agent and professional repairer.

No touching!

Please do NOT touch the machine during thunderstorm.

No pressing heavily!

Please do NOT put too much pressure on the machine.

Depart From Dampness!

Do not use the machine in the area with high humidity or put it in the water or wet place.

Danger! Electricity!

Please use the outlet with the grounded pin. If not use the machine for a long period, please pull out the power plug from the outlet to avoid the damage by the lightening or electric wave. Make proper layout of circuitry to protect the machine from the destruction by hoof or extrusion and impact by something laid on it.

DCP-4000P

IP:10.10.70.111

Note: The IP could be configured by user.

Main Menu

System

Main Menu

Inputs

Main Menu

Outputs

IP IN: No Link

IP in unlock

ASI unlock

Tuner 0.00000M

Inputs

Status

Main Menu

Inputs

Inputs

QPSK

LNB Frequency

5150MHz

Satellite Frequency

4043MHz

Symbol Rate

17778KBand

LNB Voltage

Off

LNB 22KHz

Off

Inputs

Ethernet

Source IP Addr

0.0.0.0

Source Network

255.255.255.0

Source Gateway

1.0.0.0

Source Mac Address

00:0e:26:ff:aa:41

Multicast IP Addr

0.0.0.0

Multicast UDP Port

3000

Protocol

UDP

Output Smoothing

Auto

Main Menu

Outputs

Outputs

Status

Status

Decoder OK

PMT: 1024  PN: 101

A/V: 80/160

Video: OK

Audio: OK

Status

CI

CI Slot1

No Module

CI Slot2

No Module

Status

Ethernet

Outputs

CI

CI Source

TUNER

CI

Setup

Outputs

Decoder

Decoder

Program

Decoder

Video

Decoder

Audio

Outputs

ASI

ASI Source

TUNER

ASI Package Length

Bypass

Outputs

ASI 2/SDI

ASI 2/SDI

ASI 2

ASI 2

Setup

Main Menu

System

System

Local Setup

IP Address

10.10.70.111

Network Mask

255.255.255.0

Gateway

10.10.70.1

System

Trap IP Addr

Trap IP Addr

10.10.70.85

System

Unit Name

Unit Name

DCH-4000P

System

Properties

MAC Address

00:0e:26:ff:aa:19

FW Version

81.00.83

SW Version

03.48.07

System

Factory Settings

Factory Settings?

ENTER=Yes EXIT=No

Password

000000

System

Machine Type

Show the status of inputs and could not be configured by user.

Press ENTER button to enter the edit mode. Use  to key in the value. Press ENTER to confirm and EXIT to cancel

Press ENTER button to enter the edit mode. Use  to modify the value. Press ENTER to confirm and EXIT to cancel.

Press ENTER button to enter the edit mode. Use  to modify the value. Press ENTER to confirm and EXIT to cancel

Use  to modify the value.

Show the source Mac address. This option cannot be configured by user.

Use  to modify the source gateway.

Use  to modify the value of the UDP Port.

User can configure the protocol to be UDP or RTP

User can choose Auto, Disable and Fixed Rate.

Press ENTER button. Use & to choose menus, Enter button to enter the menu and EXIT button to back to the previous menu.

Show the information of outputs.

Show the information of CI. If there is no CAM card in CI Slot, it will show No Module on the LCD. If there is, it will show the information of CAM card.

Use  to change the CI source. There are TUNER, ASI Input and IP to choose.

Video Standard

Auto

EUB Subtitle lang

eng

Screen

4:3 Full

DVB Subtitle lang

eng

Audio Level

49

Audio Mode

Stereo

Audio lang

eng

Subtitle Priority

DVB first

There are Auto, SECAM, NTSC and PAL to choose.

There are 4:3 Full, 16:9 Full and 4:3 Letter box to choose.

Use  to change the letters to spell the language.

e.g.: To choose English subtitle, please spell eng.

Change the subtitle priority. There are DVB First and EUB first to choose.

Use  to modify the audio level.

There are Stereo, Left, Right and Mono to choose in Audio mode.

Use  to change the letters to spell the language.

Use  to change the ASI Source. There are Tuner, ASI Input, CI De-encrypted and IP to choose.

User could select Bypass or 188.

ASI 2/SDI

SDI

SDI

Setup

ASI 2 Package Length

Bypass

ASI 2 Source

TUNER

Audio DID

Group 1

Embed Audios

None

You could follow the same method to set the ASI 2 output as ASI output.

Use  to choose ASI 2, and then press EXIT. You will find the ASI 2 Setup option in previous menu

Use  to choose SDI, and then press EXIT. You will find the SDI Setup option in previous menu

There are Group 1, Group 2, Group 3 and Group 4 to choose.

You could choose None, One, Two, and One&Two.

Show the IP address, network mask and gateway of the DCH-4000P itself. Press ENTER to enter the edit mode. Use  to modify them.

Press ENTER to enter the edit mode. Use  to modify the value to set the Trap IP address

The user could change unit name. The default is DCH-4000P.

Press ENTER button to recover to factory default settings; Press EXIT button to cancel.

Show the DCH-4000P Mac address. This option cannot be edited.

Show the FW version and SW version of DCH-4000P. This option cannot be edited.

Default password is “10000”, User can configure the DCH-4000P to be IP input or IP output by pressing.

Note: configuration will be effective after reboot.

Inputs

DVB-S2

There are three factors: 0.2, 0.25 and 0.35.

Roll-off Factor

0.2

Use  to change demodulator mode to DVB-S or DVB-S2.

Use  to change On or Off.

Pilot

On

There are 14 operation modes: eight QPKS (1/2, 2/3, 3/4, 3/5, 4/5, 5/6, 8/9, 9/10) and six 8PSK (2/3, 3/4, 3/5, 5/6, 8/9, 9/10)

Operation Mode

QPSK 1/2

Use  to change demodulator mode to DVB-S or DVB-S2.

Demodulator Mode

DVB-S

Use  to change On or Off.

LNB 22KHz

Off

Symbol Rate

26850KBaud

Press ENTER button to enter the edit mode. Use  to modify the value. Press ENTER to confirm and EXIT to cancel

Satellite Frequency

4000MHz

LNB Frequency

5150MHz

User can configure Off, 13V and 18V

LNB Voltage

Off