2200MX update

- To ensure web access control is ok, the “IP Control” status indicator light is green

- To enter “System Setting”, and click the button to “Update”

- Download the update file from the mail to the computer's local hard disk.

- Open this file (this file is rar format file, please don’t unzip), please check the update file name is correct.

5, On message windows and click YES

- Start the upgrade process, please wait for several minutes

6, Web control will show a windows automatically after upgrade, it mean, later please manually clear the Cookies in the browser which you are using data, must be cleaned late, and then click YES

7，Prompt to restart the machine, please select YES

8， Module became to restart, and network management prompts network connection lost, please refresh web control again after restart.

9.At this time, please unplug immediately control cable, Power supply for module can't outage , please check module has started successfully by 1000CU. If start-up successful (if can't automatically return to IP control display, please wait for about 5 minutes, please turn on power), please use 1000CU, ENTER in the SYSTEM SETTING, to the FACTORY SETTING, use 1000CU to check module became to factor status, (if back to control IP status that is successful)

10. In part 9, please turn off the control page, and open a new page, to clear browser data capture for Internet.

11. Reconnect control cable between the module and computer, open a webpage, input control IP address, the username is root, password is 12345

12 Enter the control network, and fill in the corresponding to the two port's MAC address (according to 1.2.3.4.5 steps), the address can only fill in once, can't change, please carefully fill in, don't forget after fill in, press APPLY

13 After input the MAC, module’s TCP will restart, and then show a window, click OK, wait for about 30 seconds, please refresh the page again. Once again into the network.

14. Check the updated version was successful.

15，Special note: control network ports and IP data networks can’t set in the same network segment.

16, End of the upgrade