Contents

INTRODUCING	6

THANK YOU FOR YOUR PURCHASING SNR-VP-7050	6

SAFETY INSTRUCTIONS	6

DELIVERY CONTENT	6

KEYPAD	8

PORT FOR CONNECTING	9

ICON INTRODUCTION	10

LED INTRODUCTION	10

INITIAL CONNECTING AND SETTING	11

CONNECT THE PHONE	11

CONNECT TO NETWORK	11

POWER ADAPTOR CONNECTION	12

BASIC INITIALIZATION	12

NETWORK SETTINGS	13

BASIC FUNCTION	14

MAKING A CALL	14

CALL DEVICE	14

ANSWERING A CALL	14

DND	14

CALL WAITING	15

MUTE	15

CALL TRANSFER	15

BLIND TRANSFER	15

ATTENDED TRANSFER	15

SEMI ATTENDED TRANSFER	15

PHONE BOOK NUMBER STORE/DEDIT/DELETE	15

CALL LIST CHECK/DELETE/DIAL OUT	16

3-WAY CONNERENCE CALL	16

MULTIPLE-WAY CALL	16

ADVANCED FUNCTION	16

CALL PICKUP	16

JOIN CALL	17

REDIAL / UNREDIAL	17

CLICK TO DIAL	18

CALL BACK	18

AUTO ANSWER	18

HOTLINE	18

APPLICATION	18

SMS	18

MEMO	18

VOICE MAIL	19

PROGRAMMABLE KEY CONFIGURATION	19

SET THE TYPE AS MEMORY KEY	19

SET THE TYPE AS LINE	20

SET THE TYPE AS KEY EVENT	20

SET THE TYPE AS DTMF	20

SET THE TYPE AS REMOTE	20

SET THE TYPE AS BLF LIST KEY	20

BASIC SETTING	21

KEYBOAD	21

SCREEN SET	21

RINGER SET	21

VOICE VOLUME	21

TIME & DATE	21

5.6 GREETING WORD	21

LANGUAGE SET	22

ADVANCED SETTINGS	22

ACCOUNT	22

6.2 NETWORK	22

SECURITY	22

MAINTENANCE	22

FACTORY RESET	22

WEB CONFIGURATION	22

INTRODUCTION OF CONFIGURATION	22

WAYS TO CONFIGURE	22

PASSWORD CONFIGURATION	23

SETTING VIA WEB BROWSER	23

CONFIGURATION VIA WEB	24

BASIC	24

STATUS	24

WIZARD	25

CALL LOG	28

You can query all the outgoing through this page.	28

MMI SET	28

NETWORK	29

LAN CONFIG	31

Qos CONFIG	32

SERVICE PORT	34

DHCP SERVER	35

TIME&DATE	36

VOIP	37

SIP CONFIG	37

IAX2 CONFIG	44

STUN CONFIG	45

DIAL PEER SETTING	46

PHONE	49

DSP CONGFIG	49

FEATURE	50

DIAL PLAN	53

CONTACT	55

REMOTE CONTACT	57

WEB DIAL	57

FUNTION KEY	58

MAINTENCE	61

AUTO PROVISION	61

61

SYSLOG CONFIG	63

CONFIG SETTING	64

UPDATE	65

ACCESS	66

REBOOT	68

SECURITY	68

WEB FILTER	68

FIREWALL	69

NAT CONFIG	70

VPN CONFIG	72

SECURITY CONFIG	74

LOGOUT	74

APPENDIX	75

HIGHLIGHTS	75

FEATURES	75

SPECIFICATIONS & NETWORK STANDARDS	75

SIP PROTOCAL SPEC	75

DSP SPEC	76

HARDWARE SPEC	76

NETWORK STANDARDS	76

OTHER SPEC & PHYSICAL & ENVIRONMENTAL	76

OTHER SPEC	76

PHYSICAL & ENVIRONMENTAL	76

MAINTENANCE AND MANAGEMENT	77

# INTRODUCING

## THANK YOU FOR YOUR PURCHASING SNR-VP-7050

Thank you for purchasing SNR-VP-7050. SNR-VP-7050 is a full-feature telephone that provides voice communication over the same IP network that your computer uses. This phone’s functions not only much like a traditional phone, allowing to place and receive calls, and enjoy other features that traditional phone has, but also it owns many data services features which you could not expect from a traditional telephone.

This guide will help you easily to use the various features and services available on your phone.

## SAFETY INSTRUCTIONS

Please read the following safety notices before installing or using this phone. They are crucial for the safe and reliable operation of the device.

●   Please use the external power supply that is included in the package. Other power supplies may cause damage to the phone, affect the behavior or induce noise.

●   Before using the external power supply in the package, please check with home power voltage. Inaccurate power voltage may cause fire and damage.

●   Please do not damage the power cord. If power cord or plug is impaired, do not use it, it may cause fire or electric shock.

●   The plug-socket combination must be accessible at all times because it serves as the main disconnecting device.

●   Do not drop, knock or shake it. Rough handling can break internal circuit boards.

●   Do not install the device in places where there is direct sunlight. Also do not put the device on carpets or cushions. It may cause fire or breakdown.

●   Avoid exposure the phone to high temperature, below 0℃ or high humidity. Avoid wetting the unit with any liquid.

●   Do not attempt to open it. Non-expert handling of the device could damage it. Consult your authorized dealer for help, or else it may cause fire, electric shock and breakdown.

●   Do not use harsh chemicals, cleaning solvents, or strong detergents to clean it. Wipe it with a soft cloth that has been slightly dampened in a mild soap and water solution.

●   When lightning, do not touch power plug or phone line, it may cause an electric shock.

●   Do not install this phone in an ill-ventilated place.

●   You are in a situation that could cause bodily injury. Before you work on any equipment, be aware of the hazards involved with electrical circuitry and be familiar with standard practices for preventing accidents.

## DELIVERY CONTENT

Please check whether the delivery contains the following parts:

● The base unit with display and keypad

● The handset

● The handset cable

● The power supply

● The Ethernet cable

● The User Manual

IP Phone is designed to look like conventional phone; the following photo shows a broad overview of the IP Phone.

## KEYPAD

| KEY | KEY NAME | Function Description |
| --- | --- | --- |
|  | Navigation | Navigation key assists users for operating. In idle state they have special function. You can configure through the web page according to your patterns of use. |
|  | Volume -/+ | Turn down or turn up the volume by pressing these two keys. |
|  | SPEAKER | activate/deactivate the hands-free function |
|  | Call List | browse the call logs |
|  | PHONE BOOK | Access to phone book, and check the record list by adding new records and revising the record. When check the phone book records, press this key again will return to idle interface. |
|  | VOICE MAIL | Enter to voice mail |
|  | Soft key 1/2/3/4 | Keys combination, include functions such as History/Phonebook /DND/Menu /Del /Redial /Send /Quit/Answer/Divert/Reject/Hold/Transfer/Conf/Close and so on. |
|  | Transfer | used as blind transfer, attended transfer and half attended transfer |
|  | Redial | 1. In the hook off /hands-free mode, use the key to dial the last call number; 2. In stand-by mode, it has a function to check the Outgoing Call. |
|  | mute | Press this key in calling mode, and you can hear the other side, and the other side cannot hear you. |
|  | Line1/2/3/4 | Here are four SIP lines; user could select any one to make the call, if it has been registered. |
|  | Digital keyboard | Inputting the phone number or DTMF. |
|  | DSS keys | You can configure them with your own functions in the web page. |
|  | Indicator light | If the light blinking, indicate the phone has missed call. It also can indicate there is new incoming call. |

## PORT FOR CONNECTING

| Port | Port name | description |
| --- | --- | --- |
|  | Power switch | Input: 5V AC, O.8A |
|  | WAN | 10/100M Connect it to ether Network |
|  | LAN | 10/100M Connect it to PC |
|  | Handset | Port type: RJ-9 connector |

## ICON INTRODUCTION

| Icon | Description |
| --- | --- |
|  | Call out |
|  | Call in |
|  | Call hold |
|  | Auto answer |
|  | Call mute |
|  | Contact |
|  | DND(Do not Disturb) |
|  | In hand free mode |
|  | In handset mode |
|  | In headset mode |
|  | SMS |
|  | Missed call |
|  | Call forward |

## LED INTRODUCTION

Table 1 Call/Line Appearance Button LEDs for BLF

| LED Status | Description |
| --- | --- |
| Steady green | The object is in idle status |
| Slow blinking red | The object is ringing |
| Steady red | The object is active |
| Fast blinking red | The object is not available |
| Off | It is not active as call/line appearance |

Table 2 Call/Line Appearance Button LEDs for Presence

| LED Status | Description |
| --- | --- |
| Steady green | The object is online |
| Slow blinking red | The object is ringing |
| Steady red | The object is active |
| Fast blinking red | The object is not available |
| Off | It is not active as call/line appearance |

Table 3Line key LEDs

| LED Status | Description |
| --- | --- |
| Steady green | The account is active |
| Fast Blinking red | There is an incoming call to the account |
| Slow Blinking red | The call is on hold |
| Off | Call/line appearance is active |

Table 4 Power Indication LED

| LED Status | Description |
| --- | --- |
| Steady green | Power on |
| Fast Blinking red | There is an incoming call |
| Slow Blinking red | There is a missed call |
| Off | Power off |

# INITIAL CONNECTING AND SETTING

## CONNECT THE PHONE

### CONNECT TO NETWORK

Step 1: Connect the IP Phone to the corporate IP network. Before you connect the phone to the network, please check if your network can be accessed normally.

You can do this in one of two ways, depending on how your workspace is set up.

Direct network connection—by this method, you need at least one available Ethernet port in your workspace. Use the Ethernet cable in the package to connect WAN port on the back of your phone to the Ethernet port in your workspace. Since this VOIP Phone has router functionality, whether you have a broadband router or not, you can make direct network connect. The following two figures are for your reference.

Shared network connection—Use this method if you have a single Ethernet port in your workspace with your desktop computer already connected to it.First, disconnect the Ethernet cable from the computer and attach it to the WAN port on the back of your phone. Next, use the Ethernet cable in the package to connect LAN port on the back of your phone to your desktop computer. Your IP Phone now shares a network connection with your computer.The following figure is for your reference.

Step 2: Connect the handset to the handset port by the handset cable in the package.

Step 3: connect the power supply plug to the DC 5V adapter port on the back of the phone. Use the power cable to connect the power supply to a standard power outlet in your workspace.

Step 4: After power up, the phone’s LCD screen displays “Initializing”. Later, a ready screen typically displays the date, time.

If your LCD screen displays different information from the above, you need refer to the next section “Initial setting” to set your network online mode.

If your VOIP phone registers into corporate IP telephony Server, your phone is ready to use.

### POWER ADAPTOR CONNECTION

Make sure that the power you use is comply with the parameters of power adaptor.

Plug power adaptor to power socket.

Plug power adaptor’s DC output to the DC5V port of SNR-VP-7050 to start up.

There will be displayed “initializing” on the screen. After finishing startup, phone will show current date and time and so forth.

If phone has registered to the server, you can place or answer calls.

## BASIC INITIALIZATION

SNR-VP-7050 is provided with a plenty of functions and parameters for configuration. User needs some network and VoIP knowledge so that he could understand the meanings of parameters. In order to make user use the phone more easily and conveniently, there are basic configurations introduced which is mandatory to ensure phone calls available.

### NETWORK SETTINGS

Make sure that network is connected already before setting network of phone. SNR-VP-7050 uses DHCP to get WAN IP configurations, so phone could access to network as long as there is DHCP server in it. If there is no DHCP server available, phone has to be changed WAN network setting to Static IP or PPPoE.

Setting PPPoE mode (for ADSL connection)

Get PPPoE account and password first.

Press soft4 (Menu)->Settings->Advanced Setting, then enter passwords(123), and choose network ->WAN->Net Mode, enter and choose PPPoE through navigation keys and press the Save key.

Press Soft4 (Quit), then choose PPPoE Set, press soft3 (enter).

The screen will show the current information. Press Soft1 (Del) to delete it, then input your PPPoE user and password and press Soft3 (Save).

Press Soft3 (Quit) six times to return to the idle screen.

Check the status. If the screen shows “Negotiating…” it shows that the phone is trying to access to the PPPoE Server; if it shows an IP address, then the phone has already get IP with PPPoE.

Setting Static IP mode (static ADSL/Cable, or no PPPoE / DHCP network)

Prepare the network’s parameters first, such as IP Address, Net mask,Default Gateway and DNS server IP addresses. If you don’t know these information, please contact the service provider or technician of network.

Press Menu->Settings->Advanced Setting, then enter passwords(123), and choose network ->WAN->Net Mode, enter and choose Static through navigation keys and press the Save key.

Press Quit, then choose Static Set, press Enter.

The screen will show the current information, and then press Del to delete. Input your IP address, Mask, Gateway, DNS, and press “save” key to save what you input.

Press Quit six times to return to the idle screen.

Check the status, the screen shows “Static” .the screen shows the IP address and gateway which were set just now, if the phone could display the right time, it shows that Static IP mode takes effect.

Setting DHCP mode

Press Menu->Settings->Advanced Setting, then enter passwords, and choose network ->WAN->Net Mode, enter and choose DHCP through navigation keys and press the Save key.

Press Quit six times to return to the idle screen.

Check the status, the screen shows “DHCP”，If the screen shows the IP address and gateway which were set just now, it shows that DHCP mode takes effect.

# BASIC FUNCTION

## MAKING A CALL

### CALL DEVICE

You can make a phone call via the following devices:

Pick up the handset,   icon will be showed in the idle screen.

Press the Speaker button,   icon will be showed in the idle screen.

Press the Headset button if the headset is connected to the Headset Port in advance. The icon  will be showed in the idle screen.

## ANSWERING A CALL

Answering an incoming call

If you have just one incoming call, lift the handset, or press the Speaker button/ Answer softkey to answer using the speakerphone, or press the headset button to answer the call.

If you have already in calls and need to answer the new call, press the answer softkey.

During the conversation, you can alternate between Headset, Handset and Speaker phone by pressing the corresponding buttons or picking up the handset.

## DND

Press DND softkey to active DND Mode. Further incoming calls will be rejected and the display shows:  icon. Press DND softkey again to deactivate DND mode. If there are some incoming calls rejected in DND mode, you can find the incoming call records in the Call History.

## CALL WAITING

Press Menu ->Features->Enter->Call Waiting->Enter.

Use the navigation keys to active or deactivate call waiting.

Then press the Save to save the changes.

## MUTE

Press Mute button during the conversation, icon  will be showed in the LCD.

Then the other side will not hear you, but you can hear him. Press it again to get the phone to normal conversation.

## CALL TRANSFER

### BLIND TRANSFER

During talk, press the key Transf, and then dial the number that you want to transfer to, and finished by "#". Phone will transfer the current call to the third party. After finishing transfer, the call you talk to will be hanged up. User can not select SIP line when phone transfers call.

### ATTENDED TRANSFER

During talk, press the key Transf, then input the number that you want to transfer to and press soft key-Send. After that third party answers, then press Transfer to complete the transfer. (You need enable call waiting and call transfer first). If there are two calls, you can just talk to one, and keep hold to the other one. The one who is keep hold cannot speak to you or hear from you. Note: the server that user uses must support RFC3515 or it might not be used.

### SEMI ATTENDED TRANSFER

During the talk, press Transf firstly, and then press soft key-Send after inputting the number that you want to transfer. You are waiting for answering; now, press Transf and the transfer will be done. (To use this feature, you need enable call waiting and call transfer first).

## PHONE BOOK NUMBER STORE/DEDIT/DELETE

In standby, -press"" button, LCD display “Phone Book Current”

-press Menu to check first record, press "" and "" to review others.

-press "" till LCD display “ADD”, then press "Menu" to input name, number, ring types. During the operation, press Local IP/DEL to delete wrong digit.

-press ""till LCD display “Search”, then press "Menu", input name of desired number and press "Menu" to check the item, if you want to edit it, press Local IP/DEL while LCD displays “0=mod 1=del”, then press 0/1 to modify/delete.

## CALL LIST CHECK/DELETE/DIAL OUT

In standby, press"", LCD display “Call Record Dialed”,

-Press "Menu" to check last dialed out number and conversation time, press "" and ""to review others; press "#"to dial out this item; press Local IP/DEL to delete, LCD displays “Are you sure?”, press "Menu" to confirm.

- press""till LCD display “Received”, then press "Menu" to check latest received call, press""and ""to review others and press ”#” to dial out; press Local IP/DEL to delete.

- press "" till LCD display “Call Record missed”, then press "Menu" to check latest miss call, press "" and "" to review other and press “#” to dial out; Press Local IP/DEL to delete.

## 3-WAY CONNERENCE CALL

1. Press the Conf softkey during an active call.

2. The first call is placed on hold. Then you will hear a dial tone. Dial the

number to conference in, then press Send key.

3. When the call is answered, press Conf and add the first call to the

conference.

4. If you want to release the conference, press Split key.

## MULTIPLE-WAY CALL

If user has 4 line calls and wants to invite the five party during the call, they

can press Conf or Transf “New Call”, press OK, enter the number ,then press

Send and wait for the other party to answer. When the multiple-way calls, you

can press the arrow keys to select a call.

# ADVANCED FUNCTION

## CALL PICKUP

Call pickup is implemented by simulating pickup function of PBX. it’s that, when A calls B, B rings but no answer, at this moment, C can hook off and input an appointed prefix plus B’s number, pick up A’s call and talk with A.

The following chart shows how to configure an appointed prefix in dial peer to have call pick up function.

*1* means appointed prefix code. After making the above configuration, C can dial *1* plus B’s phone number to pick up A’s call. User can set prefix in random, in the case of no affecting current dialing rules.

## JOIN CALL

When B is calling C, A can join in the existing call by inputting an appointed prefix numbers plus B or C number, if B or C also supports join call.

The following chart shows how to configure an appointed prefix in dial peer to have join call function.

*2* means appointed prefix code. After making the above configuration, A can dial *2* plus B or C number to join B and C’s call. User can set prefix in random, in the case of no affecting current dialing rules.

## REDIAL / UNREDIAL

If B is in busy line when A calls B, A will get notice: busy, please hang up. If A want to connect B as soon as B is in idle, he can use redial function at the moment and he can dials an appointed prefix number plus B’s number to realize redial function.

What is redial function? A can’t not build a call with B when B is in busy, then A will subscribe B’s calling mode at 60 second intervals. Once B is available, A will get reminder of rings to hook off, while A hooks off, A will call B automatically. If at this time A is occupied temporarily and unwilling to contact B, A also can cancel the redial function by dialing an appointed prefix plus B’s number before making the redial function.

*3* is appointed prefix code. After making the above configuration, A can dial *3* plus B’s phone number to make the redial function.

*4* is appointed prefix code. After configuration, A can dial *4* to cancel redial function.

User can set prefix in random, in the case of no affecting current dialing rules.

## CLICK TO DIAL

When user A browses in an appointed Web page, user A can click to call user B via a link (this link to user B), then user A’s phone will ring, after A hooks off, the phone will dial to B.

## CALL BACK

This function allows you dial out the last incoming phone call.

## AUTO ANSWER

When there is an incoming call, after no answer time arrived, the phone will answer the call automatically.

## HOTLINE

You can set hotline number for every sip, and dial the number immediately when you hook off; if you set up Warm Line Time, the phone will play dial tone first. After warm line time is timed out, phone would call out the hotline number automatically.

## APPLICATION

### SMS

Press Menu ->Application->Enter->SMS->Enter.

Use the navigation keys to highlight the options. You can read the message in the Inbox/Outbox.

After view the new message, you can press Reply to reply the message, and use the 123 softkey to change the Input Method, when enter the reply message, press OK, then use the navigation keys to select the line from which you want to send, then Send.

If you want to write a message, you can press New and enter message. Use the 123 softkey to change the Input Method. When you input the message you want to send, press OK, then use the navigation keys to select the line from which you want to send, then Send.

If you want to delete the message, after view the message, press Del, then you have three options to choose: Yes, All, No.

### MEMO

You can add some memos to record some important things to remind you. Press Menu->Application->Memo->Enter->Add.

There are some options to configure: Mode, Date, Time, text, Ring. When the configuration is completed, press Save.

### VOICE MAIL

Press Menu->Voice Mail->Enter.

Use the navigation keys to highlight the line for which you want to set, press Edit, and use the navigation key to turn on the mode, and the input the number. Press 123 softkey to choose the proper input method.

Press Save to save the change.

To view the new voice mail, Press the Voice mail softkey directly. Press Dial, then you may be prompted to enter the password, then you can listen to your new and old messages.

## PROGRAMMABLE KEY CONFIGURATION

The phone has 10 programmable keys which are able to set up to many functions per key. The following list shows the functions you can set on the programmable keys and provides a description for each function. The default configuration for each key is N/A which means the key hasn’t been set for any functions.

### SET THE TYPE AS MEMORY KEY

Press Menu->Settings->Basic Setting->Enter->DSS Key, you have two options: Line As DSS Keys and Memory As DSS Keys, choose one you want to make the assignment, use the navigation key to choose the type as memory key. In the Dial field, you have some options, such as Normal, Speed Dial, Intercom,BLF, Presence, and MWI.

Speed dial

You can configure the key as a simplified speed dial key. This key function allows you to easily access your most dialed numbers.

INTERCOM

You can configure the key for Intercom code and it is useful in an office environment as a quick access to connect to the operator or the secretary. Note: Your VoIP PBX must support this feature. And make sure the intercom extension enable the Auto-answer function.

BLF

BLF is also called “Busy lamp field”, and it is used to prompt the user to pay attention to the state of the object than has been subscribed, and used to cooperate with the server to pick up the phone call. You can configure the key for Busy Lamp Field (BLF) which allows you to monitor the status (idle,ringing, or busy) of other SIP account. User can dial out on a BLF configured

key. Please refer to “LED Instruction” for more detail about the LED status in

different situation.Note: In the Web interface, you can also set the pickup number to active the pickup function. For example, if you set the BLF number as 212, and the pickup number is 189, then when there is an incoming call to 212, press the BLF key, it will call out the 189 automatically to pick up the incoming call on 212.

PRESENCE

Presence is called present, and compared to the BLF, it can also check whether object online.

MWI

When the key is configured as MWI, you are allowed to access voice mail quickly by pressing this key.

### SET THE TYPE AS LINE

You can set these keys as line keys, and press it, it will enter dialer interface.

### SET THE TYPE AS KEY EVENT

You can set these keys as Key Event, and the subtype have many options.Choose one and it will have corresponding function.

● None

● MWI

● DND (Do Not Disable)

● Hold

● A_Transfer (Attended Transfer)

● B_Transfer (Blind Transfer)

● Phone Book

● Redial

● Pick up

● Join

● Auto-redial

● CFwd (Call Forward)

● History (Call Record)

● Flash

● Memo

● Headset

● Release: Press the key you can end the call.

● Lock: Press the key you can lock the keyboard.

● SMS

● Call Back

### SET THE TYPE AS DTMF

You can configure the key as DTMF. This key function allows you to easily dial or edit dial number.

### SET THE TYPE AS REMOTE

You need to match a XML Phonebook address, pressing the button you can directly access the corresponding remote phonebook.

### SET THE TYPE AS BLF LIST KEY

It needs the cooperation with the Broadsoft server. The traditional BLF is that every number will need to be subscribed, so if the numbers that subscribed is so many that it will cause to obstruction. However, BLF List Key will put the numbers that needed to be subscribed in a group, and the phone use the URL of the group to subscribe and analyze the specific information of each number such as number, name, state and so on according to the notifications from the

server. Then set the idle Memory key as BLF List Key, later if the state of an object changes, the corresponding LED will change.

# BASIC SETTING

## KEYBOAD

Press Menu ->Settings-> Enter->Basic Setting-> Enter->Keyboard->Enter.

There are four items: DSS Keys, Multiplex, Long Click, SoftKey. You can set up respectively on them. Press the key Enter to the interface, then use the navigation keys to choose the function for the key according to you want.

Press the key OK to save.

## SCREEN SET

1. Press Menu ->Settings-> Enter->Basic Setting-> Enter->Screen Set->Enter.

2. You can set Contrast and Brightness, press Enter and use the navigation keys

to set, then press the key Save.

## RINGER SET

1. Press Menu ->Settings-> Enter->Basic Setting-> Enter->Ringer Set->Enter.

2. You can set Ringer Volume and Ringer Type, press Enter and use the

navigation keys to set, then press the key Save. In the Ringer Type, the default

system rings have 12 that can be set through the web page.

## VOICE VOLUME

1. Press Menu ->Settings-> Enter->Basic Setting-> Enter->Voice Volume->Enter.

2. Use the navigation keys to turn down or turn up the voice volume, the press

the key Save.

## TIME & DATE

1. Press Menu ->Settings->Enter->Basic Setting-> Enter->Time & Date->Enter.

2. You have two options to choose: Auto and Manual, use the navigation keys

to choose, then press Save.

## 5.6 GREETING WORD

1. Press Menu ->Settings-> Enter->Basic Setting-> Enter->Greeting Word->Enter.

2. You can enter the message and press Save, it will display in the phone screen

when the phone start up.

## LANGUAGE SET

1. Press Menu ->Settings-> Enter->Basic Setting-> Enter->Language Set->Enter.

2. Ｔhe DUT supports 2 languages,(English/Chinese) you can use navigation keys to choose.

# ADVANCED SETTINGS

## ACCOUNT

Press Menu->Enter->Advanced settings, and then input the password to enter the interface, the default password is 123. You can set it through the web page.Then choose Account then press Enter, you can do some sip settings.

## 6.2 NETWORK

Press Menu->Enter->Advanced settings, and then input the password to enter the interface. Then choose Network and press Enter, you can do network settings, you can refer to 2.2.1 Network settings.

## SECURITY

Press Menu->Enter->Advanced settings, and then input the password to enter the interface. Then choose Security, you can configure Menu Password, Keylock Password, Keylock Status and whether to ban Outgoing.

## MAINTENANCE

Press Menu->Enter->Advanced settings, and then input the password to enter the interface. Then choose Maintenance and press Enter, you can configure Auto Provision, Backup, and Upgrade.

## FACTORY RESET

Press Menu->Enter->Advanced settings, and then input the password to enter the interface. Then choose Factory Reset and press Enter, you can choose Yes or No.

# WEB CONFIGURATION

## INTRODUCTION OF CONFIGURATION

### WAYS TO CONFIGURE

SNR-VP-7050 has three different ways to different users.

Use phone keypad.

Use web browser(recommendatory way).

Use telnet with CLI command.

### PASSWORD CONFIGURATION

There are two levels to access to phone: root level and general level. User with root level can browse and set all configuration parameters, while user with general level can set all configuration parameters except SIP (1-2) or IAX2’s that some parameters cannot be changed, such as server address and port. User will has different access level with different username and password.

- Default User with general level:

Username:guest

Password:guest

- Default user with root level:

Username:admin

Password:admin

The default password of phone screen menu is 123.

## SETTING VIA WEB BROWSER

When this phone and PC are connected to network, enter the IP address of the

wan port in this phone as the URL (e.g. http://xxx.xxx.xxx.xxx/ or

http://xxx.xxx.xxx.xxx:xxxx/).

If you do not know the IP address, you can look it up on the phone’s display by

pressing Status button.

The login page is as below picture

After you configure the ip phone, you need click save button in config under

Maintenance in the left catalog to save your configuration. Otherwise the phone

will lose your modification after power off and on.

## CONFIGURATION VIA WEB

### BASIC

#### STATUS

| Field name | Explanation |
| --- | --- |
| Network | Shows the configuration information on WAN and LAN port, including the connect mode of WAN port (Static, DHCP, PPPoE), MAC address, the IP address of WAN port and LAN port, ON or OFF of DHCP mode of LAN port. |
| Phone Number | Shows the phone numbers provided by the SIP LINE 1-4 servers and IAX2.The last line shows the version number and issued date. |

#### WIZARD

Please select the proper network mode according to the network condition.BW530 provide three different network settings: ● Static: If your ISP server provides you the static IP address, please select this mode, then finish Static Mode setting. If you don’t know about parameters of Static Mode setting, please ask your ISP for them. ● DHCP: In this mode, you will get the information from the DHCP server automatically; need not to input this information artificially. ● PPPoE: In this mode, your must input your ADSL account and password. You can also refer to 3.2.1 Network setting to speed setting your network.

Choose Static IP MODE, Click “NEXT” can config the network and SIP(default SIP1) simply, also can browse too. Click “BACK” can return to the last page.

| Static IP Address | Input the IP address distributed to you. |
| --- | --- |
| Netmask | Input the Netmask distributed to you. |
| Gateway | Input the Gateway address distributed to you. |
| DNS Domain | Set DNS domain postfix. When the domain which you input cannot be parsed, phone will automatically add this domain to the end of the domain which you input before and parse it again. |
| Primary DNS | Input your primary DNS server address. |
| Alter DNS | Input your standby DNS server address. |

| Display Name | Set the display name. |
| --- | --- |
| Server Address | Input your SIP server address. |
| Server Port | Set your SIP server port. |
| User Name | Input your SIP register account name. |
| Password | Input your SIP register password. |
| Phone Number | Input the phone number assigned by your VOIP service provider. |
| Enable Register | Start to register or not by selecting it or not. |

Display detailed information that you manual config. Choose DHCP MODE, click “NEXT” can config SIP(default:SIP1) simply, also can browse too. Click “BACK” can return to the last page. Like Static IP MODE. Choose PPPoE MODE, click “NEXT” can config the PPPoE account/password and SIP(default:SIP1) simply, also can browse too. Click “BACK” can return to the last page. Like Static IP MODE.

| PPPoE Server | It will be provided by ISP. |
| --- | --- |
| Username | Input your ADSL account. |
| Password | Input your ADSL password. |
| Notice: Click"Finish"button after finished your setting, IP Phone will save the setting automatically and reboot, After reboot, you can dial by the SIP account. |

#### CALL LOG

#### You can query all the outgoing through this page.

| Field name | explanation |
| --- | --- |
| Start Time | Display the start time of the outgoing record. |
| Last Time | Display the conversation time of the outgoing record. |
| Called Number | Display the account/protocol/line of the outgoing record. |

#### MMI SET

| Field name | explanation |
| --- | --- |
| Language Set | Set the language of phone, English is default. |
| Greeting Message | The greeting message will display on LCD when phone is idle. It can support 16 chars. the default chars are VOIP PHONE. |

### NETWORK

WAN Config page

WAN CONFIG

| Active IP | The current IP address of the phone. |
| --- | --- |
| Current Netmask | The current Netmask address. |
| MAC Address | The current MAC address of the phone. |
| Current Gateway | The current Gateway IP address. |
| Get MAC Time | Shows the time of getting MAC address |

| Please select the proper network mode according to the network condition. The DUT provide three different network settings: ● Static: If your ISP server provides you the static IP address, please select this mode, and then finish Static Mode setting. If you don’t know about parameters of Static Mode setting, please ask your ISP for them. ● DHCP: In this mode, you will get the information from the DHCP server automatically; need not to input this information artificially. ● PPPoE: In this mode, your must input your ADSL account and password. You can also refer to 3.2.1 Network setting to speed setting your network. |
| --- |
| Obtain DNS server automatically | Select it to use DHCP mode to get DNS address, if you don’t select it, you will use static DNS server. The default is selecting it. |

| If you use static mode, you need set it. |
| --- |
| IP Address | Input the IP address distributed to you. |
| Netmask | Input the Netmask distributed to you. |
| Gateway | Input the Gateway address distributed to you. |
| DNS Domain | Set DNS domain postfix. When the domain which you input cannot be parsed, phone will automatically add this domain to the end of the domain which you input before and parse it again. |
| Primary DNS | Input your primary DNS server address. |
| Alter DNS | Input your standby DNS server address. |

| If you uses PPPoE mode， you need to make the above setting. |
| --- |
| PPPoE Server | It will be provided by ISP. |
| Username | Input your ADSL account. |
| Password | Input your ADSL password. |
| Notice: 1) Click “Apply” button after finished your setting, IP Phone will save the setting automatically and new setting will take effect. 2) If you modify the IP address, the web will not response by the old IP address. Your need input new IP address in the address column to logon in the phone. 3) If networks ID which is DHCP server distributed is same as network ID which is used by LAN of system, system will use the DHCP IP to set WAN,and modify LAN’s networks ID(for example, system will change LAN IP from 192.168.10.1 to 192.168.11.1) when system uses DHCP client to get IP in startup; If system uses DHCP client to get IP in running status and network ID is also same as LAN’s, system will refuse to accept the IP to configure WAN. So WAN’s active IP will be 0.0.0.0 |

802.1X Settings

| If you uses 802.1X, you need to make the above setting. |
| --- |
| User | User name |
| Password | Password |
| Enable 802.1X | ON/OFF |

#### LAN CONFIG

| LAN Config |
| --- |
| Field name | explanation |
| LAN IP | Specify LAN static IP. |
| Netmask | Specify LAN Netmask. |
| DHCP Service | Select the DHCP server of LAN port or not. After you modify the LAN IP address, phone will amend and adjust the DHCP Lease Table and save the result amended automatically according to the IP address and Netmask. You need restart the phone and the DHCP server setting will take effect. |
| NAT | Select NAT or not. |
| Bridge Mode | Select Bridge Mode or not: If you select Bridge Mode,the phone will no longer set IP address for LAN physical port，LAN and WAN will join in the same network. Click “Apply”, the phone will reboot. |
| Notice: If you choose the bridge mode, the LAN configuration will be disabled. |

#### Qos CONFIG

The VOIP phone support 802.1Q/P protocol and DiffServ configuration. VLAN functionality can use different VLAN IDs for WAN and LAN port. The VLAN application of this phone is very flexible.

In chart 1, there is a layer 2 that switches without setting VLAN. Any broadcast frame will be transmitted to the other ports except the send port. For example, a broadcast information is sent out from port 1 then transmitted to port 2,3and 4.In chart 2, red and blue indicate two different VLANs in the switch, and port 1 and port 2 belong to red VLAN, port 3 and port 4 belong to blue VLAN. If a broadcast frame is sent out from port 1, switch will transmit it to port 2, the other port in the red VLAN and not transmit it to port3 and port 4 in blue VLAN. By this means, VLAN divide the broadcast domain via restricting the range of broadcast frame transition. Note: chart 2 use red and blue to identify the different VLAN, but in practice,

VLAN uses different VLAN IDs to identify.

| QoS Configuration |
| --- |
| Field name | explanation |
| VLAN Enable | Before select it to enable VLAN, you need enable Bridge mode in LAN config. |
| VLAN ID Check Enable | Enable VLAN ID check by selecting it. After enable VLAN ID check, if VLAN ID of a data package is not the same with the phones or a data package do not have VLAN ID, the data package will be discarded. |
| Voice/Data VLAN differentiated | After enable VLAN, system will set packets with different type of VLAN ID. Undifferentiated means after using VLAN, both VoIP packets and other data packets will use the voice VLAN ID; tag differentiated means after using VLAN, VoIP(signal and voice) packets will add voice VLAN ID, and other data packets will add data VLAN ID; data untagged means after using VLAN, only VoIP packets will add voice VLAN ID. Other data packets will not use VLAN. |
| DiffServ Enable | Select it or not to Enable or disable DiffServ. |
| DiffServ Value | Set DiffServ value, the common value is 0x00. |
| Voice 802.1P Priority | Specify 802.1P Priority of voice/signal data package. |
| Data 802.1P Priority | Set 802.1p of data VLAN. Non-VoIP data (such as http, telnet, ping etc) will use this value to set VLAN package. |
| Voice VLAN ID | Set VLAN ID of voice/signal data package. |
| Data VLAN ID | Set 802.1q of data VLAN ID. Non-VoIP data (such as http, telnet, ping etc) will use this value to set VLAN package. |

#### SERVICE PORT

You can set the port of telnet/HTTP/RTP by this page.

| SERVICE PORT |
| --- |
| Field name | explanation |
| HTTP Port | Set web browser port, the default port is 80, if you want to enhance system safety, you’d better change it into non-80 standard port. Example: the IP address is 192.168.0.70, and the port is 8090, the accessing address is http://192.168.0.70:8090. |
| HTTPS Port | Set HTTPS Port,the default is 443 port. |
| Telnet Port | Set Telnet Port, the default is 23. You can change the value into others. Example: the IP address is 192.168.0.70. the telnet port value is 8023, the accessing address is telnet 192.168.0.70 8023 |
| RTP Initial Port | Set the RTP Initial Port. It is dynamic allocation. |
| RTP Port Quantity | Set the maximum quantity of RTP Port, the default is 200. |
| Notice: 1) You need save the configuration and reboot the phone after set this page. 2) If you modify the port of Telnet and HTTP, you would better set the value more than 1024 because the port value less than 1024 is system port reserved. 3) If you set 0 for the HTTP port, it will disable HTTP service. |

#### DHCP SERVER

| DHCP SERVER |
| --- |
| Field name | explanation |
| DHCP Leased Table | IP-MAC mapping table. If the LAN port of the phone connects to a device, this table will show the IP and MAC address of this device. |
| Shows the DHCP Lease Table， the unit of Lease time is Minute. |
| Lease Table Name | Specify the name of the lease table |
| Start IP | Set the start IP address of the lease table |
| End IP | Set the end IP address of the lease table, the network device connected to LAN port will get IP address between Start IP and End IP by DHCP. |
| Netmask | Set the Netmask of the lease table |
| Gateway | Set the Gateway of the lease table |
| Lease Time | Set the Lease Time of the lease table |
| DNS | Set the default DNS server IP of the lease table; Click the Add button to submit and add this lease table |
| Select name of lease table, click the Delete button will delete the selected lease table from DHCP lease table. |
| Enable DNS Relay | Select Enable DNS Relay, the default is enabled. Click the Apply button to become effective. |
| Notice: 1) The size of lease table cannot be larger than the quantity of C network IP address. We recommend you to use the default lease table and not modify it. 2) If you modify the DHCP lease table, you need save the configuration and reboot. |

#### TIME&DATE

| TIME&DATE |
| --- |
| Field name | explanation |
| Enable STNP | Select the Enable SNTP, and click Apply to make the SNTP Times effective. |
| Enable DHCP Time | Enable DHCP Time by selecting it, then the phone will automatically synchronize the standard time. |
| Primary Server | Set SNTP Primary Server IP address. |
| Time Zone | Select the Time zone according to your location. |
| Resync Period | Set the Resync Period, the default is 60 seconds. |
| 12-Hour clock | Switch the time mechanism between 12 hours and 24 hours. Default is 24 hours mode. |
| Enable | Enable daylight saving time |
| Offset | Setup the variety length |
| Month | Setup stat and end month |
| Week | Setup start and end week |
| Day | Setup start and end day |
| Hour | Setup start and end hours |
| Minute | Setup start and end minutes |
| Notice: You need specify the above all items. |

### VOIP

#### SIP CONFIG

| SIP Config |
| --- |
| Choose line to set info about SIP, there are 6 lines to choose. |
| Status | Shows if the phone has been registered the SIP server or not; or so, show Unapplied. |
| Server Address | Input your SIP server address. |
| Server Port | Set your SIP server port. |
| Authentication User | Input your SIP registered account name. |
| Authentication Password | Input your SIP registered password. |
| SIP User | Input the phone number assigned by your VoIP service provider. Phone will not register if there is no phone number configured. |
| Display Name | Set the display name. |
| Enable Registration | Start to register or not by selecting it or not. |
| Domain Realm | Set the sip domain if needed, otherwise this VoIP phone will use the Register server address as sip domain automatically. (Usually it is same with registered server and proxy server IP address). |
| Proxy Server Address | Set Proxy server IP address: Usually, register SIP server configuration is the same as proxy SIP server. But if your VoIP service providers give different configurations between register SIP server and proxy SIP server, you need make different settings. |
| Proxy Server Port | Set your Proxy SIP server port. |
| Proxy User | Input your Proxy SIP server account. |
| Proxy Password | Input your Proxy SIP server password. |
| Backup Server Address | Input the Backup Server Address, if the primary server is unavailable, then the phone will enable the Backup Server Address. |
| Backup Server Port | Specify the Backup Server Port. |
| Server Name | Set the server name. |
| Disable Codes/Enable Codes | Use the navigation keys to highlight the desired one in the Enable/Disable codec’s list, and press the desired to move to the other list. |
| Forward Type | Select call forward mode The default is Off: Close down calling Forward Busy: If the phone is busy, incoming calls will be forwarded to the appointed phone. No answer: If there is no answer, incoming calls will be forwarded to the appointed phone after a specific. Always: Incoming calls will be forwarded to the appoint phone Immediately. The phone will prompt the incoming while doing forward. |
| Forward Number | Specify the number you want to forward. |
| No Ans. Fwd Wait Time | Specify the No Answer Forward Delay Time, if the forward type is NO Answer, incoming calls will be forwarded after. |
| Transfer Timeout | For the phone supports the transfer of certain special features server, set interval time between sending “bye” and hanging up after the phone transfers a call. |
| Enable Hotline | Specify Hot Line by selecting it. |
| Hotline Number | Specify Hot Line Number, the phone dial the hot line number automatically at hands-free mode or handset mode after warm line time. |
| Warm Line Wait Time | Specify the Warm Line Time |
| SIP Encryption | Enable/Disable Signal Encrypt |
| SIP Encryption Key | Set the key for signal encryption. |
| RTP Encryption | Enable/Disable RTP Encrypt. |
| RTP Encryption Key | Set the key for RTP encryption |
| Enable Auto Answer | Enable Auto Answer by selecting it |
| Auto Answer Timeout | Specify Auto Answer Time, the phone auto answers the incoming call after Auto Answer Time. |
| Enable Session Timer | Set Enable/Disable Session Timer, whether support RFC4028.It will refresh the SIP sessions. |
| Session Timeout | Set the session timeout |
| Subscribe For MWI | Enable the Subscribe for MWI by selecting it, the phone will send subscribe message for MWI to the SIP Server. |
| MWI Number | Specify the MWI Number; Please contact your system 26 administrator for the connecting code. Different systems have different codes. |
| Subscribe Period | Overtime of resending subscribe packet. Suggest using the default configuration. |
| Conference Type | Specify the Conference Type, if you select the local, you needn’t input the conference number |
| Conference Number | Specify the network conference number; please contact your system administrator for the network conference number. |
| Registration Expires | Set expire time of SIP server register, default is 60 seconds. If the register time of the server requested is longer or shorter than the expired time set, the phone will change automatically the time into the time recommended by the server, and register again. |
| Enable Service Code | If you want to realize the following function by the server, please enter the On Code and Off Code option, then when you choose to enable/disable following function on your IP phone, it will send message to the server, and the server will turn on/off the function immediately. |
| DND On Code | Set the DND On Code, When you press the DND hot key, the phone will send a message to the server, and the server will turn on the DND function. Then any calls to the extension will be rejected by the server automatically. And the incoming call record will not be displayed in the Call History. |
| DND Off Code | Set the DND Off Code, When you press the DND hot key, the phone will send a message to the server, and the server will turn off the DND function. |
| Always CFwd On Code | Set the Always CFW On Code, when you choose to enable the always forward function on your phone, it will send message to the server, and the server will turn on the function immediately. When there are calls to the extension, the server will always forward it to the set number automatically. And the IP phone will not show the record in the call history anymore. |
| Always CFwd Off Code | Set the Always CFW Off Code, when you choose to disable the always forward function on your phone, it will send message to the server, and the server will turn off the function immediately. |
| Busy CFwd On Code | Set the Busy CFW On Code, when you choose to enable the busy forward function v on your phone, it will send message to the server, and the server will turn on the function immediately. When there are calls to the extension, the server will forward it to the set number automatically based the forward type. And the IP phone will not show the record in the call history anymore. |
| Busy CFwd Off Code | Set the Busy CFW Off Code, when you choose to disable the busy forward function on your phone, it will send message to the server, and the server will turn off the function immediately. |
| No Ans. CFwd On Code | Set the No Answer CFW On Code, when you choose to enable the on answer forward function on your phone, it will send message to the server, and the server will turn on the function immediately. When there are calls to the extension, the server will forward it to the set number automatically based the forward type. And the IP phone will not show the record in the call history anymore. |
| No Ans. CFwd Off Code | Set the No Answer CFW Off Code, when you choose to disable the busy forward function on your phone, it will send message to the server, and the server will turn off the function immediately. |
| Anonymous On Code | Set the Anonymous On Code, When you choose to enable the anonymous call function on your IP phone, it will send information to the server, and the server will enable the anonymous call function for your IP phone automatically. |
| Anonymous Off Code | Set the Anonymous Off Code, When you choose to disable the anonymous call function on your IP phone, it will send information to the server, and the server will disable the anonymous call function for your IP phone automatically. |
| Keep Alive Type | Specify the keep alive type, if the type is option, the phone will send option sip message to server every NAT Keep Alive Period(s), then the server responses with 200 to keep alive.If the type is UDP, the phone will send UDP message to server to keep alive every NAT Keep Alive Period(s). |
| Keep Alive Interval | Set examining interval of the server, default is 60 seconds |
| User Agent | Set the user agent if have, the default is VoIP Phone 1.0 |
| DTMF Mode | Select DTMF sending mode, there are three modes: ● DTMF_RELAY ● DTMF_RFC2833 ● DTMF_SIP_INFO Different VoIP Service providers may provide different modes. |
| Local port | Set sip port of each line |
| Ring type | Set ring type of each line |
| Enable Rport | Enable/Disable system to support RFC3581. Via rport is special way to realize SIP NAT. |
| Enable PRACK | Enable or disable SIP PRACK function, suggest use the default config. |
| Long Long Contact | Set more parameters in contact field; connection with SEM server |
| Convert URI | Convert # to %23 when send the URI. |
| Dial Without Registered | Set call out by proxy without registration; |
| Ban Anonymous Call | Set to ban Anonymous Call; |
| Enable DNS SRV | Support DNS looking up with _sip. udp mode |
| Server Type | Select the special type of server which is encrypted, or has some unique requirements or call flows. |
| RFC Protocol Edition | Select SIP protocol version to adapt for the SIP server which uses the same version as you select. For example, if the server is CISCO5300, you need to change to RFC2543, else phone may not cancel call normally. System uses RFC3261 as default. |
| Transport Protocol | Set transport protocols, TCP or UDP or TLS; |
| Anonymous Call Edition | Set Anonymous call out safely; Support RFC3323 and RFC3325; |
| Keep Authentication | Enable/Disable Keep Authentication System will take the last authentication field which is passed the authentication by server to the request packet. It will decrease the server’s repeat authorization work, if it is enable. |
| Ans. With a Single Codec | Enable/Disable the function when call is incoming, phone replies SIP message with just one codec which phone supports. |
| Auto TCP | Set to use automatically TCP protocol to guarantee usability of transport as message is above 1300 byte |
| Enable Strict Proxy | Support the special sip server When phone receives the packets sent from server, phone will use the source IP address, not the address in via field. |
| Enable GRUU | Set to support GRUU |
| Enable Display name Quote | Set to make quotation mark to display name as the phone sends out signal, in order to be compatible with server. |
| Enable user=phone | Enable user=phone by selecting it, it is contained in the invite sip message, in order to be compatible with server |
| Enable Missed Call Log | Enable the missed call log by it, the phone will save the missed call log into the call history record and display the missed calls on the idle screen, or won’t save the missed call log into the call history record and display the missed calls on the idle screen. |
| Click to Talk | Set click to Talk (need practical software support). |
| Enable BLF List | Enable BLF List by selecting it, BLF list is a function which can monitor the group status, it is not one to one monitoring, but the information feedback from the sever to decide which BLF list will monitor |
| BLF List Number | Specify the BLF List Number |
| Strict Branch | Enable the Strict Branch, the value of the branch must be in the beginning of z9hG4k in via field of the invite sip message received, or the phone won’t response to the invite sip message. Notice: the deployment will become effective in all sip lines |
| Enable Group | Enable Group by selecting it, then the phone enable the sip group backup function. Notice: the deployment will become effective in all sip lines |
| Registration Failure Retry Time | Specify the registration failure retry time, if the phone register failed, the phone will register again after registration failure Retry time. Notice: the deployment will become effective in all sip lines. |

#### IAX2 CONFIG

| IAX2 Config |
| --- |
| Field name | explanation |
| Status | Shows if the phone has been registered the IAX2 server or not. |
| Server Address | Input your IAX2 server address. |
| Server Port | Set your IAX2 server port, the default is 4569. |
| Account | Input your IAX2 register account name. |
| Password | Input your IAX2 register password. |
| Phone Number | Input your assigned phone number (usually it is same you’re your IAX2 account name). |
| Local Port | Set your local sport, the default is 4569. |
| Voice Mail Number | Specify the voice mail’s number. |
| Voice Mail Text | Specify the voice mail’s name. |
| Echo Test Number | Set echo test number. If IAX2 server supports echo test,and echo test number is non- numeric, system could set an echo test number to replace the echo test text. So user can dial the numeric number to test echo voice test. This function is provided with server to make endpoint to test whether endpoint could talk through server normally. |
| Echo Test Text | Specify echo test text’s name. |
| Refresh Time | Set expire time of IAX2 server register, you can set it between 60 and 3600 seconds. |
| Enable Registration | Start to register the IAX2 server or not by selecting it or not. |
| Enable G.729AB | Enable or disable code G.729 by selecting it or not |

#### STUN CONFIG

In this web page, you can config SIP STUN.STUN: By STUN server, the phone in private network could know the type of NAT and the NAT mapping IP and port of SIP. The phone might register itself to SIP server with global IP and port to realize the device both calling and being called in private network.

| STUN |
| --- |
| Field name | explanation |
| STUN NAT Transversal | Shows STUN NAT Transverse estimation, true means STUN can penetrate NAT, while False means not. |
| Server Address | Set your SIP STUN Server IP address |
| Server Port | Set your SIP STUN Server Port |
| Binding Period | Set STUN blinding period(s). If NAT server finds that a NAT mapping is idle after time out, it will release the mapping and the system need send a STUN packet to keep the mapping effective and alive. |
| SIP Waiting Time | Specify the sip wait stun time, you can input the time depended on your network condition. |
| Choose line to set info about SIP, There are 6lines to choose. |
| Use STUN | Enable/Disable SIP STUN. |
| Notice: SIP STUN is used to realize SIP penetration to NAT. If your phone configures STUN Server IP and Port (default is 3478), and enable SIP Stun, you can use the ordinary SIP Server to realize penetration to NAT. |

#### DIAL PEER SETTING

This functionality offers you more flexible dial rule, you can refer to the following content to know how to use this dial rule. When you want to dial an IP address, the entry of IP addresses is very cumbersome, but by this functionality, you can set number 156 to replace 192.168.1.119 here.

When you want to dial a long distance call to Beijing, you need dial an area code 010 before local phone number, but you can also dial number 1 instead of 010 after we make a setting according to this dial rule. For example, you want to dial 01062213123, but you need dial only 162213123 to realize your long distance call

after you make this setting.

| DIAL PEER |
| --- |
| Field name | explanation |
| Phone number | There are two types of matching conditions: one is full matching, the other is prefix matching. In the Full matching, you need input your desired phone number in this blank, and then you need dial the phone number to realize calling to what the phone number is mapped. In the prefix matching, you need input your desired prefix number and T; then dial the prefix and a phone number to realize calling to what your prefix number is mapped. The prefix number supports at most 30 digits. |
| Destination | Set Destination address. This is optional config item. If you want to set peer to peer call, please input destination IP address or domain name. If you want to use this dial rule on SIP2 line, you need input 255.255.255.255 or 0.0.0.2 in it.SIP3 into 0.0.0.3 |
| Port | Set the Signal port, the default is 5060 for SIP. |
| Alias | Set alias. This is optional config item. If you don’t set Alias, it will show no alias. |
| Note: There are four types of aliases. |
| 1) Add: xxx, it means that you need dial xxx in front of phone number, which will reduce dialing number length. 2) All: xxx, it means that xxx will replace some phone number. 3) Del: It means that phone will delete the number with length appointed. 4) Rep: It means that phone will replace the number with length and number appointed.You can refer to the following examples of different alias application to know more how to use different aliases and this dial rule. |
| Call Mode | Select different signal protocol, SIP or IAX2 |
| Suffix | Set suffix, this is optional config item. It will show no suffix if you don’t set it. |
| Delete Length | Set delete length. This is optional config item. For example: if the delete length is 3, the phone will delete the first 3 digits then send out the rest digits. You can refer to examples of different alias application to know how to set delete length. |
| Examples of different alias application |
| Set by web | explanation | example |
|  | You need set phone number, Destination, Alias and Delete Length.Phone number is XXXT; Destination is 255.255.255.255 (0.0.0.2) and Alias is del.This means any phone No. That starts with your set phone number will be sent via SIP2 line after the first several digits of your dialed phone number are deleted according to delete length. | If you dial “93333”,the SIP2 server will receive “3333” |
|  | This setting will realize speed dial function, after you dialing the numeric key “2”, the number after all will be sent out. | When you dial “2”,the SIP1 server will receive 33334444 |
|  | The phone will automatically send out alias number adding your dialed number, if your dialed number starts with your set phone number. | When you dial“8309“, the SIP1 server will receive“07558309” |
|  | You need set Phone Number,Alias and Delete Length. Phone number is XXXT and Alias is rep: xxx If your dialed phone number starts with your set phone number, the first digits same as your set phone number will be replaced by the alias number specified and New phone number will be send out. | When you dial“0106228”, the SIP1 server will receive“86106228” |
|  | If your dialed phone number starts with your set phone number. The phone will send out your dialed phone number adding suffix number. | When you dial “147”,the SIP1 server will receive “1470011” |

### PHONE

### DSP CONGFIG

| DSP Configuration |
| --- |
| Field name | explanation |
| First Codec | The fist preferential DSP codec: G.711A/u, G.722, G.723, G.729 |
| Second Codec | The second preferential DSP codec: G.711A/u, G.722, G.723,G.729 |
| Third Codec | The third preferential DSP codec: G.711A/u, G.722, G.723, G.729 |
| Fourth Codec | The forth preferential DSP codec: G.711A/u, G.722, G.723, G.729 |
| Fifth Codec | The fifth preferential DSP codec: G.711A/u, G.722, G.723, G.729 |
| Sixth codec | The sixth preferential DSP codec: G.711A/u, G.722, G.723, G.729 |
| Handset Input Volume | Specify Input (MIC) Volume grade. |
| Speakerphone Volume | Specify Hands-free Volume grade |
| G729 Payload Length | Set G729 Payload Length |
| Onhook Time | Specify the least reflection time of Hand down, the default is 200ms. |
| Default Ring Type | Select Ring Type |
| Handset Output Volume | Specify Output (receiver) Volume grade. |
| Speakerphone volume | Specify Speakerphone Volume grade. |
| Ring Volume | Specify Ring Volume grade |
| G722 Timestamps | 160/20ms or 320/20ms is available |
| G723 Bit Rate | 5.3kb/s or 6.3kb/s is available |
| Default Ring Type | Set up the ring by default |
| Tone Standard | Select Signal Standard. |
| Enable VAD | Select it or not to enable or disable VAD. If enable VAD, G729 Payload length could not be set over 20ms. |

#### FEATURE

In this web page, you can configure Hotline, Call Transfer, Call Waiting, 3 Ways Call, Black List, white list Limit List and so on.

| Call Service |
| --- |
| Field name | explanation |
| DND (Do Not Disturb) | Select NO Disturb, the phone will reject any incoming call, the callers will be reminded by busy, but any outgoing call from the phone will work well. |
| Enable Call Transfer | Enable Call Transfer by selecting it. |
| Semi-Attended Transfer | Enable Semi-Attended Transfer by selecting it |
| Enable Auto Handdown | The phone will hang up and return to the idle automatically at hands-free mode |
| Auto Handdown Time | Specify Auto Hand down Time, the phone will hang up and return to the idle automatically after Auto Hand down Time at hands-free mode, and play dial tone Auto Hand down Time at handset mode |
| Enable Auto Redial | Enable system to redial a call automatically |
| Auto Redial Interval |  |
| Auto Redial Times |  |
| Auto Headset |  |
| Enable Intercom | Enable Intercom Mode by selecting it |
| Enable Intercom Tone | If the incoming call is intercom call, the phone plays the intercom tone |
| P2P IP Prefix | Set Prefix in peer to peer IP call. For example: what you want to dial is 192.168.1.119, If you define P2P IP Prefix as 192.168.1. you dial only #119 to reach 192.168.1.119. Default is “.”. If there is no “.” Set, it means to disable dialing IP. |
| Turn Off Power Light | Enable Turn Off Power Light by selecting it |
| Emergency Call Number | Set up an available called number if key lock is enabled |
| Enable Password Dial |  |
| Password Dial Prefix |  |
| Password Length |  |
| Enable Multi Line | Enable system without ring play |
| Ban Outgoing | If you select Ban Outgoing to enable it, and you cannot dial out any number. |
| Enable Call Waiting | Enable Call Waiting by selecting it. Then the phone reminds whether redial, when the callee is busy or rejects. if it’s ok and the phone finds out that the callee is idle by sip message, it will reminds whether redial |
| Enable 3-way Conference | Enable 3-way conference by selecting it |
| Accept Any Call | If select it, the phone will accept the call even if the called number is not belong to the phone. |
| Enable Call Completion | Enable system to redial a call via SIP automatically. |
| Enable Pre-Dial |  |
| Enable Silent Mode | Enable Mute Mode by selecting it, the phone light will red blink to remind that there is a missed call instead of playing ring tone |
| Hide DTMF |  |
| Ring From Headset |  |
| Enable Intercom Mute | Enable mute mode during the intercom call |
| Enable Intercom Barge | Enable Intercom Barge by selecting it, the phone auto answers the intercom call during a call. If the current call is intercom call, the phone will reject the second intercom call |
| DND Return Code | Specify DND Return code |
| Busy Return Code | Specify Busy Return Code |
| Reject Return Code | Specify Reject Return Code |
| Active URI Limit IP | Specify the server IP that remote control phone forcorresponding operation. |
| Push XML Server |  |
| Enable Call Waiting Tone | Select Enable call waiting tone |

#### DIAL PLAN

This phone supports 4 dial modes:

1). End with “#”: dial your desired number, and then press #.35

2). Fixed Length: the phone will intersect the number according to your specified length.

3). Time Out: After you stop dialing and waiting time out, system will send the number collected.

4). User defined: you can customize digital map rules to make dialing more flexible. It is realized by defining the prefix of phone number and number length of dialing.

In order to keep some users' secondary dialing manner when dialing the external line with PBX, phone can be added a special rule to realize it. Souser can dial a number as external line prefix and get the secondary dial tone to keep dial the external number. After finishing dialing, phone will send the prefix and external number totally to their server.

For example, there is a rule 9,xxxxxxxx in the digital map table. After dialing 9, phone will send the secondary dial tone, user may keep going dialing. After finished, phone will call the number which starts with 9; actually the number sent out is 9-digit with 9.

| Digital Map Configuration |
| --- |
| Field name | explanation |
| Press “#” to Send | Set Enable/Disable the phone ended with “#” dial. |
| Dial Fixed Length xx to Send | Specify the Fixed Length of phone ending with. |
| Send after xx second | Set the timeout of the last dial digit. The call will be sent after timeout. |
| Press # to Do Blind Transfer | Enable Blind Transfer OnHook, when executing Blind Transfer End with #, press # after inputting the number that you want to transfer, the phone will transfer the current call to the third party. |
| Blind Transfer OnHook | Enable Blind Transfer OnHook, when executing Blind Transfer,hang up after inputting the number that you want to transfer, the phone will transfer the current call to the third party. |
| Attend Transfer OnHook | Enable Attend Trans OnHook, when executing Attended Transfer,hang up after the third party answers, the phone will transfer the current call to the third party. |
| Below is user-defined digital map rule: [] Specifies a range that will match digit. May be a range, a list of ranges separated by commas, or a list of digits. * Match any single digit that is dialed. Match any arbitrary number of digits including none. Tn Indicates an additional time out period before digits are sent of n seconds in length. n is mandatory and can have a value of 0 to 9 seconds. Tn must be the last 2 characters of a dial plan. If Tn is not specified it is assumed to be T0 by default on all dial plans. |
| Cause extensions 1000-8999 to be dialed immediately Cause 8 digit numbers started with 9 to be dialed immediately Cause 911 to be dialed immediately after it is entered. Cause 99 to be dialed after 4 seconds. Cause any number started with 9911 to be dialed 4 seconds after dialing ceases. |
| Notice: End with “#”, Fixed Length, Time out and Digital Map Table can be used simultaneously, System will stop dialing and send number according to your set rules. |

#### CONTACT

| Phone Book |
| --- |
| Field name | explanation |
| Shows the detail of current phonebook. |
| Name | Shows the name corresponding to the phone number |
| Office Number | Shows the phone number |
| Ring Type | Shows the ring type of the incoming call. |
| Notice: the maximum capability of the phonebook is 500 items, you can select many or a contact to add to group and add to blacklist, and delete many or a contact, and delete all contacts. |
| Add Contact |
| Name | Shows the name corresponding to the phone number |
| Office Number | Shows the phone number |
| Ring Type | Shows the ring type of the incoming call. |
| Notice: the add button for adding a new contact, the modify button for modifying the added contact, the clear all button for clear all input information of the contact |
| Import Contact List |
| Select File | Click the browse button to select the phonebook file that you want to import, than click update button, the phonebook file selected will be added to the phone. |
| Export Contact File |
| Export XML | Click export xml button to export phonebook file of xml model |
| Export CSV | Click export xml button to export phonebook file of csv model |
| Export VCF | Click export xml button to export phonebook file of vcf model |
| Blacklist Settings |
| Type | Select the blacklist type, you can select number or prefix of number |
| Value | Input number or prefix of number |
| Line | Select the sip line |
| Notice: the add button for adding a new blacklist, the delete button for deleting one item, the delete all button for deleting all items.If user does not want to answer some phone calls, add these phone numbers to the Black List, and these calls will be rejected.x and are wildcard x means matching any single digit. for example, 4xxx expresses any number with prefix 4 which length is 4 will be forbidden to be responded.DOT (.) means matching any arbitrary number digit. for example, 6. expresses any number with prefix 6 will be forbidden to be responded.If user wants to allow a number or a series of number incoming, he may add the number(s) to the list as the white list rule. the configuration rule is -number, for example, -123456, or -1234xx Means any incoming number is forbidden except for 4119. Note: End with DOT (.) when set up the white list |

#### REMOTE CONTACT

You need to match a XML Phonebook address and you can directly access the corresponding remote phonebook.

#### WEB DIAL

You can make a call through the WEB DIAL, enter the Dial Num then press Dial, if you want to finish the talk, press Hang-up.

### FUNTION KEY

| Function Key |
| --- |
| Field name | explanation |
| Contrast | Set contrast of screen |
| Enable Backlight | Select it |
| Line: select Auto, SIP1, SIP2, SIP3, SIP4, or IAX2 in function key type.After you set it, you pick up handset or hands-free, press this function key,and then you can use the corresponding IP line. |
| Memory key | Set the memory key's serial number |
| Type | Memory Key: settings can be stored in key storage for each number, the standby or off-hook, select the function keys on the keyboard can call this number. Line, set the dial mode (Auto, SIP1, SIP2, SIP3,SIP4, IAX2).Key Key Event functions, monitor state.DTMF：In the call, send DTMF |
| Value | Set the type parameter values |
| Line | Choose which lines to use this feature |
| Subtype | Select the function parameters Key Event |
| NOTICE： memory keys can be configured through the following:Speed Dial function, through the configuration of the key corresponding to the number of ways as shown below User can press the F1 key to allocate this number by line1 line.Push To Talk function, you can press this key in standby to automatically answer the call and make each other; |
| User can be configured in accordance with push to talk function the way: 4116 was the other number; Then press the standby button and make it automatically answer the call 4116;key can be configured through the following events:For example: |

EXT KEY

External Console has the same usage with the Function key. “In” port connects the phone, “Out” port connects the next one, if there is only, you don’t need for power supply, if there are more than one, you need supply 5V power for the first one, and use RJ-45 direct connector.

### MAINTENCE

#### AUTO PROVISION

The endpoint supports PnP and DHCP and Phone Flash to obtain the parameters. The PnP and DHCP and Phone Flash are all deployed, endpoint will go by the following process to try to obtain the server address and other parameters, when it boots up:DHCP option →PnP server →Phone Flash

| Auto Provision |
| --- |
| Field name | explanation |
| Auto Provision Settings |
| Current Config Version | Show the current config file’s version. If the version of the configuration downloaded is higher than the version of the running configurations, the auto provision would upgrade, or stop here. If the endpoints confirm the configuration by Digest method, the endpoints wouldn’t upgrade configuration unless the configuration in the server is different with the running configuration. |
| Common Config Version | Show the common config file’s version. If the configuration downloaded and the running configurations are the same, the auto 40 provision would stop here. If the endpoints confirm the configuration by Digest method, the endpoints wouldn’t upgrade configuration unless the configuration in the server is different with the running configuration. |
| User | Set FTP/HTTP/HTTPS server Username. System will use anonymous if username keep blank. |
| Password | Set FTP/HTTP/HTTPS server Password. |
| Config Encrypt Key | Input the Encrypt Key, if the configuration file is encrypted. |
| Common Config Encrypt Key | Input the Common Encrypt Key, if the Common Configuration file is encrypted. |
| Save Auto Provision Information | When you finished the settings,you must select it to save. |
| DHCP Option Settings |
| DHCP Option Setting | Specify DHCP Option. DHCP option supports DHCP custom option and DHCP option 66 and DHCP option 43 to obtain the parameters. You could choose one method among them，the default is DHCP option disable. |
| Custom DHCP Option | A valid Custom DHCP Option is from 128 to 254. The Custom DHCP Option must be in accordance with the one defined in the DHCP server. |
| Plug and Play Settings |
| Enable PnP | Enable PnP by selecting it, than the phone will send SIP SUBSCRIBE messages to a multicast address when it boots up.Any SIP server understanding that message will reply with a SIP NOTIFY message containing the Auto Provisioning Server URL where the phones can request their configuration. |
| PnP Server | Specify the PnP Server |
| PnP Port | Specify the PnP Server |
| PnP Transport | Specify the PnP Transfer protocol |
| PnP Interval | Specify the Interval time, unit is hour |
| Phone Flash Settings |
| Server Address | Set FTP/TFTP/HTTP server IP address for auto update. The address can be IP address or Domain name with subdirectory. |
| Protocol Type | Specify the Protocol type FTP、TFTP or HTTP. |
| Config File Name | Set configuration file’s name which need to update. System will use MAC as config file name if config file name keep blank. For example, 000102030405. |
| Update Interval | Specify update interval time, unit is hour. |
| Update Mode | Different update modes: 1. Disable: means no update 2. Update after reboot: means update after reboot. 3. Update at time interval: means periodic update. |

#### SYSLOG CONFIG

Syslog is a protocol which is used to record the log messages with client/server mechanism. Syslog server receives the messages from clients, and classifies them based on priority and type. Then these messages will be written into log by some rules which administrator can configure. This is a better way for log management.

8 levels in debug information:

Level 0---emergency: This is highest default debug info level. You system can not work.

Level 1---alert: Your system has deadly problem.

Level 2---critical: Your system has serious problem.

Level 3---error: The error will affect your system working.

Level 4---warning: There are some potential dangers. But your system can work.

Level 5---notice: Your system works well in special condition, but you need to check its working

environment and parameter.

Level 6---info: the daily debugging info.

Level 7---debug: the lowest debug info. Output debugging information for R&D person.

At present, the lowest level of debug information send to Syslog is info; debug level only can be displayed on telnet.

| Syslog Configuration |
| --- |
| Field name | explanation |
| Syslog Settings |
| Server IP | Set Syslog server IP address. |
| Server Port | Set Syslog server port. |
| MGR Log Level | Set the level of MGR log. |
| SIP Log Level | Set the level of SIP log. |
| IAX2 Log Level | Set the level of IAX2 log. |
| Enable Syslog | Select it or not to enable or disable syslog. |
| Web Capture |
| Start | Click the start button when you need capture the WAN packet stream of the phone, then open or save the file as the interface. |
| Stop | Click the end button to stop capturing the packet stream |

#### CONFIG SETTING

| Config Setting |
| --- |
| Field name | explanation |
| Save Configuration | You can save all changes of configurations. Click the Save button, all changes of configuration will be saved, and be effective immediately. |
| Backup Configuration | Right clicks on “Right click here…” and select “Save Target As config File(.txt)” then you will save the config file in .txt format, or select “Save Target As config File(.xml)” then you will save the config file in .xml format |
| Clear Configuration | User can restore factory default configuration and reboot the phone. If you login as Admin, the phone will reset all configurations and restore factory default; if you login as Guest, the phone will reset all configurations except for VoIP accounts (SIP1-4 and IAX2) and version number. |

#### UPDATE

| Update |
| --- |
| Field name | explanation |
| Web Update | Click the browse button, find out the config file saved before or provided by manufacturer, download it to the phone directly, press “Update” to save. You can also update downloaded update file, logo picture, ring, mmiset file by web. |
| Server Address | Set the FTP/TFTP server address for download/upload. The address can be IP address or Domain name with subdirectory. |
| User | Set the FTP server Username for download/upload. |
| Password | Set the FTP server password for download/upload. |
| File name | Set the name of update file or config file. The default name is the MAC of the phone, such as 000102030405. |
| Notice:You can modify the exported config file. And you can also download config file which includes several modules that need to be imported. For example, you can download a config file just keep with SIP module. After reboot, other modules of system still use previous setting and are not lost. |
| Type | Action type that system want to execute： 1. Application update: download system update file 2. Config file export: Upload the config file to FTP/TFTP server, name and save it. 3. Config fie import: Download the config file to phone from 43 FTP/TFTP server. The configuration will be effective after the phone is reset. 4. Phone book export (.vcf, .csv, .xml): Upload the phonebook file to FTP/TFTP server, name and save it. 5. PhoneBook import (.vcf, .csv, .xml): Download the phonebook file to phone from FTP/TFTP server. |
| Protocol | Select FTP/TFTP server |

#### ACCESS

You can add or delete user account, and change the authority of each user account in this web

page.

| Access Configuration |
| --- |
| Field name | explanation |
| LCD Menu Password Settings | Set the password for entering the setting menu of the phone by the phone’s key board. The password is digit. |
| Keylock settings | Set up the key lock password. It must be digit and no longer than 6. |
| Enable keyboard lock | Enable or disable keylock function. |
| This table shows the current user existed. |
| User | Set account user name. |
| User Level | Set user level, Root user has the right to modify configuration,General can only read. |
| Password | Set the password. |
| Confirm | Confirm the password. |
| Select the account and click the Modify to modify the selected account, and click the Delete to delete the selected account.General user only can add the user whose level is General. |

#### REBOOT

If you modified some configurations which need the phone’s reboot to be effective, you need click the Reboot, then the phone will reboot immediately.

Notice: Before reboot, you need confirm that you have saved all configurations.

### SECURITY

#### WEB FILTER

| MMI Filter |
| --- |
| User could make some device own IP, which is pre-specified, access to the MMI of the phone to config and manage the phone. |
| Field name | explanation |
| MMI Filter IP Table list: |
| Add or delete the IP address segments that access to the phone.Set initial IP address in the Start IP column, Set end IP address in the End IP column, and click Add to add this IP segment. You can also click Delete to delete the selected IP segment. |
| Enable Web Filter | Select it or not to enable or disable MMI Filter. Click Apply to make it effective. |
| Notice: Do not set your visiting IP outside the MMI filter range; otherwise, you can not logon through the web. |

#### FIREWALL

| Firewall Configuration |
| --- |
| In this web interface, you can set up firewall to prevent unauthorized Internet users from accessing private networks connected to the Internet (input rule), or prevent unauthorized private network devices from accessing the Internet (output rule).Firewall supports two types of rules: input access rule and output access rule. Each type supports at most 10 items. Through this web page, you could set up and enable/disable firewall with input/output rules. System could prevent unauthorized access, or access other networks set in rules for security. Firewall, is also called access list, is a simple implementation of a Cisco-like access list (firewall). It supports two access lists: one for filtering input packets, and the other for filtering output packets. Each kind of list could be added 10 items.We will give you an instance for your reference. |
| Field name | explanation |
| Enable Input Rules | Select it to Enable in_ access rule |
| Enable Output Rules | Select it to Enable out_ access rule |
| Input/Output | Specify current adding rule by selecting input rule or output rule. |
| Deny/Permit | Specify current adding rule by selecting Deny rule or Permit rule. |
| Protocol | Filter protocol type. You can select TCP, UDP, ICMP, or IP. |
| Port Range | Set the filter Port range |
| Src Address | Set source address. It can be single IP address, network address, complete address 0.0.0.0, or network address similar to *.*.*.0 |
| Dest Address | Set the destination address. It can be IP address, network address, complete address 0.0.0.0, or network address similar to *.*.*.* |
| Src Mask | Set the source address’ mask. For example, 255.255.255.255 means just point to one host; 255.255.255.0 means point to a network 47 which network ID is C type. |
| Dest Mask | Set the destination address’ mask. For example, 255.255.255.255 means just point to one host; 255.255.255.0 means point to a network which network ID is C type. |
| Click the Add button if you want to add a new output rule. Then enable out access, and click the Apply button.So when devices execute to ping 192.168.1.118, system will deny the request to send icmp request to 192.168.1.118 for the out access rule. But if devices ping other devices which network ID is 192.168.1.0, it will be normal. |
| Click the Delete button to delete the selected rule. |

#### NAT CONFIG

NAT is abbreviated from Net Address Translation; it’s a protocol responsible for IP address translation. In other word, it is responsible for transforming IP and port of private network to public, also is the IP address mapping which we usually say.

DMZ CONFIG：

In order to make some intranet equipments support better service for extranet,and make internal network security more effectively, these equipments open to extranet need be separated from the other equipments not open to extranet by the corresponding isolation method according to different demands. We can provide the different security level protection in terms of the different resources by building a DMZ region which can provide the network level protection for the equipments environment, reduce the risk which is caused by providing service to distrust customer, and is the best position to put public information The following chart describes the network access control of DMZ.

| NAT Configuration |
| --- |
| Field name | explanation |
| IPSec ALG | It is an encryption technology. Select it to enable IPSec ALG, the default is enable |
| FTP ALG | FTP is a service of connection layer which can transform intranet IP into extranet IP when intranet IP is sending out packet.Select it to enable FTP ALG, the default is enable |
| PPTP ALG | Select it enable PPTP ALG, the default is enable |
| Shows the NAT TCP mapping table |
| Shows the NAT UDP mapping table |
| Transfer Type | Select the NAT mapping protocol style, TCP or UDP |
| Inside IP | Set the IP address of device which is connected to LAN interface to do NAT mapping. |
| Inside Port | Set the LAN port of the NAT mapping |
| Outside Port | Set the WAN port of the NAT mapping |
| Notice: After finish setting, click the Add button to add new mapping table;click the Delete button to delete the selected mapping table. |
| Shows the outside WAN port IP address and the inside LAN port IP address. |
| Outside IP | Set the outside Wan port IP address of DMZ. |
| Inside IP | Set the inside LAN port IP address of DMZ. |
| Click the Add button to add new table; click the Delete button to delete the selected mapping table. |
| Notice: 10M/100M adaptive means the network card, and other equipment physical consultations speed, testing speed under bridge mode near to 100M,in order to ensure the quality of voice and communications real-time performance, we made some sacrifices of NAT under the transmission performance. Transmit with full capability only when system is idle, so cannot guarantee that the transmission speed reach to 100M. |

#### VPN CONFIG

This web page provides us a safe connect mode by which we can make remote access to enterprise inner network from public network. That is to say, you can set it to connect public networks in different areas into inner network via a special tunnel.

| VPN Configuration |
| --- |
| Field name | explanation |
| Virtual Private Network (VPN) Status | Shows the current VPN IP address |
| Select OpenVPN. You can choose only one for current state. After you select it,you’d better save configuration and reboot your phone. |
| VPN Server Addr | Set VPN L2TP Server IP address |
| VPN User Name | Set User Name access to VPN L2TP Server |
| VPN Password | Set Password access to VPN L2TP Server |

#### Config Security

### Logout

Click Logout，and you will exit web page. If you want to enter it next time, you need input user name and password again.

# APPENDIX

## HIGHLIGHTS

Large LCD with 5 lines display, Multi-languages

2 SIP accounts,1 IAX2 account

HD voice

BLF, DND

Auto provisioning, Headset, Wall mountable

PoE(optional)

## FEATURES

Multi Languages

Flexible Dial Map: Fix length; End with #; Dial with time out

9 Selectable ringers, 2 user-defined ringers; Volume control

Speakerphone

5 Speed dial keys with BLF option

2 SIP account

Black list for reject authenticated call

Reject incoming call

Limit dialing out No. list

Direct IP call without SIP proxy

Call Forward, Call Hold, Call Waiting, Call Return

Call Transfer(blind/semi-attended/attended)

3 Way conference

Phone book store quantity: 500 entries

Call Log (100 for each): dialed call, received call and missed call

## SPECIFICATIONS & NETWORK STANDARDS

### SIP PROTOCAL SPEC

RFC Protocol E dition: RFC3261 and RFC2543

Compatible with all major SIP Servers:Cisco, Osip,Vocal, ser,

DTMF Mode: RFC2833, RELAY , SIP INFO

Server authentication m ode: none, basic, MD5

DNS name of SIP server

SIP signaling port setting

NAT traverse, STUN

NAT traverse, SIP Express router

Pubic Server/ Private server

Dual back- up server

### DSP SPEC

Codec: G.71 1A/u, G.723.1(5.3k/6.3k), G.729a/b,G.722,G.726

G.168 echo cancel

Full duplex hand-free

VAD (Voice Activity Detection)

CNG (Comfortable Noise Generation)

AEC (Acoustic Echo Cancellation)

Adaptive voice jitter buffer

Codec negotiation supported for fixed and dynamic

### HARDWARE SPEC

32-bit 150MHz MIPS CPU

16-bit 100MHz DSP

4MB flash memory

16MB SDARM

128x64 pixel graphic LCD

LCD backlight: white (option)

34 keys, 12 LEDs

WAN: 10/100M RJ45

LAN: 10/100M RJ45

### NETWORK STANDARDS

WAN/LAN port with Router or Bridge Mode

NAT ALG

PPPoE for xDSL, automatically keep alive

DHCP Client on WAN

DHCP Server on LAN

DNS client with 2 servers IP

SNTP

RTP: RFC3550

802.1P QOS

## OTHER SPEC & PHYSICAL & ENVIRONMENTAL

### OTHER SPEC

Boot Monitor

Upgrade firmware through POST mode

Keyboard Configuration

HTTP Web-Based Configuration

FTP,TFTP upgrade firmware

WEB upgrade firmware(HTTP)

FTP, TFTP, HTTP upload/download configuration file

### PHYSICAL & ENVIRONMENTAL

Desktop / Wall mounting

Power Input: 100 to 240 ACV ;

50/60Hz Output:5 DCV 800mA

Dimensions: 210 x 170 x 45 mm

Weight: 680g (base unit & handset)

Operating Temperature: 0 C to +40 C

Storage Temperature:-20 Cto +70 C

Humidity: 5%-95% non-condensing

## MAINTENANCE AND MANAGEMENT

● The phone supports post mode, can update firmware by post mode.

● Supports different levels of administration.

● Support Boot Monitor

● Can upgrade firmware through boot monitor

● access with different authority

● support auto provisioning

● Can config through Web, Keypad, Telnet

● Can upgrade firmware and configuration file through HTTP, FTP, TFTP

● Support syslog8.6 DIGIT-CHARACTER MAP TABLE

8.6 DIGIT-CHARACTER MAP TABLE

| Keypad | Character | Keypad | Character |
| --- | --- | --- | --- |
|  | 1 |  | 7pqrs |
|  | 2abc |  | 8tuv |
|  | 3def |  | 9wxyz |
|  | 4ghi |  | * |
|  | 5jkl |  | 0 |
|  | 6mno |  | # |