POST UPDATE

Part one: boot file ungrade

1.configure PC with below IP address:

- configure FTP server

- copy boot file to location of FTP:

- connect IP phone WAN port to PC，and set phone to POST mode:

(press and hold key #, then connect power adaptor to phone)

- on PC run windows command:

- Via Telnet to update new boot file.

steps：

- input 0

- input password

- input FTP server address

- input new boot file name

- input FTP user name

- input FTP password

While new boot file upgraded successfully:

Part two: new Firmware upgrade

While done, reboot unit